| Air Pollution Source Inspection Report Form Florida Department of Environmental Protection, Southwest District | PAGE 1 OF 1 |
| --- | --- |
| FACILITY: American Fiberglass Pools dba Pettit Pools | ID#: 1010351-004-AO |
|  | COUNTY: Pasco |
| ADDRESS: 7110 21st Street E. Sarasota, FL 34243 | INSPECTION DATE: 09/24/2009 |
|  | TIME IN: 1108 | TIME OUT: 1258 |
| CONTACT: Robert Donaldson (Owner) Off:727-847-7665 Cell: 727-457-9301 | INSPECTION TYPE: FCE/INS2 |
|  | EU(s) INSPECTED: EU 001 |
| SOURCE DESCRIPTION: Fiberglass Pool Manufacturing Facility. | CURRENT PERMIT: 1010351-004-AO |
|  | PERMIT EXPIRATION DATE: 10/01/2013 |
| INSPECTION FINDINGS |
| On September 24, 2009 Joseph V. Panetta performed a Full Compliance Evaluation inspection in order to determine this facility’s compliance with its current air permit. Mr. Robert Donaldson from American Fiberglass Pools accompanied me through the inspection. The facility was not operating at the time of inspection. Only two office personnel and the owner were on site. American Fiberglass Pools manufactures fiberglass pools and is regulated for styrene, HAPs and VOC emissions. This facility utilizes “Flow Coater” application system, which results in low styrene emissions. Styrene emissions established for this facility is 9.75 tons in any consecutive 12 month period. The styrene emissions ending for August 2009 is 0.67 tons for that consecutive 12 month period. Individual HAP emissions (other than styrene) shall not exceed 2.0 tons in any consecutive 12 month period and the individual HAP emissions (other than styrene) ending for August 2009 are 0.02 tons for that consecutive 12 month period. Total combined emissions of all VOCs shall not exceed 24.0 tons in any consecutive 12 month period and total combined emissions of all VOCs ending for August 2009 are 0.96 tons for that consecutive 12 month period. By these reported emissions the facility is well under the permit allowable limits. Three years of records were available for review at facility. MSDS sheets were available for each compound used. The filter for the exhaust fan was not on the fan. Again the facility and the fan were not operating. Owner knows to use filter in the exhaust fan when in operation. All equipment, pipes, hoses, lids, fittings, etc., seemed to be operated, maintained and stored in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials. Talked with Mr. Donaldson about performing the mixing and blending operations with vessel lids in place to limit emissions; Talked with Mr. Donaldson about tightly covering or closing all VOC and/or solvent containing vessels, drums, totes, etc., when they are not in use; Talked with Mr. Donaldson about immediately confining and cleaning up VOC and/or solvent spills, and making sure waste materials are placed in closed containers for reuse, recycling or proper disposal; and used cleanup solvents shall be captured and stored in closed containers, recycled or disposed of as required by the appropriate waste disposal regulations. All VOC and or solvent containing vessels, drums, totes, etc are tightly closed when not in use. Used solvents are captured and stored in a closed red metal container and are ready for pick up from an approved disposal source. Seems reasonable precautions are taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320, F.A.C. |
| COMPLIANCE STATUS: IN |
| INSPECTOR’S SIGNATURE: ________________________________ | INSPECTOR’S NAME: Joseph V. Panetta | DATE: 10/05/2009 |