| 1030026 88764 |
| --- |
| FACILITY: Ajax Paving Industries of Florida, LLC | PERMIT ID: 3556 |
| Largo Facility - Plant 7 | DISTRICT: Southwest |
| ADDRESS: 1550 Starkey Road | CONTACT PHONE: |
| Largo, FL | 727-584-3329 |
| ARMS NO: 1030026 004 | PERMIT NO: | Expiration Date: 4/27/16 Renewal Date: 2/27/16 |
|  | 1030026-012-AC & 1030026-009-AO |  |
|  |  | Test Due Date: 1/10/00 |
| EMISSION UNIT DESCRIPTION : Portable RAP crushing may be owned by a different company. Powered by an exempt 450 HP (max) diesel engine, max heat input 3.2 MMBtu/hr; exempt power generator - max heat input rate of 1.0 MMBtu/hr. Fired on No. 2 fuel oil (max sulfur 0.5% by weight) |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | April 23, 2014 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: I met on site with Mr. Sindelarand Kyle Holmes |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Vince L. Hafeli? |  | Yes |  | No |
|  | Comments: yes, still RO The Responsible Official/Authorized Representative’s e-mail is: vhafeli@ajaxpaving.com |
| 4. | Is the facility contact still: Vince L. Hafeli or Klye Holmes? |  | Yes |  | No |
|  | Comments: These are the correct contacts The facility contact’s e-mail is: vhafeli@ajaxpaving.com? |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: This permit became effective on 3/12/13 to modify the Portable RAP Crushing System (EU 004). 8. Application for Non-Title V Air Operation Permit - This permit authorizes modification of the permitted emissions units and initial operation to determine compliance with Department rules. A Non-Title V air operation permit is required for continued operation of the permitted emissions unit. The permittee shall apply for a Non-Title V air operation permit at least 90 days prior to expiration of this permit, but no later than 180 days after commencing operation or commencing operation as modified. Commencing operation means setting into operation of any emissions unit for any purpose. Comments: Expiration date of this permit is 4/27/16. This is not applicable at this time. A.1. Federal Regulatory Requirements - a. If any affected piece(s) of equipment of a portable crushing system used at this asphalt plant is not subject to the attached Title 40, Code of Federal Regulations (CFR), Part 60, Subpart OOO – Standards of Performance for Nonmetallic Mineral Processing Plants (see Appendix E.) and the attached general provisions of 40 CFR 60, Subpart A (see Appendix F.), where applicable, then Specific Conditions A.6., A.8. - A.16., A.18. and A.19.f. do not apply. b. If any affected piece(s) of equipment of a portable crushing system used at this asphalt plant is subject to the attached Title 40, Code of Federal Regulations (CFR), Part 60, Subpart OOO – Standards of Performance for Nonmetallic Mineral Processing Plants (see Appendix E.) and the attached general provisions of 40 CFR 60, Subpart A (see Appendix F.), where applicable, then all of the following specific conditions apply. [Rule 62-4.070(3); 40 CFR 60, Subparts A and OOO] Comments: The crusher is operating under section a. A.2. Florida Air Permit Requirement - Every portable crushing system operated at this facility shall have a valid Florida Air General Permit or a non-Title V relocatable air permit. While on site, any portable crushing system is also subject to all the terms and conditions contained in this document. [Rule 62-4.070 (3) F.A.C.] Comments: This emission unit was no site and operating under permit 7775757. A.3. Authorized Materials – Following are the materials authorized to be processed through the crushing system: a. reclaimed asphalt pavement (RAP); b. concrete; c. stone; d. rock; and e. other materials with emission factors equal to or less than those in AP-42, Table 11.19.2-2. Each material must have documentation of their emission factor(s). [Rule 62-4.070(3), F.A.C.; as requested by the applicant in construction permit application received 10/09/12] Comments: This facility cannot crush items b-e without prior approval of the Board of County Commissioners, due to zoning restrictions. I observed the crushing inc unit to be crushing only a. RAP material during the inspection. A.4. Permitted Capacity - This emission unit is limited to the following operating parameters: Hours of Operation (hours/year) Maximum throughput of RAP, concrete, stone or rock (tons/any consecutive 12-month period) Unlimited (8,760) 250,000 Note - Only one portable crushing system can be operated at this site at any one time. [Rules 62-210.200 (“Potential to Emit”), F.A.C.; as requested by the applicant in construction permit application received 10/09/12] Comments: The hours of operation on site are maintained by the AJAX facility. The crushing Inc operator Mr. Sindelar gives the hours and tons of operation based on the scale meter on the crushing unit to Mr. Holmes. The hours of operation were reviewed in the facility records. The highest recorded hours of operation were based on 8 hour days as recorded in the fuel and tonnage log. The records were reviewed for April 2013 – April 2014 and the highest 12 month consecutive total was 23,166 tons during August 2013. The source is in compliance of this permit limitation. A.5. Maximum Emission Points - The crushing system located with the asphalt concrete plant shall not have more emission points and specific pieces of equipment than shown in the table below. (See Appendix G. for a flow diagram of the Portable Crushing System) Emission Point No. Brief Description 1 Hopper Loading 2 Crusher 3 Crusher to Screen Conveyor 4 Screen Conveyor to Screen 5 Screen 6 Screen to Product Conveyor 7 Product Conveyor to Transfer Conveyor 8 Transfer Conveyor to Stacker Conveyor 9 Stacker Conveyor to Pile 10 Screen to Oversize Conveyor 11 Oversize Conveyor to Hopper [Rule 62-210.200 (“Potential to Emit”), F.A.C.] Comments: I spoke with Mr. Sindelar and went over the points on site at this time, which were 1-9. The screen and its conveyor were not on site. (See photo. A.6. Visible Emissions (VE) Limitations - Each emission point associated with this emission unit shall comply with the following maximum visible emission limitations: Emission Point No. Brief Description Max.VE Limit (% Opacity)1 Max.VE Limit (% Opacity)2 Max.VE Limit (% Opacity)3 1 Hopper Loading <20* <20* <20* 2 Crusher <20* 15** 12** 3 Crusher to Screen Conveyor <20* 15** 12** 4 Screen Conveyor to Screen <20* 10** 7** 5 Screen <20* 10** 7** 6 Screen to Product Conveyor <20* 10** 7** 7 Product Conveyor to Transfer Conveyor <20* 10** 7** 8 Transfer Conveyor to Stacker Conveyor <20* 10** 7** 9 Stacker Conveyor to Pile <20* <20* <20* 10 Screen to Oversize Conveyor <20* 10** 7** 11 Oversize Conveyor to Hopper <20* 10** 7** * Rule 62-296.320(4)(b), F.A.C. ** 40 CFR 60.672(b 1 While processing non-OOO regulated materials and for crushers and affected pieces of equipment (e.g., screens) that commenced construction, modification or reconstruction on or before 8/31/1983. 2 For crushers and affected pieces of equipment (e.g., screens) that commenced construction, modification or reconstruction after 8/31/1983, but before 4/22/2008. 3 For crushers and affected pieces of equipment (e.g., screens) that commenced construction, modification or reconstruction on or after 4/22/2008. Permitting Note: Emission Point Nos. 1 and 9 do not require regular scheduled VE compliance testing, since the applicable visible emission limitation is a facility-wide limitation and there is no applicable allowable mass emission limitation. Emission points 4 & 5 and 1 & 11 are the same for visible emissions testing purposes. [Rules 62-210.200 (“Potential to Emit”) and 62-296.320(4)(b), F.A.C.; 40 CFR 60.672(b) and (c)] Comments: The crusher was observed to be in operation during the inspection of site, and there were no visible emissions of opacities noted for any of the points. This is typical of the crushing of RAP due to the nature of the product. The aggregate has been bond with asphalt, and rarely results in visible emissions. A.7. Unconfined Emissions of Particulate Matter - Unconfined emissions shall be controlled by using a water suppression system with spray bars located wherever unconfined emissions occur at the feeder, the entrance and exit of the crusher, the screen, and the conveyor drop points. [Rule 62-296.320(4)(c), F.A.C.] Comments: The water suppression system was in operation, and the yard was being wetted by the facilities water truck. The traffic for the processing of the material was operating with reduced speed to keep under control. A.8. Visible Emissions Test Requirements - In order to determine compliance with the visible emission limitations of Specific Condition No. A.6. for each crushing system that is brought on-site, the permittee shall maintain on site either documentation of the most recent* annual visible emissions test that complies with the crushing system’s General Permit or non-Title V relocatable air permit requirements prior to locating at this site (see Specific Condition A.9.) or shall test on-site according to Specific Conditions A.10. - A.12., below. [Rule 62-4.070 (3) F.A.C.] *Permitting Note: The most recent test shall not be older than the previous federal fiscal year. Comments: The annual visible emission test was performed off site in Hillsborough for this crushing unit on 1/10/13. (See test in file) The annual test for 2014 should be scheduled for prior to 9/30/14. A.9. Off-Site Test Requirements - An off-site test may be accepted by the Department provided the required documentation listed in Specific Condition A.15., below can be provided to the Compliance Authority with the test report required in Specific Condition No. A.16., below. In addition, the crushing system must have been tested while operating with the same or more emission points and equipment that will be operating while on-site. If an off-site visible emissions test is used to demonstrate compliance with Specific Condition No. A.6., the crusher shall not be operated at rates greater than 110% of the actual processing rate measured during that test. [Rule 62-4.070 (3) F.A.C.] Comments: The annual visible emission test was performed off site in Hillsborough for this crushing unit on 1/10/13. (See test in file) A.10. On-Site Test Requirements – If adequate documentation as required by Specific Condition No. A.8. is not available, the permittee shall test Emission Point Nos. 2 through 11 except 9 (as applicable) for visible emissions as soon as possible but no later than 30 days of placing the crushing system into operation after the effective date of this permit. Once tested, the crushing system may not operate in a configuration that has more pieces of equipment and/or emission points than were operating during the test unless a new compliance test is conducted with the greater number of pieces of equipment and/or emission points. In no case shall the pieces of equipment and/or emission points exceed those in Specific Condition No. A.5. In addition, the daily average crushing rate is limited to 110% of the rate at which the most recent compliance test was conducted until a new test is conducted as required by Section 5., Appendix D, No. 1. If the crusher remains on-site, the crushing system shall be tested for visible emissions annually during each federal fiscal year (October 1 – September 30) that the crushing system is on-site. [Rules 62-4.070(3) and 62-297.310 (7)(a), F.A.C.] Comments: This is not applicable at this time. The annual visible emission test was performed off site in Hillsborough for this crushing unit on 1/10/13. (See test in file) A.11. Visible Emission Testing Requirements - On-site visible emission testing shall be conducted in accordance with the applicable requirements specified in Appendix D (Common Testing Requirements) of this permit and shall also comply with the following: a. The minimum distance between the observer and the emission source shall be 15 feet. b. The observer shall, when possible, select a position that minimizes interference from other fugitive emission sources (e.g., road dust). The required observer position relative to the sun (Method 9, Section 2.1) must be followed. c. The duration of the Method 9 observations must be 30 minutes (five 6-minute averages). Compliance with Specific Condition A.6., must be based on the average of the five 6-minute averages. d. As an alternative to the Method 9 requirement to conduct visible emission observations of only one emission point at a time, a single visible emission observer may conduct visible emission observations for up to three fugitive, stack, or vent emission points within a 15-second interval if the following conditions are met: (1) No more than three emission points may be read concurrently. (2) All three emission points must be within a 70 degree viewing sector or angle in front of the observer such that the proper sun position can be maintained for all three points. (3) If an opacity reading for any one of the three emission points equals or exceeds the applicable standard, then the observer must stop taking readings for the other two points and continue reading just that single point. [Rules 62-297.310(4), and 62-297.401, F.A.C.; 40 CFR 60.675 (c) and (e)(2)] Comments: a. the test results show the observer was located from 60’ – 110’ to 200 ‘ from the emission points. b. can not be determined from test results. c. the test were all 30 minutes. d. there was not an alternate method used of visible emissions observations. (1) there was one observer for the test of this unit. there were some points which appeared to be observed at the same time during testing, but not more then two points were observed concurrently (2) The proper sun angle was met (3) The results of all test were 0% opacity A.12. Test Method - Required tests shall be performed in accordance with the following reference method. Method Description of Method and Comments 9 Visual Determination of the Opacity of Emissions from Stationary Sources The above method is described in Appendix A of 40 CFR 60 and is adopted by reference in Rule 62-204.800, F.A.C. No other method(s) may be used unless prior written approval is received from the Department. [Rules 62-204.800 and 62-297.401, F.A.C.; Appendix A-4 of 40 CFR 60] Comments: The test method 9 protocols were met according to test reviewed for the emission units. A.13. Monitoring Requirements - If any affected piece(s) of equipment of the Portable Crushing System (i.e., crusher, screen or conveyor belt) was constructed, modified, or began reconstruction on or after April 22, 2008, a monthly inspection must be performed to check that water is flowing to discharge spray nozzles of the wet suppression system. The owner or operator must initiate corrective action within 24 hours and complete corrective action as expediently as practical if water is not flowing properly during the inspection. [40 CFR 60, 60.674(b)] Comments: the crushing Inc operation and AJAX paving are monitoring and maintaining the water suppression system and yard irrigation. A.14. On-Site Test Notification - The permittee shall notify the Compliance Authority in writing at least 15 days prior to any required on-site tests. The notification must include the following information: the date, time, and location of each test; the name and telephone number of the facility’s contact person who will be responsible for coordinating the test; and the name, company, and the telephone number of the person conducting the test. Permitting Note: The notification should also include the relevant emission unit ID No(s)., test method(s) to be used, and pollutants to be tested. [Rules 62-4.070(3) and 62-297.310(7)(a)9., F.A.C.] Comments: : the responsible official of AJAX gave notification of that the crusher would be located on site for Crushing and the ARMS show notification to FDEP was received on 1/28/2013 re Gary Robbins entry. (See attached ARMS entry) A.15. On-Site Test Report Requirements - The permittee shall prepare and submit to the Compliance Authority reports for all required tests in accordance with the requirement specified in Appendix D (Common Testing Requirements) of this permit. The test report must include the following: a. owner name; b. General or non-Title V Air Operation Permit number (e.g., 7771234-XXX-AX); c. manufacturer’s maximum rated capacity for any material (i.e. the rated TPH capacity of the material with the highest processing rate); d. date each affected piece of equipment of the crushing system commenced construction, modification or reconstruction; e. type of material processed; f. actual material handling rate during the test period (tons/hour); g. configuration of the crushing system during the test to include specific pieces of equipment, emission points and/or a process flow diagram; and h. a copy of the operation logs as required by Specific Condition No. A.17. for the day and month the test was conducted. [Rules 62-4.070(3) and 62-297.310(8), F.A.C.] Comments: The method 9 tests were received from Vince Hafeli as required (See attached copies in file) A.16. Off-Site Crushing System Test Reports - When demonstrating compliance with Specific Condition A.6. with an off-site visible emissions test, the permittee shall submit a copy of the most recent VE test report for each crushing system operated on site at the same time the test report for the drum mix asphalt plant (EU 001) is submitted (see Specific Condition A.16. in Operation Permit 1030026-009-AO). If testing was not required for EU 001 (e.g., the plant was shut down), the test reports for each crushing system that operated on site shall be submitted at the end of each Federal Fiscal Year. The test reports must include the information specified in A.15. a.-g. above. [Rule 62-4.070(3) F.A.C.] Comments: The facility submitted copies of the annual VE test to PCAQ . (See test attached) A.17. Operation Records - The permittee shall record the following while the portable crushing system is on-site: Daily, when the crusher is operating: a. facility name, facility ID No., emission unit ID No., crushing system owner’s name, Florida General or non-Title V Air Permit No., and any other identification information so each crushing system can be clearly distinguished from another crushing system; b. hours of operation; c. type of material being crushed (e.g., RAP, concrete, stone and/or rock); d. total material throughput (tons); e. daily average throughput rate based on b. and c. above (tons/hour); Monthly: f. facility name, facility ID No. and emission unit ID No.; g. total material (e.g., RAP, concrete, stone and/or rock) throughput (tons); h. most recent consecutive 12-month rolling total material throughput (tons/consecutive 12-month period); i. hours of operation for the month; j. most recent consecutive 12-month rolling total hours of operation (hours/consecutive 12-month period); Daily records shall be completed within 3 business days and monthly records shall be completed by the end of the following month. [Rule 62-4.070(3), F.A.C.] Comments: The records reviewed met the conditions subparts a-e on the Crushing Inc record kept by Mr. Holmes for fuel and tonnage. The monthly records(f-j) are maintained by Mr. Hafeli. (See attached records) A.18. Monitoring Records - If any affected piece(s) of equipment of the portable crushing system was constructed, modified, or began reconstruction on or after April 22, 2008, the owner or operator must record each inspection of the water spray nozzles, including the date of each inspection and any corrective actions taken. (see also Specific Condition A.13.) [40 CFR 60, 60.674(b)] Comments: the facility has not made any modifications to the water suppression system from the tested configuration and emission points.. The water suppression nozzles with daily operation of crusher unit. (See records) A.19. General Recordkeeping Requirements - The permittee shall keep records for each portable crushing system operated on site as follows: a. owner name; b. General or non-Title V Air Operation Permit number(s) (e.g., 7771234-xxx-AX) and permit effective date(s); c. dates on site; d. manufacturer’s maximum rated capacity for any material (i.e. the rated TPH capacity of the material with the highest processing rate); e. operating configuration while on-site to include specific pieces of equipment, emission points and/or a process flow diagram; and f. date of most recent visible emissions test and a copy of the test report. [Rules 62-4.070(3), F.A.C.] Comments: The material production and fuel usage are recorded by the crushing Inc operator, and then records are kept by plant operators who forwarded to the authorized representative for maintaining. (See attached records) Appendix F. - 40 CFR 60, Subpart OOO Federal Regulations Adopted by Reference § 60.672 Standard for particulate matter (PM). (b) Affected facilities must meet the fugitive emission limits and compliance requirements in Table 3 of this subpart within 60 days after achieving the maximum production rate at which the affected facility will be operated, but not later than 180 days after initial startup as required under §60.11. The requirements in Table 3 of this subpart apply for fugitive emissions from affected facilities without capture systems and for fugitive emissions escaping capture systems. (d) Truck dumping of nonmetallic minerals into any screening operation, feed hopper, or crusher is exempt from the requirements of this section. Table 3 to Subpart OOO—Fugitive Emission Limits For *** The owner or operator must meet the following fugitive emissions limit for grinding mills, screening operations, bucket elevators, transfer points on belt conveyors, bagging operations, storage bins, enclosed truck or railcar loading stations or from any other affected facility (as defined in §§60.670 and 60.671) * * * The owner or operator must meet the following fugitive emissions limit for crushers at which a capture system is not used * * * The owner or operator must demonstrate compliance with these limits by conducting * * * Affected facilities (as defined in §§60.670 and 60.671) that commenced construction, modification, or reconstruction after August 31, 1983 but before April 22, 2008 10 percent opacity 15 percent opacity An initial performance test according to §60.11 of this part and §60.675 of this subpart. Comments: the crushing inc crusher while operating on the AJAX paving facility is taking reasonable precautions to reduce fugitive emissions. The AJAX water truck is wetting the construction yard to reduce unconfined emissions. § 60.673 Reconstruction. (a) The cost of replacement of ore-contact surfaces on processing equipment shall not be considered in calculating either the “fixed capital cost of the new components” or the “fixed capital cost that would be required to construct a comparable new facility” under §60.15. Ore-contact surfaces are crushing surfaces; screen meshes, bars, and plates; conveyor belts; and elevator buckets. (b) Under §60.15, the “fixed capital cost of the new components” includes the fixed capital cost of all depreciable components (except components specified in paragraph (a) of this section) which are or will be replaced pursuant to all continuous programs of component replacement commenced within any 2-year period following August 31, 1983. Comments: There is no proposed reconstruction at this time. § 60.675 Test methods and procedures. (a) In conducting the performance tests required in §60.8, the owner or operator shall use as reference methods and procedures the test methods in appendices A–1 through A–7 of this part or other methods and procedures as specified in this section, except as provided in §60.8(b). Acceptable alternative methods and procedures are given in paragraph (e) of this section. (c) (1) In determining compliance with the particulate matter standards in §60.672(b) or §60.672(e)(1), the owner or operator shall use Method 9 of Appendix A–4 of this part and the procedures in §60.11, with the following additions: (i) The minimum distance between the observer and the emission source shall be 4.57 meters (15 feet). (ii) The observer shall, when possible, select a position that minimizes interference from other fugitive emission sources ( e.g., road dust). The required observer position relative to the sun (Method 9 of Appendix A–4 of this part, Section 2.1) must be followed. (iii) For affected facilities using wet dust suppression for particulate matter control, a visible mist is sometimes generated by the spray. The water mist must not be confused with particulate matter emissions and is not to be considered a visible emission. When a water mist of this nature is present, the observation of emissions is to be made at a point in the plume where the mist is no longer visible. (3) When determining compliance with the fugitive emissions standard for any affected facility described under §60.672(b) or §60.672(e)(1) of this subpart, the duration of the Method 9 (40 CFR part 60, Appendix A–4) observations must be 30 minutes (five 6-minute averages). Compliance with the applicable fugitive emission limits in Table 3 of this subpart must be based on the average of the five 6-minute averages. (e) The owner or operator may use the following as alternatives to the reference methods and procedures specified in this section: (2) A single visible emission observer may conduct visible emission observations for up to three fugitive, stack, or vent emission points within a 15-second interval if the following conditions are met: (i) No more than three emission points may be read concurrently. (ii) All three emission points must be within a 70 degree viewing sector or angle in front of the observer such that the proper sun position can be maintained for all three points. (iii) If an opacity reading for any one of the three emission points equals or exceeds the applicable standard, then the observer must stop taking readings for the other two points and continue reading just that single point. (g) For performance tests involving only Method 9 (40 CFR part 60 Appendix A–4) testing, the owner or operator may reduce the 30-day advance notification of performance test in §60.7(a)(6) and 60.8(d) to a 7-day advance notification. Comments: the testing of the crusher emission units and assigned emission points were tested as required under the Method 9 requirements. An alternate test method was not used for the Crusher inc 7775757 VE tests. The test results show the observer was located from 60’ – 110’ to 200 ‘from the emission points. the test were all 30 minutes. There was one observer for the test of this unit. Some points were observed at the same time during testing, but not more than two points were observed concurrently. The proper sun angle was met, The results of all tests were 0% opacity. § 60.676 Reporting and recordkeeping. (f) The owner or operator of any affected facility shall submit written reports of the results of all performance tests conducted to demonstrate compliance with the standards set forth in §60.672 of this subpart, including reports of opacity observations made using Method 9 (40 CFR part 60, Appendix A–4) to demonstrate compliance with §60.672(b), (e) and (f). (g) The owner or operator of any wet material processing operation that processes saturated and subsequently processes unsaturated materials, shall submit a report of this change within 30 days following such change. At the time of such change, this screening operation, bucket elevator, or belt conveyor becomes subject to the applicable opacity limit in §60.672(b) and the emission test requirements of §60.11. (h) The subpart A requirement under §60.7(a)(1) for notification of the date construction or reconstruction commenced is waived for affected facilities under this subpart. (i) A notification of the actual date of initial startup of each affected facility shall be submitted to the Administrator. (1) For a combination of affected facilities in a production line that begin actual initial startup on the same day, a single notification of startup may be submitted by the owner or operator to the Administrator. The notification shall be postmarked within 15 days after such date and shall include a description of each affected facility, equipment manufacturer, and serial number of the equipment, if available. (2) For portable aggregate processing plants, the notification of the actual date of initial startup shall include both the home office and the current address or location of the portable plant. (j) The requirements of this section remain in force until and unless the Agency, in delegating enforcement authority to a State under section 111(c) of the Act, approves reporting requirements or an alternative means of compliance surveillance adopted by such States. In that event, affected facilities within the State will be relieved of the obligation to comply with the reporting requirements of this section, provided that they comply with requirements established by the State. (k) Notifications and reports required under this subpart and under subpart A of this part to demonstrate compliance with this subpart need only to be sent to the EPA Region or the State which has been delegated authority according to §60.4(b). Comments: The AJAX Paving submitted the performance Method 9 tests for the crusher emission unit under 7775757 GP, on 1/26/13 by email. The tests demonstrated operating at 0% opacities and under the opacity limitations of the permit requirements. There have been no changes to the water suppression system, is in use during operations on site. Gary Robbins received the notification for the start up on 1/28/13. 40 CFR Part 60, Subpart A - General Provisions § 60.7 Notification and record keeping. (a) Any owner or operator subject to the provisions of this part shall furnish the Administrator written notification or, if acceptable to both the Administrator and the owner or operator of a source, electronic notification, as follows: (3) A notification of the actual date of initial startup of an affected facility postmarked within 15 days after such date. (4) A notification of any physical or operational change to an existing facility which may increase the emission rate of any air pollutant to which a standard applies, unless that change is specifically exempted under an applicable subpart or in §60.14(e). This notice shall be postmarked 60 days or as soon as practicable before the change is commenced and shall include information describing the precise nature of the change, present and proposed emission control systems, productive capacity of the facility before and after the change, and the expected completion date of the change. The Administrator may request additional relevant information subsequent to this notice. § 60.8 Performance tests. (b) Performance tests shall be conducted and data reduced in accordance with the test methods and procedures contained in each applicable subpart unless the Administrator (1) specifies or approves, in specific cases, the use of a reference method with minor changes in methodology, (2) approves the use of an equivalent method, (3) approves the use of an alternative method the results of which he has determined to be adequate for indicating whether a specific source is in compliance, (4) waives the requirement for performance tests because the owner or operator of a source has demonstrated by other means to the Administrator's satisfaction that the affected facility is in compliance with the standard, or (5) approves shorter sampling times and smaller sample volumes when necessitated by process variables or other factors. Nothing in this paragraph shall be construed to abrogate the Administrator's authority to require testing under section 114 of the Act. (c) Performance tests shall be conducted under such conditions as the Administrator shall specify to the plant operator based on representative performance of the affected facility. The owner or operator shall make available to the Administrator such records as may be necessary to determine the conditions of the performance tests. Operations during periods of startup, shutdown, and malfunction shall not constitute representative conditions for the purpose of a performance test nor shall emissions in excess of the level of the applicable emission limit during periods of startup, shutdown, and malfunction be considered a violation of the applicable emission limit unless otherwise specified in the applicable standard. (d) The owner or operator of an affected facility shall provide the Administrator at least 30 7 days prior notice of any performance test, except as specified under other subparts, to afford the Administrator the opportunity to have an observer present. If after 30 days notice for an initially scheduled performance test, there is a delay (due to operational problems, etc.) in conducting the scheduled performance test, the owner or operator of an affected facility shall notify the Administrator (or delegated State or local agency) as soon as possible of any delay in the original test date, either by providing at least 7 days prior notice of the rescheduled date of the performance test, or by arranging a rescheduled date with the Administrator (or delegated State or local agency) by mutual agreement. [36 FR 24877, Dec. 23, 1971, as amended at 39 FR 9314, Mar. 8, 1974; 42 FR 57126, Nov. 1, 1977; 44 FR 33612, June 11, 1979; 54 FR 6662, Feb. 14, 1989; 54 FR 21344, May 17, 1989; 64 FR 7463, Feb. 12, 1999; 72 FR 27442, May 16, 2007] Comments: Notification, recordkeeping, and performance tests were performed as required by rule and permit conditions. § 60.11 Compliance with standards and maintenance requirements. (a) Compliance with standards in this part, other than opacity standards, shall be determined in accordance with performance tests established by §60.8, unless otherwise specified in the applicable standard. (b) Compliance with opacity standards in this part shall be determined by conducting observations in accordance with Method 9 in appendix A of this part, any alternative method that is approved by the Administrator, or as provided in paragraph (e)(5) of this section. For purposes of determining initial compliance, the minimum total time of observations shall be 3 hours 30 minutes (30 6-minute averages) for the performance test or other set of observations (meaning those fugitive-type emission sources subject only to an opacity standard). (c) The opacity standards set forth in this part shall apply at all times except during periods of startup, shutdown, malfunction, and as otherwise provided in the applicable standard. (d) At all times, including periods of startup, shutdown, and malfunction, owners and operators shall, to the extent practicable, maintain and operate any affected facility including associated air pollution control equipment in a manner consistent with good air pollution control practice for minimizing emissions. Determination of whether acceptable operating and maintenance procedures are being used will be based on information available to the Administrator which may include, but is not limited to, monitoring results, opacity observations, review of operating and maintenance procedures, and inspection of the source. (e) (2) Except as provided in paragraph (e)(3) of this section, the owner or operator of an affected facility to which an opacity standard in this part applies shall conduct opacity observations in accordance with paragraph (b) of this section, shall record the opacity of emissions, and shall report to the Administrator the opacity results along with the results of the initial performance test required under §60.8. The inability of an owner or operator to secure a visible emissions observer shall not be considered a reason for not conducting the opacity observations concurrent with the initial performance test. (3) The owner or operator of an affected facility to which an opacity standard in this part applies may request the Administrator to determine and to record the opacity of emissions from the affected facility during the initial performance test and at such times as may be required. The owner or operator of the affected facility shall report the opacity results. Any request to the Administrator to determine and to record the opacity of emissions from an affected facility shall be included in the notification required in §60.7(a)(6). If, for some reason, the Administrator cannot determine and record the opacity of emissions from the affected facility during the performance test, then the provisions of paragraph (e)(1) of this section shall apply. (6) Upon receipt from an owner or operator of the written reports of the results of the performance tests required by §60.8, the opacity observation results and observer certification required by §60.11(e)(1), and the COMS results, if applicable, the Administrator will make a finding concerning compliance with opacity and other applicable standards. If COMS data results are used to comply with an opacity standard, only those results are required to be submitted along with the performance test results required by §60.8. If the Administrator finds that an affected facility is in compliance with all applicable standards for which performance tests are conducted in accordance with §60.8 of this part but during the time such performance tests are being conducted fails to meet any applicable opacity standard, he shall notify the owner or operator and advise him that he may petition the Administrator within 10 days of receipt of notification to make appropriate adjustment to the opacity standard for the affected facility. (7) The Administrator will grant such a petition upon a demonstration by the owner or operator that the affected facility and associated air pollution control equipment was operated and maintained in a manner to minimize the opacity of emissions during the performance tests; that the performance tests were performed under the conditions established by the Administrator; and that the affected facility and associated air pollution control equipment were incapable of being adjusted or operated to meet the applicable opacity standard. (8) The Administrator will establish an opacity standard for the affected facility meeting the above requirements at a level at which the source will be able, as indicated by the performance and opacity tests, to meet the opacity standard at all times during which the source is meeting the mass or concentration emission standard. The Administrator will promulgate the new opacity standard in the Federal Register. (f) Special provisions set forth under an applicable subpart shall supersede any conflicting provisions in paragraphs (a) through (e) of this section. (g) For the purpose of submitting compliance certifications or establishing whether or not a person has violated or is in violation of any standard in this part, nothing in this part shall preclude the use, including the exclusive use, of any credible evidence or information, relevant to whether a source would have been in compliance with applicable requirements if the appropriate performance or compliance test or procedure had been performed. [38 FR 28565, Oct. 15, 1973, as amended at 39 FR 39873, Nov. 12, 1974; 43 FR 8800, Mar. 3, 1978; 45 FR 23379, Apr. 4, 1980; 48 FR 48335, Oct. 18, 1983; 50 FR 53113, Dec. 27, 1985; 51 FR 1790, Jan. 15, 1986; 52 FR 9781, Mar. 26, 1987; 62 FR 8328, Feb. 24, 1997; 65 FR 61749, Oct. 17, 2000] Comments: The testing of the crusher and emission points was performed per method 9 requirements, and resulting in 0% opacity as well as observations of the crusher operations resulting in 0% opacity. The facility is meeting with the opacity standards. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: The crusher and the associated emissions points observed on site, matched the emissions points tested on 1/10/13. |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: Recycling RAP with crusher for used in plant asphalt production. |
| Closing Conference: I informed Mr. Sindelar, the crusher appeared to be operating in compliance with the facility permit, at this inspection and will finish determination pending review of the records. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: May 29, 2014 |
| ACCESS? | ( | ARMS? | ( |

Ajax Paving Industries of Florida, LLC  Largo Facility - Plant 7

1550 Starkey Road, Largo

Project Id:	88764    Permit No: 1030026-012-AC & 1030026-009-AO	Arms Number: 0026 004

Inspector:	Shea Jackson	Inspection Date / Time: 4/23/14  / _______

Source (EU):	Portable RAP crushing may be owned by a different company.  Powered by an exempt 450 HP (max) diesel engine, max heat input  3.2 MMBtu/hr; exempt power generator - max heat input rate of 1.0 MMBtu/hr.  Fired on No. 2 fuel oil (max sulfur 0.5% by weight)

# Description:	[The crusher operation was in compliance with visible emissions opacity limitations]

Ajax Paving Industries of Florida, LLC  Largo Facility - Plant 7

1550 Starkey Road, Largo

Project Id:	88764	Permit No: 1030026-012-AC & 1030026-009-AO	Arms Number: 0026 004

Inspector:	Shea Jackson	Inspection Date / Time: 4/23/14  / _______

Source (EU):	Portable RAP crushing may be owned by a different company.  Powered by an exempt 450 HP (max) diesel engine, max heat input  3.2 MMBtu/hr; exempt power generator - max heat input rate of 1.0 MMBtu/hr.  Fired on No. 2 fuel oil (max sulfur 0.5% by weight)

# Description:	[The units serial number information were located on the unit ]

Ajax Paving Industries of Florida, LLC  Largo Facility - Plant 7

1550 Starkey Road, Largo

Project Id:	88764	Permit No: 1030026-012-AC & 1030026-009-AO	Arms Number: 0026 004

Inspector:	Shea Jackson	Inspection Date / Time: 4/23/14  / _______

Source (EU):	Portable RAP crushing may be owned by a different company.  Powered by an exempt 450 HP (max) diesel engine, max heat input  3.2 MMBtu/hr; exempt power generator - max heat input rate of 1.0 MMBtu/hr.  Fired on No. 2 fuel oil (max sulfur 0.5% by weight)

# Description:	[The scale meter records the tons of RAP processed  ]

Ajax Paving Industries of Florida, LLC  Largo Facility - Plant 7

1550 Starkey Road, Largo

Project Id:	88764	Permit No: 1030026-012-AC & 1030026-009-AO	Arms Number: 0026 004

Inspector:	Shea Jackson	Inspection Date / Time: 4/23/14  / _______

Source (EU):	Portable RAP crushing may be owned by a different company.  Powered by an exempt 450 HP (max) diesel engine, max heat input  3.2 MMBtu/hr; exempt power generator - max heat input rate of 1.0 MMBtu/hr.  Fired on No. 2 fuel oil (max sulfur 0.5% by weight)

# Description:	[The diesel engine operating the crusher was observed to be operating without visible emissions]

| AIRS ID 1030026 | OWNER Ajax Paving Industries of Florida, LLC | FACILITY NAME Largo Facility - Plant 7 |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE 5/29/14 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE 9/15/12 |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | The 2013 AOR was received by FDEP 1/20/14, and PCAQ review completed on 4/24/14 |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 4/23/14 | 5/28/14 |  |  | access data base |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) | 0% passed 1/10/13 |
| DONE N/A | Review of facility records and logs | Reviewed 4/1/2013 – 4/23/14 |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) | Within 250 tons/ hour etc |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) | Water suppression system operating correctly |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  | access data base |
| Applicable requirements |  |  |  | access data base |
| Inventory of emission units |  |  |  | access data base |
| Enforcement history |  |  |  | access data base |
| Compliance activities |  |  |  | access data base |
| Findings and recommendations |  |  |  | access data base |
| COMMENTS The facility was in compliance with its permit conditions for this period |

Other Comments

Prepared by:	   Shea Jackson		Date: 		9/15/14

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record