| 1030095 002 58183 |
| --- |
| FACILITY: Bayfront Medical Center | PERMIT ID: 24 |
|  | DISTRICT: Southwest |
| ADDRESS: 750 5th Avenue South | CONTACT PHONE: |
| St. Petersburg, FL | 727-893-6825 |
| ARMS NO: 1030095 002 | PERMIT NO: | EXPIRATION DATE: |
|  | 1030095-004-AV | 3/15/12 |
| EMISSION UNIT DESCRIPTION : Hospital/Medical/Infectious Waste -Joy Energy Systems, Inc., Model 1500 TE, Serial No. 15-TE-91-20, emissions controlled by a Calvert Flux force/Condensation collision Scrubber System, Model FC. Srical No. 1280. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | 28 June 2007 |  |  | INS1 |  | INS2 |  | INS3 |  | FUI |  | IN |  | MNC |  | SNC |
| INSPECTION TYPE: |  | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: William A. Christie? |  | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Robert Fairburn? |  | Yes |  | No |
|  | Comments: An alternate contact is Mr. Horace Tomlinson. |
| IN | MNC | SNC | B. Specific Conditions: |
|  |  |  | Inspection Notes: This permit became effective on 3/15/07. The Florida Department Waste Management Section shall be responsible for conducting inspections, handling compliance issues, and enforcement matters regarding the "ITALIZED" portions of this permit. This permit or a copy thereof shall be kept at the work site of the permitted activity. [APPENDIX TV-6, TITLE V CONDITION 12(12)] Comments: The facility contacts stated that they had not received a hard copy of the renewed Title V permit , 1030095-004-AV. that now expires in 2012. Mr. Tomlinson took note of the permit number and said he will inquire with the FDEP re: the hard copy of the new permit. 2. General Pollutant Emission Limiting Standards. Objectionable Odor Prohibited. No person shall cause, suffer, allow, or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200 and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178; AC52-189392] Comments: There were mo objectionable odors associated with the waste combusted inside or outside the facility. 3. General Particulate Emission Limiting Standards. General Visible Emissions Standard. Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1. & 4., F.A.C.] A.17.a. Visible emissions shall not exceed 10 percent opacity (6-minute block average). [40 CFR 60.33e(c)]. -and- A.17.b. Visible emissions shall not exceed 5 percent opacity, except that visible emissions not exceeding 20 percent opacity are allowed up to three minutes in any one hour period. [Rule 62-296.401(1)(a), F.A.C.; AC52-189392] A.21. The opacity standards set forth in 40 CFR 60 shall apply at all times except during periods of startup, shutdown, malfunction, and as otherwise provided in the applicable standard. [40 CFR 60.11(c)] A.53. Compliance with standards in 40 CFR 60, other than opacity standards, shall be determined in accordance with performance tests established by 40 CFR 60.8, unless otherwise specified in the applicable standard. [40 CFR 60.11(a)] A.54. Compliance with opacity standards in 40 CFR 60 shall be determined by conducting observations in accordance with Reference Method 9 in Appendix A of 40 CFR 60, any alternative method that is approved by the Administrator, or as provided in 40 CFR 60.11(e)(5). [40 CFR 60.11(b)] Comments: I did not perform a Method 9 VE test but I observed the stack before entering the building and did not see any visible emissions emanating from in. 4. Prevention of Accidental Releases (Section 112(r) of CAA). If required by 40 CFR 68, the permittee shall submit to the implementing agency: A. A risk management plan (RMP) when, and if, such requirement becomes applicable; and B. Certification forms and/or RMPs according to the promulgated rule schedule. [40 CFR 68] Comments: This facility submitted the RMP with the original permit application. 6. Emission of Unconfined Particulate Matter. Pursuant to Rules 62-296.320(4)(c)1., 3., and 4., F.A.C., reasonable precautions to prevent emissions of unconfined particulate matter at this facility include the following requirements (see Condition 57. of APPENDIX TV-6, TITLE V CONDITIONS): The following requirements are "not federally enforceable": A. Paving and maintenance of roads, parking areas and yards, when necessary. B. application of water or non-hazardous chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. C. Application of water or non-hazardous chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. D. Removal of particulate matter from roads and other paved areas to prevent entrainment, and from buildings or work areas to prevent particulates from becoming airborne. E. Landscaping or planting of vegetation. F. Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. G. Confine abrasive blasting where possible. [Rule 62-293.320(4)(c)2., F.A.C.; and requested by permittee in the renewal Title V permit application dated January 9, 2006] Comments: There were mo fugitive emissions emanating from anywhere in the facility - 9. Statement of Compliance. The annual statement of compliance pursuant to Rule 62-213.440(3)(a)2., F.A.C., shall be submitted to Air Compliance Section of the Department's Southwest District Office and the EPA within 60 (sixty) days after the end of the calendar year using DEP Form No. 62-213.900(7), F.A.C. [Rules 62-213.440(3) and 62-213.900, F.A.C.] {Permitting Note: This condition implements the requirements of Rules 62-213.440(3)(a)2. and 3., F.A.C. (see Condition No. 51 of Appendix TV-6, Title V Conditions)} Comments: The facility submitted its ASOC for 2006 in February of 2007. A.1. Capacity. The burning rate (actual waste charged in any 1-hour period, which is considered as any 60- minute period) of the incinerator shall not exceed 1,500 pounds per hour. [Rules 62-4.160(2) and 62-210.200(PTE), F.A.C.; AC52-189392] Comments: The logs examined showed no exceedences of the operating rate of 1,500 lbs/hr. A.3. Methods of Operation - Fuels. The facility is allowed to burn items and materials that fit within the definition of hospital, medical and infectious waste (HMIW) contained in 40 CFR 60.51c. The only auxiliary fuel authorized to be burned in this incinerator is natural gas or propane. Solid waste that is not hospital, medical, or infectious waste may be burned unless prohibited in this permit, however this waste may not be stored in packages marked as biomedical waste. Transportation of solid waste, which is improperly labeled is a violation of USDOT Hazmat regulations under 49 CFR 172.303, 172.401, and 173.134 and OSHA regulations 29 CFR 1910.1030. [Rules 62-4.160(2), 62-4.070(3), 62-210.200, and 62-213.440(1), F.A.C.; 40 CFR 60.51c] Comments: This facility operates the incinerator on natural gas and burns only materials that fit the. Definitions of hospital medical, infectious waste. A.4. Methods of Operation - Fuels. Subject to the limitations contained in this permit, the facility shall not burn: A. those materials that are prohibited by state or federal law, B. those materials that are prohibited by this permit; C. lead acid batteries; D. ash from incineration of medical/infectious waste, once the incineration process has been completed; E. nuclear waste; F. sewage sludge; G. explosives; H. human corpses, remains, and anatomical parts that are intended for interment. [Rule 62-4.160(2), F.A.C. and 40 CFR 60.51c] A.5. Methods of Operation - Fuels. Radioactive waste may not be burned in an incinerator subject to Rule 62-296.401(4), F.A.C., unless the incinerator has been issued a Department of Health and Rehabilitative Services (DHRS) license to incinerate radioactive waste or the waste is of such quantity to be exempt in accordance with DHRS Rule 10D-91 (transferred to 64E-5) or 10D-104.003 (transferred to 64E-16), F.A.C. The permittee shall establish screening and inspection procedures to ensure that regulated hazardous wastes are not burned. [Rules 62-296.401(4)(d)(5) and 62-701.700, F.A.C.; AC52-189392] A.6. Methods of Operation - Fuels. Hazardous waste may not be burned in an incinerator subject to this rule [Rule 62-296.401, F.A.C.] unless the incinerator has been issued a hazardous waste permit by the Department or the waste of such quantity to be exempt in accordance with Chapter 62-730, F.A.C. [Rule 62-296.401(4)(d)(6), F.A.C.; AC52-189392] Comments: This facility operates the incinerator on natural gas and burns only materials that fit the. Definitions of hospital medical, infectious waste. A.7. Hours of Operation. The incinerator is allowed to operate (burn waste material) a maximum of 7,300 hrs./yr. [Rule 62-210.200(PTE), F.A.C.; AC52-189392 Comments: The incinerator operated 1,011 hours from 1 March 2007 to 25 June 2007. A.18. Standards for Hospital/Medical/Infectious Waste Incinerators operator training and certification. (a) No owner or operator of an affected facility shall allow the affected facility to operate at any time unless a fully trained and qualified HMIWI operator is accessible, either at the facility or available within 1 hour. The trained and qualified HMIWI operator may operate the HMIWI directly or be the direct supervisor of one or more HMIWI operators. (b) Operator training and qualification shall be obtained through a State-approved program or by completing the requirements included in paragraphs (c) through (g) as follows: (c) Training shall be obtained by completing an HMIWI operator training course that includes, at a minimum, the following provisions: (1) 24 hours of training on the following subjects: (i) Environmental concerns, including pathogen destruction and types of emissions; (ii) Basic combustion principles, including products of combustion; (iii) Operation of the type of incinerator to be used by the operator, including proper startup, waste charging, and shutdown procedures; (iv) Combustion controls and monitoring; (v) Operation of air pollution control equipment and factors affecting performance (if applicable); (vi) Methods to monitor pollutants (continuous emission monitoring systems and monitoring of HMIWI and air pollution control device operating parameters) and equipment calibration procedures (where applicable); (vii) Inspection and maintenance of the HMIWI, air pollution control devices, and continuous emission monitoring systems; (viii) Actions to correct malfunctions or conditions that may lead to malfunction; (ix) Bottom and fly ash characteristics and handling procedures; (x) Applicable Federal, State, and local regulations; (xi) Work safety procedures; (xii) Pre-startup inspections; and (xiii) Recordkeeping requirements. (2) An examination designed and administered by the instructor. (3) Reference material distributed to the attendees covering the course topics. (d) Qualification shall be obtained by: (1) Completion of a training course that satisfies the criteria under paragraph (c) of this section; and (2) Either 6 months experience as an HMIWI operator, 6 months experience as a direct supervisor of an HMIWI operator, or completion of at least two burn cycles under the observation of two qualified HMIWI operators. (e) Qualification is valid from the date on which the examination is passed or the completion of the required experience, whichever is later. (f) To maintain qualification, the trained and qualified HMIWI operator shall complete and pass an annual review or refresher course of at least 4 hours covering, at a minimum, the following: (1) Update of regulations; (2) Incinerator operation, including startup and shutdown procedures; (3) Inspection and maintenance; (4) Responses to malfunctions or conditions that may lead to malfunction; and (5) Discussion of operating problems encountered by attendees. (g) A lapsed qualification shall be renewed by one of the following methods: (1) For a lapse of less than 3 years, the HMIWI operator shall complete and pass a standard annual refresher course described in paragraph (f). (2) For a lapse of 3 years or more, the HMIWI operator shall complete and pass a training course with the minimum criteria described in paragraph (c). (h) The owner or operator of an affected facility shall maintain documentation at the facility that address the following: (1) Summary of the applicable standards under this subpart; (2) Description of basic combustion theory applicable to an HMIWI; (3) Procedures for receiving, handling, and charging waste; (4) HMIWI startup, shutdown, and malfunction procedures; (5) Procedures for maintaining proper combustion air supply levels; (6) Procedures for operating the HMIWI and associated air pollution control systems within the standards established under this subpart; (7) Procedures for responding to periodic malfunction or conditions that may lead to malfunction; (8) Procedures for monitoring HMIWI emissions; (9) Reporting and recordkeeping procedures; and (10) Procedures for handling ash. (i) The owner or operator of an affected facility shall establish a program for reviewing the information listed in paragraph (h) annually with each HMIWI operator (defined in § 60.51c). (1) The initial review of the information listed in paragraph (h) shall be conducted prior to assumption of responsibilities affecting HMIWI operation. (2) Subsequent reviews of the information listed in paragraph (h) shall be conducted annually. (j) The information listed in paragraph (h) shall be kept in a readily accessible location for all HMIWI operators. This information, along with records of training shall be available for inspection by the EPA or its delegated enforcement agent upon request. [40 CFR 60.34e and 40 CFR 60.53c] A.19. The initial training requirements specified in 40 CFR 60.53c(i) shall be completed no later than the date prior to the day when the person assumes responsibilities affecting hospital/medical/infectious waste incinerator unit operation. [40 CFR 60.39e(e)] A.20. Any operator of an incinerator subject to Rule 62-296.401(4), F.A.C., shall be trained by the equipment manufacturer's representative or an equivalent organization using a state-approved training program. (a) The content of the training program shall be submitted to the Department for approval. Construction permit applicants shall submit a training program, or reference a previously submitted training program, with the construction permit application. The training shall provide a basic understanding of the principles of the combustion process, provide instruction on proper operating practices and procedures, and increase awareness of regulation requirements and safety concerns. Training programs shall be a minimum of 16 hours of instruction. The Department shall approve training programs which meet, at a minimum, the criteria set forth in the EPA Medical Waste Incinerator Operator Training Program Course Handbook EPA 453/B-93-018 and Instructor's Guide EPA 453/B-93-019. (b) A copy of the training certificate for each operator having satisfactorily completed the Department-approved training program must be submitted to the Department within 15 days of training. If the incinerator is modified to the extent that a Department construction permit is required, the operators shall be retrained to operate the modified incinerator. Owners of new and modified incinerators shall submit copies of the operator training certificates within 15 days after completion of the initial compliance test. (c) An operator's certificate must be kept on file at the facility for the duration of the operator's employment and for an additional two years after termination of employment. The owner shall not allow the incinerator to be operated unless it is operated by an operator who has satisfactorily completed the required training program. [Rule 62-296.401(4)(d)(7), F.A.C.; AC52-189392] Comments: The operator’s certificates for Donald Koster, Robert Fairburn, and Horace Tomlinson were on display on the bulletin board on the staircase landing leading to the incinerator control room office, and they revealed that training was given to the 3 individuals mentioned above, on September 9, 2006. A.22. At all times, including periods of startup, shutdown, and malfunction, owners and operators shall, to the extent practicable, maintain and operate any affected facility including associated air pollution control equipment in a manner consistent with good air pollution control practice for minimizing emissions. Determination of whether acceptable operating and maintenance procedures are being used will be based on information available to the Administrator which may include, but is not limited to, monitoring results, opacity observations, review of operating and maintenance procedures, and inspection of the source. [40 CFR 60.11(d)] Comments: Examinations of the operating parameter logs and the O&M logs appears to show that the facility was being operated in a manner consistent with Best Operational Practices. A.23. Excess emissions resulting from startup, shutdown, and malfunction shall be permitted provided that best operational practices to minimize emissions are adhered to and the duration of excess emissions shall be minimized but in no case exceed two hours in any 24 hour period unless specifically authorized by the Department for longer duration. [Rule 62-210.700(1), F.A.C.] A.24. Excess emissions which are caused entirely or in part by poor maintenance, poor operation, or any other equipment or process failure which may reasonably be prevented during startup, shutdown, or malfunction shall be prohibited. [Rule 62-210.700(4), F.A.C.] Comments: The facility did not have excess emissions to report for the 3rd quarter of the compliance year up to the date of this inspection. A.25. Performance tests shall be conducted under such conditions as the Administrator shall specify to the plant operator based on representative performance of the affected facility. The owner or operator shall make available to the Administrator such records as may be necessary to determine the conditions of the performance tests. Operations during periods of startup, shutdown, and malfunction shall not constitute representative conditions for the purpose of a performance test nor shall emissions in excess of the level of the applicable emission limit during periods of startup, shutdown, and malfunction be considered a violation of the applicable emission limit unless otherwise specified in the applicable standard. [40 CFR 60.8(c)] Comments: No tests have been ordered or deemed necessary. A.26. The emission limits under 40 CFR 60.56c and 40 CFR 60.37e, apply at all times except during periods of startup, shutdown, or malfunction, provided that no hospital waste or medical/infectious waste is charged to the affected facility during startup, shutdown, or malfunction. [40 CFR 60.56c and 40 CFR 60.37e] Comments: There were no exceedences of the emission limits during periods of startups, shutdowns or malfunctions during the period covering this quarter. A.41. During the burning of waste, the permittee shall demonstrate via temperature probe placement at the exit of the primary and secondary chamber that the combustion gas temperature is no less than 1,400 (F and 1,800 (F, respectively. The secondary chamber, during the burning of waste, shall not operate with a gas residence time of less than 1.0 seconds. Primary chamber and stack shall not be used in calculating this residence time. [Rule 62-296.401(4)(d)1., F.A.C.; AC52-189392] Comments: The primary and secondary chamber temperatures did not go below 400 (F and 1,800 (F, respectively for the period covered by this quarter. A.42. Mechanically fed facilities shall incorporate an air lock system to prevent opening the incinerator to the room environment. The volume of the loading system shall be designed to prevent overcharging thereby assuring complete combustion of the waste. [Rule 62-296.401(4)(d)2., F.A.C.; AC52-189392] Comments: The facility has an airlock system that prevents emissions from the Incinerator getting out into the control room. A.43. Incineration or ignition of waste shall not begin until the secondary (or last) combustion chamber temperature has reached the minimum required operating temperature of 1,800 (F. The secondary (or last) combustion chamber temperature requirement shall be maintained until the wastes are completely combusted. All air pollution control and continuous emission monitoring equipment shall be operational and functioning properly prior to the incineration or ignition of waste and until all the wastes are incinerated. [Rule 62-296.401(4)(d)4., F.A.C.; AC52-189392] Comments: Incineration or ignition of waste did not begin until the secondary (or last) combustion chamber temperature had reached the minimum required operating temperature of 1,800 (F. A.48. Required Stack Sampling Facilities. When a mass emissions stack test is required, the permittee shall comply with the requirements contained in Appendix SS-1, Stack Sampling Facilities, attached to this permit. [Rule 62-297.310(6), F.A.C.] Comments: The facility stack sampling facilities comply with 62-297.310(6) FAC. A.49. Frequency of Compliance Tests. The following provisions apply only to those emissions units that are subject to an emissions limiting standard for which compliance testing is required. (a) General Compliance Testing. 1. The owner or operator of an emissions unit that is subject to any emission limiting standard shall conduct a compliance test that demonstrates compliance with the applicable emission limiting standard prior to obtaining a renewed operation permit. Emissions units that are required to conduct an annual compliance test may submit the most recent annual compliance test to satisfy the requirements of this provision. 2. The owner or operator shall notify the Air Compliance Section of the PCDEM, at least 15 days prior to the date on which each formal compliance test is to begin, of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted for the owner or operator. {Note: The owner or operator of the affected facility should include in the notification a statement of the purpose of the compliance test, i.e. annual performance testing, testing for operation parameter re-determination, and etc.} 3. Annual emission testing for Visible Emission, Particulate Matter, Carbon Monoxide, and Hydrochloric Acid shall be required per Rule 62-296.401(4)(f)2., F.A.C. {Permitting Note: Certain annual tests are required for particulate matter, opacity, carbon monoxide, dioxin/furan, cadmium, lead, mercury, hydrogen chloride, sulfur dioxide, and nitrogen oxides, as specified in Conditions A.29 - A.35.} [Rules 62-296.401(4)(f)2. and 62-297.310(7), F.A.C.] Comments: There were no tests scheduled during this visit. A.50. The owner or operator of an affected facility shall prepare a waste management plan. The waste management plan shall identify both the feasibility and the approach to separate certain components of solid waste from the health care waste stream in order to reduce the amount of toxic emissions from incinerated waste. A waste management plan may include, but is not limited to, elements such as paper, cardboard, plastics, glass, battery, or metal recycling; or purchasing recycled or recyclable products. A waste management plan may include different goals or approaches for different areas or departments of the facility and need not include new waste management goals for every waste stream. It should identify, where possible, reasonably available additional waste management measures, taking into account the effectiveness of waste management measures already in place, the costs of additional measures, the emission reductions expected to be achieved, and any other environmental or energy impacts they might have. The American Hospital Association publication entitled "An Ounce of Prevention: Waste Reduction Strategies for Health Care Facilities" (incorporated by reference, see § 60.17) shall be considered in the development of the waste management plan. [40 CFR 60.35e and 40 CFR 60.55c] Comments: The facility has a waste management plan that complies wilt permit conditions A. 5O A.51. The permittee shall demonstrate compliance with the following: A. That all the biomedical waste storage, operation and contingency procedure requirements set forth in Chapter 64E-16.004, F.A.C. are met. B. Solid waste, such as waste pharmaceuticals, that is not hospital, medical, or infectious waste shall not be commingled with hospital, medical, or infectious waste prior to placement in the incinerator, pursuant to Chapter 62-701, F.A.C. and 29 CFR 1910.1030. C. Per Rule 62-701.710(4)(b), F.A.C. - Stored putrescible waste shall not be allowed to remain on site for more than 48 hours unless provisions are made to control vectors and odors. Non putrescible solid waste should be removed from the facility within 30 days of generation or within an approved time period approved by the Department's Solid Waste Section. The permittee shall ensure that the materials, which are disposed, have been adequately characterized to meet the intended disposal facilities acceptance criteria. D. Per Rule 62-701.300(6), F.A.C. - Biohazardous waste shall be properly incinerated so that little or no organic matter remains in the ash residue, or shall be processed by a method approved by the Department of Health, and the provisions in Rule 62-701.520(5)(c), F.A.C., are complied with. No untreated biohazardous wastes shall be knowingly deposited in any landfill. [Rules 64E-16.004 and 62-701.700, F.A.C.; AC52-189392] None of the waste permitted: to be combusted had been on site for more than 24hours. A.52. Not Federally Enforceable. Ash residue shall be managed in accordance with the requirements of Chapter 62-701, F.A.C. If the facility is permitted to incinerate 50 tons per day or more of biohazardous waste, an ash management plan must be submitted for approval to the Department [Solid Waste Section] and kept on file with the air permit. Biomedical waste incinerator ash is known to contain heavy metals regulated under 40 CFR 261.24. Ash must be tested in accordance with 40 CFR 262.11 for hazardous waste characteristics prior to disposal. Ash residue that is a hazardous waste as defined in 40 CFR Part 261 must be managed in accordance with Rule 62-730, F.A.C. If the ash is not hazardous as defined above, it shall be disposed of at a Class I landfill in the state of Florida, or other disposal facilities as specifically approved by the Department. Comments: Bayfront now tests the ash residue from the incinerator on a quarterly basis. Except for discharges at a permitted wastewater treatment plant, leachate shall not be discharged, spilled, dumped, or leaked onto the ground or into surface or ground waters. Leachate is defined in accordance with Rule 62-701.200(66), F.A.C., as liquid that has passed through or emerged from solid waste and may contain soluble, suspended, or miscible materials. Per Rule 62-62-701.300(1)(b), F.A.C. – No person shall store, process, or dispose of solid waste (including leachate) in a manner or location that causes air quality standards to be violated or water quality standards or criteria of receiving waters to be violated. [Chapters 62-701 and 62-730, F.A.C.] Comments: There were no signs of leachate being spilled, dumped or leaked on the incinerator room floor. A.55. The owner or operator shall install, operate and maintain in accordance with the manufacturer's instructions continuous emission monitoring equipment for measuring oxygen. Note, the oxygen monitor used at this facility is not subject to any of the requirements of 40 CFR 60 Subparts Ce and Ec. [Rule 62-296.401(4)(g), F.A.C.] Comments The facility operates and maintains an Oxygen monitor. The O2 was reading 12.3% when I arrived on site. A.56. The owner or operator shall install, calibrate (to manufacturers' specifications), maintain, and operate devices (or establish methods) for monitoring the applicable maximum and minimum operating parameters listed in Table OP-1 such that these devices (or methods) measure and record values for these operating parameters at the frequencies indicated in Table OP-1 at all times except during periods of startup and shutdown. [40 CFR 60.37e(c) and 40 CFR 60.57c(a)] A.57. The owner or operator of an affected facility shall install, calibrate, (to manufacturers' specifications), maintain, and operate a device or method for measuring the use of the bypass stack including date, time, and duration. [40 CFR 60.37e(c) and 40 CFR 60.57c(b)] Comments: The automated system keeps track of the use of the Bypass stack. A.58. The owner or operator of an affected facility using something other than a dry scrubber followed by a fabric filter, a wet scrubber, or a dry scrubber followed by a fabric filter and a wet scrubber to comply with the emission limits under 40 CFR 60.52c shall install, calibrate (to the manufacturers' specifications), maintain, and operate the equipment necessary to monitor the site-specific operating parameters developed pursuant to 40 CFR 60.56c(i). [40 CFR 60.37e(c) and 60 CFR 60.57c(c)] Comments: The Facility had the calibration records on hand for all of the automated equipment that send data to the computer. All equipment was calibrated from December of ’06 to April of ’07, during several visits. A.59. The owner or operator of an affected facility shall obtain monitoring data at all times during HMIWI operation except during periods of monitoring equipment malfunction, calibration, or repair. At a minimum, valid monitoring data shall be obtained for 75 percent of the operating hours per day and for 90 percent of the operating days per calendar quarter that the affected facility is combusting hospital waste and/or medical/infectious waste. [40 CFR 60.37e(c) and 40 CFR 60.57c(d)] Comments: Valid monitoring data was obtained for 75 percent of the operating hours per day and for 90 percent of the operating days per calendar quarter during the period covered by try inspection. A.64. All continuous monitoring systems (CMS) or monitoring devices shall be installed such that representative measurements of emissions or process parameters from the affected facility are obtained. Additional procedures for location of continuous monitoring systems contained in the applicable Performance Specifications of Appendix B of 40 CFR 60 shall be used. [40 CFR 60.13(f)] Comments: The monitoring devices derived measurement of process parameters that were representative of the equipment parameters. 67. Determination of Process Variables. (a) Required Equipment. The owner or operator of an emissions unit for which compliance tests are required shall install, operate, and maintain equipment or instruments necessary to determine process variables, such as process weight input or heat input, when such data are needed in conjunction with emissions data to determine the compliance of the emissions unit with applicable emission limiting standards. (b) Accuracy of Equipment. Equipment or instruments used to directly or indirectly determine process variables, including devices such as belt scales, weight hoppers, flow meters, and tank scales, shall be calibrated and adjusted to indicate the true value of the parameter being measured with sufficient accuracy to allow the applicable process variable to be determined within 10% of its true value. [Rule 62-297.310(5), F.A.C.] Comments: The facility was in compliance with 67 a & b above, A.68. The permittee shall at a minimum install, operate, and maintain, in accordance with the manufacturer’s instructions, the following equipment: Equipment Monitored Parameter Monitoring Type Incinerator: Primary Chamber (Exit) Temperature - (F CM & CR Secondary Chamber (Exit) Temperature - (F CM & CR Waste Heat Boiler: Gas Outlet Temperature - (F CM Steam Outlet PSI CM Saturator/Quencher: Gas Outlet (2) Temperature - (F CM Saturator Skin Temperature - (F CM Saturator Sump Liquid Level CM Fresh Water Inlet (6) GPM CM Liquid Outflow GPM CM Liquid Outflow pH CM Condenser/Absorber Tower: Sump Liquid Level CM Liquid Outflow (11) GPM CM Liquid Outflow (11) pH CM Recycle to Saturator (14) GPM CM Gas Outlet (3) Temperature - (F CM Calvert Collision Scrubber: Gas Outlet Delta P, "Water" CM Entrainment Separator: Gas Outlet (4) Temperature - (F CM Gas Outlet (4) Inches of Water CM Recycle to Scrubber GPM CM Fresh Water (16) GPM CM Recycle to C/A (10) GPM CM Exhaust Stack O2 CM & CR NOTE: CM - Continuous Monitor; CR - Continuous Recording; Numbers appearing in parenthesis relate to stream flows on a flow diagram attached to the construction application. A complete file of all measurements, including continuous emissions monitoring system, monitoring device, and performance testing measurements; all continuous emissions monitoring system performance evaluations; all continuous emissions monitoring system or monitoring device calibration checks; adjustments and maintenance performed on these systems or devices; and all other information required, shall be recorded in a permanent legible form available for inspection. The file shall be retained for at least 5 years following the date of such measurements, maintenance, reports, and records. [Rules 62-296.401(4)(g) and 62-213.440(1), F.A.C.; AC52-189392] Comments: The facility was in compliance with A 68 above. A.69. Temperature and oxygen sensors and recorders shall be calibrated and adjusted to indicate the true value of the parameter being measured with sufficient accuracy to allow the parameter to be determined within 10% of its true value. Scales used to determine process (waste charging) rate shall be calibrated and adjusted to indicate the true weight of the waste to be incinerated with sufficient accuracy to allow the weight to be determined within 10% of its true value. [Rule 62-297.310(5)(b), F.A.C.] Comments: The temperature and oxygen sensors were calibrated in December of ’06. A.70. The operator of the incinerator shall daily record the following: a. Facility name, emission unit number, date and name of operator. b. The measurement of each monitor without a continuous recorder during operation. c. Hourly (see Condition A.1.) record the total weight of the materials (as weighed on scale) placed in the primary chamber to be burned, in pounds. d. Total daily hours of operation. e. The total cumulative calendar year hours of operation. [Rule 62-4.070(3), F.A.C.; AC52-189392] Comments: The facility was in compliance with a, b, c. d and e above. A.71. (a) The owner or operator of an affected facility shall maintain the following information (as applicable) for a period of at least 5 years: (1) Calendar date of each record; (2) Records of the following data: (i) Concentrations of any pollutant listed in § 60.52c (Table 1 of 40 CFR 60, Subpart Ce) or measurements of opacity as determined by the continuous emission monitoring system (if applicable); (iii) HMIWI charge dates, times, and weights and hourly charge rates; (iv) Fabric filter inlet temperatures during each minute of operation, as applicable; (v) Amount and type of dioxin/furan sorbent used during each hour of operation, as applicable; (vi) Amount and type of Hg sorbent used during each hour of operation, as applicable; (vii) Amount and type of HCl sorbent used during each hour of operation, as applicable; (viii) Secondary chamber temperatures recorded during each minute of operation; (ix) Liquor flow rate to the wet scrubber inlet during each minute of operation, as applicable. (x) Horsepower or amperage to the wet scrubber during each minute of operation, as applicable. (xi) Pressure drop across the wet scrubber system during each minute of operation, as applicable. (xii) Temperature at the outlet from the wet scrubber during each minute of operation, as applicable. (xiii) pH at the inlet to the wet scrubber during each minute of operation, as applicable. (xiv) Records indicating use of the bypass stack including dates, times, and durations. (xv) NOT APPLICABLE (since this is considered an existing facility subject to 40 CFR Ce) (3) Identification of calendar days for which data on emission rates or operating parameters specified under paragraph (a)(2) of this section have not been obtained, with an identification of the emission rates or operating parameters not measured, reasons for not obtaining the data, and a description of corrective actions taken. (4) Identification of calendar days, times and durations of malfunctions, a description of the malfunction and the corrective action taken. (5) Identification of calendar days for which data on emission rates or operating parameters specified under paragraph (a)(2) of this section exceeded the applicable limits, with a description of the exceedances, reasons for such exceedances, and a description of corrective actions taken. (6) The results of the initial, annual, and any subsequent performance tests conducted to determine compliance with the emission limits and/or to establish operating parameters, as applicable. (7) Records showing the names of HMIWI operators who have completed review of the information in § 60.53c(h) as required by § 60.53c(i), including the date of the initial review and all subsequent annual reviews; (8) Records showing the names of the HMIWI operators who have completed the operator training requirements, including documentation of training and the dates of the training; (9) Records showing the names of the HMIWI operators who have met the criteria for qualification under § 60.53c and the dates of their qualification; and (10) Records of calibration of any monitoring devices as required under § 60.57c(a), (b), and (c). (b) The owner or operator of an affected facility shall submit the information specified in paragraphs (b)(1) through (b)(3) of this section no later than 60 days following the initial performance test. All reports shall be signed by the facilities manager. (1) The initial performance test data as recorded under § 60.56c(b)(1) through (b)(12), as applicable. (2) The values for the site-specific operating parameters established pursuant to § 60.56c(d) or (i), as applicable. (3) The waste management plan as specified in § 60.55c. (c) An annual report shall be submitted 1 year following the submission of the information in paragraph (b) of this section and subsequent reports shall be submitted no more than 12 months following the previous report (once the unit is subject to permitting requirements under Title V of the Clean Air Act, the owner or operator of an affected facility must submit these reports semiannually). The annual report shall include the information specified in paragraphs (c)(1) through (c)(8) of this section. All reports shall be signed by the facilities manager. (1) The values for the site-specific operating parameters established pursuant to § 60.56c(d) or (i), as applicable. (2) The highest maximum operating parameter and the lowest minimum operating parameter, as applicable, for each operating parameter recorded for the calendar year being reported, pursuant to § 60.56c(d) or (i), as applicable. (3) The highest maximum operating parameter and the lowest minimum operating parameter, as applicable for each operating parameter recorded pursuant to § 60.56c(d) or (i) for the calendar year preceding the year being reported, in order to provide the Administrator with a summary of the performance of the affected facility over a 2-year period. (4) Any information recorded under paragraphs (a)(3) through (a)(5) of this section for the calendar year being reported. (5) Any information recorded under paragraphs (a)(3) through (a)(5) of this section for the calendar year preceding the year being reported, in order to provide the Administrator with a summary of the performance of the affected facility over a 2-year period. (6) If a performance test was conducted during the reporting period, the results of that test. (7) If no exceedances or malfunctions were reported under paragraphs (a)(3) through (a)(5) of this section for the calendar year being reported, a statement that no exceedances occurred during the reporting period. (8) Any use of the bypass stack, the duration, reason for malfunction, and corrective action taken. (d) The owner or operator of an affected facility shall submit semiannual reports containing any information recorded under paragraphs (a)(3) through (a)(5) of this section no later than 60 days following the reporting period. The first semiannual reporting period ends 6 months following the submission of information in paragraph (b) of this section. Subsequent reports shall be submitted no later than 6 calendar months following the previous report. All reports shall be signed by the facilities manager. (e) All records specified under paragraph (a) of this section shall be maintained onsite in either paper copy or computer-readable format, unless an alternative format is approved by the Administrator. [40 CFR 60.58c] Comments: The facility has records dating back to the beginning of automated database data-gathering, which goes back to 1998. A.73. The owner or operator subject to the provisions of 40 CFR 60 shall furnish the Administrator written notification as follows: (4) A notification of any physical or operational change to an existing facility which may increase the emission rate of any air pollutant to which a standard applies, unless that change is specifically exempted under an applicable subpart or in 40 CFR 60.14(e). This notice shall be postmarked 60 days or as soon as practicable before the change is commenced and shall include information describing the precise nature of the change, present and proposed emission control systems, productive capacity of the facility before and after the change, and the expected completion date of the change. The Administrator may request additional relevant information subsequent to this notice. [40 CFR 60.7(a)(4)] Comments: There were no changes to the facility that could increase the emissions. A.74. Department Notification. The permittee shall give written notification to the Department when there is any modification to this facility. This notice shall be resubmitted timely and in advance of any critical date involved to allow sufficient time for review, discussion, and revision of plans, if necessary. Such notice shall include, but not be limited to, information describing the precise nature of the change; modifications to any emission control system; production capacity of the facility before and after the change; and, the anticipated completion date of the change. [40 CFR 60.8(d)] Comments: I read the permit conditions to Messrs. Fairburn & Tomlinson. A.75. The following shall not, by themselves, be considered modifications under 40 CFR 60: (1) Maintenance, repair, and replacement which the Department determines to be routine for a source category, subject to the provisions of 40 CFR 60.14(c) and 40 CFR 60.15. (2) An increase in production rate of an existing facility, if that increase can be accomplished without a capital expenditure on that facility. (3) An increase in the hours of operation. (4) Use of an alternative fuel or raw material if, prior to the date any standard under 40 CFR 60 becomes applicable to that source type, as provided by 40 CFR 60.1, the existing facility was designed to accommodate that alternative use. A facility shall be considered to be designed to accommodate an alternative fuel or raw material if that use could be accomplished under the facility's construction specifications as amended prior to the change. Conversion to coal required for energy considerations, as specified in section 111(a)(8) of the Act, shall not be considered a modification. (5) The addition or use of any system or device whose primary function is the reduction of air pollutants, except when an emission control system is removed or is replaced by a system which the Department determines to be less environmentally beneficial. (6) The relocation or change in ownership of an existing facility. [40 CFR 60.14(e)] Comments: None of the possible modifications in 1 thru 6 above were noted at Bayfront. A.76. The owner or operator subject to the provisions of 40 CFR 60 shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of an affected facility; any malfunction of the air pollution control equipment; or, any periods during which a continuous monitoring system or monitoring device is inoperative. [40 CFR 60.7(b)] Comments: The facility has records of all startup, shutdowns and upset conditions. A.77. Each owner or operator required to install a continuous monitoring system (CMS) or monitoring device shall submit an excess emissions and monitoring systems performance report (excess emissions are defined in applicable subparts) and/or a summary report form [see 40 CFR 60.7(d)] to the Administrator semiannually, except when: more frequent reporting is specifically required by an applicable subpart; or, the CMS data are to be used directly for compliance determination, in which case quarterly reports shall be submitted; or, the Administrator, on a case-by-case basis, determines that more frequent reporting is necessary to accurately assess the compliance status of the source. All reports shall be postmarked by the 30th day following the end of each calendar half (or quarter, as appropriate). Written reports of excess emissions shall include the following information: (1) The magnitude of excess emissions computed in accordance with 40 CFR 60.13(h), any conversion factor(s) used, and the date and time of commencement and completion of each time period of excess emissions. The process operating time during the reporting period. (2) Specific identification of each period of excess emissions that occurs during startups, shutdowns, and malfunctions of the affected facility. The nature and cause of any malfunction (if known), the corrective action taken or preventative measures adopted. (3) The date and time identifying each period during which the continuous monitoring system was inoperative except for zero and span checks and the nature of the system repairs or adjustments. (4) When no excess emissions have occurred or the continuous monitoring system(s) have not been inoperative, repaired, or adjusted, such information shall be stated in the report. [40 CFR 60.7(c)(1), (2), (3), and (4)] Comments: There were no excess emissions to report in the months covered by this quarter. A.78. The summary report form shall contain the information and be in the format shown in Figure 1 (attached) unless otherwise specified by the Administrator. One summary report form shall be submitted for each pollutant monitored at each affected facility. (1) If the total duration of excess emissions for the reporting period is less than 1 percent of the total operating time for the reporting period and CMS downtime for the reporting period is less than 5 percent of the total operating time for the reporting period, only the summary report form shall be submitted and the excess emission report described in 40 CFR 60.7(c) need not be submitted unless requested by the Administrator. (2) If the total duration of excess emissions for the reporting period is 1 percent or greater of the total operating time for the reporting period or the total CMS downtime for the reporting period is 5 percent or greater of the total operating time for the reporting period, the summary report form and the excess emission report described in 40 CFR 60.7(c) shall both be submitted. {See attached Figure 1: Summary Report-Gaseous and Opacity Excess Emission and Monitoring System Performance} (electronic file name: figure1.doc) [40 CFR 60.7(d)(1) and (2)] Comments: There were no excess emissions to report in the months covered by this quarter. A.80. Any owner or operator subject to the provisions of 40 CFR 60 shall maintain a file of all measurements, including continuous monitoring system, monitoring device, and performance testing measurements; all continuous monitoring system performance evaluations; all continuous monitoring system or monitoring device calibration checks; adjustments and maintenance performed on these systems or devices; and, all other information required by 40 CFR 60 recorded in a permanent form suitable for inspection. The file shall be retained for at least 5 (five) years following the date of such measurements, maintenance, reports, and records. [40 CFR 60.7(f); and, Rule 62-213.440(1)(b)2.b., F.A.C.] Comments: Bayfront Medical Center has records on its computer database dating back more than five (5) years. A.81. In case of excess emissions resulting from malfunctions, each owner or operator shall notify the Air Compliance Section of the PCDEM in accordance with Rule 62-4.130, F.A.C. A full written report on the malfunctions shall be submitted in a quarterly report, if requested by the Department. [Rule 62-210.700(6), F.A.C.] A.84. Submit to the Department a written report of emissions in excess of emission limits for each calendar quarter. The nature and cause of the excess emissions shall be explained. This report does not relieve the owner or operator of the legal liability for violations. All recorded data shall be maintained on file by the Source for a period of five years. [Rule 62-213.440, F.A.C.] Comments: There were no excess emissions in the months covered by this quarterly inspection. A.86. Circumvention. A. No owner or operator subject to the provisions of 40 CFR 60 shall build, erect, install, or use any article, machine, equipment or process, the use of which conceals an emission which would otherwise constitute a violation of an applicable standard. Such concealment includes, but is not limited to, the use of gaseous diluents to achieve compliance with an opacity standard or with a standard which is based on the concentration of a pollutant in the gases discharged to the atmosphere. [40 CFR 60.12] B. No person shall circumvent any air pollution control device, or allow the emission of air pollutants without the applicable air pollution control device operating properly. [Rule 62-210.650, F.A.C.; 40 CFR 60.12] Comments: I did not observe any devices or equipment which would conceal or be used to bypass the control equipment. A.89. General Pollutant Emission Limiting Standards. Objectionable Odor Prohibited. No person shall cause, suffer, allow, or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200, 62-296.320(2), and 62-296.401(2)(b), F.A.C.; Pinellas County Code, Section 58-178] Comments: There were no objectionable odors in or out of the facility. A.91. Compliance Assurance Monitoring (CAM) Requirements. This emission unit is subject to the Compliance Assurance Monitoring (CAM) requirements contained in the attached Appendix CAM. The CAM requirements are only applicable for hydrochloric acid emissions established in Rule 62-296.401(4), F.A.C. Failure to adhere to the monitoring requirements specified does not necessarily indicate an exceedance of a specific emissions limitation; however, it may constitute good reason to require testing pursuant to Rule 62-297.310(7)(b), F.A.C.). [40 CFR 64; Rules 62-204.800 and 62-213.440(1)(b)1.a., F.A.C.] Comments: The emission unit has been complying with the CAM requirements for several years. A.92. Not Federally Enforceable: The operation of the incinerator shall be in compliance with the Operation and Maintenance (O&M) Plan submitted with the Title V renewal permit application dated January 9, 2006 and the additional information letter dated August 7, 2006, and as revised with the prior approval of the PCDEM. The documents referred to above are not attached to this permit, but are on file with the Department and/or PCDEM and available upon request. [Pinellas County Code, Section 58-128] Comments: The O & M logs were completed and therefore indicated adherence let the Maintenance Plan and the use of Best Operational Practices to run the emissions unit CAM Plan 1. Proper maintenance. At all times, the owner or operator shall maintain the monitoring, including but not limited to, maintaining necessary parts for routine repairs of the monitoring equipment. [40 CFR 64.7(b)] Comments: As indicated in previous permit conditions, the facility was performing the routine maintenance of the equipment and has a moderately large storage area which contains many spare parts for the incinerator.. 2. Continued operation. Except for, as applicable, monitoring malfunctions, associated repairs, and required quality assurance or control activities (including, as applicable, calibration checks and required zero and span adjustments), the owner or operator shall conduct all monitoring in continuous operation (or shall collect data at all required intervals) at all times that the pollutant-specific emissions unit is operating. Data recorded during monitoring malfunctions, associated repairs, and required quality assurance or control activities shall not be used for purposes of this part, including data averages and calculations, or fulfilling a minimum data availability requirement, if applicable. The owner or operator shall use all the data collected during all other periods in assessing the operation of the control device and associated control system. A monitoring malfunction is any sudden, infrequent, not reasonably preventable failure of the monitoring to provide valid data. Monitoring failures that are caused in part by poor maintenance or careless operation are not malfunctions. [40 CFR 64.7(c)] Comments: Monitoring and automated database storing of data is performed in real time on a continuous basis. 3. Response to excursions or exceedances. a. Upon detecting an excursion or exceedance, the owner or operator shall restore operation of the pollutant-specific emissions unit (including the control device and associated capture system) to its normal or usual manner of operation as expeditiously as practicable in accordance with good air pollution control practices for minimizing emissions. The response shall include minimizing the period of any startup, shutdown or malfunction and taking any necessary corrective actions to restore normal operation and prevent the likely recurrence of the cause of an excursion or exceedance (other than those caused by excused startup or shutdown conditions, if allowed by this permit). Such actions may include initial inspection and evaluation, recording that operations returned to normal without operator action (such as through response by a computerized distribution control system), or any necessary follow-up actions to return operation to within the indicator range, designated condition, or below the applicable emission limitation or standard, as applicable. b. Determination of whether the owner or operator has used acceptable procedures in response to an excursion or exceedance will be based on information available, which may include but is not limited to, monitoring results, review of operation and maintenance procedures and records, and inspection of the control device, associated capture system, and the process. [40 CFR 64.7(d)(1) & (2)] Comments: There were no reportable excursions or exceedences 40 CFR 64.8 Quality Improvement Plan (QIP) Requirements. 4. Based on the results of a determination made under CAM Condition Comments: Monitoring and automated database storing of data is performed in real time on a continuous basis. 3.a., above, the permitting authority may require the owner or operator to develop and implement a QIP. Consistent with CAM Condition Error! Reference source not found., an accumulation of exceedances or excursions exceeding 5 percent duration of a pollutant-specific emissions unit's operating time for a reporting period, may require the implementation of a QIP. The threshold may be set at a higher or lower percent or may rely on other criteria for purposes of indicating whether a pollutant-specific emissions unit is being maintained and operated in a manner consistent with good air pollution control practices. [40 CFR 64.8(a)] Comments: There were no exceedences or excursions during the quarter period examined that lasted 5 minutes or more. 5. If a QIP is required, the owner or operator shall develop and implement a QIP as expeditiously as practicable and shall notify the permitting authority if the period for completing the improvements contained in the QIP exceeds 180 days from the date on which the need to implement the QIP was determined. [40 CFR 64.8(c)] Comments: A QIP is not and has not been required at this time. 6. Following implementation of a QIP, upon any subsequent determination pursuant to CAM Condition Comments: Monitoring and automated database storing of data is performed in real time on a continuous basis. 3.b., the permitting authority may require that an owner or operator make reasonable changes to the QIP if the QIP is found to have: a. Failed to address the cause of the control device performance problems; or b. Failed to provide adequate procedures for correcting control device performance problems as expeditiously as practicable in accordance with good air pollution control practices for minimizing emissions. [40 CFR 64.8(d)] Comments: NA 40 CFR 64.9 Reporting And Recordkeeping Requirements. 7. General reporting requirements. a. On and after the date specified in CAM Condition Error! Reference source not found. by which the owner or operator must use monitoring that meets the requirements of this appendix, the owner or operator shall submit monitoring reports semi-annually to the permitting authority in accordance with Rule 62-213.440(1)(b)3.a., F.A.C. b. A report for monitoring under this part shall include, at a minimum, the information required under Rule 62-213.440(1)(b)3.a., F.A.C., and the following information, as applicable: (i) Summary information on the number, duration and cause (including unknown cause, if applicable) of excursions or exceedances, as applicable, and the corrective actions taken; (ii) Summary information on the number, duration and cause (including unknown cause, if applicable) for monitor downtime incidents (other than downtime associated with zero and span or other daily calibration checks, if applicable); and (iii) A description of the actions taken to implement a QIP during the reporting period as specified in CAM Conditions 4. through Error! Reference source not found. Upon completion of a QIP, the owner or operator shall include in the next summary report documentation that the implementation of the plan has been completed and reduced the likelihood of similar levels of excursions or exceedances occurring. [40 CFR 64.9(a)] Comments: The facility is using monitoring and record-keeping equipment that meets the requirements of this CAM Appendix . 8. General recordkeeping requirements. |
|  |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: I reminded Mr. Fairburn that Bayfront has A stack test pending for this compliance year. Mr. Fairburn stated that the test has, tentatively, been scheduled for September 18th, 2007. |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: 3 July 2007 |
| ACCESS? |  | ESIIR |  |

H:\USERS\WPDOCS\Airqual\Air_Compliance\AQI\1030095 002 58183.doc