1030036 004 65343

CONCRETE BATCHING PLANT

COMPLIANCE INSPECTION CHECKLIST

INSPECTION TYPE:	ANNUAL (INS1, INS2)		COMPLAINT/DISCOVERY (CI)

RE-INSPECTION (FUI)		ARMS COMPLAINT NO:

AIRS ID#: 1030036 004	  DATE:    6/19/08		ARRIVE:    12:30 PM		DEPART:   2:00 PM

FACILITY NAME:  Cemex Construction Materials, L.P

FACILITY LOCATION:	2063 20th Avenue S.E.

Largo, FL

RESPONSIBLE OFFICIAL:  Jason Jones?	PHONE:  813-269-1240

CONTACT NAME:   Jason Jones?	PHONE:  813-269-1240

REMITTANCE YEAR:    n/a		  ENTITLEMENT PERIOD:  5/18/2008	/	5/18/13

(effective date)	(end date)

PART I:  INSPECTION COMPLIANCE STATUS (check  only one box)

 IN COMPLIANCE         MINOR Non-COMPLIANCE 	 SIGNIFICANT Non-COMPLIANCE

PART II: TESTING/RECORDKEEPING REQUIREMENTS – Rule 62-296.414, F.A.C.

(check  appropriate box(es))

Stack Emissions

1.  Were visible emissions tests conducted during this site visit according to EPA Method 9 (Ref.: Chapter

62-297, F.A.C.)?-----------------------------------------------------------------------------------------------------------	Yes	  No

2.	Are emissions from silos, weigh hoppers (batchers), and other enclosed storage and conveying equipment

controlled to the extent necessary to limit visible emissions to 5 percent opacity?-----------------------------	Yes	  No

3.	During visible emissions tests of the silo dust collector exhaust points was the loading of the silo conducted

at a rate that is representative of the normal silo loading rate, or at least at the minimum 25 tons per hour rate,

unless such rate is unachievable in practice?--------------------------------------------------------------------------	Yes	  No

4.	Are emissions from the weigh hopper (batcher) operation controlled by the silo dust collector? (If answer

to this question is “Yes”, then continue on to questions 4.a) and 4.b) below. If answer is “No” then

skip 4.a) and 4.b) and continue on to question 5.)--------------------------------------------------------------------	Yes	  No

a)  Was the batching operation in operation during the visible emissions test?----------------------------------	Yes	 No

b)  During the visible emissions test, was the batching rate representative of the normal batching rate and

duration?---------------------------------------------------------------------------------------------------------------------	Yes	 No

5.	If emissions from the weigh hopper (batcher) operation are controlled by a dust collector, which is separate

from the silo dust collector, are the visible emissions tests of the weigh hopper (batcher) dust collector

conducted while batching at a rate that is representative of the normal batching rate and duration?---------	Yes	 No

PART II: TESTING/RECORDKEEPING REQUIREMENTS – Rule 62-296.414, F.A.C. – (continued)

(check  appropriate box(es)

Compliance Demonstration - (Rule 62-296.401(5)(i), F.A.C.)

1.	Is each dust collector exhaust point tested according to the visible emissions limiting standard as part of the

annual compliance demonstration? (Rule 62-297.310(7)(a), F.A.C.)--------------------------------------------	Yes	  No

New Facilities – (permitted pursuant to Rule 62-210.300(4), F.A.C., Air General Permits)

2.	Did this facility demonstrate:

a)	initial compliance no later than 30 days after beginning operation?-----------------------------------------	Yes   No

b)	annual compliance within 60 days prior to each anniversary of the air general permit notification form

submittal date?--------------------------------------------------------------------------------------------------------	Yes   No

Existing Facilities – (permitted pursuant to Rule 62-210.300(4), F.A.C., Air General Permits)

3.  	In order to demonstrate annual compliance, was an annual visible emissions test conducted 60days prior to

the AGP Notification form submission, and within 60 days prior to each anniversary date?----------------	Yes	  No

Test Reports – (Rules 62-213.440, F.A.C. and 62-297.310(8)(b), F.A.C.)

4.  Was the required test report filed with the department as soon as practical, but no later than 45 days after the

test was completed?------------------------------------------------------------------------------------------------------	Yes	  No

PART III:  OPERATING/RECORDKEEPING REQUIREMENTS – Rule 62-210.300(4)(c)2., F.A.C.

(check  appropriate box(es))

1.  Is this facility:   1) a stationary ;   2) a relocatable ; or does it have:  3) both, stationary and relocatable

concrete batching and/or nonmetallic mineral processing plants? (Please check  only one box.)

2.  If this is a stationary concrete batching plant, is there one or more relocatable nonmetallic mineral processing

plants using individual air general permits at the same location? (If your answer to this question is YES,

then proceed to questions 2.a), thru  2.d),) below.)----------------------------------------------------------------	Yes   No

a)	Are there any additional nonexempt units located at this facility?------------------------------------------	Yes   No

b)	Is the total combined annual facility-wide fuel oil usage of all plants less than 240,000 gallons per

calendar year?--------------------------------------------------------------------------------------------------------	Yes   No

c)	Is the quantity of material processed less than ten million tons per calendar year?----------------------	Yes   No

d)	Is the fuel oil sulfur content 0.5% by weight or less?---------------------------------------------------------	Yes   No

3.  Does the owner/operator of the concrete batching plant maintain a log book or books to account for:

a)	fuel consumption on a monthly basis?---------------------------------------------------------------------------	Yes   No

b)	material processed on a monthly basis?-------------------------------------------------------------------------	Yes   No

c)  the sulfur content of the fuel being burned (Fuel supplier certifications)?--------------------------------	Yes   No

PART III:  OPERATING/RECORDKEEPING REQUIREMENTS – Rule 62-296.414(2)(a) and (b), F.A.C. (continued)

(check  appropriate box(es))

Unconfined Emissions – (Rule 62-296.320(4)(c), F.A.C.)

1.  Does the owner /operator of the concrete batching plant take reasonable precautions to control unconfined

emissions by:

a)  management of roads, parking areas, stock piles, and yards, which shall include one or more of the following:

1)  paving and maintenance of roads, parking areas, stock piles, and yards?------------------------------	Yes   No

2)  application of water or environmentally safe dust-suppressant chemicals when necessary to control

emissions?---------------------------------------------------------------------------------------------------------	Yes   No 			3)	removal of particulate matter from roads and other paved areas under control of the owner/operator to

re-entrainment, and from building or work areas to reduce airborne particulate matter?------------	Yes   No

4)  reduction of stock pile height, or installation of wind breaks to mitigate wind entrainment of

particulate matter from stock piles?---------------------------------------------------------------------------	Yes   No

b)  use of spray bar, chute, or partial enclosure to mitigate emissions at the drop point to the truck?-----	Yes   No

PART IV:  SPECIAL CONDITIONS AND PROCEDURES – Rule 62-210.300(4)(d)4., F.A.C.

A.  New or Modified Process Equipment

1.  Since the last inspection has there been

a)  installation of any new process equipment?------------------------------------------------------------------	Yes	 No

b)  alterations to existing process equipment without replacement?------------------------------------------	Yes	 No

c)  replacement of existing equipment substantially different than that noted on the most

recent notification form?-----------------------------------------------------------------------------------------	Yes	 No

d)  If you answered YES to any of the above, did the owner submit a new and complete

notification form and appropriate fee (Rule 62-4.050, FAC) to the appropriate DEP or

local program office?---------------------------------------------------------------------------------------------	Yes	 No

Mike Ojo Thomas

_______________________________________________		__6/19/08___

Inspector’s Name (Please Print)				     Date of Inspection

_______________________________________________		___________________________________

Inspector’s Signature				     Approximate Date of Next Inspection

COMMENTS:  See the attached Pinellas County inspection report form for additional information

CONCRETE BATCHING PLANT

| FACILITY: Cemex Construction Materials, L.P | PERMIT ID: 2486 |
| --- | --- |
| Largo East RM Facility | DISTRICT: Southwest |
| ADDRESS: 2063 20th Avenue S.E. | CONTACT PHONE: |
| Largo, FL | 813-269-1240 |
| ARMS NO: 1030036 004 | PERMIT NO: | Expiration Date: 5/18/13 Renewal Date: 3/19/13 |
|  | 1030036-005-AG |  |
|  |  | Test Date: 4/30/00 |
| EMISSION UNIT DESCRIPTION: Truck load-out controlled by a C&W Manufacturing and Sales Co. Model CW-RA-140 Central Baghouse |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
| 6/19/08 | INS2 or INS_____ | IN MNC SNC |
| Type of Inspection: Initial Re-inspection Complaint Drive-by Quarterly A. General Review: |
| 1. | Permit File Review Yes No |
| 2. | Introduction and Entry Yes No Comments: I met onsite with the facility contact Mr. Rick Shanks, plant manager. He stated the emission unit is temporary shutdown due to lack of business. |
| 3. | Is the Authorized Representative still: Jason Jones? Yes No Comments: Mr. Jones stills the Authorized Representative |
| 4. | Is the facility contact still: Jason Jones? Yes No Comments: Mr. Jones stills the facility contact. |

| IN | MNC | SNC | B. Specific Conditions |
| --- | --- | --- | --- |
|  |  |  | The owner or operator of any equipment used to mix cement and soil for onsite soil augmentation or stabilization shall notify the Department by telephone, e-mail, fax, or written communication at least one (1) business day prior to changing location and transmit (by e-mail, fax, post, or courier) a Facility Relocation Notification Form (DEP Form No. 62-210.900(6)) to the Department no later than five (5) business days following relocation. The owner or operator of any other relocatable concrete batching plant proposing to change location shall transmit a Facility Relocation Notification Form to the Department at least five (5) business days prior to relocation. [62-210.310(5)(b)3.b., F.A.C.] Comments: This facility is not a relocatable concrete batch plant. |
|  |  |  | A facility using this air general permit may collocate with other facilities that separately registered for, and are also using, the concrete batching plant air general permit, and with facilities using the nonmetallic mineral processing plant air general permit at paragraph 62-210.310(5)(e), F.A.C., even if under the control of different persons, provided the following conditions are met. a. The collocation site does not contain any emissions units and pollutant-emitting activities other than concrete batching plants using air general permits, nonmetallic mineral processing plants using air general permits, and nonmetallic mineral processing plants or other emissions units and pollutant-emitting activities exempted from permitting pursuant to subsection 62- 210.300(3), F.A.C., or Rule 62-4.040, F.A.C. b. The total fuel consumption by all emissions units at the collocation site shall not exceed 275,000 gallons of diesel fuel, 23,000 gallons per year of gasoline, 44 million standard cubic feet per year of natural gas, or 1.3 million gallons per year of propane, or an equivalent prorated amount if multiple fuels are used. c. If multiple fuels are used, the equivalent prorated amount of each fuel burned shall not exceed the total amount of such fuel allowed to be burned, as given in sub-subparagraph b., multiplied by a fuel percentage. The fuel percentage is the percentage ratio of the amount of the fuel burned at the facility to the total amount of such fuel allowed to be burned at the facility pursuant to subparagraph b. The sum of the fuel percentages for all fuels burned by the facility shall not exceed one hundred percent (100%). d. The owners or operators of all collocated concrete batching plants and nonmetallic mineral processing plants shall maintain records to account for site-wide fuel consumption for each calendar month and each consecutive twelve (12) months. The owners or operators shall retain these records, available for Department inspection, for a period of at least five (5) years. [62-210.310(5)(b)4., F.A.C.] Comments: The facility does does not operate operated a nonmetallic mineral processing plant on-site under general permit No. _1030036-005-AG . Reviewed the records for the months of _n/a___, __n/a__, and __n/a__. The maximum 12 month totals of _n/a__gallons/year of fuel and _n/a__ tons/year of material processed. Pressure relief pop-up valve(s) – is there a accumulation of cement around the pop-off valves? Yes No Silo housings & duct work – are there any apparent leaks? Yes No |
|  |  |  | Unconfined Emissions. The owner or operator shall take reasonable precautions to control unconfined emissions from hoppers, storage and conveying equipment, conveyor drop points, truck loading and unloading, roads, parking areas, stock piles, and yards as required by Rule 62-296.320(4)(c), F.A.C. For concrete batching plants the following shall constitute reasonable precautions: (a) Management of roads, parking areas, stock piles, and yards, which shall include one or more of the following: 1. Paving and maintenance of roads, parking areas, and yards. 2. Application of water or environmentally safe dust- suppressant chemicals when necessary to control emissions. 3. Removal of particulate matter from roads and other paved areas under control of the owner or operator to mitigate re-entrainment, and from building or work areas to reduce airborne particulate matter. 4. Reduction of stock pile height or installation of wind breaks to mitigate wind entrainment of particulate matter from stock piles. (b) Use of spray bar, chute, or partial enclosure to mitigate emissions at the drop point to the truck. [62-296.414(2)] Comments: The facility yard was being maintained. There were no unconfined emissions observed. The entire yard at this facility is paved. |
|  |  |  | Visible emissions tests of silo dust collector exhaust points shall be conducted while loading the silo at a rate that is representative of the normal silo loading rate. The minimum loading rate shall be 25 tons per hour unless such rate is unachievable in practice. If emissions from the weigh hopper (batcher) operation are also controlled by the silo dust collector, the batching operation shall be in operation during the visible emissions test. The batching rate during the emissions test shall be representative of the normal batching rate and duration. Each test report shall state the actual silo loading rate during emissions testing and, if applicable, whether or not batching occurred during emissions testing. [62-296.414(3)(c), F.A.C.] Comments: The last test, on 4/30/08, was conducted at a process rate of _n/a__. Based on that test, the facility process rate was limited to _n/a__. Note: This is truck load-out process. |
|  |  |  | If emissions from the weigh hopper (batcher) operation are controlled by a dust collector which is separate from the silo dust collector, visible emissions tests of the weigh hopper (batcher) dust collector exhaust point shall be conducted while batching at a rate that is representative of the normal batching rate and duration. Each test report shall state the actual batching rate during emissions testing. [62-296.414(3)(d), F.A.C.] Comments: Emissions from the weigh hopper are not controlled by a separate dust collector. A separate test was not conducted at the appropriate rate. |
|  |  |  | Each dust collector exhaust point shall be tested annually. New facilities permitted pursuant to Rule 62-210.300(4), F.A.C., Air General Permits, shall demonstrate initial compliance no later than 30 days after beginning operation, and annual compliance within 60 days prior to each anniversary of the air general permit notification form submittal date. Existing facilities permitted pursuant to Rule 62-210.300(4), F.A.C., Air General Permits, shall demonstrate compliance within 60 days prior to submitting an air general permit notification form and within 60 days prior to each anniversary of the air general permit notification form submittal date. [62-296.414(4), F.A.C.] Comments: The visible emission test is required to be conducted annually. The last test was conducted on 4/30/08, and the test results were submitted on 5/02/08. |
|  |  |  | Test Reports. - The required test report shall be filed with the PCDEM as soon as practical but no later than 45 days after the test is completed. [Rules 62-213.440 and 62-297.310(8)(b), F.A.C.] Comments: The last test was conducted on 4/30/08, and the test results were submitted on 5/2/08. |
|  |  |  | The pollution control equipment shall be operated and maintained in accordance to the operation and maintenance (O&M) plan. The O&M plan shall include, but is not limited to: (1) Operating parameters of the pollution control device; (2) Time table for the routine maintenance of the pollution control device as specified by the manufacturer; (3) Time table for routine periodic observations of the pollution control device sufficient to ensure proper operation; (4) A list of the type and quantity of the required spare parts for the pollution control device which are stored on the premises of the permit applicant; (5) A record log which will indicate, at a minimum: a. When maintenance and observations were performed; b. What maintenance and observations were performed; and Who performed said maintenance and observations. Acceptable parameter ranges for each operational check. [Pinellas County Code, Subsection 58-128] Comments: Reviewed records for the months of 6/1/07 through 6/19/08 indicated emission unit in compliance. |

| C. General Procedure Requirements and Conditions |
| --- |
|  |  |  | Administrative Corrections. Within thirty (30) days of any minor changes requiring corrections to information contained in the registration form, the owner or operator shall notify the Department in writing. Such changes shall include: 1. Any change in the name, address, or phone number of the facility or authorized representative not associated with a change in ownership or with a physical relocation of the facility or any emissions units or operations comprising the facility; or 2. Any other similar minor administrative change at the facility. 62-210.310(2)(d), F.A.C.] Comments: Not applicable at this time. |
|  |  |  | Equipment Changes. The owner or operator shall maintain records of all equipment changes. In the case of installation of new process or air pollution control equipment, alteration of existing process or control equipment without replacement, or replacement of existing process or control equipment with equipment substantially different in terms of capacity, method of operation, material processed, or intended use than that noted on the most recent registration form, the owner or operator shall submit a new and complete air general permit registration form for the facility with the appropriate fee pursuant to Rule 62-4.050, F.A.C. to the Department, provided, however, that any change that would constitute a new major stationary source, major modification, or modification that would be a major modification but for the provisions of paragraph 62-212.400(2)(a), F.A.C., shall require authorization by air construction permit. 62-210.310(2)(e), F.A.C.] Comments: No changes at facility at this time. |
|  |  |  | The owner or operator’s use of an air general permit is limited to five (5) years. Prior to the end of the five (5) year term, the owner or operator who intends to continue using the air general permit for the facility shall re-register with the Department pursuant to subparagraph 62-210.310(2)(b)2., F.A.C. To avoid lapse of authority to operate, the owner or operator must submit the proper registration form and processing fee at least thirty (30) days prior to expiration of the facility’s existing air general permit. The air general permit re-registration form shall contain all current information regarding the facility. [General Conditions - 62-210.310(3)(a), F.A.C.] Comments: The permit expires on 5/18/13. A new notification form is required to be submitted no later than 3/19/13. |

D. Other:

Pollution Prevention Activities Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments:

Closing Conference Yes No Comments: I told Mr. Rick Shanks the emission unit is deemed to be in compliance.

Other Comments: The emission unit is temporary shutdown due to lack of business. An AQD VE test was not performed during this site visit. The emission unit is deemed to be in compliance.

Inspector(s): Mike Ojo Thomas, Pinellas County, Air Quality Division

Signature(s) Date: 7/1/08

CONTACT LOG? ___yes_,    ACCESS? _yes,    ARMs? _yes_

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030036 004 65343.doc