1030147 002 80742

NON-METALLIC MINERAL PROCESSING

PLANTS

COMPLIANCE INSPECTION CHECKLIST

INSPECTION TYPE:	ANNUAL (INS1, INS2)		COMPLAINT/DISCOVERY (CI)

RE-INSPECTION (FUI)		ARMS COMPLAINT NO:

AIRS ID#: 1030147 002	DATE:     4/2/2012		ARRIVE:     11:30am		DEPART:     1:00 pm

FACILITY NAME:  Sonny Glasbrenner, Inc.

FACILITY LOCATION:		3741 126th Avenue North

Clearwater, FL

RESPONSIBLE OFFICIAL:  Justin Strecker	PHONE:  727-573-1110

CONTACT NAME:   Justin Strecker?	PHONE:  727-573-1110

REMITTANCE YEAR:     		  ENTITLEMENT PERIOD:  	/	10/15/2012

(effective date)	(end date)

PART I:  INSPECTION COMPLIANCE STATUS (check  only one box)

 IN COMPLIANCE         MINOR Non-COMPLIANCE 	 SIGNIFICANT Non-COMPLIANCE

PART II:  DETERMINATION OF FACILITY TYPE/APPLICABILITY

(check  only one box)

FOR FACILTIES SUBJECT TO:  (40 CFR Part 60, Subpart OOO, §60.670(a)(1))

(If you have checked  this category, answer all questions INCLUDING those with **.)

Subject Facilities: (applicable fixed or portable facilities include each crusher, grinding mill, screening operation, bucket 	elevator, belt conveyor, bagging operation, storage bin, enclosed truck or railcar loading station, crushers & grinding mills at hot 	mix asphalt facilities that reduce the size of non-mettalic minerals embedded in recycled asphalt pavement & subsequent affected 	facilities up to, but not including the first storage silo or bin.)

FOR FACILITIES NOT SUBJECT TO:  (40 CFR Part 60, Subpart OOO, §60.670(a)(2), (b), (c), and (d))

(If you have checked  this category, answer all questions EXCEPT those with **.)

Non-Subject Facilities: (includes all facilities in underground mines; stand-alone screening operations at plants w/o crushers or 	grinding mills; facilities not subject to subparts F (Portland Cement Plants) or I (Hot Mix Asphalt Facilities) of this part; fixed 	sand & gravel plants, & crushed stone plants w/capacities of 23 megagrams/hr (25 tons/hr) or less; portable sand & gravel plants, 	& crushed stone plants w/capacities of 136 megagrams/hr (150 tons/hr) or less; common clay plants, and pumice plants 	w/capacities of 9 megagrams/hr (10 tons/hr) or less.)

PART III: EMISSION STANDARDS – Chapter 62-210.300(4)(c)5., F.A.C.

(check  appropriate box(es))

Stack Emissions - 40 CFR Part 60, Subpart OOO adopted by reference Chapter 62-204.800, F.A.C.

**1.  Were visible stack emissions tests conducted during this site visit according to EPA Method 9 (40 CFR 60,

Appendix A)?--------------------------------------------------------------------------------------------------------------	Yes	  No

**2.	Do stack emissions from any crusher, grinding mill, screening operation, bucket elevator, transfer point on

belt conveyors, bagging operation, storage bin, enclosed truck or railcar loading station or any other

affected emission point:

**a)	exceed 7% percent opacity?----------------------------------------------------------------------------------------	Yes	  No

**b)	exceed the particulate matter standard of  0.05 grams per dry standard cubic meter (g/dscm)?--------	Yes	  No

**3.	Do stack emissions from any baghouse that controls emissions from only an individual, enclosed storage

bin exceed 7% percent opacity?----------------------------------------------------------------------------------------	Yes    No

Visible Emissions - 40 CFR Part 60, Subpart OOO adopted by reference Chapter 62-204.800, F.A.C.

**1.  Were visible emissions tests conducted during this site visit according to EPA Method 9 (40 CFR 60,

Appendix A)?--------------------------------------------------------------------------------------------------------------	Yes    No

**2.	Do visible emissions from any:

**a)	grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging operation,

storage bin, enclosed truck or railcar loading station or any other affected emission point exceed 10%

percent opacity?-----------------------------------------------------------------------------------------------------------	Yes    No

**b)	crusher without a capture system, exceed 15 % opacity?------------------------------------------------------	Yes    No

3.	Pursuant to subparagraph 62-296.320(4)(b)1., F.A.C., are visible emissions from any crusher, grinding,

screening operation, bucket elevator, transfer points on belt conveyors, bagging operation, storage bin,

enclosed truck or railcar loading station, or any other emission point NOT subject to 40 CFR Part 60,

Subpart OOO, equal to or greater than 20% percent opacity?-----------------------------------------------------	Yes    No

Emission Points Enclosed in Buildings - 40 CFR Part 60, Subpart OOO adopted by reference Chapter 62-204.800, F.A.C.

**4.  Is any crusher, grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging

operation, storage bin, enclosed truck or railcar loading station, or any other affected emission point enclosed

in a building? (If answer to question #4 is YES, then proceed to #4.a)).---------------------------------------	Yes    No

**a)	If enclosed in a building are the stack emissions discharged from a wet scrubbing control device? (If

answer to this question is NO, then proceed to the next question #4.b)1) & 2). If YES skip to #4.c).)--	Yes    No

**b)	If the stack emissions from enclosed emission points are not discharged from a wet scrubbing control device is:

1)	the particulate matter in excess of 0.05 grams per dry standard cubic meter (g/dscm)?-------------	Yes    No

2)	the opacity greater than 7% percent?--------------------------------------------------------------------------	Yes    No

**c)	Do the stack emissions from the baghouse(s) inside of the building(s) exceed 7% percent opacity?---	Yes    No

**5.	Do visible emissions from any:

**a)	grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging operation,

storage bin, enclosed truck or railcar loading station or any other affected emission point exceed 10%

percent opacity?-------------------------------------------------------------------------------------------------------	Yes    No		**b)	crusher without a capture system, exceed 15 % opacity?------------------------------------------------------	Yes    No

Wet Screening/Wet Mining Operations:

**6.	Are there any visible emissions discharges at the wet screening operations and subsequent screening

operations, bucket elevators and belt conveyors that process saturated material in the production line up to

the next crusher, grinding mill, or storage bin?----------------------------------------------------------------------	Yes    No

**7.	Are there any visible emissions discharges at the screening operations, bucket elevators, and belt conveyors

in the production line downstream of wet mining operations, where such screening operations, bucket

elevators, and belt conveyors process saturated materials up to the first crusher , grinding mill, or storage bin

in the production line?----------------------------------------------------------------------------------------------------	Yes    No

PART IV: TESTING/RECORDKEEPING REQUIREMENTS – Rule 62-210.300, F.A.C.

(check  appropriate box(es)

Compliance Demonstration – (Rule 62-210.300(4)(c)5.h., F.A.C.)

1.	Is each affected emission point tested according to the visible emissions and stack emissions standards as

part of the annual compliance demonstration? (Rule 62-210.300(4)(c)5.e., F.A.C.)--------------------------	Yes    No

Compliance New Facilities – (Rule 62-210.300(4)(c)5.h., F.A.C.)

2.	Did this facility demonstrate, according to the visible emissions and stack emissions standards of

Rule 62-210.300(4)(c)5.e., F.A.C.,:

a)	initial compliance prior to beginning commercial operation? ------------------------------------------------	Yes    No

b)	renewal compliance within 60 days prior to the anniversary of the initial air general permit notification

form submittal date?------------------------------------------------------------------------------------------------------	Yes    No

Compliance Existing Facilities – (Rule 62-210.300(4)(c)5.h., F.A.C.)

3.  Did this facility demonstrate, according to the visible emissions and stack emissions standards of

Rule 62-210.300(4)(c)5.e., F.A.C.,:

a)	compliance within 60 days prior to submitting an air general permit notification form?-----------------	Yes    No

b)	renewal compliance within 60 days prior to the anniversary of the initial air general permit notification

form submittal date? -------------------------------------------------------------------------------------------------	Yes    No

Test Methods and Procedures – Chapter 62-297, F.A.C., 40 CFR 60.675, and 40 CFR Part 60, Appendix A adopted and 	incorporated by reference at Rule 62-204.800, F.A.C.

4.	Were all referenced visible emissions tests conducted using EPA Method 9?----------------------------------	Yes    No

5.	Were all referenced unconfined or fugitive emissions tests conducted using EPA Method 22?-------------	Yes    No

6.	Were all referenced stack emissions or particulate matter tests conducted using EPA Methods 5 or 17?	Yes    No

Reporting and Recordkeeping – (Rule 62-210.300(4)(c)5.e., F.A.C. )[Chapter 62-297, F.A.C. and

40 CFR Part 60.670 – 60.676, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C.]

Facility and/or Equipment Replacement

**7.  Did the owner or operator submit to the Administrator, the following information about the replacement of existing facility 		and/or equipment:

**a)	for a Crusher, Grinding Mill, Bucket Elevator, Bagging Operation, or enclosed truck, or Railcar Loading Station,

**1)	the rated capacity in megagrams or tons per hour of the existing facility being replaced and the rated

capacity in tons per hour of the replacement equipment?--------------------------------------------------	Yes    No

**b)	for a Screening Operation,

**1)	the total surface area of the top screen of the existing screening operation being replaced and the total

surface area of the top screen of the replacement screening operation?---------------------------------	Yes    No

**c)	for a Conveyor Belt,

**1)	the width of the existing belt being replaced and the width of the replacement conveyor belt?-----	Yes    No

**d)	for a Storage Bin,

**1)	the rated capacity in megagrams or tons of the existing storage bin being replaced and the rated

capacity in megagrams or tons of replacement storage bins?----------------------------------------------	Yes    No

Performance/Compliance Testing

**8.	During the initial performance test, did the owner or operator record the measurements of both the change

in pressure of the gas stream across the scrubber and the scrubbing liquid flow rate?------------------------	Yes    No

**9.	After the initial performance test of a wet scrubber, did the owner or operator submit semiannual reports to

the Administrator of occurrences when the measurements of the scrubber pressure loss (or gain) and liquid

flow rate differ by more than ±30 percent from the averaged determined during the most recent performance

test?--------------------------------------------------------------------------------------------------------------------------	Yes    No

**a)  Were the reports postmarked within 30 days following the end of the second and fourth calendar

quarters?--------------------------------------------------------------------------------------------------------------------	Yes    No

PART IV: TESTING/RECORDKEEPING REQUIREMENTS – Rule 62-210.300, F.A.C. (Continued)

(check  appropriate box(es)

**10.	Did the owner or operator of the facility submit written reports of the results of all performance tests

conducted to demonstrate compliance with the particulate matter standards (40 CFR Part 60.672), opacity

(using EPA Method 9 to demonstrate compliance with 40 CFR Part 60.672(b), (c), and (f)), and emission

observations of transfer points enclosed in buildings (using EPA Method 22 to demonstrate compliance with

40 CFR Part 60.672(e))?------------------------------------------------------------------------------------------------	Yes    No

Process Changes

**11.	Does this facility have a screening operation, bucket elevator, and/or a belt conveyor system?  (If your

answer to this question is YES, then answer either a)1) or a)2) below.)--------------------------------------	Yes    No

**a)	Did this screening operation, bucket elevator, and/or belt conveyor system:

**1)	originally process saturated material and switch to unsaturated material? (Note: The unsaturated

material handling processes would now be subject to the 10% opacity limit in 40 CFR 60.672(b)

and the emission test requirements of 40 CFR 60.11 and Subpart OOO.)---------------------------	Yes    No

**2)	originally process unsaturated material and switch to saturated material? (Note:  The saturated								material handling processes would now be subject to the no visible emission limit in 40 CFR 60.672(h).)							(If answer to 1) or 2) above is YES then proceed to question  b) below.)-----------------------------	Yes    No		**b)	Did the owner or operator submit a report of the process change within thirty (30) days following the							change?-----------------------------------------------------------------------------------------------------------------	Yes    No

Notification Requirements

**12.	Was notification of the actual date of startup for each affected or combination of affected facilities

submitted to the Administrator and postmarked within 15 days after such date?------------------------------	Yes    No

**a)		Did the notification include a description of each affected facility, equipment manufacturer, and serial

number of the equipment, if available?---------------------------------------------------------------------------	Yes    No

**b)	For portable aggregate processing plants, did the notification of actual date of initial start up also

include both the home office and the current address or location of the portable plant?-----------------	Yes    No

PART V:  OPERATING REQUIREMENTS/CONTROL TECHNOLOGY – Rule 62-210.300, F.A.C.

(check  appropriate box(es))

1.	Is this facility a:   1) relocatable;    2) stationary;   or does it have:  3) both, stationary and relocatable

concrete batching and/or nonmetallic mineral processing plants? (Please check  only one box above.)

(NOTE: If you have checked the box for relocatable go to questions 1.a) & 1.b).  If you have checked the box for

stationary go to question 1.c). If you have checked box #3, both, stationary and relocatable then answer all

relocatable and stationary questions 1.a), 1.b), & 1.c) below, respectively.)

a)	If this is a relocatable facility was the Department notified by phone prior to this relocation, and was a

Facility Relocation Notification form submitted within 1 business day following the relocation?------	Yes    No

b)	If this is a relocatable facility, is it located at a mine and/or quarry, and processing only material from onsite

deposits? (If your answer to this question is NO, please proceed to question 1) below.)---------------	Yes    No

1)	Does the owner or operator of this relocatable facility have a water suppression system with spray

bars located at the feeder(s), the entrance, and the exit of the crusher(s), the classifier screens and the

conveyor drop points?------------------------------------------------------------------------------------------------	Yes    No

c)	If this is a stationary facility, does the owner or operator of this stationary facility have a water

suppression system with spray bars located at the feeder(s), the entrance, and the exit of the crusher(s),

the classifier screens and the conveyor drop points?------------------------------------------------------------	Yes    No

PART V:  OPERATING REQUIREMENTS/CONTROL TECHNOLOGY – Rule 62-210.300, F.A.C. (Continued)

(check  appropriate box(es))

**2.	Does this facility incorporate the use of a wet scrubber to control emissions? (40 CFR Part 60, Subpart OOO

adopted by reference Chapter 62-204.800, F.A.C.) (If your answer to this question is YES, then proceed to

questions 2.a) and 2.b), below.)----------------------------------------------------------------------------------------	Yes    No	**a)	Does the wet scrubber have continuous monitoring systems (CMS) for:

**1)  the measurement of the pressure loss of the gas stream through the scrubber?--------------------------	Yes    No		**2)  the measurement of the scrubbing liquid flow rate to the wet scrubber?----------------------------------	Yes    No	**b)	Has each CMS been certified by the manufacturer and calibrated annually in accordance with the						manufacturer’s instructions and to the tolerances below?------------------------------------------------------	Yes    No		**1)  ±250 pascals ±1 inch water guage pressure for measuring pressure losses of the gas stream?--------	Yes    No		**2)  ±5 percent of design scrubbing liquid flow rate?--------------------------------------------------------------	Yes    No

3.  Is this is a stationary nonmetallic mineral processing plant, with a stationary concrete batching plant using an 					individual concrete batching plant air general permit at the same location? (If your answer to this question

is YES, then proceed to questions 3.a), thru  3.d),) below. If NO, proceed to question #4.)--------------	Yes    No		a)	Is there more than one nonmetallic mineral processing plant in operation at this location?-------------	Yes    No		b)	If there is more than one nonmetallic mineral processing plant at this location, do they all operate under

a single nonmetallic mineral processing plant air general permit?-------------------------------------------	Yes    No		c)	Are there any additional nonexempt units located at this facility?-------------------------------------------	Yes    No		d)	Are there any Title V sources located at this facility?---------------------------------------------------------	Yes    No	4.	Is this is a stationary nonmetallic mineral processing plant, with one or more relocatable concrete

batching plants using individual air general permits at the same location? (If your answer to this

question is YES, then proceed to questions 4.a), thru  4.b) below.  If NO, then proceed to question 5.)	Yes    No

a)	Are there any additional nonexempt units located at this facility?-------------------------------------------	Yes    No

b)	Are there any Title V sources located at this facility?---------------------------------------------------------	Yes    No

5.	Does the owner or operator of this facility operate multiple relocatable nonmetallic mineral processing

plants using individual nonmetallic mineral processing plant air general permits at this location?--------	 Yes    No

a)	Are there any additional nonexempt units located at this facility?-------------------------------------------	Yes    No

b)	Is the total combined annual facility-wide fuel oil usage of all plants less than 240,000 gallons per

calendar year?---------------------------------------------------------------------------------------------------------	Yes    No

c)	Is the quantity of material processed less than ten million tons per calendar year?-----------------------	Yes    No

d)	Is the fuel oil sulfur content 0.5% by weight or less?----------------------------------------------------------	Yes    No

6.	Does the owner/operator of the concrete batching plant maintain a log book or books to account for:

a)	fuel consumption on a monthly basis?----------------------------------------------------------------------------	Yes    No

b)	material processed on a monthly basis?--------------------------------------------------------------------------	Yes    No

c)	the sulfur content of the fuel being burned (Fuel supplier certifications)?---------------------------------	Yes    No

7.	Is this relocatable nonmetallic mineral processing plant used to perform a routine function of a facility (not

a Title V source) subject to regular air permitting, such as crushing recycled asphalt (rap) at an asphalt

plant?-----------------------------------------------------------------------------------------------------------------------	Yes    No

a)	If YES, does the regularly permitted facility air construction or air operation permit(s) provide for the

operation of the nonmetallic mineral processing plant as an emission unit?-------------------------------	Yes    No

8.	Is this relocatable nonmetallic mineral processing plant used to perform a non-routine activity, such as

destruction of a building, at a regularly permitted facility (not a Title V source)?----------------------------	Yes    No

a)	If YES, does it operate under the authority of its air general permit?---------------------------------------	Yes    No

PART VI:  REASONABLE PRECAUTIONS/EMISSION CONTROL MEASURES & TECHNOLOGY – Rule 62-			210.300(4)(c)5.d.(i) and (ii), F.A.C.

(check  appropriate box(es))

Unconfined Emissions – (Rule 62-296.320(4)(c), F.A.C.)

1.  Does the owner /operator of the nonmetallic mineral processing plant take reasonable precautions to control unconfined

emissions by:

a)  use of a water suppression system with spray bars located at the feeder(s), the entrance and exit of the

crusher(s), the classifier screens, and the conveyor drop points?--------------------------------------------	Yes    No

b)  management of roads, parking areas, stock piles, and yards, which shall include one or more of the following:

1)  paving and maintenance of roads, parking areas, stock piles, and yards?------------------------------	Yes    No

2)  application of water or environmentally safe dust-suppressant chemicals when necessary to control

emissions?---------------------------------------------------------------------------------------------------------	Yes    No 			3)	removal of particulate matter from roads and other paved areas under control of the owner/operator to

re-entrainment, and from building or work areas to reduce airborne particulate matter?-----------	Yes    No

4)  reduction of stock pile height, or installation of wind breaks to mitigate wind entrainment of

particulate matter from stock piles?--------------------------------------------------------------------------	Yes    No

5)  landscaping and/or the planting of vegetation?-------------------------------------------------------------	Yes    No

6)	the use of hoods, fans, filters and similar equipment to contain, capture and/or vent particulate 							matter?------------------------------------------------------------------------------------------------------------	Yes    No			7)	the enclosure or covering of  conveyor systems?----------------------------------------------------------	Yes    No

PART VII:  SPECIAL CONDITIONS AND PROCEDURES – Rule 62-210.300(4)(d)4., F.A.C.

A.  New or Modified Process Equipment

1.  Since the last inspection has there been

a)  installation of any new process equipment?-----------------------------------------------------------------	Yes	No

b)  alteration of existing process equipment without replacement?------------------------------------------	Yes	No

c)  replacement of existing equipment substantially different than that noted on the most

recent notification form?----------------------------------------------------------------------------------------	Yes	No

d)  If you answered YES to any of the above, did the owner submit a new and complete

notification form and appropriate fee (Rule 62-4.050, F.A.C.) to the appropriate DEP or

local program office?--------------------------------------------------------------------------------------------	Yes	No

Shea  Jackson 	4/2/2012

_______________________________________________		___________________________________

Inspector’s Name (Please Print)				     Date of Inspection

2013

_______________________________________________		___________________________________

Inspector’s Signature				     Approximate Date of Next Inspection

COMMENTS:  See the attached Pinellas County inspection report form for additional information

| FACILITY: Sonny Glasbrenner, Inc. | PERMIT ID: 385 |
| --- | --- |
| Reclaimed Concrete and Asphalt Processing Plant | DISTRICT: Southwest |
| ADDRESS: 3741 126th Avenue North | CONTACT PHONE: |
| Clearwater, FL | 727-573-1110 |
| ARMS NO: 1030147 002 | PERMIT NO: | Expiration Date: 10/15/2012 Renewal Date: 9/15/2012 |
|  | 1030147-009-AG |  |
|  |  | Test Date: 12/10/2000 |
| EMISSION UNIT DESCRIPTION: Concrete and Asphalt Processing System: Bohringer Model RC14 Jow Crusher, Grizzly Feeder, 2 Screening Operations, 5 Conveyor Belt, and Truck Loading |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
| April 2, 2012 | INS2 or INS_____ | IN MNC SNC |
| Type of Inspection: Initial Re-inspection Complaint Drive-by Quarterly A. General Review: |
| 1. | Permit File Review Yes No |
| 2. | Introduction and Entry Yes No Comments: I met on site with Andy Risi, owner, and Laura Ferriolo, facility contact to reviewed the crusher records. |
| 3. | Is the Authorized Representative still: Justin Strecker? Yes No Comments: yes, he was not on site at this time |
| 4. | Is the facility contact still: Justin Strecker? Yes No Comments: yes, not on site |
| 5. | Does the equipment on-site match the notification form [Rule 62-210.300] Yes No Comments: yes, no changes. |

| IN | MNC | SNC | B. Specific Conditions |
| --- | --- | --- | --- |
|  |  |  | The owner or operator of any relocatable nonmetallic mineral processing plant proposing to change location shall notify the Department by phone prior to changing location and submit a Facility Relocation Notification Form (DEP Form No. 62-210.900(6)) to the Department no later than one (1) business day following relocation [62-210.300(4)(c)5.b., F.A.C.] Comments: This facility is or is not a relocatable nonmetallic mineral processing plant. |
|  |  |  | For all relocatable nonmetallic mineral processing plants, except those located at mines or quarries and processing only material from onsite natural deposits, and for all stationary nonmetallic mineral processing plants processing dry material, the owner or operator shall have a water suppression system with spray bars located at the feeder(s), the entrance and exit of the crusher(s), the classifier screens, and the conveyor drop points [62-210.300(4)(c)5.c., F.A.C.] Comments: The facility does does not operate a water suppression system, and the system is is not functional. |
|  |  |  | The owner or operator shall comply with paragraph 62-296.320(4)(c), F.A.C., using the following reasonable precautions: (i) Unconfined emissions that might be generated from various activities throughout a nonmetallic mineral processing plant processing dry material shall be controlled by using a water suppression system with spray bars located at the feeder(s), the entrance and exit of the crusher(s), the classifier screens, and the conveyor drop points. (ii) Unconfined emissions that might be generated by vehicular traffic or wind shall be controlled by applying water (by water trucks equipped with spray bars) or effective dust suppressant(s) on a regular basis to all stockpiles, roadways and work-yards where this nonmetallic mineral processing plant is located; [62-210.300(4)(c)5.d., F.A.C.] Comments: I advised Mr. Risi, that there were some very dry areas which needed additional water where the vehicular traffic was crossing into areas not wetted by the water truck. I noted that the vehicular traffic was heavier due to the additional trucks on site connected to the Greenway recycling operations. I told him that some of the traffic going to the building to unload were generating more dust where the water truck could not keep up with the activities connected to the crusher and the recycling operations. Mr. Risi stated he would speak with the owners in regards to getting an additional water truck, and wetting the stock piles with sprinklers so that the payloaders when loading the materials into the crusher hopper.. Mr. Risi stated they could put a sprinkler system on the stockpiles to wet over night to help maintain moisture in stock pile to reduce dust. |
|  |  |  | Stack emissions from any crusher, grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging operation, storage bin, enclosed truck or railcar loading station, or any other affected emission point subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., shall not contain particulate matter in excess of 0.05 grams per dry standard cubic meter (g/dscm) nor exceed 7% opacity, unless the stack emissions are discharged from a wet scrubbing control device. [62-210.300(4)(c)5.e.(i), F.A.C.] Comments: An AQD VE test was performed during this site visit; Yes , or No , or NA . The results of the various points were: There is not a stack connected to the crusher and screening operations. |
|  |  |  | Stack emissions from any baghouse that controls emissions from only an individual, enclosed storage bin subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., shall not exceed 7% opacity. [62-210.300(4)(c)5.e.(ii), F.A.C.] Comments: The facility does does not operate an enclosed storage bin with a baghouse. There is not a stack or baghouse control system or enclosed storage bin connected to the crusher and screening operations. |
|  |  |  | Visible emissions from any grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging operation, storage bin, enclosed truck or railcar loading station, or any other affected emission point subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., shall not exceed 10% opacity; and visible emissions from any crusher without a capture system subject to 40 CFR Part 60, Subpart OOO, shall not exceed 15% opacity. [62-210.300(4)(c)5.e.(iii), F.A.C.] Comments: An AQD VE test was performed during this site visit; Yes , or No , or NA The results of the various points were: |
|  |  |  | Truck dumping of nonmetallic minerals into any screening operation, feed hopper, or crusher subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., is exempt from the emissions standards of sub-subparagraph 62-210.300(4)(c)5.e., F.A.C.; [62-210.300(4)(c)5.e.(vi), F.A.C.] Comments: There is no truck dumping into the hopper or screening operation for the crusher. |
|  |  |  | The owner or operator shall ensure that wet screening operations and subsequent screening operations, bucket elevators, and belt conveyors that process saturated material in the production line up to the next crusher, grinding mill or storage bin and are subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., do not discharge any visible emissions. The owner or operator shall also ensure that screening operations, bucket elevators, and belt conveyors in the production line downstream of wet mining operations, where such screening operations, bucket elevators, and belt conveyors process saturated materials up to the first crusher, grinding mill, or storage bin in the production line and are subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., do not discharge any visible emissions; [62-210.300(4)(c)5.f., F.A.C.] Comments: There is no wet mining operation connected to the operation of the crusher screening operations. |
|  |  |  | The owner or operator of a nonmetallic mineral processing plant subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., and using a wet scrubber to control emissions shall comply with the monitoring requirements of 40 CFR 60.674, adopted and incorporated by reference at Rule 62-204.800, F.A.C.; [62-210.300(4)(c)5.g., F.A.C.] §60.674 Monitoring of operations. The owner or operator of any affected facility subject to the provisions of this subpart which uses a wet scrubber to control emissions shall install, calibrate, maintain and operate the following monitoring devices: (a) A device for the continuous measurement of the pressure loss of the gas stream through the scrubber. The monitoring device must be certified by the manufacturer to be accurate within ±250 pascals ±1 inch water gauge pressure and must be calibrated on an annual basis in accordance with manufacturer's instructions. (b) A device for the continuous measurement of the scrubbing liquid flow rate to the wet scrubber. The monitoring device must be certified by the manufacturer to be accurate within ±5 percent of design scrubbing liquid flow rate and must be calibrated on an annual basis in accordance with manufacturer's instructions. Comments: The facility does does not operate a wet scrubber. |
|  |  |  | The owner or operator of any existing facility shall demonstrate compliance with the emission standards of sub-subparagraph 62-210.300(4)(c)5.e., F.A.C., within 60 days prior to submitting an air general permit notification form and shall demonstrate renewal compliance within 60 days prior to the anniversary of the initial air general permit notification form submittal date. [62-210.300(4)(c)5.h., F.A.C.] Comments: The test for renewal should be completed within 60 days prior to 12/10/2012. I informed Mr. Risi, the owner that the permit expiration and the VE test requirement for the permit renewal could be the same if coordinated for the permit application. The last test was performed on 12/8/2011 |
|  |  |  | The owner or operator shall meet all applicable reporting and recordkeeping requirements of Chapter 62-297, F.A.C. and 40 CFR 60.676, adopted and incorporated by reference at Rule 62-204.800, F.A.C.; [62-210.300(4)(c)5.i., F.A.C.] §60.676 Reporting and recordkeeping. (a) Each owner or operator seeking to comply with §60.670(d) shall submit to the Administrator the following information about the existing facility being replaced and the replacement piece of equipment. (1) For a crusher, grinding mill, bucket elevator, bagging operation, or enclosed truck or railcar loading station: (i) The rated capacity in megagrams or tons per hour of the existing facility being replaced and (ii) The rated capacity in tons per hour of the replacement equipment. (2) For a screening operation: (i) The total surface area of the top screen of the existing screening operation being replaced and (ii) The total surface area of the top screen of the replacement screening operation. (3) For a conveyor belt: (i) The width of the existing belt being replaced and (ii) The width of the replacement conveyor belt. (4) For a storage bin: (i) The rated capacity in megagrams or tons of the existing storage bin being replaced and (ii) The rated capacity in megagrams or tons of replacement storage bins. (c) During the initial performance test of a wet scrubber, and daily thereafter, the owner or operator shall record the measurements of both the change in pressure of the gas stream across the scrubber and the scrubbing liquid flow rate. (d) After the initial performance test of a wet scrubber, the owner or operator shall submit semiannual reports to the Administrator of occurrences when the measurements of the scrubber pressure loss (or gain) and liquid flow rate differ by more than ±30 percent from the averaged determined during the most recent performance test. (e) The reports required under paragraph (d) shall be postmarked within 30 days following end of the second and fourth calendar quarters. (f) The owner or operator of any affected facility shall submit written reports of the results of all performance tests conducted to demonstrate compliance with the standards set forth in §60.672 of this subpart, including reports of opacity observations made using Method 9 to demonstrate compliance with § 60.672(b), (c), and (f), and reports of observations using Method 22 to demonstrate compliance with § 60.672(e). (g) The owner or operator of any screening operation, bucket elevator, or belt conveyor that processes saturated material and is subject to §60.672(h) and subsequently processes unsaturated materials, shall submit a report of this change within 30 days following such change. This screening operation, bucket elevator, or belt conveyor is then subject to the 10 percent opacity limit in §60.672(b) and the emission test requirements of § 60.11 and this subpart. Likewise a screening operation, bucket elevator, or belt conveyor that processes unsaturated material but subsequently processes saturated material shall submit a report of this change within 30 days following such change. This screening operation, bucket elevator, or belt conveyor is then subject to the no visible emission limit in §60.672(h). (h) The subpart A requirement under §60.7(a)(2) for notification of the anticipated date of initial startup of an affected facility shall be waived for owners or operators of affected facilities regulated under this subpart. (i) A notification of the actual date of initial startup of each affected facility shall be submitted to the Administrator. (1) For a combination of affected facilities in a production line that begin actual initial startup on the same day, a single notification of startup may be submitted by the owner or operator to the Administrator. The notification shall be postmarked within 15 days after such date and shall include a description of each affected facility, equipment manufacturer, and serial number of the equipment, if available. (2) For portable aggregate processing plants, the notification of the actual date of initial startup shall include both the home office and the current address or location of the portable plant. (j) The requirements of this section remain in force until and unless the Agency, in delegating enforcement authority to a State under section 111(c) of the Act, approves reporting requirements or an alternative means of compliance surveillance adopted by such States. In that event, affected facilities within the State will be relieved of the obligation to comply with the reporting requirements of this section, provided that they comply with requirements established by the State. Comments: The most recent performance testing Method 9 performed on 12/8/2011 , showed the unit process rate to be 150 Tons in 30 minutes, with 0% opacity. There were no additional equipment changes to the crushers at this time, no additional emission points added. |
|  |  |  | The owner or operator of a stationary nonmetallic mineral processing plant using an air general permit may operate a stationary concrete batching plant using an air general permit at the same location provided all nonmetallic mineral processing plant units operate under a single nonmetallic mineral processing plant air general permit, all concrete batching plant units operate under a single concrete batching plant air general permit, and the resultant facility contains no additional nonexempt units and would not be a Title V source; [62-210.300(4)(c)5.j., F.A.C.] Comments: The crushing operation is located independently or with a stationary concrete batch plant. The operations are are not considered a Title V source. (See below) |
|  |  |  | The owner or operator of a stationary nonmetallic mineral processing plant using an air general permit may operate, or allow the operation of, one or more relocatable concrete batching plants using individual air general permits at the same location as the nonmetallic mineral processing plant provided the resultant facility contains no additional nonexempt units and would not be a Title V source; [62-210.300(4)(c)5.k., F.A.C.] Comments: The crushing operation is located independently or with relocatable concrete batch plant(s). The operations are are not considered a Title V source. (See below) |
|  |  |  | The owner or operator of multiple relocatable nonmetallic mineral processing plants using individual nonmetallic mineral processing plant air general permits may operate more than one such plant at the same location provided the resultant facility contains no additional nonexempt units, the total combined annual facility-wide fuel oil usage of all plants is less than 240,000 gallons per calendar year, the material processed is less than 10 million tons per calendar year, and the fuel oil sulfur content does not exceed 0.5%, by weight. The owner or operator of the nonmetallic mineral processing plants shall maintain a log book to account for fuel consumption and material processed on a monthly basis. Fuel supplier certifications shall be maintained to account for the sulfur content of the fuel being burned; and [62-210.300(4)(c)5.l., F.A.C.] Comments: The facility does does not operate multiple nonmetallic mineral processing plants using an individual air general permit. Records are required, yes no. If required, records reviewed from Jan 2010_ to March 30, 2012_ The maximum 12 month totals of 11,208 gallons/ year of fuel and 60,612_ tons/year of material processed. The sulfur content 0.08_% . |
|  |  |  | If a relocatable nonmetallic mineral processing plant is used to perform a routine function of a facility subject to regular air permitting, such as crushing recycled asphalt (rap) at an asphalt plant, it shall not operate under the authority of an air general permit. In such case, the regularly permitted facility air construction or air operation permit(s) must provide for operation of the nonmetallic mineral processing plant as an emission unit. If a relocatable nonmetallic mineral processing plant is used at a regularly permitted facility for a non-routine activity, such as destruction of a building, it may do so under the authority of its air general permit. In either case, the resultant facility shall not be a Title V source. [62-210.300(4)(c)5.m., F.A.C.] Comments: The crushing operation is is not operating at a regularly permitted facility, for the purposes of a routine function crushing concrete. non-routine activity (______________________). |

| IN | MNC | SNC | C. Selected General Conditions and Procedures |
| --- | --- | --- | --- |
|  |  |  | Administrative Corrections. Within 30 days of any changes requiring corrections to information contained in the notification form, the owner or operator shall notify the Department in writing. Such changes shall include: a. Any change in the name of the authorized representative or facility address or phone number; or b. Any other similar minor administrative change at the facility or emissions unit. [62-210.300(4)(d)3., F.A.C.] Comments: there have been no changes in the authorized representative or etc. |
|  |  |  | Equipment Changes. In case of the installation of new process equipment, alteration of existing process equipment without replacement, or the replacement of existing process equipment with equipment substantially different than that noted on the most recent notification form, the owner or operator shall submit a new and complete general permit notification form with the appropriate fee pursuant to Rule 62-4.050, F.A.C., to the appropriate Department of Environmental Protection district office or local air pollution control program office to which the Department has delegated its permitting authority. [62-210.300(4)(d)3., F.A.C.] Comments: there have been no changes. |
|  |  |  | If, for any reason, the owner or operator of any facility operating under an air general permit pursuant to Rule 62-210.300(4)(a), F.A.C., does not comply with or will be unable to comply with any condition or limitation of the permit, the permittee shall immediately provide the Department with the following information: 1. A description of and cause of noncompliance; and 2. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result. [62-210.300(4)(e)13., F.A.C.] Comments: there have been no non compliance issues to report. |
|  |  |  | Valid Permit Throughout the term of the general permit: a. The facility operates no emissions units other than a unit described in an air general permit and emissions units which are exempt from permitting pursuant to the criteria of Rule 62-210.300(3)(a) or (b), F.A.C.; b. The facility is not a Title V source as defined in Rule 62-210.200, F.A.C. [62-210.300(4)(c), F.A.C. Comments: The facility permit is valid for the operation for the crushers. The Greenway recycling operation equipment is being evaluated to determine if there would be |
|  |  |  | A permittee’s use of a general permit is limited to five years. No later than 30 days prior to the fifth anniversary of the filing of intent to use the general permit, the owner or operator shall submit a new notice of intent which shall contain all current information regarding the facility or emissions unit. Eligibility to use the general permit is not transferable and does not follow a change in ownership of the facility or emissions unit. Prior to any sale, other change of ownership, or permanent shutdown of the facility, the owner or operator is encouraged to notify the Department of the pending action. The owner shall remain liable for corrective actions that may be required as a result of any violations occurring in the time after the sale or legal transfer of the facility or emissions unit, but before a new owner is entitled to use an air general permit. [General Conditions - 62-210.300(4)(e)1., F.A.C.] Comments: The permit expires on 10/15/2012. A new notification form is required to be submitted no later than 9/15/2012. I informed Mr. Risi of the permit renewal date verbally and in an additional email. |
|  |  |  | No person shall circumvent any air pollution control device or allow the emission of air pollutants without the proper operation of all applicable air pollution control devices. [62-210.300(4)(e)12., F.A.C.] Comments: there is no circumvention of the water suppressant system for the crushers. |

D. Other:

Closing Conference Yes  No

Other Comments: I informed Mr. Risi of the need to apply additional reasonable precautions due to dry conditions and additional site activities. I asked him to propose remedies and submit information requested for the Greenway recycling facility.

Inspector(s): Shea Jackson, Pinellas County, Air Quality Division

Signature(s) Date: April 3, 2012

ACCESS? __yes_______,    GCPIs? ___yes________

H:\USERS\WPDOCS\Airqual\Air_Compliance\AQI\1030147 002 80742.doc

Sonny Glasbrenner, Inc.  Reclaimed Concrete and Asphalt Processing Plant

3741 126th Avenue North, Clearwater

Project Id:	80742	Permit No: 1030147-009-AG	Arms Number: 0147 002

Inspector:	Shea Jackson	Inspection Date / Time: 4/2/2012  / _______

Source (EU):	Concrete and Asphalt Processing System:  Bohringer Model RC14 Jow Crusher, Grizzly Feeder, 2 Screening Operations, 5 Conveyor Belt, and Truck Loading

# Description:	[This unit was crushing asphalt, today normal crushes concrete]

Sonny Glasbrenner, Inc.  Reclaimed Concrete and Asphalt Processing Plant

3741 126th Avenue North, Clearwater

Project Id:	80742	Permit No: 1030147-009-AG	Arms Number: 0147 002

Inspector:	Shea Jackson	Inspection Date / Time: 4/2/2012  / _______

Source (EU):	Concrete and Asphalt Processing System:  Bohringer Model RC14 Jow Crusher, Grizzly Feeder, 2 Screening Operations, 5 Conveyor Belt, and Truck Loading

# Description:	[ The crusher emission unit was crushing asphalt ]

Sonny Glasbrenner, Inc.  Reclaimed Concrete and Asphalt Processing Plant

3741 126th Avenue North, Clearwater

Project Id:	80742	Permit No: 1030147-009-AG	Arms Number: 0147 002

Inspector:	Shea Jackson		Inspection Date / Time: 4/2/2012

Source (EU):	Concrete and Asphalt Processing System:  Bohringer Model RC14 Jow Crusher, Grizzly Feeder, 2 Screening Operations, 5 Conveyor Belt, and Truck Loading

Description:	[Records for the crushers is maintained by the scale house operator]