FLORIDA DEPARTMENT OF ENVIRONMENTAL PROTECTION

INSPECTION REPORT FORM

AIR POLLUTANT EMISSION SOURCES

| FACILITY: Heritage Marble, LLC | DISTRICT: Northwest | COUNTY: Okaloosa |
| --- | --- | --- |
| ADDRESS: 501-07 Highway 190 Valparaiso, FL 32580 | PHONE: 850/678-6368 | CONTACT: Clay Brunson, Owner |
| CONTACT OR FACILITY EMAIL ADDRESS: none |
| AIRS #: 0910087 | PERMIT#: 0910087-002-AG | EXPIRES: 7/10/2010 |
| RENEWAL NOTIFICATION DUE DATE: 6/10/2010 |
| SOURCE DESCRIPTION: Synthetic Marble Fixtures Manufacturer |
| INSPECTED BY: Charles Norman INSPECTION DATE: 7/27/2006 | AUDIT TYPE: Ins2 | COMPLIANCE STATUS: In compliance |

INSPECTION COMMENTS:

- The combined quantity of styrene-containing resin and gel coat used by the polyester resin plastic products fabrication activity shall not exceed 76,000 pounds (38 tons) in any consecutive twelve-month period.  [Rule 62-310.300(3)(c) 5.c., F.A.C.]

Purchase records for May 2005 through June 2006 indicated the following usage: Resin: 54,000 lbs Gel coat: 4,148 lbs Total: 58,148 lbs

- The owner or operator of the facility shall maintain records to document the quantity of resin and gel coat used on a monthly basis.  The owner or operator shall retain these records, available for Department inspection, for a period of at least five years.  [Rule 62-210.300(3)(c) 5.d., F.A.C.]

Ms. Williams provided records of resin and gel coat use summarized by month. There is a break in the records. The previous owner took the purchase records with him. The current owner is maintaining the records. Inspection records back to 2001 indicated the material usage was in compliance with permitted conditions.

- The facility shall not cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor.  [Rule 62-596.320(2), F.A.C.]

No objectionable odors were noted.

- The owner or operator shall voluntarily encourage pollution prevention through such measures as training employees involved in product fabrication on methods of reducing evaporative losses by lessening the exposure of fresh resin surfaces to the air, maintaining spray lay-up equipment to ensure effective application with a minimum of overspray, monitoring the coating thickness to avoid excessive resin/gelcoat application, implementing inventory control practices to prevent spillage, and managing cleanup solvents.  (Rule 62-210.300(4)(b)4.c., F.A.C.)

I did a walk around inspection of the plant with Royce Whatley, Plant Manager. The facility has good environmental practices. Equipment seems to be in good condition and there were no open containers of VOC containing material. The facility distills and recycles its used acetone. There is a filter system to control particulate matter from grinding operations. The spray booth filter has a pressure gauge for determining the need to change the filters. Mr. Whatley said they change the filters when the pressure reading reaches 0.1 iWG.

August 1, 2006

Mr. Clay Brunson

Heritage Marble, LLC

Post Office Box 605

Valparaiso, Florida 32580

Dear Mr. Brunson:

A Department representative inspected your facility (I.D. 0910087) on July 27, 2006.  A copy of the inspection report is enclosed for your reference.  This letter applies only to activities covered by the Air Resources Management Program.  It indicates the facility was in compliance at the time of inspection for those sources specifically listed on the inspection report.

If you have any questions or comments, please contact Charles Norman at 850/595-8300, extension 1222 or charles.norman@dep.state.fl.us.

Sincerely,

Rick Bradburn

Air Compliance Supervisor

RB:cnc

Encl:  Insp Rpt