| AIR POLLUTION SOURCE INSPECTION REPORT FORM DEPARTMENT OF ENVIRONMENTAL PROTECTION |
| --- |
| FACILITY: C & M Road Builders | PAGE: 1 OF 1 |
| FACILITY ADDRESS: Center Ice Parkway & Lakewood Ranch Blvd Intersection | CITY: Bradenton, FL 34211 | COUNTY: Manatee |
| MAILING ADDRESS: 6735 33rd Street | CITY: Sarasota | STATE: FL | ZIP: 34243 |
| INSP. DATE: 2/12/2010 | TIME IN: 10:15 a.m. | TIME OUT: 12:45 p.m. | INSP TYPE: INS2 | STATUS: IN |
| IDENTIFICATION NO: 7775266 | EU ID # 001: EXTEC Crusher |
| SOURCE/FACILITY DESCRIPTION: Non-Metallic Mineral Processing Plant |
| CONTACT(S): Mark McCabe, President, (941)-758-1933 – Office (941) 376-4885 - Cell |
| I, James Burkholder (JB), went to C & M Road Builders AIRS ID# 7775266 facility to audit the annual visible emissions testing on the relocateable EXTEC Crusher. A relocation notice was received two days prior to the relocation, which had a startup date of 2/4/2010. The site was located on Center Ice Parkway ~1/4 mile east of the Lakewood Ranch Blvd intersection and approximately 100 years North of Center Ice Parkway. I arrived on site at approximately 10:10 a.m. and Lynn Robinson, P.E. of Southern Environmental Sciences just started performing the VE testing. The following Points were tested: EP #1 – Crusher Feed Hopper EP #5 – Conv. Belt #1 TP to Power Screen EP #2 – Crusher Exit to Discharge Belt #1 EP #6 – Power Screen TP to Discharge Belt #2 EP #3 – Discharge Belt #1 TP to Grizzly Hopper EP #7 – Power Screen TP to Discharge Belt #3 EP #4 – Grizzly Hopper TP to Conveyor Belt #1 EP #8 – Power Screen TP to Discharge Belt #4 Discharge Belt #2 conveyed material to the Wonder Rock pile. The Wonder Rock pile is similar to an Oversize pile and the Wonder Rock was re-fed into the crusher via a front end loader. Discharge Belt #3 conveyed material to the fines pile and Discharge Belt #4 conveyed material to the 57 Rock pile. The sun was to the observers back; however, it was overcast conditions and the sun angle was unable to be determined using a pencil on the field observer sheet. No visible emissions were observed at any emission point. Some emissions were observed from the Diesel Engine exhaust, but only 5-10% opacity was observed which is well under the 20% limit and a VE was not performed by the Department. At the time of inspection the facility appeared to be in compliance. No visible emissions were observed and all emissions points were properly tested. A records review was not performed at this time. The crusher is an EXTEC Crusher with a Grizzly Screener/Hopper and a Turbo Chieftan 1400 Power Screen. The facility operates on diesel fuel and is not believe to be over the 275,000 gallon 12 month limit. On the next page is a diagram of the facility layout at the time of Inspection. |
| INSPECTOR(S): James Burkholder | TIME EXPENDED: JB – 210 mins | REPORT DATE: 2/12/2010 |

| DEPARTMENT OF ENVIRONMENTAL PROTECTION CONTINUATION PAGE 2 OF 2 |
| --- |
| FACILITY: C & M Road Builders | INSPECTION DATE: 2/12/2010 |
| Facility Layout with the 57 Rock as the North Pile and the Wonder Rock as the South pile: |
| INSPECTOR: James Burkholder | REPORT DATE: 2/12/2010 | FACILITY ID NUMBER: 7775266 |