Department of

Environmental Protection

Northwest District

160 Governmental Center

Pensacola, Florida 32502

June 12, 2006

Jeb Bush

Governor

Colleen Castille

Secretary

BY ELECTRONIC MAIL

MarcT@rmusainc.com

Mr. Marc Bryant Tyson, President

Ready Mix USA

Post Office Box 101868

Birmingham, Alabama 35210

Dear Mr. Tyson:

A Department representative inspected your facility in Villa Tasso, I.D. Number 7775286, on May 9, 2006.  A copy of the inspection report is enclosed for your reference.  Please note the recommendation in the report concerning installation of an emissions control system for the truck loading drop point.

This letter applies only to activities covered by the Air Resources Management Program.  It indicates the facility was in compliance at the time of the inspection for those sources specifically listed on the report.

If you have any questions or comments, please contact Charles Norman of this office at 850/595-8300, extension 1222 or charles.norman@dep.state.fl.us.

Sincerely,

/s/

Rick Bradburn

Air Compliance Supervisor

RB:cnc

Encl:  Insp Rpt

David Gulley, Plant Superintendent (Coastal640@couchusa.com)

FLORIDA DEPARTMENT OF ENVIRONMENTAL PROTECTION

# INSPECTION REPORT FORM

AIR POLLUTANT EMISSION SOURCES

| FACILITY: Couch Ready Mix USA (Mini Tasso Plant) | DISTRICT: Northwest | COUNTY: Walton |
| --- | --- | --- |
| ADDRESS: 16040 Highway 20 West, Walton County | PHONE: (850) 897-2868 | CONTACT: David Gulley, Plant Superintendent |
| AIRS I.D. #: 7775286 | PERMIT: 7775286-001-AG | EXPIRES: 6/18/2010 |
| RENEWAL NOTIFICATION DUE DATE: 5/18/2010 |
| SOURCE DESCRIPTION: Cement Concrete Batch Plant |
| INSPECTED BY: Charles Norman INSPECTION DATE: 5/9/2006 | AUDIT TYPE: Ins2 | COMPLIANCE STATUS: In Compliance |

This facility is a cement concrete batch plant.  It consists of two 58-ton silos.  One silo is used for cement and the other for fly ash.

INSPECTION COMMENTS:

Emissions from silos, weigh hoppers (batchers), and other enclosed storage and conveying equipment shall be controlled to the extent necessary to limit visible emissions to 5% opacity.  Notification Part II, Condition (4)(a).

Emissions from the silos are controlled by a baghouse on top of each silo.  No loading was being done during the inspection.

The owner or operator shall take reasonable precautions to control unconfined emissions from hoppers, storage and conveying equipment, conveyor drop points, truck loading and unloading, roads, parking areas, stock piles, and yards.  Notification Part II, Condition (4)(b).

The yard operations area is paved/graveled.  No yard operations or truck loading were being done during the inspection.

Use of spray bar, chute, or partial enclosure to mitigate emissions at the drop point to the truck.  Notification Part II, Condition (4)(b) 2.

The plant does not have a spray bar.  Mr. Gulley said the loading is done using a screw type conveyor which is slower in loading than the usual conveyor type of loading.  He said very little, if any, emissions are seen from truck loading.  Truck loading did not occur during the inspection. Therefore, I was not able to make a judgment on the need for a spray bar or some other emissions control system.   Usually, cement plants have a dust control system for the drop point.  Since this plant has none, I recommend a visible emissions test be done on the truck loading operation to determine if there are excessive visible emissions and, if so, that an emissions control device be added to the plant.

The test method for visible emissions shall be DEP Method 9, incorporated in Chapter 62-297, F.A.C.  Testing is to be performed within 60 days prior to the anniversary of the air general permit notification form submittal date.   Notification Part II, Condition (4)(c) 1and (4)(d).

Visible emissions testing of the baghouses was scheduled for and accomplished 5/18/2006.  Results were 0% opacity.

RECOMMENDATOINS:  Recommend a visible emissions test be done on the truck loading operation to determine if there are excessive visible emissions and, if so, that an emissions control device be added to the plant.  Advise the Department of your plan of action by June 23. 2006.