Department of

Environmental Protection

Northwest District

160 Governmental Center

Pensacola, Florida 32502

Jeb Bush

Governor

Colleen Castille

Secretary

BY ELECTRONIC MAIL

tonyh@couchusa.com

This Inspection report was not sent.  The inspection form was attached to a WL.

Mr. Tony Hatcher

Pensacola Ready Mix USA

Post Office Box 7142

Cantonment, Florida 32534

Dear Mr. Hatcher:

A Department representative recently inspected your Concrete Batch Plant #1, I.D. 0330071, located on Highway 95A south of Cantonment.  A copy of the inspection report is enclosed.  The report shows non-compliance for failure to perform visible emissions testing as required.

This letter applies only to activities covered by the Air Resources Management Program.  In order to assure compliance for the future, please refer to the Recommendations section of that report.

If you have any questions, please contact Charles Norman at 850/595-8300, extension 1222 or charles.norman@dep.state.fl.us.

Sincerely,

Encl:  Insp Rpt

JRB:cnc

cc:  Noah McBride, Plant Facilities Manager, Pensacola Ready Mix, noahm@prmusa.com

FLORIDA DEPARTMENT OF ENVIRONMENTAL PROTECTION

INSPECTION REPORT FORM

AIR POLLUTANT EMISSION SOURCES

| FACILITY: Pensacola Ready Mix, Plant #1 | DISTRICT: Northwest | COUNTY: Escambia |
| --- | --- | --- |
| ADDRESS: 3008 S Hwy 95-A (PO Box 7142) Cantonment, FL 32534 | PHONE: 850 477-2899 | CONTACT: Tony Hatcher, Operations Mgr. Noah McBride, Plant Facilities Mgr. |
| CONTACT OR FACILITY EMAIL ADDRESS: tonyh@couchusa.com |
| ARMS I.D. #: 0330071 | PERMIT: 0330071-008-AG | EXPIRES: March 5, 2010 |
| RENEWAL NOTIFICATION DUE DATE: February 2, 2010 |
| SOURCE DESCRIPTION: Concrete Batch Plant |
| INSPECTED BY: Charles Norman INSPECTION DATE: 4/14/2006 | AUDIT TYPE: Ins2 | COMPLIANCE STATUS: Non-compliance |

Mr. McBride and I toured the facility.  It consists of two silos for cement and fly ash.  Emissions from silo loading are controlled by three baghouses (one silo has a split compartment with one baghouse each).  The weigh hopper has a small dust collector which exhausts internally into the drop point for the cement mixer truck.  A spray bar controls emissions from the drop point.  Mr. McBride said they plan to replace the existing emission controls with a vacuum system in the near future.  I told him that they would need to submit a new Air General Permit Notification Form.  This plant is adjacent to Plant #2, permit 0330063-004-AG.  The facility is non-compliant for failure to conduct the visible emissions testing due within the 60-day period prior to February 2, 2006.

| Part II. Permit Terms and Conditions |
| --- |
| Permit Condition | Comments |
| (4)(a) | Visible emissions limits from silos, weigh hoppers and other enclosed storage and conveying equipment shall be controlled to limit the opacity to 5%. Loading operations for several cement mixer trucks were observed. Also, one silo was being loaded with cement. No visible emissions were observed. |
| (4)(b)1 | Reasonable precautions shall be taken to control unconfined emissions from hoppers, storage and conveying equipment, conveyor drop points, tuck loading and unloading roads, parking area, stock piles and yards. The yard is paved and a water trailer is available to wet down the yard when needed to control dust. Material piles have sprinklers to control fugitive emissions. The yard was wet at the inspection. No fugitive emissions were seen from yard operations. |
| (4)(b)2 | Controlling fugitive dust from the drop point into the cement mixer truck. A spray bar controls these emissions. No emissions were seen from truck loading.. |
| (4)(c), (d) & (e) | Annual VE Testing. The anniversary date of Permit 0330071-008-AG is February 2, thus annual VE testing is required to be performed in the 60-day period prior to February 2. The facility last tested 1/21/2005. Visible emissions testing should have been done in the 60 day period prior to February 2, 2006 (4 Dec 2005--2 Feb 2006) |

RECOMMENDATIONS:

1.Complete the required visible emissions testing at the earliest possible time.

2. Contact Kevin White, Permitting Supervisor, concerning the planned upgrade of the emissions control system.  He may be contacted at 850-595-8300 ext. 1226 or kevin.white@dep.state.fl.us.