June 27, 2005

Mr. Tim Lister

Safety Supervisor

Berg Steel Pipe Corp

P.O. Box 59209

Panama City, Florida  32412-0209

Dear Mr. Lister,

Enclosed is a copy of the report completed by Mr. Richard S. Brookins Jr. describing his inspection of your facility on Thursday, June 16, 2005.  The cooperation and assistance of Mr. Willie Green during the inspection is greatly appreciated.

This letter applies only to activities covered by the Air Resources Management Program.  It indicates a state of compliance for the sources specifically listed in the report.

If you have any questions regarding this inspection report, please contact Mr. Richard S. Brookins Jr. at the Northwest District Branch Office in Panama City, phone (850) 872-4375 x108 or e-mail at Richard.Brookins@dep.state.fl.us.

Sincerely,

Josie Penton

Environmental Manager

INSPECTION REPORT

AIR POLLUTANT EMISSION SOURCES

| FACILITY: | E.B. Pipe Coating, Inc. | DISTRICT: 10 | COUNTY: 32 |
| --- | --- | --- | --- |
|  | 1412 C Avenue | CONTACT: Tim Lister |
|  | Port of Panama City | TELEPHONE: (850) 769-2273 |
| Email Address: tim@bergpipe.com |

| AIRS ID#: 0050048 | PERMIT#: 0050048-003-AV | EXPIRATION DATE: 04/26/2010 |
| --- | --- | --- |
| Permit Renewal Application/Notification Due Date: 10/28/2009 |

| INSPECTION DATE | AUDIT TYPE | COMPLIANCE STATUS |
| --- | --- | --- |
| 06/16/2005 | II | In Compliance |
| SKY | WIND | TEMPERATURE |
| Clear | 3-5 mph | High 80’s |

SOURCE DESCRIPTION:  This facility is a pipe cleaning and coating plant.  Steel pipes are cleaned using steel shot abrasive blasting methods and then coated using either a solvent based coating or a fused epoxy coating.  Particulate emissions are controlled by filtered dust collectors.  There are also a total of eight (8) natural gas fired pipe heaters used during the process.

INSPECTION COMMENTS:

I arrived at the facility and was greeted by Mr. Willie Green.  Mr. Green accompanied me during the inspection tour of the facility and provided copies of requested operating records.  The facility was operating at the time of the inspection.  Due to market conditions the facility has only operated only sporadically for the past three years and is scheduled to temporarily shut down again for an indeterminate time in approximately three weeks.

There were no objectionable odors noticed during the inspection.  [Facility-wide Condition 2]

Fugitive emissions approaching 20% opacity were noticed from the outside pipe moving operations.  While the lay down yard areas are now gravel covered additional work needs to be done in the main driving areas of the facility.  Water, paving, or new rock needs to be used in these areas as the previously applied gravel has been pulverized.  There were no other fugitive emissions noticed during this inspection.  [Facility-wide Condition 3]

VOC control appeared to be in compliance.  There were no open containers of VOC containing compounds noticed during this inspection.  Spills appeared to be cleaned up promptly.  [Facility-wide Condition 6]

Reasonable Precautions, with the exception of the needed maintenance on the main driving areas of the lay down yard mentioned above, appear to be adequate.  [Facility-wide Condition 7]

According to the records supplied by Mr. Green, VOC emissions for the facility have been 17.9 tons for the previous 12-month period ending May 31, 2005.  This is within the facility’s maximum permitted limit of 245 tons in any 12-month rolling period.  [Facility-wide Condition 9]

According to the records supplied by Mr. Green, HAP emissions for the facility have been 4.01 tons for the previous 12-month period ending May 31, 2005.  This is within the facility’s maximum permitted limit of 80 tons in any 12-month rolling period.  [Facility-wide Condition 10]

The facility uses computerized records for tracking material and fuel usage.  This system allows easy access and retrieval of information.  [Facility-wide Condition 11a, Facility-wide Condition 11b, Facility-wide Condition 11c]

## EU008   Eight natural gas fired pipe heaters

A monthly and annual summary of fuel consumption and operating hours was obtained from Mr. Green.  According to the information supplied the facility used 233,830 therms of natural gas and operated for approximately 1,270 hours during the previous 12 month period ending May 31, 2005.   [Specific Condition A.4]

## EU009   Cleaning and Blasting Activities

### Documentation of abrasive blasting materials used was obtained from Mr. Green.  According to the information provided, the facility used 120tons of abrasives during the previous 12-month period ending May 31, 2005.  This is within the facility’s maximum permitted limit of 2,102 tons in any 12-month rolling period.  [Specific Condition B.3]

#### EU010   Fusion Bonded Epoxy Powder Surface Coating Activities

### Documentation of epoxy powder material materials used was also obtained from Mr. Green.  According to the information provided, the facility used 417.42 tons of epoxy powder during the previous 12-month period ending May 31, 2005.  [Specific Condition C.3]

#### EU011   Solvent Based Paint Surface Coating Activities

### An annual summary of paint and solvents used was obtained from Mr. Green. According to the information provided, the facility used 18,746 gallons of solvent based coatings during the previous 12-month period.  This is within the facility’s limit of 193,425 gallons in any 12-month rolling period.   [Specific Condition D.3]

RECOMMENDATIONS:

1.	Implement the fugitive emission controls in the lay-down yard as discussed during the inspection.

| INSPECTOR’S NAME | SIGNATURE | DATE |
| --- | --- | --- |
| Richard S. Brookins Jr. |  |  |
| Environmental Specialist |  | June 27, 2005 |