June 7, 2006

Mr. Tim Lister

Safety Supervisor

Berg Steel Pipe Corp

P.O. Box 59209

Panama City, Florida  32412-0209

Dear Mr. Lister:

A Department representative recently inspected your facility.  A copy of the inspection report is enclosed.  Please note the permit expiration date and renewal application due date shown on the report.

This letter applies only to activities covered by the Air Resources Management Program.  It indicates compliance at the time of inspection for those sources specifically listed on the inspection report.

If you have any questions, please contact Richard Brookins at 850/872-4375, extension 108 or Richard.Brookins@dep.state.fl.us.

Sincerely,

Marlane Castellanos

Branch Office Manager

FLORIDA DEPARTMENT OF ENVIRONMENTAL PROTECTION

INSPECTION REPORT FORM

AIR POLLUTANT EMISSION SOURCES

| FACILITY: E.B. Pipe Coating, Inc. | DISTRICT: Northwest | COUNTY: |
| --- | --- | --- |
| ADDRESS: 1412 C Avenue | PHONE: (850) 769-2273 | CONTACT: : Tim Lister |
| CONTACT OR FACILITY EMAIL ADDRESS: tim@bergpipe.com |
| ARMS I.D. #: 0050048 | PERMIT: 0050048-003-AV | EXPIRES: 04/26/2010 |
| RENEWAL APPLICATION/NOTIFICATION DUE DATE: 10/28/2009 |
| SOURCE DESCRIPTION: Pipe cleaning and coating plant |
| INSPECTED BY: Richard Brookins INSPECTION DATE: 06/07/2006 | AUDIT TYPE: Ins2 | COMPLIANCE STATUS: MNC / In Compliance |

INSPECTION COMMENTS

I arrived at the facility and was greeted by Mr. Dan Etter, Plant Superintendent.  Mr. Etter notified Mr. Willie Green, Safety Manager, that I was on-site to perform an inspection.  While we waited Mr. Etter and I discussed the excessive fugitive emissions that I noticed upon arrival at the facility.  Mr. Etter explained that the company was aware of the problem and was looking at purchasing a new water truck as their old one was down for repairs again.  This water truck would be co-owned with Berg Steel and would be used to also wet down their lay down area.  After Mr. Green’s arrival and further discussion regarding the excessive fugitive emissions, the walk-thru inspection of the facility was begun.  Mr. Green accompanied me during the inspection tour of the facility and provided copies of requested operating records.  The facility was operating at the time of the inspection.  Due to market conditions the facility has only operated only sporadically for the past four years.

There were no objectionable odors noticed during the inspection.  [Facility-wide Condition 2]

As mentioned above, fugitive emissions above 20% opacity were noticed from the outside pipe moving operations.  While the lay down yard areas are gravel covered, additional work needs to be done in the main driving areas of the facility.  Water, paving, or new rock needs to be used in these areas as the previously applied gravel has been pulverized.  There were no other fugitive emissions noticed during this inspection.  [Facility-wide Condition 3]

VOC control appeared to be in compliance.  There were no open containers of VOC containing compounds noticed during this inspection.  Spills appeared to be cleaned up promptly.  [Facility-wide Condition 6]

Reasonable Precautions, with the exception of the needed maintenance on the main driving areas of the lay down yard mentioned above, appear to be adequate.  [Facility-wide Condition 7]

According to the records supplied by Mr. Green, VOC emissions for the facility have been 8.14 tons for the current Year-to-Date.  This is within the facility’s maximum permitted limit of 245 tons in any 12-month rolling period.  [Facility-wide Condition 9]

According to the records supplied by Mr. Green, HAP emissions for the facility have been 2.81 tons for the current Year-to-Date.  This is within the facility’s maximum permitted limit of 80 tons in any 12-month rolling period.  [Facility-wide Condition 10]

The facility uses computerized records for tracking material and fuel usage.  This system allows easy access and retrieval of information.  [Facility-wide Condition 11a, Facility-wide Condition 11b, Facility-wide Condition 11c]

## EU008   Eight natural gas fired pipe heaters

A monthly and annual summary of fuel consumption and operating hours was obtained from Mr. Green.  According to the information supplied the facility used 114542 therms of natural gas and operated for approximately 603.4 hours during the current Year-to-Date.   [Specific Condition A.4]

## EU009   Cleaning and Blasting Activities

### Documentation of abrasive blasting materials used was obtained from Mr. Green.  According to the information provided, the facility used 64 tons of abrasives during the current Year-to-Date.  This is within the facility’s maximum permitted limit of 2,102 tons in any 12-month rolling period.  [Specific Condition B.3]

#### EU010   Fusion Bonded Epoxy Powder Surface Coating Activities

### Documentation of epoxy powder material usage was also obtained from Mr. Green.  According to the information provided, the facility used 572.7 tons of epoxy powder during the previous 12-month period ending April 30, 2006.  [Specific Condition C.3]

#### EU011   Solvent Based Paint Surface Coating Activities

### An annual summary of paint and solvents used was obtained from Mr. Green. According to the information provided, the facility used 11,690 gallons of solvent based coatings during the previous 12-month period.  This is within the facility’s limit of 193,425 gallons in any 12-month rolling period.   [Specific Condition D.3]

RECOMMENDATIONS:

1.	Implement the fugitive emission controls in the lay-down yard as discussed during the inspection.