May 15, 2006

Mr. Robert Olsen

Director of Public Works

City of Lynn Haven

825 Ohio Avenue

Lynn Haven, Florida  32444

Dear Olsen:

A Department representative recently inspected your facility.  A copy of the inspection report is enclosed.  Please note the permit expiration date and renewal application due date shown on the report.

This letter applies only to activities covered by the Air Resources Management Program.  It indicates compliance at the time of inspection for those sources specifically listed on the inspection report.

If you have any questions, please contact Richard Brookins at 850/872-4375, extension 108 or Richard.Brookins@dep.state.fl.us.

Sincerely,

Marlane Castellanos

Branch Office Manager

FLORIDA DEPARTMENT OF ENVIRONMENTAL PROTECTION

INSPECTION REPORT FORM

AIR POLLUTANT EMISSION SOURCES

| FACILITY: City of Lynn Haven ACI | DISTRICT: Northwest | COUNTY: Bay |
| --- | --- | --- |
| ADDRESS: Hatcher Road | PHONE: (850) 265-5989 | CONTACT: Robert Olsen |
| CONTACT OR FACILITY EMAIL ADDRESS: |
| ARMS I.D. #: 0050070 | PERMIT: 0050070-003-AO | EXPIRES: 07/07/2008 |
| RENEWAL APPLICATION/NOTIFICATION DUE DATE: 05/08/2008 |
| SOURCE DESCRIPTION: Stationary air curtain incinerator |
| INSPECTED BY: Richard Brookins INSPECTION DATE: 05/15/2006 | AUDIT TYPE: Ins2 | COMPLIANCE STATUS: In Compliance |

INSPECTION COMMENTS

I arrived at the facility was greeted by Mr. Tony Strickland, the facility operator.  Visible emission testing was scheduled to be performed by Ms. Lisa Swain but had to be rescheduled due to the facility receiving approximately ½ inch of rain overnight.  Mr. Strickland accompanied me during the inspection and provided access to requested records.  The facility was not operating at the time of the inspection due to the abovementioned rainfall.  An opportunity was taken to enter the firebox for visual observations of the condition of the emission unit.  The stainless steel top and a number of the refractory lined panels were recently replaced during routine inspection and maintenance.

The facility had a fuel fire on March 7, 2006.  Since that time the fuel storage area has been moved further away and in a different direction from its previous location.  Hopefully this will alleviate the problem of burning embers landing in the working fuel pile.

There were no objectionable odors noticed during the inspection.  [Facility-wide Condition 2]

There were no fugitive visible emissions in excess of 20% noticed during the inspection.  [Facility-wide Condition 3]

Reasonable precautions to prevent fugitive emissions appear to be adequate.  The limited amount of vehicular and equipment traffic, along with the relatively remote location of the facility aid in this effort.   [Facility-wide Condition 4]

## EU001	Air Curtain Incinerator

This facility has a maximum permitted capacity of 6.25 tons per hour.  The facility has a scale on the front end loader.  Each bucket of waste is weighed and the weight is recorded prior to being tipped into the firebox.  These daily weights are recorded in a separate log book which also records operating hours for the incinerator.  [Specific Condition A.1]

The working fuel pile was inspected for the presence of prohibited waste materials.  Other than plastic lawn bags, the only noticed fuels were vegetative debris.  According to Mr. Strickland these bags are removed prior to incineration.  An inspection of the ramp going to the incinerator revealed only a few minor pieces of plastic with no overt evidence of the burning of prohibited materials.  [Specific Condition A.2.a, Specific Condition A.2.b]

An LP burner gas burner is used to start the incinerator as required by the permit.  [Specific Condition A.2.c]

An inspection of the combustion pit revealed ash to be less than 1/3 the pit depth as required.  [Specific Condition A.2.g]

A locked gate across the access road restricts public access when the facility is not in operation.  [Specific Condition A.3]

Documentation of the operating hours was reviewed as part of this inspection.  This information is maintained in a notebook that is carried by the plant operator.  These records do not account for the burnout time in the evening.  [Specific Condition A.4]

There were no visible emissions noticed during the inspection.  [Specific Condition A.6]

A copy of the permit and an operating and maintenance guide are available on site as required.  [Specific Condition A.10]

As mentioned above, documentation of the facility’s operating hours and tonnages is being maintained.  Calculation of the monthly and 12-month operating hours is not routinely performed but it is readily apparent from the sporadic operation of the facility that the limitations of the hours of operation are not being exceeded. An analysis of the operating hours and tonnages for January 2006 showed the unit operated for approximately 89 hours and burned approximately 364.98 tons of debris.  This equates to an average operating rate of 4.1 TPH.    [Specific Condition A.11]

RECOMMENDATIONS:

None