March 13, 2006

Mr. Harry Rogers

Big River Cypress & Hardwood, Inc.

PO Box 189

Blountstown, Florida 32424

Dear Mr. Rogers:

A Department representative recently inspected your facility.  A copy of the inspection report is enclosed.  Please note the permit expiration date and renewal application due date shown on the report.

This letter applies only to activities covered by the Air Resources Management Program.  It indicates compliance at the time of inspection for those sources specifically listed on the inspection report.

If you have any questions, please contact Richard Brookins at 850/872-4375, extension 108 or Richard.Brookins@dep.state.fl.us.

Sincerely,

Marlane Castellanos

Branch Office Manager

FLORIDA DEPARTMENT OF ENVIRONMENTAL PROTECTION

INSPECTION REPORT FORM

AIR POLLUTANT EMISSION SOURCES

| FACILITY: Big River Cypress & Hardwood, Inc. | DISTRICT: Northwest | COUNTY: Calhoun |
| --- | --- | --- |
| ADDRESS: 19431 Highway 71 North, Blountstown | PHONE: (850) 674-5991 | CONTACT: Harry Rogers |
| CONTACT OR FACILITY EMAIL ADDRESS: |
| ARMS I.D. #: 0130008 | PERMIT: 0130008-003-AO | EXPIRES: 01/24/2011 |
| RENEWAL APPLICATION/NOTIFICATION DUE DATE: 11/25/2010 |
| SOURCE DESCRIPTION: Hardwood lumber mill and kiln with a 7 MMBtu/hr wood-waste fired boiler |
| INSPECTED BY: Richard Brookins INSPECTION DATE: 02/28/2006 | AUDIT TYPE: Ins2 | COMPLIANCE STATUS: In Compliance |

INSPECTION COMMENTS

I arrived at the facility and was greeted by Mr. Terrell Holland.  Mr. Holland provided copies of requested records and accompanied me during the walk through inspection of the facility.

## There were no objectionable odors noticed during the inspection.  [Facility-wide Condition 2]

There were no fugitive visible emissions above 20% opacity noticed during the inspection.  The main potential for fugitive emissions continues to appear to be the heavy equipment operating in the yard.   [Facility-wide Condition 3, Facility-wide Condition 5]

VOC control at the facility appeared to be adequate.  There were no open containers of VOC’s or other organic solvents noticed during the inspection.  [Facility-wide Condition 4]

Monthly production records are maintained on a spreadsheet and were reviewed as part of this inspection.  According to information provided by the facility, 1,664,335 Bd. Ft. have been processed through the kiln during the previous 12 month period ending January 31, 2006.  [Facility-wide Condition 7]

### EU-001	7 MMBtu/hr Heat Input Wood Waste Fired Boiler

According to information provided by the facility, maximum firing rate was 4.2 MMBtu/hr during April 2005.  [Specific Condition A.1]

Visible emissions were 0 % at the time of the inspection.  [Specific Condition A.3]

## The operating records for the boiler were reviewed during the inspection.  [Specific Condition A.7]

All equipment continues to appear to be in good condition.  There were no leaks or spills noticed during the inspection.  [General Condition 6]

RECOMMENDATIONS:

Continue to monitor fugitive emissions from the general yard area during the dry months of the year.  As an alternative to using water the facility may want to investigate the potential use of organic dust suppressing chemicals