COMPLIANCE ASSURANCE MONITORING FOR EU003

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the dry saw planer, board mill stacker, tipple pan dust collection, dry saw table saw and dry broke pulper. See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 3, EU003 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility ID No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 4.0 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic, Type UW-4Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.1. The selected indicator of performance is the scrubber water supply pressure. Water flow rate appears to be the critical parameter for scrubber cleaning efficiency. Scrubber water supply pressure directly correlates to water flow based on the size of the scrubber nozzles. Air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU009

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the FMS Line operations. See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 4, EU009 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility ID No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 2.0 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic Type UW-4 Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.1. The selected indicator of performance is the scrubber water supply pressure. Scrubber water supply pressure directly correlates to water flow based on the size of the scrubber nozzles. Air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU010

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the plant’s PIF Line sources. See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 6, EU010 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 2.0 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic Type UW-4 Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.1. The selected indicator of performance is the scrubber water supply pressure. Scrubber water supply pressure directly correlates to water flow based on the size of the scrubber nozzles. Air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU011

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the Mylar Line Equalizer, Salvage Equalizer and PIF Line Equalizer. See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 2, EU011 |
|  |  | Facility: | Armstrong World Industries |
|  |  |  | Pensacola Plant, Facility ID No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 3.0 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic Type UW-4 Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.2. The selected indicator of performance is the scrubber water flow rate. Air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU012

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the PIF Line 2 pass tenoners and PIF air knife hood. See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 7, EU012 |
|  |  | Facility: | Armstrong World Industries |
|  |  |  | Pensacola Plant, Facility ID No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 4.5 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic Type UW-4 Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.1. The selected indicator of performance is the scrubber water supply pressure. Scrubber water supply directly correlates to water flow based on the size of the scrubber nozzles. Air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU014

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the Kiln Line Feeder and FMS tenoners (2). See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 5, EU014 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility ID No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 3.5 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic Type UW-4 Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.2. The selected indicator of performance is the scrubber water flow rate. Scrubber water supply pressure directly correlates to water flow based on the size of the scrubber nozzles. Air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU050 (SCRUBBER)

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the North Board Dryer Exhaust Stack. See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 53, EU050 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility ID No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 11.0 pounds per hour (for both north and south dryer stacks combined) |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.3. The selected indicator of performance is the scrubber water inlet pressure. Water flow appears to be a critical parameter for scrubber cleaning efficiency. Scrubber water supply pressure directly correlates to water flow. Air inlet static pressure is an indicator of airflow from the process and is not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU050 (MULTICYCLONE)

MULTICYCLONE NO. 54 FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This multicyclone controls dust from the South Board Dryer Exhaust Stack. See drawings in Attachment A. |
|  |  | Identification: | Multicyclone No. 54, EU050 |
|  |  | Facility: | Armstrong World Industries |
|  |  |  | Pensacola Plant, Facility I.D. No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 11.0 pounds per hour (for both north and south dryer stacks combined) |
|  |  | Monitoring Requirements: | Process rates, and air flow differential pressure. |
|  | C. | Control Technology | Ducon Model 6 UP Multicyclone |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.4. The selected indicator of performance is the static air pressure. It is continuously monitored via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU054

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the Dry Saw and PIF Line Slice Feeders. See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 9, EU054 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility ID No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 3.0 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic Type UW-4 Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.1. The selected indicator of performance is the scrubber water supply pressure. Water flow appears to be a critical parameter for scrubber cleaning efficiency. Scrubber water supply pressure directly correlates to water flow based on the size of the scrubber nozzles. Air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU055

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the plant’s two Perlite Expanders. See drawings in Attachment A. |
|  |  | Identification: | Perlite Scrubber, EU055 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility I.D. No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 9.0 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic Type UW-4 Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.2. The selected indicator of performance is the scrubber water flow. Water flow appears to be a critical parameter for scrubber cleaning efficiency. Scrubber water supply pressure directly correlates to water flow based on the size of the scrubber nozzles. Air inlet static pressure was found to be an indicator of airflow for conveying Perlite from the process and is not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU056

WET SCRUBBERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This scrubber controls dust from the plant’s Paint Mix operations. See drawings in Attachment A. |
|  |  | Identification: | Scrubber No. 8, EU056 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility I.D. No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 3.0 pounds per hour |
|  |  | Existing Monitoring Requirements: | Process rates Scrubber water flow rates Air flow differential pressure |
|  | C. | Control Technology | Ducon Dynamic Type UW-4 Wet Scrubber |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.1. The selected indicator of performance is the scrubber water supply pressure. Water flow appears to be a critical parameter for scrubber cleaning efficiency. Scrubber water supply pressure directly correlates to water flow based on the size of the scrubber nozzles. Air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Data is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU065

BAGHOUSE FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This baghouse filter controls dust from various sources on the Travertone Line. See drawings in Attachment A. |
|  |  | Identification: | Baghouse No. 1, EU065 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility I.D. No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 2.4 pounds per hour |
|  |  | Monitoring Requirements: | Process rates and baghouse air flow differential pressure. |
|  | C. | Control Technology | Baghouse Filter |
| II. | Proposed Monitoring Approach |
|  | The Travertone line associated with Baghouse No. 1 has been out of service since 2000 due to low demand of that particular product. If and when the line is placed back in service, the FDEP would be notified in advance and a Method 9 visible emissions test would be performed prior to placing the line back in service. The selected indicator of performance is the pressure drop across the baghouse which would be monitored continuously via the plant’s Data Historian system. Baghouse No. 1 was installed in 1984. The manufacturer’s representative, Mr. Kevin Bahnline, was contacted regarding their recommended specifications. He indicated the operating range would be from 2 – 6 inches WC. He can be contacted at 1-800-621-0734; email address is kbahnline@met-pro.com. |

COMPLIANCE ASSURANCE MONITORING FOR EU080

BAGHOUSE FILTERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This baghouse filter controls dust from the PIF Line Sander operations. See drawings in Attachment A. |
|  |  | Identification: | Baghouse No. 21, EU080 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 0.75 pounds per hour |
|  |  | Monitoring Requirements: | Process rates and baghouse air flow differential pressure. |
|  | C. | Control Technology | Baghouse Filter |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.5. The selected indicator of performance is the pressure drop across the baghouse. It is monitored continuously via the plant’s Data Historian system. |

COMPLIANCE ASSURANCE MONITORING FOR EU081

BAGHOUSE FILTERS FOR PM CONTROL

ARMSTRONG WORLD INDUSTRIES, INC.

| I. | Background |
| --- | --- |
|  | A. | Emissions Unit |
|  |  | Description: | This baghouse controls dust from the PIF Line Flipper and Wheelabrator operations. See drawings in Attachment A. |
|  |  | Identification: | Baghouse No. 22, EU081 |
|  |  | Facility: | Armstrong World Industries, Inc. |
|  |  |  | Pensacola Plant, Facility I.D. No. 0330006 |
|  | B. | Applicable Regulation, Emissions Limit, and Monitoring Requirements |
|  |  | Regulation: | Permit 0330006-010-AV |
|  |  | PM Emissions Limit: | 0.75 pounds per hour |
|  |  | Monitoring Requirements: | Process rates and baghouse air flow differential pressure. |
|  | C. | Control Technology | Baghouse Filter |
| II. | Proposed Monitoring Approach |
|  | The key elements of the monitoring approach for PM are presented in Table E.5. The selected indicator of performance is the pressure drop across the baghouse. It is monitored continuously via the plant’s Data Historian system. |

TABLE  E.1

MONITORING APPROACH FOR:

EU003, EU009, EU010, EU012, EU054 and EU056

SCRUBBERS 3, 4, 6, 7, 8, & 9

| I. | Indicator | Scrubber water inlet pressure. |
| --- | --- | --- |
|  | Measurement Approach | The scrubber water pressure is monitored continuously using a pressure transmitter connected to the plant’s Data Historian system. |
| II. | Indicator Range | While the scrubber is operating, an excursion is defined as water pressure outside the range specified below for a continuous period of 2 hours. (Note: If the fan shuts down, the process line shuts down immediately. This is not considered an excursion). An excursion will trigger an investigation of the occurrence and corrective action. Scrubber No. 3: 15 psi to 35 psi Scrubber No. 4: 15 psi to 35 psi Scrubber No. 6: 15 psi to 35 psi Scrubber No. 7: 15 psi to 35 psi Scrubber No. 8: 15 psi to 35 psi Scrubber No. 9: 15 psi to 35 psi |
| III. | Performance Criteria | The pressure transmitter is located at the water inlet to the scrubber. |
|  | A. | Data Representativeness |  |
|  | B. | Verification of Operational Status | NA |
|  | C. | Quality Assurance and Control Practices | Install, calibrate, maintain and operate pressure transmitters following manufacturer’s specifications. |
|  | D. | Monitoring Frequency | Water pressure is continuously monitored via the plant’s Data Historian system. |
|  |  | Data Collection Procedures | The plant’s Data Historian system collects and retains an instantaneous data point every 15 minutes. This data is stored electronically and archived for 5 years. |
|  |  | Averaging Period | None |

TABLE E.2

MONITORING APPROACH FOR:

EU011, EU014, and EU 055

SCRUBBER 2, SCRUBBER 5 & PERLITE SCRUBBER

| I. | Indicator | Scrubber water flow. |
| --- | --- | --- |
|  | Measurement Approach | The scrubber water flow is monitored continuously using a flow meter connected to the plant’s Data Historian system. |
| II. | Indicator Range | While the scrubber is operating, an excursion is defined as water flow less than those specified below for a continuous period of 2 hours. (Note: If the fan shuts down, the process line shuts down immediately. This is not considered an excursion). An excursion will trigger an investigation of the occurrence and corrective action. Scrubber No. 2: 165 gpm minimum Scrubber No. 5: 80 gpm minimum Perlite Scrubber: 165 gpm minimum |
| III. | Performance Criteria | The flow meter is located at the water inlet to the scrubber. |
|  | A. | Data Representativeness |  |
|  | B. | Verification of Operational Status | NA |
|  | C. | Quality Assurance and Control Practices | Install, calibrate, maintain and operate flow meters following manufacturer’s specifications. |
|  | D. | Monitoring Frequency | Water flow is continuously monitored via the plant’s Data Historian system. |
|  |  | Data Collection Procedures | The plant’s Data Historian system collects and retains an instantaneous data point every 15 minutes. This data is stored electronically and archived for 5 years. |
|  |  | Averaging Period | None |

TABLE E.3

MONITORING APPROACH FOR:

EU050 – SCRUBBER NO. 53

| I. | Indicator | Scrubber water inlet pressure. |
| --- | --- | --- |
|  | Measurement Approach | The scrubber water pressure is monitored continuously using a pressure transmitter connected to the plant’s Data Historian system. |
| II. | Indicator Range | While the scrubber is operating, an excursion is defined as a scrubber water inlet pressure less than 10 psi for a continuous period of 2 hours. (Note: If the fan shuts down, the process line shuts down immediately. This is not considered an excursion). An excursion will trigger an investigation of the occurrence and corrective action. |
| III. | Performance Criteria | The water pressure is monitored using a pressure transmitter. The pressure transmitter is located in the water inlet line. |
|  | A. | Data Representativeness |  |
|  | B. | Verification of Operational Status | NA |
|  | C. | Quality Assurance and Control Practices | Maintain and operate transmitters following manufacturer’s specifications. |
|  | D. | Monitoring Frequency | The scrubber water inlet pressure is continuously monitored via the plant’s Data Historian system. |
|  |  | Data Collection Procedures | The plant’s Data Historian system collects and retains an instantaneous data point every 15 minutes. This data is stored electronically and archived for 5 years. |
|  |  | Averaging Period | None |

TABLE E.4

MONITORING APPROACH FOR:

EU050 – MULTICYCLONE NO. 54

| I. | Indicator | Static air pressure. |
| --- | --- | --- |
|  | Measurement Approach | The static air pressure is monitored continuously using a pressure transmitter connected to the plant’s Data Historian system |
| II. | Indicator Range | While the multicyclone is operating, an excursion is defined as static air pressure which falls outside the range of 5 to 15 inches water column for a continuous period of 2 hours. (Note: If the fan shuts down, the process line shuts down immediately. This is not considered an excursion). An excursion will trigger an investigation of the occurrence and corrective action. |
| III. | Performance Criteria | The static air pressure is measured using a pressure transmitter. The pressure transmitter is located at the Multicyclone inlet. |
|  | A. | Data Representativeness |  |
|  | B. | Verification of Operational Status | NA |
|  | C. | Quality Assurance and Control Practices | Maintain and operate transmitter following manufacturer’s specifications. |
|  | D. | Monitoring Frequency | The static air pressure is continuously monitored via the plant’s Data Historian system. |
|  |  | Data Collection Procedures | The plant’s Data Historian system collects and retains an instantaneous data point every 15 minutes. This data is stored electronically and archived for 5 years. |
|  |  | Averaging Period | None |

TABLE E.5

MONITORING APPROACH FOR:

EU065, EU080 and EU081

BAGHOUSES 1, 21 and 22

| I. | Indicator | Static pressure across the baghouse. |
| --- | --- | --- |
|  | Measurement Approach | The static air pressure is measured using a pressure transmitter. |
| II. | Indicator Range | While the baghouse is operating, an excursion is defined as pressure drop across the baghouse outside the range specified below for a continuous period of 2 hours. (Note: If the fan shuts down, the process line shuts down immediately. This is not considered an excursion). An excursion will trigger an investigation of the occurrence and corrective action. Baghouse 1: between 2 and 6 inches water column (note: This baghouse has been out of service since 2000) Baghouse 21: between 2.8 and 8 inches water column Baghouse 22: between 2 and 8 inches water column |
| III. | Performance Criteria | The pressure transmitter measures the static pressure across the baghouse. |
|  | A. | Data Representativeness |  |
|  | B. | Verification of Operational Status | NA |
|  | C. | Quality Assurance and Control Practices | Maintain and operate transmitter following manufacturer’s specifications. |
|  | D. | Monitoring Frequency | Pressure is continuously monitored via the plant’s Data Historian system. |
|  |  | Data Collection Procedures | The plant’s Data Historian system collects and retains an instantaneous data point every 15 minutes. This data is stored electronically and archived for 5 years. |
|  |  | Averaging Period | None |

MONITORING APPROACH JUSTIFICATION FOR

EU003, EU009, EU010, EU011, EU012, EU014, EU054, EU055 and EU056

| I. | Background |
| --- | --- |
|  | Activities associated with these scrubbers (except for EU055) include various dust sources associated with the manufacture of ceiling tile. These sources include feeders, stackers, conveyors, equalizers, tile knives, saws and sanders. Process flow diagrams are included in Attachment A. Fume hoods collect dust from the process equipment and a fan pulls the vapors through vent lines and into the scrubber. For EU 055, raw perlite is expanded with natural gas fired perlite expanders. Expanded perlite is separated from the flue gases in cyclones, and particulate and combustion by-product emissions are controlled by a Ducon Dynamic Gas Scrubber, Type UW-4 (EU 055). Each of the nine Scrubbers is a Ducon Dynamic Gas Scrubber, Type UW-4. A detailed description of the scrubbers is included in the permit application forms and in Attachment H. |
| II. | Rationale for Selection of Performance Indicators |
|  | In February 2004, the Armstrong plant commenced an extensive Six Sigma Greenbelt engineering project to evaluate certain operational aspects of the plant’s Ducon wet scrubbers, optimize overall scrubber performance, and determine performance indicators and their respective operating ranges. The ultimate goal of the project was to maintain stable operating conditions to ensure scrubber efficiency, maintain compliance with the plant’s Title V air operating permit, ensure that the emission control devices are operating in accordance with manufacturer specifications, and validate maintenance procedures for the scrubbers to ensure compliance with applicable permit limits. Considerable progress and improvements have been made as a result of the Six Sigma project. All nine of the scrubbers have been outfitted with new instrumentation and monitoring devices, and tied into the plant’s Data Historian system, which will continuously monitor the required performance indicators. This is a substantial improvement over the previous monitoring method of manually recording the data once each eight-hour shift. The scope of the recent Six Sigma engineering project provided that Scrubbers No. 2 and 5 were equipped with flow meters and monitored for water flow rate. The remaining wet scrubbers are monitored for water supply pressure which is a direct indicator of flow rate. One of the findings of the study was that air inlet static pressure is a good indicator of vacuum for dust removal from the process, but not a critical variable in scrubber cleaning performance. Ducon Technologies’ technical engineer, Mr. Thomas Kelleher, further validated this finding by stating that while air inlet static pressure is a good measure of performance for a Venturi and other types of scrubbers, it is not for the Dynamic Scrubbers, Type UW-4 which are used at the Pensacola Plant. He stated that neither pressure drop nor static pressure is a good indicator of scrubber performance for this type of scrubber. Based on these findings, Armstrong is proposing water pressure or water flow rate as the sole CAM performance indicator for the scrubbers. By monitoring one relevant indicator continuously, we expect to collect more meaningful performance data than by the previous monitoring scheme whereby two questionably relevant parameters were monitored every eight hours. |

| III. | Rationale for Selection of Indicator Levels |
| --- | --- |
|  | Performance indicator ranges included in this plan were established by a combination of manufacturer’s recommendations, engineering studies, and historical data. The indicator ranges are supported by the 2004 compliance test results, which are summarized in Tables E.6 through E.14. Operating parameters associated with compliance tests prior to 2004 are not included in the table. They are not relevant to the current operation because of the extensive changes to the scrubber monitoring system in 2004. The manufacturer of all nine of the Dynamic Type UW-4 wet scrubbers is Ducon Technologies. The manufacturer’s design liquid flow rate is165 gpm. For Scrubber No. 2, the manufacturer’s design liquid flow rate of 165 gpm was used. The minimum water flow rate for Scrubber No. 5 was based on compliance test data, and the 2004 Six Sigma engineering study. The data is shown in Table E.11. The proposed CAM range for the Perlite scrubber is supported by the manufacturer’s design liquid flow rate of 165 gpm. An engineering study was performed on Scrubber No. 3 to determine the correlation between scrubber water flow rate and scrubber water pressure. A flow rate of 150 gpm was measured at 13 psi water pressure. It was determined that a flow rate of 165 gpm would correspond to 15 psi water pressure. This information was generalized to the other scrubbers, and used as the basis for the minimum CAM indicator on Scrubbers 3, 4, 6, 7, 8, and 9. The maximum CAM indicator for Scrubbers 3, 4, 6, 7, 8, and 9 is a scrubber water pressure of 35 psi. Based on the design of the system, a back pressure of 35 psi is expected when the spray nozzles are plugged. The Ducon Dynamic Type UW-4 Scrubbers are outfitted with two ¾” nozzles in the top section, and two to four ½” nozzles in the bottom section. In accordance with the plant’s scrubber maintenance plan, a nozzle inspection is scheduled every six weeks. In addition, the possibility of clogged spray nozzles has been greatly reduced by the installation of a new strainer at the plant’s wastewater treatment plant on November 26, 2004 (see attached drawing of the water cleaning process). Because the perforations in the strainer are smaller than the orifice size of the scrubber nozzles, the water, which is recycled back to the wet scrubbers, is less likely to contain particles that could possibly plug the spray nozzles. |

TABLE E.6

COMPLIANCE TEST DATA FOR

EU003

| Scrubber No. 3 | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- |
| Particulate Emissions | 0.755 lb/hr | 4.0 lb/hr |
| Board Mill Stacker | 44 ft/min | 75 ft/min |
| Dry Broke Pulp | 2.7 TPH | 2.9 Tons Per Hour (TPH) |
| Scrubber water pressure | 23 psi | Between 15 and 35 psi |

Note: CAM range based on manufacturer’s information, and engineering studies

TABLE E.7

COMPLIANCE TEST DATA FOR

EU009

| Scrubber No. 4 | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- |
| Particulate Emissions | 1.15 lb/hr | 2.0 lb/hr |
| FMS Line | 15.2 BPM | 120 ft/min = 20 boards per minute |
| Scrubber water pressure | 28 psi | Between 15 and 35 psi |

Note: CAM range based on manufacturer’s information, and engineering studies

TABLE E.8

COMPLIANCE TEST DATA FOR

EU010

| Scrubber No. 6 | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- |
| Particulate Emissions | 0.505 lb/hr | 2.0 lb/hr |
| PIF Line | 25 BPM | 198 ft/min = 33 boards per minute (BPM) |
| Scrubber water pressure | 22 psi | Between 15 and 35 psi |

Note: CAM range based on manufacturer’s information, and engineering studies

TABLE E.9

COMPLIANCE TEST DATA FOR

EU011

| Scrubber No. 2 | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- |
| Particulate Emissions | 1.88 lb/hr | 3.0 lb/hr |
| PIF Line | 25 BPM | 198 ft/min = 33 boards per minute (BPM) |
| Equalizer | 800 sq.ft/hr | 974 sq.ft/hr |
| Mylar Line | 4.67 BPM | 28 ft/min = 4.7 boards per minute |
| Scrubber Flow Rate | 200 gpm | above 165 gpm |

Note: CAM range based on manufacturer’s information

TABLE E.10

COMPLIANCE TEST DATA FOR

EU012

| Scrubber No. 7 | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- |
| Particulate Emissions | 1.45 lb/hr | 4.5 lb/hr |
| PIF Line | 25 BPM | 198 ft/min = 33 boards per minute (BPM) |
| Scrubber water pressure | 20 psi | Between 15 and 35 psi |

Note: CAM range based on manufacturer’s information, and engineering studies

TABLE E.11

COMPLIANCE TEST DATA FOR

EU014

| Scrubber No. 5 | 2004 compliance test data | 2004 Six Sigma data | 2004 Six Sigma data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- | --- | --- |
| Particulate Emissions | 1.73 lb/hr | 0.98 lb/hr | 1.46 lb/hr | 3.5 lb/hr |
| Kiln | 3.0 BPM | 3.0 BPM | 3.0 BPM | 16 ft/min = 3.0 boards per minute (BPM) |
| FMS Line | 15.2 BPM | 15.2 BPM | 15.2 BPM | 120 ft/min = 20 boards per minute (BPM) |
| Scrubber Flow Rate | 100 gpm | 90 gpm | 80gpm | above 80 gpm |

TABLE E.12

COMPLIANCE TEST DATA FOR

EU054

| Scrubber No. 9 | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- |
| Particulate Emissions | 0.425 lb/hr | 3.0 lb/hr |
| PIF Line | 26.2 BPM | 198 ft/min = 33 boards per minute (BPM) |
| Dry Saw | 44 ft/min | 75 ft/min |
| Scrubber water pressure | 24 psi | Between 15 and 35 psi |

Note: CAM range based on manufacturer’s information, and engineering studies

TABLE E.13

COMPLIANCE TEST DATA FOR

EU056

| Scrubber No. 8 | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- |
| Particulate Emissions | 0.388 lb/hr | 3.0 lb/hr |
| Unloading Section Dust Hood | 45 ft/min | 75 ft/min |
| Scrubber water pressure | 27 psi | Between 15 and 35 psi |

Note: CAM range based on manufacturer’s information, and engineering studies

TABLE E.14

COMPLIANCE TEST DATA FOR

EU055

| Perlite Scrubber | 2000 test data | 2001 test data | 2002 test data | 2003 test data | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- | --- | --- | --- | --- |
| Particulate Emissions | 2.74 lb/hr | 4.3 lb/hr | 3.43 lb/hr | 5.08 lb/hr | 3.7 lb/hr | 9.0 lb/hr |
| Perlite | - | - | - | - | 6.0 tons/hr | 6.75 tons/hr |
| Scrubber water flow | N/A | N/A | N/A | N/A | 190 gpm | Above 165 gpm |

Note: CAM range based on manufacture’s data.

MONITORING APPROACH JUSTIFICATION FOR

EU050

| I. | Background |
| --- | --- |
|  | Formed pulp boards are dried in a 112.35 MMBtu/hr natural gas fired board dryer. The board dryer has two exhaust stacks, one on the north section of the dryer and one on the south section of the dryer. Emissions from the north board dryer exhaust are controlled by Scrubber 53. Scrubber 53 is a W.W. Sly Impinjet Wet Scrubber, Model 3140. Emissions from the south board dryer exhaust are controlled by Multicyclone 54. The multicyclone is a Ducon, Model 6UP. A detailed description of the control equipment is included in the permit application forms and in Attachment H. |
| II. | Rationale for Selection of Performance Indicators |
|  | Scrubber No. 53 has one water tray, where the air bubbles up through the tray. To ensure efficient operation, and to comply with the applicable emission limit, adequate water flow must be supplied to the scrubber. The current Title V permit requires monitoring scrubber water flow rate and air flow differential pressure. During a recent engineering study, air inlet static pressure was found to be an indicator of vacuum for dust removal from the process and not a critical variable for scrubber cleaning performance. Therefore, water pressure at the scrubber is used as the CAM performance indicator. Multicyclone No. 54: To ensure efficient operation of the multicyclone, and to comply with the applicable emission limit, adequate airflow must be supplied to the multicyclone. Control efficiency is a function of inlet velocity, and changes in velocity result in changes in pressure drop across the device. If inlet velocity exceeds a specific value, turbulence becomes excessive and control efficiency decreases. Therefore, static air pressure is the CAM performance indicator, and is monitored at the Multicyclone inlet as an indicator of air flow. |
| III. | Rationale for Selection of Indicator Level |
|  | The indicator ranges are supported by historical emissions test data. Table E.15 summarizes the relevant compliance test results. |

TABLE E.15

COMPLIANCE TEST DATA FOR

EU050

| Board Dryers | 2002 test data | 2003 test data | 2004 test data | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- | --- | --- |
| Particulate Emissions | 5.7 lb/hr | 6.24 lb/hr | 4.8 lb/hr | 11.0 lb/hr |
| Operating rate | 45 ft/min | 43 ft/min | 43 ft/min | 75 ft/min |
| Hot Water Scrubber (North Board Dryer) | 12 psi | 12 psi | 10 psi | 10 psi minimum |
| Multiclone (South Board Dryer) | 5 in WC | 5 in WC | 5 in WC | Between 5 and 15 inches WC |

MONITOR APPROACH JUSTIFICATION FOR

EU065, EU080 and EU081

| I. | Background |
| --- | --- |
|  | Baghouse No. 1 controls various dust sources associated with the Travertone fabrication and ceiling panel scoring line. This production line has not been in operation since 2000. Activities associated with Baghouses 21 and 22 include various dust sources associated with the operation of the PIF line. These sources include a line sander, flipper, and wheelabrator. Process flow diagrams are included in Attachment A. Baghouse No. 1 (EU065) is a Flex Kleen Model 120-WPWC-660-11. Baghouse No. 21 (EU080), is a Fuller Jet Pulse Model 272 C10 baghouse. Baghouse No. 22 (EU081), is a Fuller Jet Pulse Model 168 C10 baghouse. A detailed description of the baghouses is included in the permit application forms and Attachment H. |
| II. | Rationale for Selection of Performance Indicators |
|  | The current Title V permit requires monitoring airflow differential pressure across the baghouse. It is used as the CAM performance indicator, and is monitored continuously via the plant’s Data Historian system. |
| III. | Rationale for Selection of Indicator Level |
|  | The CAM indicator levels for the baghouses were based on a combination of particulate matter tests, visible emission tests, and manufacturer’s recommended specifications. Particulate matter tests were performed on Baghouses No. 21 and No. 22 in 2001, although annual PM testing is not required by the Title V permit. For Baghouse No. 21 and No. 22, the minimum pressure drop was chosen based on the minimum pressure drop observed during recent VE tests. The observed pressure drop is not a strong function of the bag cleaning cycle, as the bag cleaning pulses are every 25 seconds. For Baghouse No. 1, the manufacturer was contacted. Their representative, Mr. Kevin Bahnline, stated that the recommended ranges for this model was from 2 to 6 inches WC. His contact number is 1-800-621-0734, email address is: kbahnline@met-pro.com. Relevant test results are summarized in Tables E.16 through E.18 |

TABLE E.16

COMPLIANCE TEST DATA FOR

EU065

| Baghouse No. 1 |  | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- |
| Particulate Emissions |  | 2.4 lb/hr |
| Travertone Line |  | 11 board/min (9 tons/hr) |
| Pressure drop across baghouse |  | Between 2 and 6 inches water column (in WC) |

Notes:  This unit has not operated since 2000.  The CAM operating ranges were determined using the manufacturer’s recommended specifications of from 2 to 6 inches WC.

TABLE E.17

COMPLIANCE TEST DATA FOR

EU080

| Baghouse No. 21 | 2001 PM test | 2000 VE test | 2001 VE test | 2002 VE test | 2003 VE test | 2004 VE test | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Particulate Emissions | 0.25 lb/hr | VE passed | VE passed | VE passed | VE passed | VE passed | 0.75 lb/hr |
| PIF line Sander | 26.2 BPM | 26.2 BPM | 26.2 BPM | 25 BPM | 26.2 BPM | 26.2 BPM | 33 boards/min |
| Pressure drop across baghouse | 5 in WC | 4.0 in WC | 2.8 in WC | 6 in WC | 5 in WC | 6.5 in WC | Between 2.8 and 8 inches water column (inches WC) |

Notes:  A PM10 test was conducted in 2001.  Annual PM testing is not required.  The 2001 PM test and the 2001 VE test were done at different times during the year.

TABLE E.18

COMPLIANCE TEST DATA FOR

EU081

| Baghouse No. 22 | 2001 VE test | 2002 VE test | 2003 VE test | 2004 VE test | 2005 VE test | Allowable emissions and operating rate, and proposed CAM ranges |
| --- | --- | --- | --- | --- | --- | --- |
| Particulate Emissions | VE passed | VE passed | VE passed | VE passed | VE passed | 0.75 lb/hr |
| PIF line flipper and Wheelabrator | 25 BPM | 25 BPM | 25 BPM | 25 BPM | 25 BPM | 33 boards/min |
| Pressure drop across baghouse | 3.0 in WC | 5 in WC | 4 in WC | 7.8 in WC | 2.8 | Between 2 and 8 inches water column (in WC) |

Notes:  A PM10 test was conducted in 2001; however annual PM testing is not a permit requirement.  VE only.  The particulate emission rate was 0.60 lb/hr.  A VE test was performed by Sanders Engineering & Analytical Services, Inc. on 2/10/05.  During the VE test, the water column reading fluctuated from 1 inch to 2.8 inches in the thirty-minute period.  The readings were recorded in the plant’s Data Historian (copy attached for verification).  The average pressure drop during the test was 2 inches WC.  During the test, the highest opacity reading observed was 0 percent.  The plant was operating normally at 25 boards per minute.