##### ARMSTRONG WORLD INDUSTRIES, INC.

##### INSPECTION NOTES

##### April 2001

References:	0330006-001-AV, Effective May 12, 1999

0330006-002-AC, Effective May 13, 1999

0330006-003-AC, Effective July 1, 1999

0330006-004-AC, Effective Nov 12, 2000

The construction permitted by the above AC permits has been completed. Except 004.

# WET SCRUBBERS

###### Activities associated with ceiling tile manufacture controlled by wet scrubbers

A.1. Capacity. Permits:  033000-001AV/ 0330006-002 and 003-AC

| EU No. | Scrubber No. | Process Line | Max operation rate | Observed |
| --- | --- | --- | --- | --- |
| 003 | 3 | Dry Saw Planer Board Mill Stacker Dry Saw Table Saw Dry Broke Pulp FMS Line | Not limited 24.0 TPH Not limited 2.9 TPH |  |
| 009 | 4 | FMS | 17.6 bd/min* |  |
| 010 | 6 | PIF | 27.5 bd/min* |  |
| 011 | 2 | Mylar Equalizer Salvage Equalizer PIF | 4.67 bd/min 660 SFH* 27.5 bd/min* |  |
| 012 | 7 | PIF | 24.2 bd/min* |  |
| 014 | 5 | Kiln Line # 1 & 2 FMS Tennoners | 2.67 bd/min 20 bd/min |  |
| 054 | 9 | Board Mill Dry Saw | 24 TPH |  |
| 056 | 8 | Paint Mix Line (4 Mixers/ limestonehopper/feeder) | 0.4 TPH ???????????????0.7?????? |  |

*Limit until retested. [Rule-297.310 (2)]

A.2. Hours of Operation.  Emissions units 009 and 014 (scrubber nos. 4, 5) are limited to 8064 hours/year. Records shall be maintained of the hours of operation: Records__________CY 2000 hrs: _________

Remaining units are allowed 8760 hr/yr.

## Emission Limitations and Standards and Test Methods and Procedures

A.3. Particulate Matter:  Particulate matter (PM) shall not exceed the limits in table below. (Permits:  033000-001AV/ 0330006-002 and 003-AC)

A.4. Emissions Tests.  To demonstrate compliance with condition A.3, the permittee shall conduct annual emissions tests for particulate matter for each emission unit.   Title –V:  Annual tests are to be conducted between 15 September and 15 December.

A.5. Test Methods:  The test method shall be Method 5.

| EU No. | Scrubber No. | Permit pph | Test pph | Test Date | Permit VE % | VE Test Actual % | Test Date |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 003 | 3 | 17.8 | 1.18 | 02/28/01* | NA | 0 | 10/26/99 |
| 009 | 4 | 5.7 | 0.7 | 01/23/01 | NA | 7.9 | 09/22/99 |
| 010 | 6 | 4.9 | 0.98 | 02/22/01* | NA | 2.1 | 02/09/00 |
| 011 | 2 | 5.8 | 1.49 | 02/22/01* | NA | 4.38 | 07/06/00 |
| 012 | 7 | 6.5 | 2.85 | 10/19/00 | NA | 0 | 10/19/00 |
| 014 | 5 | 3.5 | 2.79 | 12/08/00 | NA | 1.46 | 11/03/99 |
| 054 | 9 | 13.9 | 2.35 | 12/11/00 | NA | 5.42 | 11/22/99 |
| 056 | 8 | 7.3 | 0.3 | 01/22/01 | NA | 0.21 | 04/28/00 |

*The Department agreed to extend the test date due to circumstances surrounding Chapter 11 filing.

A.6.  Monitoring of Operations.   The permittee shall maintain a record of process rates, and scrubber water flow rates and air flow differential pressure, recording the data at least at each shift change or every eight hours whichever is more frequent.  [Rule 62-4.070(3), F.A.C.] Records_________________

Review Records._________________

| Observed |
| --- |
| Emission Unit No. | Scrubber No. | Water Flow | Pressure |
|  |  |  | Fan Box | Scrubber Shell | Fan Outlet |
| 003 | 3 |  |  |  |  |
| 009 | 4 |  |  |  |  |
| 010 | 6 |  |  |  |  |
| 011 | 2 |  |  |  |  |
| 012 | 7 |  |  |  |  |
| 014 | 5 |  |  |  |  |
| 054 | 9 |  |  |  |  |
| 056 | 8 |  |  |  |  |

# PERLITE EXPANDING

Raw perlite is expanded with natural gas fired perlite expanders with 16 MMBtu/hr heat input.  Expanded perlite is separated from the flue gases in cyclones, and particulate and combustion by-product emissions are controlled by a scrubber.

B.1 Capacity

| EU No | Max Operation Rate | Observed | Max Heat Input | Observed |
| --- | --- | --- | --- | --- |
| 055 | 24 bd/min* |  | 16 MMBtu/hr |  |

*Limit until retested at higher rate

# B.2.  Methods of Operation.  Natural gas fired.  Required to maintain monthly log of fuel usage.  Review Log _____________

Emission Limitations and Standards and Test Methods and Procedures

## B.4.  Particulate Matter:  PM shall not exceed 9 pph.

B.5.  Emissions Tests.  To demonstrate compliance with condition B.3, the permittee shall conduct annual emissions tests for particulate matter for each emission unit.   Title-V:  Annual tests are to be conducted between 15 September and 15 December.

| EU No. | Scrubber No. | Permit pph | Test pph | Test Date | Permit VE % | VE Test Actual % | Test Date |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 055 |  | 9.0 | 2.74 | 10/17/00 | NA | 0 | 10/26/99 |

B.7.  Monitoring of Operations.  The permittee shall maintain a record of process rates, and scrubber water flow rates and air flow differential pressure, recording the data at least at each shift change or every eight hours whichever is more frequent.  [Rule 62-4.070(3), F.A.C.]

| Emission Unit No. | Water Flow | Pressure |
| --- | --- | --- |
|  |  | Fan Box | Scrubber Shell | Fan Outlet |
| 055 |  |  |  |  |

# BOARD DRYING:

Formed pulp boards are dried in a 112.35 MMBtu/hr natural gas fired board dryer.  Emissions from the north board dryer exhaust are controlled by scrubber no. 53 and from the south board dryer exhaust by multicyclone no. 54.  The dryer was initially permitted in the mid-1970s with PM emission limits from the process weight table, and modified in the early 1980s (AC17-51017, June 1, 1982) to allow use of up to 48 MMBtu/hr heat input from wood (since discontinued) with an increased PM emission limit of 0.2 lbs/MMBtu carbonaceous heat input (9.6 lbs/hr).  The PM emission limit of 18.1 lbs/hr reflects the limit included in permit AC17-51017 and the subsequent operating permits less the 9.6 lbs/hr associated with the wood waste heat input and is the combined limit for both the north and south dryer exhausts.

The following specific conditions apply to the emissions unit(s) listed above:

Essential Potential to Emit (PTE) Parameters

C.1.  Capacity.

| EU No. | Max Operations Rate | Observed | Max Heat Input MMBTU/HR | Observed |
| --- | --- | --- | --- | --- |
| 050 | 24 tph wet board |  | 112.35 |  |

C.2.  Methods of Operation - (i.e., Fuels).  Fired with natural gas.  Required to maintain a log showing monthly fuel usage.    Log of monthly fuel usage: ________________Review Log_______________

Emission Limitations and Standards and Test Methods and Procedures

C.4.  Particulate Matter:  Combined PM emissions from the north and south dryer stacks shall not exceed 18.1 pph.

C.5.  Emissions Tests.  To demonstrate compliance with condition C.4, the permittee shall conduct annual emissions tests for particulate matter on both the north and south dryer exhausts.  Title –V:  Annual tests are to be conducted between 15 September and 15 December.

| EU No. | Scrubber No. | Permit pph | Test pph | Test Date | Permit VE % | VE Test Actual % | Test Date |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 050 |  | 18.1 | 5.45 | 02/22/01* | NA | 0 | 10/26/99 |

*Test date extended due to circumstances surrounding Chapter 11 filing.

Monitoring of Operations

C.7.  The permittee shall maintain a record of process rate, heat input, and scrubber water flow and air flow differential pressure, recording the data at least at each shift change or every eight hours whichever is more frequent.   [Rule 62-4.070(3), F.A.C.]

| Emission Unit No. | Water Flow | Pressure |
| --- | --- | --- |
|  |  | Fan Box | Scrubber Shell | Fan Outlet |
| 050 |  |  |  |  |

# BAGHOUSES

E.U.  ID No. 065, 066 080 and 081.

Activities associated with ceiling tile manufacture controlled by baghouses.

EU 065.	Dust sources from the Travertone Fabrication and ceiling panel scoring process lines

controlled by Baghouse no. 1 and vented through vent 65.

EU 066.	 Dust sources from the Travertone Fabrication and ceiling panel scoring process lines controlled by Baghouse no. 1 and vented through vent 66.

EU 080.  A PIF line sander with emissions ducted to a Fuller model 272 C 10 baghouse or equivalent.

EU 081.  A PIF line flipper and wheelabrator with emissions ducted to a Fuller model 168C 10 baghouse or equivalent.

The following specific conditions apply to the emissions unit(s) listed above:

Essential Potential to Emit (PTE) Parameters

D.1.  Capacity.  0330006-001-AV: The process rate shall not exceed 9 tons per hour material processed through the Travertone Production line.  0330006-003-AC:  The process rate shall not exceed 198 ft/min (33 boards/min) processed through the PIF line.]

| EU No. | Production Limit | Observed |
| --- | --- | --- |
| 65 | 9 TPH |  |
| 66 |  |  |
| 80 | 33 bd/min |  |
| 81 |  |  |

## Emission Limitations and Standards

D.3.  Particulate Matter:  Total particulate matter (PM) from EUs 065 and 066 (stacks 65 and 66 from Baghouse no. 1) shall not exceed 2.4 lbs/hr.  PM matter from EU 080 shall not exceed 5.7 pph.  PM from EU 081 shall not exceed 2.1 pph.

D.5 V.E.  Each emission unit shall demonstrate compliance annually with the visible emission limit in accordance with EPA Method 9.  Annual tests are to be conducted between 15 September and 15 December.

D.6. PM.  Testing is waived if the VE limit is met.  If it is not met, PM testing must be done within 45 days of the VE test.

| EU No. | Scrubber No. | Permit pph | Test pph | Test Date | Permit VE % | VE Test Actual % | Test Date |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 065 | East Stack | 2.4 combined | NA. Waived if VE limit is met. | NA | 5 | 0 | 10/13/00 |
| 066 | West Stack |  |  | NA | 5 | 0 | 10/13/00 |
| 080 | Baghouse 21 | 5.7 |  | NA | 5 | 0 | 01/24/01* |
| 081 | Baghouse 22 | 2.1 |  | NA | 5 | 0 | 02/06/01* |

*The Department agreed to extend the test date due to circumstances surrounding Chapter 11 filing.

Monitoring of Operations

D.7.  The permittee shall maintain a record of process rate, and baghouse airflow pressure differential, recording the data at least at each shift change or every eight hours whichever is more frequent.

Review Records___________________

| Unit | Process Rate | Pressure Differential |
| --- | --- | --- |
| Baghouse 1 |  |  |
| Baghouse 21 |  |  |
| Baghouse 22 |  |  |

# UNREGULATED

Appendix U-1, List of Unregulated Emissions Units and/or Activities.

Unregulated Emissions Units and/or Activities.  An emissions unit which emits no “emissions-limited pollutant” and which is subject to no unit-specific work practice standard, though it may be subject to regulations applied on a facility-wide basis (e.g., unconfined emissions, odor, general opacity) or to regulations that require only that it be able to prove exemption from unit-specific emissions or work practice standards.

The below listed emissions units and/or activities are neither ‘regulated emissions units’ nor ‘insignificant emissions units’.

E.U.  ID No.  Brief Description of Emissions Units and/or Activity

075	Clay, Perlite, and Starch Receiving/Storage and Transport

076	Natural Gas Fired Tile Drying (0330006003 & 004-AC)

077		Paint Lines and Booths (0330006-003 & 004-AC)

079		Fugitive Emissions