| INSPECTION REPORT FORM ENVIRONMENTAL PROTECTION COMMISSION OF HILLSBOROUGH COUNTY |
| --- |
| FACILITY: Fabricated Products of Tampa Bay, Inc. | PAGE 1 OF 1 |
| FACILITY ADDRESS: 1700 2nd Avenue EAST | CITY: Tampa PHONE: |
| MAILING ADDRESS: Same | CITY: Tampa | FLA | ZIP: 33605 |
| INSPECTION DATE: October 22, 2013 | TIME IN: 8:30 AM | TIME OUT: 11:00 AM | INSPECTION TYPE: INS2 | STATUS: In-Compliance |
| NEDS NUMBER: 0570363-005-AO |
| SOURCE DESCRIPTION: Spray Painting |
| CONTACT(S): Mr. Steve Hunt Vice President |
| I went to this facility to conduct a FCE inspection at the facility. At the facility I met with Steve Hunt. The facility fabricates various structural steel components and miscellaneous metal parts like exterior and interior structural building. The fabrication of product takes place in a large cover building that is divided into 4 separate bays. All of fabrication and welding get done in the first three (3) bays and also they brushed the metal to be ready for the primer coating. No blasting of pieces takes place on-site. The pieces may be wiped clean with a solvent, typically mineral spirits, if needed prior to coating. A water based primer is the primary coating currently used at the facility. A pump attached to the 55 gallon drum and the coating was pump through two application lines using pneumatic pressure. Each line contained a Graco spray nozzle at the end and used an airless coating application method. Guns are submerged in a small bucket of water upon completion. The area between bay 3 and bay 4 has trap hung in place to help contain any overspray from affecting the other bay. The west side of bay 4 is fully enclosed and has 3 large exhaust fan a bank of filters covering the inlet of each in order to minimize overspray and better ventilate the bay. In the facility’s office I review their recordkeeping and was well organized and I requested a copy of recordkeeping and Steve said he is going to e-mail me their spread shed. The facility is in compliance at this time. At the EPC I brought up that why this facility need operation permit. It is a good to review a new permit determination for this facility it may be exempt from permitting. |
| INSPECTOR: Mohammad Nozari | REPORT DATE: October 23 , 2013 |