| FACILITY ADDRESS: 1700 2nd Avenue East, Tampa, FL 33605 | FACILITY PHONE: 813 247-6024 |
| --- | --- |
| INSPECTION DATE: 6/25/2009 | TIME IN: 9:30 AM | TIME OUT: 12:00 AM | INSPECTION TYPE INS2/FCE | STATUS: IN |
| Permit No. 0570363-004-AO | Expiration Date: September 21, 2010 | Overdue Tests NA | P2 Action: remind of Permit Renewal |
| Warning Notice: 2004-0149A Failure to maintain daily records of amount of primers and Mineral Spirit used during their operation. Failure to maintain daily, monthly and Rolling 12 month total of VOC emissions, and amount and type of primers and Mineral Spirits used during their operation. The WN was closed without enforcement. | Citizen Complaints: No records since 2000. |
| Correspondence File Review: Yes |
| Last Inspected: 8/22/2005 | Last Status: IN | Last Inspector: Lora Web |
| SOURCE DESCRIPTION: Structural Steel Products Coating Facility |
| CONTACT(S): Mr. Michael H. Hunt, President; Ms. Becky Diehl-Stephens |
| Inspection: I arrived at the facility around 9:30 AM and met with Mr. Hunt. I told him that this is an un-announced inspection for the full compliance evaluation for the facility. I asked Mr. Hunt if there will be a new site on 56th street in Tampa as stated in the air permit 0570363-004-AO. Mr. Hunt said there is no plan for that and the permit engineer must have mistaken them for another source. The facility operating site is located across the street. At the facility, there are five segregated open-end warehouse. The west-most warehouse has three spraying area with padded filters and fans. The exhaust exit to the west-side wall through three stacks. The primer is pumped through pipes to the spray area and is kept in a sealed drum. There are two spray guns on site. Mr. Hunt said they are coating the solar power frames for USF. The rest of the warehouse has welding, cutting, and fabricating on steel structure and metal parts. I did not observe any visible emissions on site. Mineral spirits are used for cleaning the metal parts, spray gun(s), hoses, and equipment. I did not observe any abrasive blasting at the facility. Mr. Hunt said they did not do blasting. We went back to the office. I requested 2007 and 2008 records for review. The facility keeps daily primer usage. However, the following data were missing: 1) The primer usage (in gallons) was not summed up for monthly usage and rolling 12-month totals. The facility uses red shop coat primer, gray heavy duty primer, metal master gray primer, and flat gray W/B primer. 2) The 12-month rolling VOC totals for 1/07 and 2/07 were not accurate. 3) The mineral spirit usage (in gallons) was not kept in the rolling 12-month totals. 4) The monthly and 12-month rolling HAP emissions were not kept. 5) The 2008 AOR registered 0 emissions for mineral spirit as no purchase was made in 2008. However, mineral spirit was used in 2008. The facility needs to revise the emissions. Mr. Hunt said that they followed the format as the last inspector requested (Felipe Ascano in 2004 WN). And he said that EPC should let the facility know if the record keeping was not complete back then. I emailed the above noncompliance items to Ms. Becky Diehl-Stephens on 6/25/09 and set a deadline for them to improve the records by 6/29/09. The facility emailed the records on 7/10/09. Permit Conditions Observation 5. The permittee shall not cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. [Rule 62-296.320, F.A.C.] The facility is in compliance. 6. As requested by the permittee, in order to establish the facility as a synthetic minor for both criteria and Hazardous Air Pollutants (HAP), the following emission limitations shall apply: [Rules 62-4.070(3) and 62-212.300, F.A.C. and Permit No. 0570363-001-AC] A) The maximum VOC emissions from the entire facility shall not exceed the following: Material tons/twelve consecutive month period Primer 8.5 Mineral Spirits 1.4 Total 9.9 B) The HAP, as defined in Rule 62-210.200, F.A.C., emissions shall be less than 10 tons in any 12 consecutive month period for any individual HAP, and less than 25 tons in any 12 consecutive month period for any combination of HAPs. The max. VOC was 6.11 tpy in 5/2007. The highest HAP emissions were 0.42 tpy in January 2009. 7. The emission limitations of Specific Condition No. 6 shall be achieved by the application of low solvent coating technology. [Rule 62-296.513(3)(a), F.A.C.] The facility is using water based primers. 8. The permittee shall not cause, allow, or permit the discharge into the atmosphere of any volatile organic compounds in excess of 3.5 pounds per gallon of coating, excluding water, delivered to a coating applicator. [Rule 62-296.513(2)(a)2., F.A.C.] The highest VOC coating has 3.43 lbs/gal. 9. All volatile organic compound emissions from solvent washings shall be considered in the emission limitation of Specific Condition No. 8, unless the solvent is directed into containers that prevent evaporation into the atmosphere. [Rule 62-296.513(2)(c), F.A.C.] The facility uses minimal amount of mineral spirit to clean hand and nozzles. 10. The following restrictions and limitations shall apply in order to ensure compliance with Specific Condition No. 6: [Rules 62-4.070(3) and 62-210.200(130), F.A.C. and 0570363-001-AC] Hours of operation are not restricted. Material usage shall not exceed the following: Material gallons/12 consecutive month period Primer 4857 Mineral Spirits 430 The permittee shall not dilute the coating prior to its application to the metal substrate. The spray coating operation shall be performed only in the designated spray coating area. The spray coating area shall have an impervious layer to prevent paint overspray and solvents from entering the soil and contaminating the ground water. Material safety data sheet for each coating and solvent shall be maintained on site and be made available upon request to any local, state, or federal air pollution agency. The permittee shall not perform prepping operations such as abrasive blasting. The highest usage for primer was 3360 gallons in 4/2007. The highest usage for mineral spirits was 110 gallons in 4/2007. The facility has impervious floor in the spry areas. The facility is in compliance with the rest of the permit conditions. 11. In order to demonstrate compliance with Specific Condition Nos. 6, 8, and 10, the permittee shall maintain daily records of operations. Records shall be kept onsite for two years and shall be made available for inspection to any local, state, or federal air pollution agency upon request. The records shall include, but not limited to, the following: [Rule 62-296.500(2)(b)1., F.A.C.] Date Types and Amount of Primer and Mineral Spirit(s) Used (gallons) VOC Content in primer and solvent(s) as Applied (lbs/gal) HAP Content in primer and solvents (lbs/gal) Monthly Summary of Types and Amount of Primer and Mineral Spirit(s) Used As Applied (gallons) Monthly Summary of VOC emissions (lbs) Monthly Summary of HAP emissions (lbs) Rolling 12 month total of E), F), and G) above The facility failed to record HAP emissions. The facility emailed the records with HAP inventory on 7/10/2009. The highest 12-month HAP were 0.42 xylene tpy in January 2009. 14. The permittee shall not store, handle, process, or use in any process the volatile organic compounds or organic solvents without applying known and existing vapor emission control devices or systems as follows and as deemed necessary and ordered by the Environmental Protection Commission of Hillsborough County: [Rule 62-296.320, F.A.C.] A) Maintain tightly fitting cover, lids, etc. on all containers when they are not being handled, tapped, etc. B) Where possible and practical, procure/fabricate a tightly fitting cover for any open trough, basin, etc. of VOC so that it can be covered when not in use. Immediately attend to all spills/waste as appropriate. The facility is in compliance. 15. All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provision in Rule 62-296.320, F.A.C. These provisions are applicable to any source, including, but not limited to, vehicular movement, transportation of materials, construction, alterations, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. Reasonable precautions shall include, but not limited to, the following: All spent material on the shop floor of the spray painting areas shall be collected on a regular basis and properly disposed of. No abrasive blasting shall be performed on site. The facility is in compliance. Mr. Hunt is aware of the permit condition. 19. Prior to sixty days before the expiration of this operating permit, the permittee shall apply for a renewal of the permit using the current version of the permit renewal application form. A renewal application shall be timely and sufficient. If the application is submitted prior to sixty days before the expiration of the permit, it will be considered timely and sufficient. If the renewal application is submitted at a later date, it will not be considered timely and sufficient unless it is submitted and made complete prior to the expiration of the operation permit. When the application for renewal is timely and sufficient, the existing permit shall remain in effect until the renewal application has been finally acted upon by the EPC or, if there is court review of the final agency action, until a later date is required by Section 120.60, Florida Statutes. [Rule 62-4.090, F.A.C.] I remind the facility of next renewal date. I left the facility around 12:00 AM. |