INSPECTION REPORT

AIR POLLUTANT EMISSION SOURCES

| FACILITY Wellcraft Marine, Plant 6 | DISTRICT Southwest | COUNTY Manatee |
| --- | --- | --- |
| ADDRESS 1651 Whitfield Avenue Sarasota FL 34243 | CONTACT(S) William McDonald, (941) 753-7811 |
| AIRS ID# 0810073 | PERMIT # 0810073-005-AV | EXPIRATION DATE May 8, 2005 | ARMS ENTRY DATE August 19, 2002 |
| SOURCE DESCRIPTION Fiberglass boat manufacturing facility |
| INSPECTION DATE July 11, 2002 | AUDIT TYPE II-CDS | COMPLIANCE STATUS In compliance |
| INSPECTION FINDINGS |
| PARAMETER | ALLOWED VALUE | OBSERVATION |
| 1. Facility Wide Conditions | No objectionable odors. No VE >20%. Hull Lamination Building exhaust fans shall be operating whenever usage of VOC containing materials occurs and remain operating for at least 2 hrs after usage stops. There shall be no device which reduces the vertical momentum of the stack gas. All VOC/OS containing materials stored in closed containers. Clean-up solvents , tools, etc. shall be in containers that prevent evaporation. Limit issue of clean-up solvents to employees. Doors and windows shall be closed. Hull Lamination Building must have audible alarm that will sound after a door has been opened for > 4 minutes. Vapor-tight line must exist from the storage tank to the delivery vehicle. Vapor line must be connected before gelcoat resin is transferred into the tank. Vehicle must be vapor tight. Maintain signs (at least 2’ X 3’) adjacent to each door reminding of the need to keep doors shut. Hull Lamination building employees shall be trained. New employees within 30 days. HLB ventilation system operated IAW manufacturer’s instructions. Hull lamination room shall be operated under negative pressure during VOC application and for at least 2 hours after stopping. Lamination Building louvered wall vents must be permanently sealed. Tamper resistant switched s must be installed on the roof mounted exhaust fans. Fiber filters shall be used to control overspray emissions from gelcoat operations. Gelcoat area fiber filters shall be changed and maintained. DEP access must be within 15 minutes of arrival. Written procedure shall be posted at the entry gate guardhouse. | In compliance |
| 2. Emission limits (SC A.2) | a. Styrene: 74.3 lb/hr 187.4 tons/consec 12 months b. Total VOCs: 247.0 tons/consec 12 months | a. 105.7 TPY b. 132.61 TPY |
| 3. Operating parameters (SCs A.1, A.3-A.6) | a. Unrestricted hours. b. All lamination operations, except minor touch-up and repair, to be done in the lamination building. c. All gelcoat ops, except minor touch-up and repair, to be done in gelcoat booths in lamination building. d. Exhaust ventilation as shown in Attachment A to permit. Stacks must meet minimum flows and velocities. e. VE from gelcoat operations not to exceed 5%. | In compliance. A new attachment A had been sent to the Department on 12/18/01 but was misfiled and did not get into the 6/5/02 permit so it was not available during the inspection. The correct Attachment A was subsequently placed into the permit. |
| 4. Testing/Compliance requirements (SCs A.7-A.10) | Test one stack from each of three groups (see permit Specific Cond. A.7) annually, within 60 days prior to anniversary date of initial tests for flow and velocity. Record condition of filters, if any. | 32S out of compliance during last test. (8/24 & 28/ 2001) Problem corrected. Enforcement action taken.. Fan J was in compliance. |
| 5. Recordkeeping (SC A.12) | Keep a log with the following (retain 5 years): a. Daily (complete by end of next business day): Hours of operation, including 2 hr after VOC use. b. Monthly (within 10 business days of the end of next month): Monthly and rolling 12 month total emission rates for each category, including emission factors. c. Above calculations assume uniform rates of material usage. Appropriate recordkeeping shall be conducted if routine and significant deviations from uniform usage are experienced. d. Supporting documentation (MSD sheets, purchase orders, etc.) shall be kept and shall include sufficient information to determine VOC emissions. e. Record date of all gelcoat booth filter changes. | Facility had records back to 1998. Employee works hours are used to track hours of operation. Receipts are used to track material usage. Emission factors in permit (guidance memo) were being used to calculate emissions. |
| 6. Reporting (SC A.13, Facility-wide Conditions, and Tab TV-3) | a. Report any proposed process changes 15 days prior to proposed implementation. b. Furnish written notification of changes to the air management system of the HLB that may render the VOC capture efficiencies ineffective. Must be made at least 7 days prior to making any changes. | See comments from Block 3 above. |
| COMMENTS Comments on Block 1 items: Propylene carbonate is the solvent that is used. The dispenser is locked and there are specific times when it is dispensed. Signs are posted by the overhead doors. One of the large doors was opened for 3½ minutes and the alarm sounded. Several doors were checked for negative pressure. Reviewed training records and operating procedures that new employees are trained on. Gelcoat filters are changed every other day. Comments on Block 2 item: Values are from the 2001 Annual Operating Report. The pounds per hour values are a hold over from toxics laws that are not in force any more. They are used for guidance only. The plan is to modify this facility to manufacture only blue water/salt water fishing boats. They plan on manufacturing ~3,500 boats/year. |
| INSPECTOR(S) NAME(S) Nancy E. Knight |
| SIGNATURE(S) | DATE August 19, 2002 |