INSPECTION REPORT

AIR POLLUTANT EMISSION SOURCES

| FACILITY Wellcraft Marine, Plant 1, EU001 Title V Facility | DISTRICT Southwest | COUNTY Manatee |
| --- | --- | --- |
| ADDRESS 7150 15th Street East Sarasota FL 34243 | CONTACT(S) William McDonald, (941) 753-7811 |
| AIRS ID# 0810074 | PERMIT # 0810074-002-AV | EXPIRATION DATE 11/22/2004 | ARMS ENTRY DATE August 19, 2002 |
| SOURCE DESCRIPTION Fiberglass boat manufacturing facility |
| INSPECTION DATE 11 July 2002 | AUDIT TYPE II-CDS | COMPLIANCE STATUS In compliance |
| INSPECTION FINDINGS |
| PARAMETER | ALLOWED VALUE | OBSERVATION |
| 1. Facility-wide conditions Specific Conditions II.2, 3, 7, &8 (SC II.2, 3, 7, &8) | a. No objectionable odors b. For visible emissions not otherwise covered by a specific rule, visible emissions must be <20%. c. Must apply all known vapor emission controls (see list of specific requirement in permit condition II.7) d. Must take reasonable precautions to prevent and control emissions of unconfined particulate matter. | In compliance. Checked negative pressure at several doors. A small quantity of gel coat is used for small parts finishing. |
| 2. Emission limits SC A.2 | a. Styrene: 178.7 tons/consec 12 months b. Total VOCs: 247.0 tons/consec 12 months | a. 54.707 tons in calendar year 2001 b. 9.653 tons in calendar year 2001 (Source: 2001 AOR) |
| 3. Operating limitations | a. Unrestricted hours. SC A.1 b. All lamination operations, except minor touch-up and repair, to be done in lamination building and all gelcoat ops, except minor touch-up and repair, to be done in gelcoat booths in lamination building. SC A.3 c. Ventilation systems to be operated and maintained IAW manufacturer’s instructions. SC A.4 d. VE from gelcoat ops limited to 20%; but VE >5% may indicate need for additional controls. SC A.5 | Solvent used is limited to certain hours. Dispenser is locked. No visible emissions noted. Exhaust fans are OK. |
| 4. Recordkeeping SC A.6 | Keep a log with the following (retain 5 years): a. Daily (complete by end of next business day): Hours of operation, including 2 hr after VOC use. b. Monthly (by end of next month): Monthly and rolling 12 month total emission rates for each category, including emission factors. c. Date of all gelcoat booth filter changes. d. Supporting documentation (MSD sheets, purchase orders, etc.) shall be kept and shall include sufficient information to determine VOC emissions. | Records are kept back to 1998. Filters are changed in the grinding booth 1/week, exhaust fan filters are changed 1/month and gel coat filters are changed 1/week. There was no log of gel coat filter changes, but that will be started immediately. |
| 5. Reporting SC A.7 | Report any proposed process changes at least 15 days prior to proposed implementation. | In compliance |
| COMMENTS |
| INSPECTOR(S) NAME(S) Nancy Knight |
| SIGNATURE(S) | DATE August 19, 2002 |