INSPECTION REPORT

AIR POLLUTANT EMISSION SOURCES

| FACILITY Donzi Marine Title V Facility | DISTRICT Southwest | COUNTY Manatee |
| --- | --- | --- |
| ADDRESS 7110 21st Street East Sarasota, FL 34243 | CONTACT(S) Michael Harrison, Plant Manager, (941) 727-0622 Richard Byron, EH&S Director, (941) 727-0622 |
| ARMS ID# 0810076 | PERMIT # 0810076-004-AV | EXPIRATION DATE 9/29/03 | ARMS ENTRY DATE February 23, 2005 |
| SOURCE DESCRIPTION Fiberglass boat manufacturing plant. |
| INSPECTION DATE February 23, 2005 | AUDIT TYPE INS2 | COMPLIANCE STATUS |
| INSPECTION FINDINGS |
| PARAMETER | ALLOWED VALUE | OBSERVATION |
| 1. Odors (II.2) | No objectionable odor | None noted during inspection |
| 2. Control of VOC and OS emissions (II.5) | Maintain tightly fitting covers on all VOC/OS containers when not being handled, tapped, etc.; prevent excessive air turbulence across exposed VOCs; properly maintain all fittings, valves, etc.; and attend to all spills immediately. | In compliance throughout plant. |
| 3. Operating (A.1) | 5,840 hours using gel-coat or resin in the Fiberglass Lamination Building in any consecutive 12-month period | In compliance |
| 4. Capacity (A.2-A.3) | Limited to only resin non-spray layup with 50% available styrene. Gelcoats must be 45% available styrene. | Using 33%-styrene resin, flowcoaters, and water-based adhesives. Consequently, emissions are very low. |
| 4. Total VOC emissions (A.4) | 248.8 tons per 12 consecutive month period (233.8 tons per 12 months from other than trivial/exempt activities) | 27.6 tons in calendar year 2004 (most recent 12-month rolling total. |
| 5. Record keeping (A.4) | a. Total monthly hours using gelcoat and/or resin and total for last 12 consecutive months. b. Total quantity of VOC-containing materials, % VOC in each, and method of application. c. VOC emissions from each material in lb/month and total VOC emissions in tons/month. d. Total tons of VOC emissions for last 12 consecutive months. e. Footnotes listing emission factors used. f. Monthly logs complete by end of following month. Records must be kept 5 years. | In compliance |
| 6. Visible emissions (A.5) | 5% opacity, as an indicator of adequate control of unconfined PM. | No visible emissions from stacks. |
| COMMENTS |
| INSPECTOR NAME Joseph H. Cox, Jr. |
| SIGNATURE | DATE February 23, 2005 |