| AIR POLLUTION SOURCE INSPECTION REPORT FORM DEPARTMENT OF ENVIRONMENTAL PROTECTION |
| --- |
| FACILITY: Precision Boat Works, Inc. | PAGE: 1 OF 1 |
| FACILITY ADDRESS: 1511 18th Avenue Drive East | CITY: Palmetto, FL 34221 | COUNTY: Manatee |
| MAILING ADDRESS: 1511 18th Avenue Drive East | CITY: Palmetto | STATE: FL | ZIP: 34221 |
| INSP. DATE: 9/10/2009 | TIME IN: n/a | TIME OUT: n/a | INSP TYPE: INS2 | STATUS: IN |
| IDENTIFICATION NO: 0810210 | EU ID # Facility Wide |
| SOURCE/FACILITY DESCRIPTION: Fiberglass Boat Manufacturing Facility |
| CONTACT(S): Richard Porter, VP, and Bill Porter |
| I, James Burkholder (JB), went to Precision Boat Works, Inc. on September 10, 2009 to perform an onsite compliance inspection as part of a full compliance evaluation. Precision Boat Works is a smaller operation and is considered a Synthetic Minor for HAPs and VOCs. The facility was well maintained and kept good housekeeping practices. There is a small paint booth located inside of the building towards the back. All of the resin and gelcoat operations are applied inside of the paint booth. Two exhaust fans exhaust air from the spray booth area and there are multiple garage bay openings to help ventilate the building. All of the solvent, resin, and gelcoat containers were properly sealed. No objectionable odors were detected; however, resin or gelcoat application was not in operation. There is a woodworking station near the front of the building by the office, which was well maintained to prevent fugitive particulate emissions. A shop-vac is used to remove excess particulate emissions from the work station. Production has slowed due to lack of business demand, which have caused a drop off in HAP and VOC emissions from the facility. The 2009 year to date records show that emissions are: 2009 YTD Emissions Permitted Limit Styrene 1.768 Tons 9.4 Tons MMA 7.03 Tons N/A Total Haps 8.798 Tons 24 Tons VOC 9.38 Tons 24 Tons At the time of Inspection, the facility appeared to be in compliance. |
| INSPECTOR(S): James Burkholder (JB) | TIME EXPENDED: JB – 180 mins | REPORT DATE: 10/9/2009 |