| AIR POLLUTION SOURCE INSPECTION REPORT FORM DEPARTMENT OF ENVIRONMENTAL PROTECTION |
| --- |
| FACILITY: A.S.A. Manufacturing, Inc. | PAGE: 1 OF 1 |
| FACILITY ADDRESS: 14879 SW 111th St | CITY: Dunnellon, FL 34432 | COUNTY: Marion |
| MAILING ADDRESS: 14879 SW 111th St | CITY: Dunnellon | STATE: FL | ZIP: 34432 |
| INSP. DATE: 9/29/2009 | TIME IN: 3:00 pm | TIME OUT: 4:00 pm | INSP TYPE: INS2 | STATUS: IN |
| IDENTIFICATION NO: 0830104 | EU ID # Facility Wide |
| SOURCE/FACILITY DESCRIPTION: Fiberglass Products Manufacturing |
| CONTACT(S): Todd Duplessis, President |
| I, James Burkholder (JB), and Joe Panetta (JP) went to A.S.A. Manufacturing on September 29, 2009 to perform an onsite compliance inspection as part of a full compliance evaluation. When we arrived on site with met with Mr. Todd Duplessis, President, of A.S.A. MFG, Inc. Mr. Duplessis pulled the requested records for VOC and HAP emissions from October of 2007 to present day. The highest 12 month rolling emissions were in October of 2007 with: 8.21 tons total HAPs, 7.60 tons Styrene, and 11.01 tons VOCs. The facility is permitted for 35.8 tons of total HAPs, 34.1 tons of an individual HAP, and 48.7 tons of VOCs. The facility is well under their permitted limits for VOC and HAP emissions. Please see the attached records for all 12 month rolling records for the referenced time frame. The facility was well maintained and all spraying is done inside of the spray booth which has two fans to ventilate the booth. Business demand is down and the fan filters are changed out approximately every 4 to 6 months. When business demand increases the filters are changed out approximately every 2 months. Fire code only permits the facility to have so much solvent inside of the building at one time because the material is very flammable. The resins/gelcoats kept inside of the facility building were properly sealed and all solvent washes are collected and stored in sealed containers. No objectionable odors were detected at the facility. Mr. Duplessis escorted JP and I to a storage shed approximately 30 yards away from the main building. All of the solvents, resins, and gelcoats were kept in the storage shed and were properly sealed with no leaks. At the time of inspection the facility appeared to be in compliance. |
| INSPECTOR(S): James Burkholder (JB); Joe Panetta (JP) | TIME EXPENDED: JB – 180 mins JP – 140 mins | REPORT DATE: 10/9/2009 |