| 1030004 001 57511 |
| --- |
| FACILITY: APAC Southeast Florida | PERMIT ID: 95 |
| Clearwater, Asphalt Plant | DISTRICT: Southwest |
| ADDRESS: 12955 40th Street North | CONTACT PHONE: |
| Clearwater, FL | 813-623-3622 |
| ARMS NO: 1030004 001 | PERMIT NO: | EXPIRATION DATE: |
|  | 1030004-011-AF | 2/2/10 |
| EMISSION UNIT DESCRIPTION : 200 TPH Asphalt Plant, Controlled by a Standard Havens, Alpha Mark III-30 Baghouse; includes Asphalt Heater fired on natural gas, new No. 2 Virgin and No. 5 reclaimed fuel oil. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | 2/12/07 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review | ( | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry | ( | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: L.F. Rollins? | ( | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Luther Ellis? ( |  | Yes |  | No |
|  | Comments: |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Rule Applicability The asphalt concrete plant is subject to NSPS requirements of 40 CFR 60, Subpart I, Standards of Performance for Hot Mix Asphalt Facilities. The facility is subject to the provisions of Rule 62-210.300(3)(c)1. F.A.C., Conditional Exemptions from Title V Air Permitting. This permit maintains the facility as a synthetic non-Title V source by limiting the facility’s emissions to less than the threshold limits required for the facility to be considered a major source per Chapter 62-213, F.A.C. Objectionable Odor – The plant shall not cause, suffer, allow or permit the discharge of air pollutants that cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere which by itself, or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rule 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- none; Wind direction – North West Upwind odor level detected-none. 4. Unconfined Emissions of Particulate Matter - All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, industrial related activities such as loading, unloading, storing and handling, hoppers, conveying equipment, conveyor drop points, roads, parking areas, stock piles, and yards. Reasonable precautions to be taken include, but not limited, to the following: Paving and maintenance of roads, parking areas, and yards or the application of water to unpaved roads, parking areas, and yards to control emissions; The use of sprinklers on stock piles, if necessary; Removal of particulate matter from roads and other paved areas under control of owner or operator to mitigate re-entrainment, and from building or work areas to prevent particulate from becoming airborne; and, Landscaping or planting of vegetation. [Rules 62-296.320(4)(c), and 62-210.300(3)(c)1.e., F.A.C.] {Permitting Note: If operating experience indicates that these reasonable precautions are not sufficient to control unconfined emissions, the Department reserves the right to require additional measures, such as recordkeeping for water truck gallons applied, etc.} Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 5. Fugitive Emissions Opacity Standard - In order to provide reasonable assurance that the precautions and practices taken at the facility are adequate, all sources of unconfined particulate matter not subject to 40 CFR 60, Subpart OOO, (see Emission Unit Nos. 004 and 005 limitations), shall not exceed 10% opacity. Exceedance of this limit shall not be considered a violation in an of itself, but may be a violation of the precautions specified in Specific Condition No. 4. [Rule 62-4.070(3), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. This does not apply at this time. 6. Circumvention – No person shall circumvent any air pollution control device, or allow the emission of air pollutants without the applicable air pollution control device operating properly. [Rule 62-210.650, F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. This does not apply at this time. 7. Fuel Usage - The total facility-wide fuel oil usage shall not exceed 1.2 million gallons per any consecutive 12-month period. [Rule 62-210.300(3)(c)1.b., F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. There has been no fuel usage in the facility in 3 three years. EMISSION UNIT NO. 001 Rule Applicability - The asphalt concrete plant is subject to the requirements of 40 CFR 60, Subpart I - Asphalt Concrete Plants and the general provisions of 40 CFR 60, Subpart A, where applicable, which are adopted by reference in Rule 62-204.800(7), F.A.C. [Rule 62-204.800(7), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 9. Conditional Exemption - As requested by the permittee, the asphalt concrete plant and liquid asphalt heater are subject to the Conditional Exemptions from Title V Air Permitting requirements of Rule 62-210.300(3)(c)1., F.A.C. (Also see Specific Condition Nos. 14.B. 15.B., 15.C., and 15.D.) [Rule 62-210.300(3)(c)1, F.A.C. and Construction Permit No. 1030004-003-AC] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 10. Operating Hours(Asphalt Plant) - The asphalt concrete plant is allowed to operate no more than 2,358 hours per any consecutive 12-month period. [Rule 62-210.200, F.A.C., Definitions (PTE) and Construction Permit No.1030004-003-AC] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 11. Operating Hours (Asphalt Heater) - The liquid asphalt heater, deemed an insignificant source, is allowed to operate continuously, i.e., 8,760 hours per any consecutive 12-month period. [Rule 62-4.040, F.A.C. and Construction Permit No. 1030004-003-AC] Comments: The source did not operate in the last 12 months. 12. PM and VE Emissions from Asphalt Plant - Emissions from the asphalt concrete plant’s baghouse shall comply with the following: A. Particulate emissions shall not exceed 0.04 grains/dscf averaged over a 3-hour period (based on a design exhaust airflow of 28,250 dscfm the expected equivalent particulate emissions are 9.7 lbs./hr. and 11.4 ton/yr.). B. Visible emissions (VE) shall not be equal to or greater than 20% opacity. [40 CFR 60 - Subpart I, Rules 62-204.800(8), F.A.C., 62-210.300(3)(c)1.d., F.A.C., and, 62-210.300(3)(c)1.f., F.A.C.] Comments: NA The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 13. VE Emissions from Asphalt Heater - Visible emissions from the liquid asphalt heater shall not be equal to or greater than 20% opacity. Since the heater is deemed an insignificant source, only a special visible emissions compliance test* may be required. * Special Compliance Tests. When the Department, after investigation, has good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it shall require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and to provide a report on the results of said tests to the Department. [Rules 62-296.320(4)(b) and 62-297.310(7)(b), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 14. The maximum permitted capacities of the asphalt concrete plant are as follows: A. Daily Process Rate - 200 tons/hr. whether producing RAP or virgin/conventional asphalt concrete production, on a daily average basis. B. Annual Process Rate - 471,600 tons of asphalt concrete production in any consecutive 12-month period. [Rule 62-210.300(3)(c)1.a., F.A.C. and Construction Permit No. 1030004-003-AC] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 15. The asphalt concrete plant’s dryer and liquid asphalt heater shall comply with the following: Dryer A. The maximum heat input rate is 84.0 MMBTU/hr. (PERMITTING NOTE: This value is based on a maximum peak fuel usage rate of 600 gals./hr., where as the expected any consecutive 12 month average fuel usage rate is 500 gals./hr.) B. Shall be only fired with natural gas, new No. 2 virgin diesel fuel oil having a maximum sulfur content of 0.5%* by weight, or on-specification No. 5 reclaimed fuel oil having a maximum sulfur content of 0.7%* by weight. Liquid Asphalt Heater C. Shall be only fired with natural gas or new No. 2 virgin diesel fuel oil having a maximum sulfur content of 0.5%* by weight. Dryer and Liquid Asphalt Heater combined D. The total fuel oil usage shall not exceed 1.2 million gallons per any consecutive 12-month period. * Permitting Note: These values are stricter than the limitation in Rule 62-210.300(3)(c)1.c., F.A.C. [Rule 62-210.300(3)(c)1.b., F.A.C. and Construction Permit No. 1030004-003-AC] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 16. Fuel Oil Specification - The permittee shall not burn "off-specification" used oil. For each delivery of "on-specification" reclaimed/used fuel oil, the vendor shall provide an analysis documenting the fuel oil meets the following requirements of 40 CFR 761.20(e)(2) and (3) [July 1, 1993] and 40 CFR 279.11 (July 1, 1993): Arsenic shall not exceed 5 ppm Cadmium shall not exceed 2 ppm Chromium shall not exceed 10 ppm Lead shall not exceed 100 ppm Total Halogens shall not exceed 1000 ppm Flash point shall not be less than 100 degrees F. PCB's shall be less than 2 ppm* * In order to be able to fire "on-specification" reclaimed/used fuel oil during startup and shutdown. Copies of the analysis shall be maintained at the facility for the most recent 5 years and made available to the Department and Pinellas County Department of Environmental Management (PCDEM) upon request. [Rules 62-710.210 and 62-4.070(3), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 17. Fuel Oil Sulfur Content - In order to document continuing compliance with the sulfur content limitations, in % by weight, of the fuel oil used in the asphalt concrete plant's dryer and liquid asphalt heater, the permittee shall keep records on either vendor provided as-shipped analysis or on analysis of as-received samples taken at the plant. The analysis shall be determined by ASTM methods ASTM D4057-88 and ASTM D129-91, ASTM D2622-94 or ASTM D4294-90, adopted and incorporated by reference in Rule 62-297.440(1), F.A.C. The above records shall be maintained at the facility for a minimum of 5 years and made available to the Department and PCDEM upon request. [Rules 62-210.300(3)(c)1.c. and 62-4.070(3), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 18. Operation and Maintenance (O & M) Plan - The Standard Havens Alpha Mark III-30 baghouse shall be operated and maintained in accordance with the Operation and Maintenance (O&M) Plan submitted with the emission compliance test report for the test conducted on July 14, 1998, and as revised with the prior approval of the PCDEM. The O&M Plan documentation shall be retained at the facility for the most recent 2 years and made available to the Department and PCDEM upon request. At a minimum, the O&M Plan shall include: A. The operating parameters of the pollution control device; B. Time table for the routine maintenance of the pollution control device as specified by the manufacturer; C. Time table of routine periodic observations of the pollution control device sufficient to ensure proper operation; D. A list of the type and quantity of the required spare parts for the pollution control device which are stored on the premises of the permit applicant; E. A record log which will indicate, as a minimum: 1. When the maintenance and observations were performed; 2. What maintenance and observations were performed; 3. Who performed the said maintenance and observations; and Acceptable parameter ranges for each parameter check. [Rule 62-4.070(3), F.A.C., Pinellas County Code, Section 58-128 and Construction Permit No. 1030004-003-AC] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 19. Recordkeeping Requirements - The following limitations apply to the asphalt concrete plant and liquid asphalt heater: All records shall contain Facility Name, Facility ID No., Emission Unit ID No. and Date. Daily Process Records A. Daily record the total asphalt concrete production, in tons, for each of the following when operating: 1. Virgin/conventional asphalt concrete 2. RAP asphalt concrete 3. Both types of asphalt concrete combined B. Daily record the hours of producing each type of asphalt concrete and the total hours of producing both types of asphalt concrete when operating. C. Daily record the daily average production rate of asphalt concrete produced, in tons/hr., for each of the following when operating: 1. RAP asphalt concrete 2. Virgin/conventional asphalt concrete Monthly Process Records D. Monthly record the total tons of both types of asphalt concrete produced, and calculate and record the most recent combined consecutive 12-month rolling total, in tons. E. Monthly record the total operating hours of the asphalt concrete plant’s dryer along with a consecutive 12-month rolling total, in hours. F. Monthly record the quantity of each of the 3 types of fuel used to fire the asphalt concrete plant's dryer along with the overall monthly average MMBTU/hr. heat input rate. If the last compliance test was conducted when the dryer was fired with new No. 2 virgin diesel fuel oil, then a daily cumulative total of the hours the dryer was fired with on-specification No. 5 reclaimed fuel oil, since that last test shall also be recorded until the 400th hour is recorded. (see Specific Condition No. 22) If the last compliance test was conducted when the dryer was fired with natural gas, then a daily cumulative total of the hours the dryer was fired with new No. 2 virgin diesel fuel oil and on-specification No. 5 reclaimed fuel oil, since that last compliance test shall also be recorded until the 400th hour is recorded. (see Specific Condition No. 22) G. Monthly record the quantity of each of the 2 types of fuel used to fire the liquid asphalt heater. H. Monthly record the total usage of all fuel oil combined in the asphalt plant’s dryer and liquid asphalt heater. I. Monthly record the most recent consecutive 12-month rolling total usage of all fuel oil combined in the asphalt plant’s dryer and liquid asphalt heater. {PERMITTING NOTE: Daily records shall be completed within 3 business days and monthly records shall be completed by the end of the following month. These records shall be maintained at the facility for at least 5 years and made available to the Department and PCDEM upon request.} [Rules 62-4.070(3) and 62-210.300(3)(c)1.g., F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 20. PM and VE Testing - Test the asphalt concrete plant dryer's baghouse exhaust for particulates and visible emissions annually within 60 days prior to or on the date of August 19. The emission test reports shall be submitted to the Air Compliance Sections of this office and the PCDEM within 45 days of testing. [Rules 62-297.310(7) and 62-297.310(8)(b), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 21. PM and VE Test Method - Compliance with the emission limitations of Specific Condition No. 11.A. shall be determined using EPA Methods 1, 2, 3, 4, and 5 or 5A. Compliance with the visible emissions limitations of Specific Condition Nos. 12.B. and 13 (if required) shall be determined using EPA Method 9. These test methods are contained in 40 CFR 60, Appendix A, and adopted by reference in Chapter 62-297, F.A.C. Note the following: A. The minimum requirements for stack sampling facilities, source sampling and reporting, shall be accordance with Rule 62-297, F.A.C. and 40 CFR 60, Appendix A. B. The visible emissions test for the asphalt concrete plant dryer's baghouse shall be at least 30 minutes in duration. C. If a special visible emissions compliance test for the liquid asphalt heater is requested by the Department, the test shall be at least 30 minutes in duration. [Rules 62-210.300(3)(c)1.i. and 62-297, F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 22. Operation during Testing - Pursuant to Rules 62-297.310(2) and 62-4.070(3), F.A.C., this plant shall comply with all of the following: A. If at any time the production rate of hot mix asphalt concrete is more than 10% above the production rate at which the most recent compliance test was conducted, then within 30 days of the date that higher production rate was recorded, the facility shall conduct new compliance tests. The new compliance tests shall be conducted at a production rate which is not less than that higher production rate recorded and no greater than 200 tons/hr. B. A compliance test submitted when the dryer is fired with natural gas will automatically constitute an amended permit to allow the dryer to be only fired with natural gas and up to 400 hrs. of firing fuel oil. Within 30 days of exceeding the 400th hour of firing the dryer with new No. 2 virgin diesel fuel oil and on-specification No. 5 reclaimed fuel oil, new compliance tests shall be conducted with the dryer being fired with fuel oil. C. A compliance test submitted when the dryer is fired with a new No. 2 virgin diesel fuel oil will automatically constitute an amended permit to allow the dryer to be only fired with new No. 2 virgin diesel fuel oil or natural gas and up to 400 hrs. of firing on-specification No 5 reclaimed fuel oil. Within 30 days of exceeding the 400th hour of firing the dryer with on-specification No. 5 reclaimed fuel oil, new compliance tests shall be conducted with the dryer being fired with on-specification No. 5 reclaimed fuel oil. D. A compliance test submitted when the dryer is fired with on-specification No. 5 reclaimed fuel oil will automatically constitute an amended permit to allow the dryer to be only fired with on-specification No. 5 reclaimed fuel oil, new No. 2 virgin diesel fuel oil, or natural gas. E. Since the Department has determined processing only virgin/conventional materials has the greatest potential to generate emissions vs. RAP, a compliance test submitted when processing RAP shall limit the plant to processing only RAP. If the plant is so limited, within 30 days upon processing virgin materials (conventional hot mix asphalt), new compliance tests (particulate & visible emissions) for the dryer’s baghouse shall be conducted using only virgin materials. A compliance test submitted when processing only virgin materials shall also allow the plant to process RAP. F. All compliance test results shall be submitted to the Air Compliance Section of this office and the PCDEM within 45 days of testing. G. Failure to submit the following with any compliance test report for the test period may invalidate the test(s): 1. Production rate of hot mix asphalt concrete in tons/hr. Be sure to include a statement indicating whether virgin materials or RAP was used. 2. Type of fuel used. 3. Fuel oil analysis of the sulfur content of the fuel oil used. 4. Used fuel oil analysis to document compliance with the on-specification used oil limits, if on-specification No. 5 reclaimed fuel oil was used to fire the dryer. 5. A copy of the records for the month the test was conducted as required by Specific Condition No. 20. [Rules 62-4.070(3) and 62-297.310, F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. SPECIFIC FACILITY REQUIREMENTS 48. Compilation of Records - Daily records shall be completed within 5 business days and monthly records shall be completed by the end of the next month. These records shall be maintained at the facility for a minimum of the most recent five (5) year period and made available to the Department and PCDEM upon request. [Rule 62-4.070(3), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 49. Testing Notification - The permittee shall notify the Air Compliance Section of the PCDEM at least 15 days prior to the date on which each formal compliance test is to begin of the date, time and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 50. Maintenance of Records - The permittee shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of an affected facility; or any malfunction of the air pollution control equipment. The records shall be recorded in a permanent form suitable for inspection and shall be retained for the most recent 5 years. [Rule 62-204.800(7), F.A.C. and 40 CFR 60.7(b)] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 51. Annual Operating Report (AOR) - Submit to the Air Compliance Sections of this office and the PCDEM (unless otherwise directed by the Department) for this facility, each calendar year and on or before March 1, an annual operating report [DEP Form 62-210.900(5)] for the preceding calendar year pursuant to Rule 62-210.370(3), F.A.C. Emission unit No. 005, a general permitted source, will not be required to submit AORs. Comments: The source must submit an AOR for 2006 before march 1st, 2007. 52. Operating Permit Renewal - An application to renew this permit shall be submitted to the Air Permitting Section of this office at least 60 days prior to the expiration date of this permit. A copy of the application should also be sent to the Air Permitting Section of the PCDEM. To properly apply for the operation permit renewal, the permittee shall submit the following: Comments: The permit expires on 2/2/10. An application is required to be submitted no later than 12/4/09. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating ( Yes No Comments: I spoke by phone with Mr. Luther Ellis who stated that there are no plans to re-open the APAC Plant. He stated that the no crushing has been performed and is not planned to be performed at this facility. He added however that the aggregate piles at this facility are being used occasionally. |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred ( Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: 2/13/07 |
| ACCESS? | ( | ARMS? | ( |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030004 001 57511.doc