| 1030004 005 57513 |
| --- |
| FACILITY: APAC Southeast Florida | PERMIT ID: 2679 |
| Clearwater, Asphalt Plant | DISTRICT: Southwest |
| ADDRESS: 12955 40th Street North | CONTACT PHONE: |
| Clearwater, FL | 813-623-3622 |
| ARMS NO: 1030004 005 | PERMIT NO: | EXPIRATION DATE: |
|  | 1030004-011-AF | 2/2/10 |
| EMISSION UNIT DESCRIPTION : 250 TPH Portable Recycle Asphalt Pavement (RAP) Crushing System. The portable RAP crusher is owned by a different company and is brought on site from time to time to crush the RAP |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | 2/12/07 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: L.F. Rollins? |  | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Luther Ellis? |  | Yes |  | No |
|  | Comments: |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Rule Applicability The facility is subject to the provisions of Rule 62-210.300(3)(c)1. F.A.C., Conditional Exemptions from Title V Air Permitting. This permit maintains the facility as a synthetic non-Title V source by limiting the facility’s emissions to less than the threshold limits required for the facility to be considered a major source per Chapter 62-213, F.A.C. The 250 tons/hour portable RAP crushing unit is subject to 40 CFR 60, Subpart OOO, Standards of Performance for Nonmetallic Mineral Processing Plants and the general provisions of 40 CFR 60, Subpart A, where applicable, which are adopted by reference in Rule 62-204.800(8), F.A.C. This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: The facility did did not have a copy of the permit on-site. 3. Objectionable Odor – The plant shall not cause, suffer, allow or permit the discharge of air pollutants that cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere which by itself, or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rule 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- ; Wind direction - Upwind odor level detected- 4. Unconfined Emissions of Particulate Matter - All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, industrial related activities such as loading, unloading, storing and handling, hoppers, conveying equipment, conveyor drop points, roads, parking areas, stock piles, and yards. Reasonable precautions to be taken include, but not limited, to the following: Paving and maintenance of roads, parking areas, and yards or the application of water to unpaved roads, parking areas, and yards to control emissions; The use of sprinklers on stock piles, if necessary; Removal of particulate matter from roads and other paved areas under control of owner or operator to mitigate re-entrainment, and from building or work areas to prevent particulate from becoming airborne; and, Landscaping or planting of vegetation. [Rules 62-296.320(4)(c), and 62-210.300(3)(c)1.e., F.A.C.] {Permitting Note: If operating experience indicates that these reasonable precautions are not sufficient to control unconfined emissions, the Department reserves the right to require additional measures, such as recordkeeping for water truck gallons applied, etc.} Comments: 5. Fugitive Emissions Opacity Standard - In order to provide reasonable assurance that the precautions and practices taken at the facility are adequate, all sources of unconfined particulate matter not subject to 40 CFR 60, Subpart OOO, (see Emission Unit Nos. 004 and 005 limitations), shall not exceed 10% opacity. Exceedance of this limit shall not be considered a violation in an of itself, but may be a violation of the precautions specified in Specific Condition No. 4. [Rule 62-4.070(3), F.A.C.] Comments: 6. Circumvention – No person shall circumvent any air pollution control device, or allow the emission of air pollutants without the applicable air pollution control device operating properly. [Rule 62-210.650, F.A.C.] Comments: 7. Fuel Usage - The total facility-wide fuel oil usage shall not exceed 1.2 million gallons per any consecutive 12-month period. [Rule 62-210.300(3)(c)1.b., F.A.C.] Comments: EMISSION UNIT NO. 005 32. Rule Applicability - The recycled asphalt or concrete (RAP) crushing unit is subject to the requirements of 40 CFR 60, Subpart OOO - Standards of Performance for Nonmetallic Mineral Processing Plants and the general provisions of 40 CFR 60, Subpart A, where applicable, which are adopted by reference in Rule 62-204.800(7), F.A.C. [Rule 62-204.800(7), F.A.C., and 40 CFR 60, Subpart OOO] Comments: 33. Operating Hours - This portable RAP crushing plant is allowed to operate a maximum of 2,000 hours per any consecutive 12-month period. [Rule 62-210.200, F.A.C. – Definitions (PTE), Construction Permit No. 1030004-009-AC] Comments: 34. Daily Process Rate - The maximum allowable material processing rate for this portable RAP crushing plant is 250 tons/hour, based on a daily average. [Rule 62-210.200, F.A.C. – Definitions (PTE), Construction Permit No. 1030004-009-AC] Comments: 35. Annual Process Rate - The maximum allowable annual RAP processing rate for this RAP crushing plant is 125,000 tons per any consecutive 12-month period. [Rule 62-210.200, F.A.C. – Definitions (PTE), Construction Permit No. 1030004-009-AC] 36. No. 2 Fuel Oil Usage Rate – The maximum No. 2 fuel oil consumption for this RAP crushing plant shall not exceed 46,000 gallons per any consecutive 12-month period. [Construction Permit No. 1030004-009-AC] Comments: 37. No. 2 Fuel Oil Sulfur Content – The sulfur content of the No. 2 fuel oil supplied for this portable RAP crushing plant shall not exceed 0.5% by weight. [Construction Permit No. 1030004-009-AC] Comments: 38. General Visible Emission Standard - No person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). [Rule 62-296.320(4)(b)1., F.A.C.] Comments: 39. Visible Emissions – The following emission points of this portable RAP crushing plant are affected sources pursuant to 40 CFR 60, Subpart OOO. The permitted maximum allowable emission from each emission point is as follows: Emission Unit ID Emission Point Opacity Rule 005 EP01-Crusher/Grinder 15% 40CFR60.672(c) 005 EP02-Conveyor Drop Points 10% 40CFR60.672(b) 005 EP03-RAP Screener 10% 40CFR60.672(b) Truck dumping of nonmetallic minerals into any screening operation, feed hopper, or crusher is exempt from the requirements of this section, but must comply with 62-296.320(4)(c), F.A.C. (see Specific Condition # 4) [40 CFR 60.672] Comments: 40. Portable RAP Crushing Plant Permit Applicability – No portable rock crushing plant shall be allowed to be brought to this asphalt plant site without having its own current Florida Air General Permit (AG). [Rule 62-4.070(3), F.A.C.] Comments: 41. Portable RAP Crushing Plant - This portable rock crushing plant, operating at this facility, is subject to all the terms and conditions of its current Florida Air General (AG) Permit and any denoted applicable condition of this Air Operation Permit. A portable rock crusher shall be tested in accordance with its current AG permit requirements. [Rule 62-4.070(3), F.A.C.] Comments: 42. Major Source Restriction – This portable rock crushing plant shall not be located in such a manner as to create a “Major Source of Air Pollution” as defined in Rule 62-210.200, F.A.C., Definitions-Major Source of Air Pollution without first obtaining a “Title V Permit” from the Department or approved local program office that has permitting/compliance jurisdiction over the current or proposed operating location. [Rule 62-210.370(1), F.A.C.] Comments: 43. Additional Compliance Testing - When the Department, after investigation, has good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it may require the owner or operator of the emissions unit to (1) conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and (2) provide a report on the results of said tests to the Department. [Rule 62-297.310(7)(b), F.A.C.] Comments: Recordkeeping Requirements 44. Daily Process Records - In order to demonstrate compliance with Specific Condition No. 34, the permittee shall daily determine and record the portable RAP Crusher’s material processing rate (tons/hour, daily average) as follows: For each day that the portable RAP Crushing Plant operates, the permittee shall record the following: Facility Name, and Facility ID No. E.U. ID No.; Date; The portable RAP Crushing Plant’s current Air General Permit ID No. The portable RAP Crushing Plant’s hours of operation; The total amount of material processed, in tons; Calculate and record the daily average RAP processing rate, tons/hour. [Rule 62-4.070(3), F.A.C.] {Permitting Note: See Specific Condition No. 48 for compilation of daily record time line.} Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 45. Monthly Process Records - In order to demonstrate compliance with the Specific Conditions Nos. 33 and 35, the permittee shall monthly record the following: Facility’s total amount of RAP produced in tons for the most recent month period. Facility’s total amount of RAP produced in tons for the most recent consecutive 12-month period. The RAP Crusher’s operating hours for the most recent consecutive 12-month period. [Rule 62-4.070(3), F.A.C.] {Permitting Note: See Specific Condition No. 48 for compilation of monthly record time line.} Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 46. Monthly Fuel Oil Usage Record - In order to demonstrate compliance with Specific Condition No. 36, the permittee shall monthly record the following: The diesel engine and diesel generator’s total amount of fuel oil consumed (gallons) for the most recent month period; The diesel engine and diesel generator’s total amount of fuel oil consumed (gallons) for the most recent consecutive 12-month period. [Rule 62-4.070(3), F.A.C.] {Permitting Note: See Specific Condition No. 48 for compilation of monthly record time line.} Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 47. No. 2 Fuel Oil Sulfur Record - In order to demonstrate compliance with Specific Condition No. 37, the permittee shall maintain the following record with every delivery of No. 2 fuel oil: A copy of a certified ASTM fuel oil analysis of the No. 2 fuel oil delivered by the fuel supplier to account for the sulfur content of the fuel being burned. [Rule 62-4.070(3), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. SPECIFIC FACILITY REQUIREMENTS 48. Compilation of Records - Daily records shall be completed within 5 business days and monthly records shall be completed by the end of the next month. These records shall be maintained at the facility for a minimum of the most recent five (5) year period and made available to the Department and PCDEM upon request. [Rule 62-4.070(3), F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 49. Testing Notification - The permittee shall notify the Air Compliance Section of the PCDEM at least 15 days prior to the date on which each formal compliance test is to begin of the date, time and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 50. Maintenance of Records - The permittee shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of an affected facility; or any malfunction of the air pollution control equipment. The records shall be recorded in a permanent form suitable for inspection and shall be retained for the most recent 5 years. [Rule 62-204.800(7), F.A.C. and 40 CFR 60.7(b)] Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 51. Annual Operating Report (AOR) - Submit to the Air Compliance Sections of this office and the PCDEM (unless otherwise directed by the Department) for this facility, each calendar year and on or before March 1, an annual operating report [DEP Form 62-210.900(5)] for the preceding calendar year pursuant to Rule 62-210.370(3), F.A.C. Emission unit No. 005, a general permitted source, will not be required to submit AORs. Comments: The facility is in cold shut down. It was not operating at the time of my visit and the gates were padlocked. 52. Operating Permit Renewal - An application to renew this permit shall be submitted to the Air Permitting Section of this office at least 60 days prior to the expiration date of this permit. A copy of the application should also be sent to the Air Permitting Section of the PCDEM. To properly apply for the operation permit renewal, the permittee shall submit the following: Comments: The permit expires on 2/2/10. An application is required to be submitted no later than 12/4/09. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030004 005 57513.doc