1030019 001 66738

| FACILITY: Honeywell, Inc. | PERMIT ID: 104 |
| --- | --- |
| Defense and Space Electronic Systems, Clearwater | DISTRICT: Southwest |
| ADDRESS: 13350 U.S. Hwy. 19 North | CONTACT PHONE: |
| Clearwater, FL | 737-539-3001 |
| ARMS NO: 1030019 001 | PERMIT NO: | Expiration Date: 11/16/09 Renewal Date: 4/5/09 |
|  | 1030019-007-AV |  |
|  |  | Test Due Date: 3/5/00 |
| EMISSION UNIT DESCRIPTION : Plant 1: Beryllium Operations Consisting of 11 De-burring and 1 Blast Station. Emissions Controlled by a Torit Cyclone Collector and Common HEPA Filter. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | February 26, 2009 |  |  | INS1 |  | INS2 | ( | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Kirk Gerber? |  | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Tom Fiedler, Dottie -5880, Rob Pendrys -2667? |  | Yes |  | No |
|  | Comments: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Section II. Facility-wide Conditions. The following conditions apply facility-wide: This permit or a copy thereof shall be kept at the work site of the permitted activity. [APPENDIX TV-1, TITLE V CONDITION 12(12)] Comments: on-site permit was reviewed by AQD. Renewals. Prior to one hundred eighty (180) days before the expiration of a permit issued pursuant to Chapter 62-213, F.A.C., the permittee shall apply for a renewal of a permit using forms incorporated by reference in the specific rule chapter for that kind of permit. [Rule 62-4.090(1), F.A.C.] Comments: The permit application is due to be submitted on, or before 12/10/03. 2. General Pollutant Emission Limiting Standards. Objectionable Odor Prohibited. The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants which cause or contribute to an objectionable odor. [Rule 62-296.320(2), F.A.C., Pinellas County Ordinance 97-05, Section 33, Sec. 58-178, and 1030226-001-AC] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor detected- None; Wind direction – E /10 mph Upwind odor detected-None 3. General Particulate Emission Limiting Standards. General Visible Emissions Standard. Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1. & 4., F.A.C.] Comments: No visible emissions observed 4. Prevention of Accidental Releases (Section 112(r) of CAA). If required by 40 CFR 68, the permittee shall submit to the implementing agency: A. A risk management plan (RMP) when, and if, such requirement becomes applicable; and B. Certification forms and/or RMPs according to the promulgated rule schedule. [40 CFR 68] Comments: A risk management plan and certification forms are not required 7. [Not Federally Enforceable.] General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds or organic solvents without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. 7. [Not Federally Enforceable.] General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds or organic solvents without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The following requirements are "not federally enforceable": A. Maintain tightly fitting cover, lids, etc. on all containers of OS/VOC/HAPs when they are not being handled, tapped, etc. B. All VOC/HAPs fittings, valve lines, etc. shall be properly maintained. C. All VOC/HAPs spills shall be attended to immediately and the waste properly disposed of, recycled, etc. D. All solvent from solvent washings (equipment clean-up) shall be directed into containers that prevent evaporation in the atmosphere. [Rule 62-296.320(1)(a), F.A.C.] All solvents are covered with tight fitting lids on all containers. All fittings and valve lines are properly maintained Honeywell’s SOP is that all VOC/HAP spills are attended to immediately and the waste is properly disposed. All solvent washings are directed in containers that are sealed and removed as hazardous waste. 8. [Not Federally Enforceable.] Emissions of Unconfined Particulate Matter. Pursuant to Rules 62-296.320(4)(c)1., 3., & 4., F.A.C., reasonable precautions to prevent emissions of unconfined particulate matter at this facility include the following requirements (see Condition No. 57 of Appendix TV-4, Title V Conditions): The following requirements are "not federally enforceable": A. Lawn and Ground Maintenance – Application of water to non-vegetative areas, as needed, landscaping and grass in other areas, as necessary. B. Parking Areas – Application of water as needed. C. Paved and Unpaved Areas – Application of water, as needed, the removal of particulate matter from paved areas, limited site access to vehicles, and establish appropriate vehicle speed limitations. As an indicator that the precautions to control unconfined particulate matter emissions as required above are adequate, emissions of unconfined particulate matter from the facility shall not exceed 5% opacity. If this value is exceeded, it shall not be a violation in and of itself, but an indication that additional control precautions and/or work practices may be necessary. [Rules 62-4.070(3) and 62-296.320(4)(c)2., F.A.C.; and, proposed by the applicant in the renewal Title V permit application dated December 1, 2003] Comments: The facility has well kept lawns, parking areas are paved and there are no unpaved lots. 10. Statement of Compliance. The annual statement of compliance pursuant to Rule 62-213.440(3)(a)2., F.A.C., shall be submitted to this office and the EPA within 60 (sixty) days after the end of the calendar year using DEP Form No. 62-213.900(7), F.A.C. {Permitting Note: This condition implements the requirements of Rules 62-213.440(3)(a)2. and 3., F.A.C. (see Condition No. 51 of Appendix TV-4, Title V Conditions)} [Rules 62-213.440(3) and 62-213.900, F.A.C.] Comments: The Statement of compliance of calendar year 2007 was reviewed on 4/4/08 15. Emission Limitations. The permittee shall comply with the following emission limitations: A. Emissions of VOC’s from the facility, which includes VOC’s from the degreasers, shall not exceed a total of 90.0 tons per any consecutive 12-month period. B. Any individual HAP shall not exceed 8.0 tons per any consecutive 12-month period. C. Total HAPs shall not exceed 20.0 tons per any consecutive 12-month period. D. The beryllium emissions from Emission Unit No. 001 shall be considered in the limitations of Condition Nos. 15.B. and 15.C. [Rule 62-210.200 – Definitions (PTE), F.A.C.; Permit No. 1030019-006-AC] Comments: The highest reported emissions were 2.19 tons VOC, 0.937 tons individual HAP, and 2.65 tons total HAPS/12-month period for the months of June, 08’, June, 08’, & June, 08’ respectively. Reviewed records for the months of Mar, 08’ through Feb, 09’. 17. Operating Records. The permittee shall comply with the following requirements in order to demonstrate compliance with Condition Nos. 15 and 16: A. A separate usage log shall be kept for the degreasers. At a minimum the log shall record the following: 1. By the end of the next business day that a VOC solvent is removed, or added to a degreaser, the date, name of the VOC solvent, and amount of VOC solvent in gallons shall be recorded for each degreaser and made available for inspection. 2. A monthly total, in pounds and gallons for each VOC solvent used along with the most recent consecutive 12-month period total in tons and gallons of all VOC solvents used, will be maintained to ensure the applicable usage and emission limitations are not exceeded. Note, the amount of VOC solvent used shall be determined on a mass balance method (amount used minus amount recycled or reclaimed and minus solids). B. In order to demonstrate compliance with Condition Nos. 15.A. through 15.C. the permittee shall maintain the following logs: 1. Monthly, calculate and record the monthly emissions* of each individual HAP (in tons), total HAPs (in tons), and total VOC's (in tons) from the materials/products** tracked by the facility tracking system (including the degreasers). 2. Monthly calculate and record emissions* for the most recent consecutive 12-month period for all individual HAP, total HAPs, and total VOC's from the materials/products** tracked by the facility tracking system, in tons. *Emissions shall be calculated using the following method: Emissions = Beginning Inventory + Purchases – Ending Inventory – Waste Shipped Off Site. As an alternate to the primary method, the facility may also calculate emissions using the following: a. Emissions = Purchases – Waste Shipped or b. Emissions = Purchases. **Only materials/products that are tracked in the facility tracking system shall be used. All materials must be tracked by the facility tracking system. Daily records/logs shall be compiled within fifteen (15) calendar days and monthly records/logs shall be completed by the end of the following month. All records/logs shall have sufficient information to determine compliance with the limitations of this permit. All records/logs shall be maintained at the facility for at least 5 years and made available to the Department and PCDEM upon request. {Note: An electronic tracking and reporting system (database) may be used to satisfy the recordkeeping requirements of this condition provided that paper reports can be generated and made available for inspection by the Department and/or PCDEM upon request. The Department and/or PCDEM has the option of accepting electronic media copies of all facility records.} [Rule 62-4.070(3), F.A.C.; Permit No. 1030019-006-AC] Comments: Reviewed records for the months of Mar, 08’ – Feb, 09’. A partial copy of the records are attached as an example of the record format. Essential Potential to Emit (PTE) Parameters A.1. Permitted Capacity. No more than 12 stations shall be operating simultaneously when processing beryllium. Permitting Note: Also see Condition No. A.3.A. [Rule 62-210.200 – Definitions (PTE)] Comments: The highest reported number of stations operating any one time was 7 de-burring stations and a soda blaster for the month of Aug, 08’. The facility did not reach its limit during the past compliance year. Reviewed records for the months of Mar, 08’ – Feb, 09’ Emission Limitations and Standards A.2. The beryllium emissions from these 12 stations at this facility shall not exceed 10 grams over a 24-hour period. {Permitting note: Unless otherwise specified, the averaging time for this condition is based on the specified averaging time of the applicable test method.} [40 CFR 61.32(a) and Rule 62-204.800(10), F.A.C.] Comments: The last annual compliance test, conducted on 2/28/08 showed emission of < 0.005 ug was detected during any of the 3 runs. Therefore the total emissions are 0.000804 grams/24-hour period. Results for this year pending submittal and review. Test Methods and Procedures A.3. Compliance testing for beryllium emissions from this emission unit shall be conducted annually within 60 days prior to or on the date of March 5. The tests shall be conducted in accordance with the methods and procedures of 40 CFR 61, Subpart C, and as follows: Testing of beryllium emissions shall be conducted when the maximum number of 12 stations are simultaneously processing beryllium. A compliance test submitted when less than the maximum permitted number of 12 stations are simultaneously processing beryllium will automatically constitute an amended permit to only allow the simultaneous operation of the maximum number of stations that were operating during that test. Within 30 days of operating more stations simultaneously, when processing beryllium, than was operating during the most recent test, a new compliance test shall be conducted with at least that higher number of stations operating simultaneously, but in no case shall the number of stations simultaneously processing beryllium exceed 12. The test results shall be submitted to the Air Compliance Sections of this office and the Pinellas County Department of Environmental Management (PCDEM) within 45 days of testing. Acceptance of the test by the Department will automatically constitute an amended permit at the higher number of stations tested when simultaneously processing beryllium, but in no case shall the maximum permitted number of 12 stations simultaneously processing beryllium be exceeded. Each compliance emission test report shall include the following: 1. A statement indicating the number of stations that were simultaneously processing beryllium during the test period. 2. A copy of the most recent compliance emission test. [Rules 62-297.310(2), 62-297.310(7)(a)4.c., 62-297.310(8)(b), and 62-4.070(3), F.A.C.] [Rules 62-297.310(2), 62-297.310(7)(a)4.c., 62-297.310(8)(b), and 62-4.070(3), F.A.C.] Comments: The test should be completed between January 4th and March 5th. The last test was conducted on 2/26/09, and the test results have not been submitted. The last test, on 2/26/09, was conducted with 9 stations operating. Based on that test, the facility process rate was limited to 0.000804 grams/24-hour period.. This year’s test results are required to be submitted by 4/15/09 A.4. Test Notification. The permittee shall notify the Air Compliance Section of the PCDEM at least 15 days prior to the date of which each formal compliance test is to begin of the date, time and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted. [Rule 62-297.310(7)(a)9, F.A.C.] Comments: The County was notified on 1/16/09, for the test that was conducted on 2/26/09. Recordkeeping and Reporting Requirements A.6. A combined daily log for the 11 de-burring and 1 blast stations shall be maintained to document compliance with the limitations of Condition B.3. At a minimum the log shall indicate the following: A. De-burring and/or Blast Station numbers (DB or BS). B. Start and stop time for each beryllium operator. C. Facility location (Plant No. 1) D. Date E. Operator name [Rule 62-213.440(1)(b), F.A.C.] Comments: Reviewed records for the months of Mar, 08’ – Feb, 09’. A partial copy of the records are attached as an example of the record format. A.7. [Not Federally Enforceable.] The permittee shall comply with the O&M Plan attached to the permittee’s letter dated June 5, 1998, and as revised with the prior approval of the PCDEM. [Pinellas County Code, Section 58-128] Comments: The facility continues to comply with the O&M plan 40 CFR 61, Subparts A and C – NESHAPs Requirements. A.8. This emission unit shall comply with 40 CFR 61, Subparts A and C incorporated into Attachments A and B, which are part of this permit. [Rule 62-204.800(10), F.A.C.] Comments: The emission unit complied with 40 CFR 61, Subparts A and C., National Emission Standard for beryllium adopted and incorporated by reference in Rule 62-204.800(10), F.A.C. 40 CFR 61, Subpart C - NESHAPs Requirements D.4. The following additional conditions are required by 40 CFR 61, Subpart C - National Emission Standard for Beryllium Section 61.12 Compliance with standards and maintenance requirements. (c) The owner or operator of each stationary source shall maintain and operate the source, including associated equipment for air pollution control, in a manner consistent with good air pollution control practice for minimizing emissions. Determination of whether acceptable operating and maintenance procedures are being used will be based on information available to the Administrator which may include, but is not limited to, monitoring results, review of operating and maintenance procedures, and inspection of the source. Comments: During the compliance year, the facility maintained and operated the source consistent with good air pollution control practices. Section 61.19 Circumvention. No owner or operator shall build, erect, install, or use any article machine, equipment, process, or method, the use of which conceals an emission which would otherwise constitute a violation of an applicable standard. Such concealment includes, but is not limited to, the use of gaseous dilutants to achieve compliance with a visible emissions standard, and the piecemeal carrying out of an operation to avoid coverage by a standard that applies only to operations larger than a specified size. Comments: There was no evidence of circumvention either with EU001 the beryllium deburring area or with the degreasing operation EU 002. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No very small emissions 0.00084 grams/day of Be Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: A Method 103 Audit was performed along with the facility-wide inspection. Additionally, the facility has applied for a FESOP (synthetic minor). Under changes of the Florida Statutes, the facility can opt out of a Title V permit and instead operate as a FESOP Correspondence from Cindy-Zhang Torres, permitting engineer with FDEP SWD to Honeywell’s consultant on 1/23/09: This facility has been designated as a Title V facility because it is subject to 40 CFR 61, Subpart C – National Emission Standard for Beryllium. The revised Florida Statutes now allows this facility to be permitted as a non-Title V source because they are not a major source of HAPs. Please let the facility know about this change. If the facility wants to change its status from Title V to non-Title V, they need to specifically request this change in their application and apply for a FESOP. Their operation permit renewal application due date will not change, i.e., 4/5/09. |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030019 | OWNER Honeywell, Inc. | FACILITY NAME Defense and Space Electronic Systems, Clearwater |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE September 15, 2009 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | Reviewed and processed 4/20/09 |
| DONE N/A | Statement of compliance | Reviewed and processed 5/7/09 |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual | Reviewed and processed 6/15/09 |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 2/16/09 | 3/2/09 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs |  |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) |  |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) | Performed 2/16/09 |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date: 	9/17/09

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.