| 1030026 001 57350 |
| --- |
| FACILITY: R.E. Purcell Construction Company, Inc. | PERMIT ID: 1 |
| Plant No. 2 | DISTRICT: Southwest |
| ADDRESS: 1550 Starkey Road | CONTACT PHONE: |
| Largo, FL | 727-584-3329 |
| ARMS NO: 1030026 001 | PERMIT NO: | EXPIRATION DATE: |
|  | 1030026-008-AO | 8/17/10 |
| EMISSION UNIT DESCRIPTION : 250 Ton/hour Asphalt Plant: Gencor Industries, Inc., Model 400 Ultra Drum Mix Asphalt Plant Controlled by a Gencor Industries Inc. Primary Collection System (knockout box) and a Caterpillar, Autopulse II, Model No. APL-720 Baghouse. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | March 6, 2007 |  |  | INS1 |  | INS2 | ( | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review | ( | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry | ( | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Dale E. Phillips? | ( | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Dale E. Phillips? | ( | Yes |  | No |
|  | Comments: Messrs. Dale Phillips and Sid Mawby answered my questions. Mr. Phillips instructed Mrs. Wanda Pettis to provide the logs required by permit. |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: The facility ( did □ did not have a copy of the permit on-site. Emission and Operating Limitations Objectionable Odor. The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants from this plant which cause or contribute to an objectionable odor. Objectionable odor is defined as “Any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance.” [Rules 62-296.320(2), 62-210.200, Definitions-(Objectionable Odor), F.A.C. and Pinellas County Code, Section 58-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- none; Wind direction – North Upwind odor level detected-none General Visible Emission (VE) Limit. Visible emissions shall not be equal to or greater than 20% opacity. [Rule 62-296.320(4)(b)(1), F.A.C.] Comments: I performed a Method 9, VE that yielded an opacity of 0.0%. Reasonable Precautions of Unconfined Emissions of Particulate Matter. All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. Reasonable precautions to be taken include the following: Paved parking and trafficked areas shall be maintained and kept free of particulate matter build-up. Sprinkling with water shall be used as necessary on paved areas, unpaved areas, stockpiles and during loading/unloading operations. Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent re-entrainment, and from building and work areas to prevent particulate from being airborne. Landscaping or planting of vegetation. All aggregate brought into the facility arrives and is dumped in a damp matter. Posting and enforcing a 5 MPH speed limit in all traffic areas. [Rules 62-4.070(3), 62-210.300(3)(c)1.e., and 62-296.320(4)(c), F.A.C.] Comments: The facility’s yard areas were wet and there were no fugitive dust emissions. Fugitive Emissions Opacity Standard. In order to provide reasonable assurance that the precautions and practices taken at the facility are adequate, all sources of unconfined particulate matter not subject to 40 CFR 60, Subpart OOO, (see Emission Unit No. 003’s limitations), shall not exceed 10% opacity. Exceedance of this limit shall not be considered a violation in and of itself, but an indication that additional control precautions and/or practices beyond those outlined in Specific Condition No. 5 may be necessary. [Rule 62-4.070(3), F.A.C.] Comments: There were no visible emissions from the Crusher’s emission points. VEs from these emission points are due to be submitted with the Stack Tests Results. Operating Changes. Any proposed change to this source which will cause the limitations of this permit to be exceeded, such as design-parameters changes or an increase in emissions may be considered a modification and must be reported. The permittee shall notify the Air Permitting Section of this office of any changes and receive written approval from this office of the changes prior to implementing the changes. [Rule 62-4.070(3), F.A.C.] Comments: Messrs. Phillips and Mawby stated that there had not been any additions or modifications made to Purcell Asphalt in the past year and I did not see anything that could be construed to be a modification or addition to the EU. Circumvention. No person shall circumvent any air pollution control device, or allow the emission of air pollutants without the applicable air pollution control device operating properly. [Rule 62-210.650, F.A.C.] Comments: I did not see any device that would circumvent the pollutions control devices at Purcell. Special Compliance Test. When the Department, after investigation, has good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it shall require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and to provide a report on the results of said tests to the Department. [Rule 62-297.310(7)(b), F.A.C.] Comments: No tests have been ordered by the Department to date. Particulate Matter Emission Limitations. Particulate matter (PM) emissions from the Drum Mix Asphalt Concrete Plant (EU ID No. 001) shall not exceed 0.04 grains per dry standard cubic foot averaged over a three-hour period. [40 CFR 60 Subpart I, 60.92(a)(1), Rule 62-210.300(3)(c)1.d., F.A.C. and adopted by reference in Rule 62-204.800(8), F.A.C.] Comments: A Method 5 PM test was performed to determine the grains per DSCF Operational Limits. This facility is limited to the following hours of operation and throughput: E.U. ID No. Brief Description Maximum Hours of Operation per consecutive 12-month period Daily Average Maximum Throughput (conventional/RAP asphalt concrete production in tons/hour) Maximum Throughput (conventional /RAP asphalt concrete production in tons/ consecutive 12 month period) 001 Drum Mix Asphalt Concrete Plant 4,000 250 1,000,000 [Rules 62-4.070(3) and 62-210.200, F.A.C., Definitions-(PTE); and Construction Permit 1030026-004-AC] Comments: The highest 12 month consecutive running total hours was reached at the end of the month of August 2006 with 1,456.9 hours. The highest average tons of Asphalt produced was during the month of February 2006 with an average of 197 tons per hour. The highest 12 mos. running cumulative total tons produced came at the end of the month of May 2006 with 268,177 tons of asphalt produced. Visible Emissions. Visible Emissions (VE) from the facility shall be limited to: E.U. ID No. Brief Description VE Limit (% Opacity) 001 Drum Mix Asphalt Concrete Plant 20 [62-204.800(8), 62-296.320(4)(b)(1) and 62-297.310(7)(b), F.A.C.; and Construction Permit 1030026-004-AC] Comments: The Opacity observed by this inspector was 0.0% opacity during a 30 minute Method 9 VE test. Fuel Usage and Specifications. The facility is limited to the following fuel usage: Type of Fuel. The facility is limited to using the following fuel(s): E.U. ID No. Brief Description Maximum Heat Input Rate (MMBtu/hr) Maximum Fuel Consumption Rate (gallons/hour) Fuel Type Maximum Weight Percent Sulfur (%) 001 (Dryer) Drum Mix Asphalt Concrete Plant (Dryer) 85 750* “On-Specification” Reclaimed No. 5 fuel oil 0.5 New No. 2 fuel oil Natural Gas N/A * The plant is limited to using a maximum of 750 gallons of fuel oil per hour. This limitation includes the asphalt tank hot oil heater. {Permitting Note: It may be necessary to have multiple fuel oil/used oil tanks to comply with these limitations under certain operational scenarios.} Comments: The facility was combusting oil at a rate of (typically) 340 gallons per hour and typically 50 MMBTU per hour. The facility is using only On-Spec used oil number 5 with an MMBTU rating of 146,000 BTU per gallon. Used Oil Specifications. The permittee shall not burn “off-specification” used oil. For each delivery of “on-specification” reclaimed/used fuel oil, the vendor shall provide an analysis* documenting the fuel oil meets the following requirements of 40 CFR 761.20(e)(2) and (3) and 40 CFR 279.11 (July 1, 2004): Constituent/Property Allowable Level Arsenic 5 ppm maximum Cadmium 2 ppm maximum Chromium 10 ppm maximum Lead 100 ppm maximum Total Halogens Shall not exceed 1000 ppm1 Flash Point 100 degrees F minimum PCB’s Shall be less than 2 ppm2 1Levels over 1000 ppm require additional testing (ref. 40 CFR 279.11) 2Required to be capable of firing on-specification used oil during startup and shutdown. Firing of 2 ppm or greater PCB containing used oil is prohibited. Used oil shall not be blended to meet this requirement. [Rules 62-4.070(3) and 62-210.300(3)(c)1.b.,c. F.A.C.; Construction permit application received 7/8/99] * Copies of the analysis shall be maintained at the facility for a minimum of 5 years and made available to the Air Compliance Section of the Southwest District of the Department and/or the Pinellas County Department of Environmental Management, Air Quality Division upon request. [Rules 62-4.070(3) and 62-710.210, F.A.C.; Construction Permit 1030026-004-AC] Comments: The On Spec Used Oil number 5 combusted met the requirements of permit condition 13B. (see copy of COA attached). Fuel Sulfur Content Record. In order to document continuing compliance with the sulfur content limitations of 0.5% S, by weight of the fuel oil used in the asphalt concrete plant's dryer and hot oil heater (Specific Condition No. 14), the permittee shall keep records on either vendor provided as-shipped analysis or on analysis of as-received samples taken at the plant. The analysis shall be determined by ASTM methods ASTM D4057-88 and ASTM D129-91, ASTM D2622-94 or ASTM D4294-90, adopted and incorporated by reference in Rule 62-297.440(1), F.A.C. The above records shall be maintained at the facility for a minimum of 5 years and made available to the Air Compliance Section of the Southwest District of the Department and the Pinellas County Department of Environmental Management, Air Quality Division upon request. [Rules 62-4.070(3) and Construction Permit 1030026-004-AC] Comments: The COA were available for inspection. A copy of one is attached. Test Methods and Procedures Emission Unit Nos. 001 & 002 Test Frequency - EU ID No. 001. In order to document compliance with Specific Condition Nos. 11 & 13, the Drum Mix Asphalt Concrete Plant (EU ID No. 001) shall be concurrently tested for visible emissions (VE) and particulate matter. The tests from the baghouse of the asphalt concrete plant dryer shall be performed annually between October 1 and September 30 (once per federal fiscal year) with a target date 60 days prior to or on the date of March 24. The required test report shall be submitted to the Air Compliance Section of the Southwest District of the Department and the Pinellas County Department of Environmental Management, Air Quality Division as soon as practical, but no later than 45 days after each test is completed. The test report submitted shall meet all applicable requirements of Rule 62-297, F.A.C. [Rules 62-210.300(3)(c)1.i, 62-297.310(7)(a), and 62-297.310(8)(b), F.A.C.] Comments: This inspection was performed during annual stack testing for VE and PM. See field sheets attached. Test Requirements – EU ID No. 001. The permittee shall comply with all of the following: Testing of emissions of the asphalt concrete plant dryer’s baghouse to show compliance shall be conducted within 90-100% of the maximum permitted process rate of 250 tons/hour. A compliance test submitted at an operating rate less than 90% of the maximum permitted rate will automatically constitute an amended permit at the lesser rate plus 10% (110% of the lesser test rate) until another test, showing compliance at no less than that higher rate is submitted. Once the unit is so limited, any time the permitted rate (limited by the most recent emissions test) of the source is exceeded, a new compliance test shall be performed within 30 days of initiation of the higher rate and the test results shall be submitted to the Air Compliance Section of the Southwest District of the Department and to the Pinellas County Department of Environmental Management, Air Quality Division within 45 days of testing. Acceptance of the test by the Department will automatically constitute an amended permit at the higher rate plus 10%, up to the maximum permitted rate of 250 tons/hour for that emission unit. The actual rate (in tons/hour) of the emission unit for the test period shall be included in the test report for each test. Failure to submit the actual rate for the test period and a copy of the daily log (see Specific Condition No. 29) for the test day in the test report may invalidate the test and fail to provide reasonable assurance of compliance. A compliance test submitted when the dryer is fired with natural gas will automatically constitute an amended permit to allow the dryer to be only fired with natural gas and up to 400 hours of firing fuel oil. Within 30 days of exceeding the 400th hour of firing the dryer with fuel oil, new compliance tests shall be conducted with the dryer being fired with fuel oil. A compliance test submitted when the dryer is fired with a new No. 2 fuel oil will automatically constitute an amended permit to allow the dryer to be only fired with new No. 2 fuel oil and/or natural gas and up to 400 hours of firing on-specification reclaimed No. 5 fuel oil. Within 30 days of exceeding the 400th hour of firing the dryer with on-specification reclaimed/used No. 5 fuel oil, new compliance tests shall be conducted with the dryer being fired with on-specification reclaimed/used No. 5 fuel oil. A compliance test submitted when the dryer is fired with on-specification reclaimed/used No. 5 fuel oil will automatically constitute an amended permit to allow the dryer to be only fired with on-specification reclaimed/used No. 5 fuel oil, new No. 2 virgin diesel fuel oil, or natural gas. Since the Department has determined processing only conventional materials has the greatest potential to generate emissions vs. RAP, a compliance test submitted when processing RAP shall limit the plant to processing only RAP. If the plant is so limited, within 30 days upon processing virgin materials (conventional hot mix asphalt), new compliance tests (particulate & visible emissions) for the asphalt concrete plant dryer’s baghouse shall be conducted using only virgin materials. A compliance test submitted when processing only virgin materials shall also allow the plant to process RAP. [Rules 62-4.070(3) and 62-297.310(2), F.A.C.] Comments: The facility is using only number 5 Used On Spec oil. Test Report- EU ID No. 001. The following shall be submitted with any compliance test report for EU ID No. 001: Production rate of hot mix asphalt concrete in tons/hr. Be sure to include a statement indicating whether virgin materials or RAP was used. Type of fuel used. Fuel oil analysis of the sulfur content of the fuel oil used. Used fuel oil analysis to document compliance with the on-specification used oil limits, if on-specification used oil was used to fire the dryer. A copy of the records for the month the test was conducted as required by Specific Condition No. 29. Failure to submit the items mentioned above with any compliance test report for the test period may invalidate the test(s). [Rules 62-4.070(3) and 62-297.310(8), F.A.C.] Comments: I read the permit conditions to Mrs. Wanda Pettis. Test Method-Particulate Matter. Compliance with the particulate matter limitation(s) specified in Specific Condition No. 11 shall be determined using EPA Methods 1,2,3,4, and 5 or 5A contained in 40 CFR 60, Appendix A and adopted by reference in Chapter 62-297, F.A.C. The minimum requirements for stack sampling facilities, source sampling and reporting, shall be in accordance with Chapter 62-297, F.A.C. and 40 CFR 60, Appendix A. [Rules 62-210.300(3)(c)1.i., 62-297.401(5), F.A.C. and 40 CFR 60.93(b)(1)] Stack Sampling. The permittee shall install and maintain stack sampling facilities (as required), including ports, work platforms, access to work platforms, electrical power, and sampling equipment support. All stack sampling facilities must meet requirements of Rule 62-297, F.A.C. and any Occupational Safety and Health Administration (OSHA) Safety and Health Standards described in 29 CFR Part 1910, Subparts D and E. [Rule 62-297.310(6), F.A.C.] Comments: The testing facilities meet the requirements of 62-210.300(3)(c)1.i. Test Method-Visible Emissions for EU ID Nos. 001 & 002. Compliance with the visible emission (VE) limitation(s) specified in Specific Condition No. 13 shall be determined using EPA Method 9 contained in 40 CFR 60, Appendix A and adopted by reference in Chapter 62-297, F.A.C. The minimum requirements for stack sampling facilities, source sampling and reporting, shall be in accordance with Chapter 62-297, F.A.C. and 40 CFR 60, Appendix A. [Rules 62-297.401(9)(c) and 62-297.310(4)(a)2., F.A.C.] Comments: The VE test was performed using EPA Method 9. General Requirements for Testing Methods and Procedures Test Notification. The owner or operator shall notify the Pinellas County Department of Environmental Management, Air Quality Division at least 15 days prior to the date on which each formal compliance test is to begin of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted for the owner. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: The facility notified that AQD of testing with 3 weeks advance notice. Required Equipment. The owner or operator of an emission unit for which compliance tests are required shall install, operate, and maintain equipment or instruments necessary to determine process variables, such as process weight input or heat input, when such data are needed in conjunction with emission data to determine the compliance of emissions units with applicable emission limiting standards. Equipment or instruments used to directly or indirectly determine process variables, including devices such as belt scales, weigh hoppers, flow meters, and tank scales, shall be calibrated and adjusted to indicate the true value of the parameter being measured with sufficient accuracy to allow the applicable process variable to be determined within 10% of its true value. [Rule 62-297.310(5), F.A.C.] Comments: The facility has installed, maintains and calibrates the equipment that determines process variables (such as belt scales, weigh hoppers, flow meters, and tank scales). Monitoring and Recordkeeping Requirements Recordkeeping for Emission Units 001 and 002. In order to demonstrate compliance with Specific Condition Nos. 12 and 14 for the asphalt concrete plant and the hot oil heater, the permittee shall comply with the following recordkeeping requirements: A. Daily Records – Daily record the following: Total conventional asphalt concrete production (tons); Total asphalt concrete containing RAP production (tons); Both types (1 and 2 above) of asphalt concrete combined (tons); Hours of operation while producing conventional asphalt concrete; Hours of operation while producing asphalt concrete which contains RAP; Total hours of production of both types (4 and 5 above) of asphalt concrete; A calculation of the daily average (tons/hour) production rate of conventional asphalt concrete based on 1 and 4 above; and A calculation of the daily average (tons/hour) RAP production rate based on 2 and 5 above. Monthly Records - Monthly record the following: Total tons of both types of asphalt concrete produced for the month (tons), and a calculation of the most recent consecutive 12-month rolling total dryer operating hours (hours/consecutive 12-month period); Total operating hours of the asphalt concrete plant’s dryer for the month (hours), and a calculation of the most recent consecutive 12-month rolling total asphalt production (tons/ consecutive 12-month period); The quantity of each of the 3 types of fuel used to fire the asphalt concrete plant’s dryer (EU ID No. 001) along with the overall monthly average MMBtu/hour heat input rate; The quantity and type of fuel used to fire the hot oil heater (EU ID No. 002); The total usage of all fuel oil used to fire the asphalt concrete plant’s dryer and hot oil heater; and The most recent consecutive 12-month rolling total usage rate of all fuel oil used to fire the asphalt concrete plant’s dryer and hot oil heater. Additional Fuel Oil Usage Recordkeeping If the last compliance test was conducted while the dryer was fired with new No. 2 virgin diesel fuel oil, the permittee shall keep a daily record of dryer operating hours while firing on-specification reclaimed/used No. 5 fuel oil, along with the cumulative total of on-specification reclaimed/used No. 5 fuel oil operating hours since the last dryer compliance test. {Permitting Note: When on-specification reclaimed/used No. 5 fuel oil dryer operating hours since the last compliance test exceed 400 hours, then additional compliance testing is required (see Specific Condition No. 17).} If the last compliance test was conducted while the dryer was fired with natural gas, the permittee shall keep a daily record of dryer operating hours while firing new No. 2 fuel oil and on-specification reclaimed/used No. 5 fuel oil, along with the cumulative total of new No. 2 fuel oil and on-specification reclaimed/used No. 5 fuel oil operating hours since the last dryer compliance test. {Permitting Note: When new No. 2 virgin diesel fuel oil and/or on-specification reclaimed/used No. 5 fuel oil dryer operating hours since the last compliance test exceed 400 hours, then additional compliance testing is required (see Specific Condition No. 17).} All records shall include the Facility Name, Facility ID, Date, Time, and Operator Initials for each measurement. [Rule 62-4.070(3), F.A.C. and Construction Permit 1030026-004-AC] Comments: The facility was keeping records that complied with items A, B and C above. Baghouse Maintenance and Operations Records. The Caterpillar, Autopulse II, Model APL-720 baghouse system for EU ID No. 001 shall be operated and maintained in accordance with the Operation & Maintenance (O&M) Plan that was submitted as part of the permit renewal application received on 8/27/90, or a revised plan approved by the Pinellas County Air Quality Division. The O&M documentation logs shall be maintained for a minimum of the most recent two years and be made available for inspection upon request. The Operation & Maintenance Plan shall include, but not be limited to the following: Operating parameters of the pollution control device; Time table for the routine maintenance of the pollution control device as specified by the manufacturer; Time table for routine periodic observations of the pollution control device sufficient to ensure proper operation; A list of the type and quantity of the required spare parts for the pollution control device which are stored on the premises of the permit applicant; A record log which will indicate, at a minimum: When maintenance and observations were performed; What maintenance and observations were performed; Who performed said maintenance and observations; and Acceptable parameter ranges for each operational check. [Pinellas County Code, Section 58-128] Comments: The O and M logs were available and demonstrated compliance with items A thru E. Recordkeeping-Reasonable Precautions. In order to demonstrate compliance with Specific Condition No. 5, the permittee shall record the Facility Name, Facility ID, Location, Date, Time, and Operator initials when water application or sweeping is used to control unconfined emissions of particulate matter from the facility. [Rule 62-4.070(3), F.A.C.] Comments: Ms. Wanda Pettis showed me workers time sheets that demonstrated compliance with this permit condition. (The sweeping of the yards or the watering of the yards with the Water Trucks is specified on the time cards.) Record Retention. All daily records shall be completed within three (3) business days and all monthly records shall be completed by the end of the following month. All recordkeeping information, supporting documentation, monitoring data, and all compliance test information required by this permit shall be maintained on-site or electronically for at least five (5) years and be made available to the Department and Pinellas County Department of Environmental Management, Air Quality Division for inspection upon request. [Rules 62-4.070(3) and 62-210.300(3)(c)1.g., F.A.C.] Comments: The daily records were available and finished by the following day and the monthly records were available and ready one week after the end of the month. Excess Emissions. Excess Emissions which are caused entirely or in part by poor maintenance, poor operation, or any other equipment or process failure which may reasonably be prevented during startup, shutdown, or malfunction shall be prohibited. [Rule 62-210.700(4), F.A.C.] Excess Emissions-Reporting. In the case of excess emissions resulting from malfunctions, each owner or operator shall notify the Department in accordance with Rule 62-4.130, F.A.C. A full written report on the malfunctions shall be submitted in a quarterly report, if requested by the Department. [Rule 62-210.700(6), F.A.C.] Comments: There were no reports of excess emissions. Startup/Shutdown/Malfunction. The permittee shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of an affected facility; or any malfunction of the air pollution control equipment. The records shall be recorded in a permanent form suitable for inspection and shall be retained for at least 5 years. [Rule 62-204.800(8), F.A.C. and 40 CFR 60.7(b)] Comments: The facility was maintaining records of startups and shutdowns. There were no malfunctions at the facility in the past 12 months. Annual Operating Report (AOR) Annual Operating Report. The permittee shall submit each calendar year on or before March 1, a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Pinellas County Department of Environmental Management, Air Quality Division. [Rules 62-210.370(3)(a)4 and 62-210.300(3)(c)1.h., F.A.C.] Comments: The 2006 EAOR for Purcell Asphalt Paving was uploaded on 2/5/07. Operation Permit Renewal Permit Renewal. A completed application to renew this operating permit shall be submitted to the Air Permitting Section of the Southwest District office and a copy to the Pinellas County Department of Environmental Management, Air Quality Division no later than 60 days prior to the expiration date of this permit….: Comments: The permit expires on 08/17/2010. An application is required to be submitted no later than 6/18/10. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating ( Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: ( P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / ( No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: I informed Mr. Phillips that Purcell was in compliance pending submittal ,of the stack test results. |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: 3/7/07 |
| ACCESS? | ( | EASIIR? |  |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030026 001 57350.doc