| 1030026 70738 |  |
| --- | --- |
| FACILITY: R.E. Purcell Construction Company, Inc. | PERMIT ID: 1686 |
| Plant No. 2 | DISTRICT: Southwest |
| ADDRESS: 1550 Starkey Road | CONTACT PHONE: |
| Largo, FL | 727-584-3329 |
| ARMS NO: 1030026 003 | PERMIT NO: | Expiration Date: 8/17/2010 Renewal Date: 6/18/2010 |
|  | 1030026-008-AO |  |
|  |  | Test Due Date: 3/24/2000 |
| EMISSION UNIT DESCRIPTION : Reclaimed Asphalt Crusher/Grinder: 90 ton/hour Gentec/Gator, Model gag-100 Crusher/Grinder with associated screening unit, and conveyers |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | May 20, 2010 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: The review consisted of review for the test performance audit and permit file |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: I met on site with Southern Environmental Dale Wingler, Kyle Holmes, plant manager. The facility contact Larry Bane was not in today |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Larry L. Bane.? |  | Yes |  | No |
|  | Comments: Mr. Bane is the R.O The Responsible Official/Authorized Representative’s e-mail is: LarryB@repurcell.com |
| 4. | Is the facility contact still: Larry L. Bane.? |  | Yes |  | No |
|  | Comments: : Mr. Bane is the facility contact The facility contact’s e-mail is: LarryB@repurcell.com |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: The facility ( did □ did not have a copy of the permit on-site. Mr. Bane maintains copy of permit in his office. Emission and Operating Limitations 3. Objectionable Odor. The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants from this plant which cause or contribute to an objectionable odor. Objectionable odor is defined as “Any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance.” [Rules 62-296.320(2), 62-210.200, Definitions-(Objectionable Odor), F.A.C. and Pinellas County Code, Section 58-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- None; Wind direction - westerly Upwind odor level detected-None General Visible Emission (VE) Limit. Visible emissions shall not be equal to or greater than 20% opacity. [Rule 62-296.320(4)(b)(1), F.A.C.] Comments: There were no visible emissions observed coming from the gator crusher pay loader loading, emission points on the conveyor during inspection, and visible emission test performance. Mr. Dale Wingler performed the facilities VE test on the 4 points. I observed the gators operation and performed visible emissions test on 3 points. There tests results for each point was 0% opacity. (See photos) 5. Reasonable Precautions of Unconfined Emissions of Particulate Matter. All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. Reasonable precautions to be taken include the following: Paved parking and trafficked areas shall be maintained and kept free of particulate matter build-up. Sprinkling with water shall be used as necessary on paved areas, unpaved areas, stockpiles and during loading/unloading operations. Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent re-entrainment, and from building and work areas to prevent particulate from being airborne. Landscaping or planting of vegetation. All aggregate brought into the facility arrives and is dumped in a damp matter. Posting and enforcing a 5 MPH speed limit in all traffic areas. [Rules 62-4.070(3), 62-210.300(3)(c)1.e., and 62-296.320(4)(c), F.A.C.] Comments: A. The facility maintaining paved areas, The observed sweeping and shoveling up particulate that fell beneath the conveyer lines, screeners and other equipments parts which have particulate accumulation. B. The facility has a water truck which has been increasing watering of site to reduce unconfined emissions. C. The facility keeps paved areas clean to reduce unconfined emissions. D. There is vegetation is allowed to stay on ~30’ height berm along the north property lines, to help assist in dust control. E. Aggregate is delivered wet, but the sand tends to dry out. There were no unconfined emissions observed coming from the stock piles during the inspection. F. The facility is posted for speed restriction, and the traffic on site was moderate, and slow. (See Photos) 6. Fugitive Emissions Opacity Standard. In order to provide reasonable assurance that the precautions and practices taken at the facility are adequate, all sources of unconfined particulate matter not subject to 40 CFR 60, Subpart OOO, (see Emission Unit No. 003’s limitations), shall not exceed 10% opacity. Exceedance of this limit shall not be considered a violation in and of itself, but an indication that additional control precautions and/or practices beyond those outlined in Specific Condition No. 5 may be necessary. [Rule 62-4.070(3), F.A.C.] Comments: There were no visible emissions observed from activities during the processing of the reclaimed asphalt in the gator crushing operations. I observed the payloader picking up materials from stockpile which was moist aggregate, and driving slowly to loading hopper. The operator slowly placed material in loading bin hopper and no opacity 0% was observed. 7. Operating Changes. Any proposed change to this source which will cause the limitations of this permit to be exceeded, such as design-parameters changes or an increase in emissions may be considered a modification and must be reported. The permittee shall notify the Air Permitting Section of this office of any changes and receive written approval from this office of the changes prior to implementing the changes. [Rule 62-4.070(3), F.A.C.] Comments: There were no changes or modifications to the facility operations or equipment observed at the time of this inspection 8. Circumvention. No person shall circumvent any air pollution control device, or allow the emission of air pollutants without the applicable air pollution control device operating properly. [Rule 62-210.650, F.A.C.] Comments: There did not appear to be any circumventing of the pollution control device. The RAP is processed and feeds directing into a loading hopper at the top of the rotary drum dryer. There was no circumvention of the baghouse observed. 9. Special Compliance Test. When the Department, after investigation, has good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it shall require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and to provide a report on the results of said tests to the Department. [Rule 62-297.310(7)(b), F.A.C.] Comments: No additional testing has been requested by the Department, beyond the stack and visible emissions test required at this facility to this date. 10. NSPS Applicability. B. The reclaimed asphalt crusher/grinder (RAP crushing unit -EU ID No. 003) is subject to the requirements of 40 CFR 60, Subpart OOO - Standards of Performance for Nonmetallic Mineral Processing Plants and the general provisions of 40 CFR 60, Subpart A, where applicable, which are adopted by reference in Rule 62-204.800(8), F.A.C. Comments: This is not applicable at this time to the stack test audit. 11. Particulate Matter Emission Limitations. Particulate matter (PM) emissions from the Drum Mix Asphalt Concrete Plant (EU ID No. 001) shall not exceed 0.04 grains per dry standard cubic foot averaged over a three-hour period. [40 CFR 60 Subpart I, 60.92(a)(1), Rule 62-210.300(3)(c)1.d., F.A.C. and adopted by reference in Rule 62-204.800(8), F.A.C.] Comments: During the Stack test a Method 5, Particulate Matter sampling was performed to determine the grains per DSCF. This information is not available at the time of the inspection will be submitted after the test. 12. Operational Limits. This facility is limited to the following hours of operation and throughput: E.U. ID No. Brief Description Maximum Hours of Operation per consecutive 12-month period Daily Average Maximum Throughput (conventional /RAP asphalt concrete production in tons/hour) Maximum Throughput (conventional/RAP asphalt concrete production in tons/consecutive 12 month period) 003 Reclaimed Asphalt Crusher/ Grinder 4,000 90 360,000 [Rules 62-4.070(3) and 62-210.200, F.A.C., Definitions-(PTE); and Construction Permit 1030026-004-AC] Comments: The total hours of RAP operations in the consecutive 12 month period was 682.75 hours. This is well below the 4000 hour permit limitation. The RAP crusher operated at a daily average of 31.9 tons in May. The daily average of RAP tons/ hour was below 50 tons on the records reviewed. This is below the maximum daily average of 90 tons/hour. The RAP production total for the consecutive 12 month total was 26,514.66 tons. These totals are within the permit emissions limitations listed in the table above. 13. Visible Emissions. Visible Emissions (VE) from the facility shall be limited to: E.U. ID No. Brief Description VE Limit (% Opacity) 003 Any transfer point on the conveyor belts 10** 003 Screen’s oversize conveyor belt to grinder 15** 003 Grinder to grinder’s exit conveyor belt 15** 003 Truck dumping of nonmetallic minerals into any screening operation 20 003 Truck dumping of nonmetallic minerals into any feed hopper 20 003 Truck dumping of nonmetallic minerals into any crusher 20 [62-204.800(8), 62-296.320(4)(b)(1) and 62-297.310(7)(b), F.A.C.; and Construction Permit 1030026-004-AC] Comments: The consultant from Southern Environmental Sciences Dale Wingler was already on site and performing the Method 9 for the testing requirement. I also performed Method 9 Visible Emissions tests on the Emission unit 003 and observed 3 of the emission unit points. Truck dumping into crusher, Screen to Grinder and Grinder to grinder exit conveyor belt. The results of the test of the points was each a 0% opacity during a 30 minute observation. The unit crushed 65 tons per hour during the plant operations. Emission Unit No. 003 22. Test Frequency - EU ID No. 003. In order to document compliance with Specific Condition No. 13, the Reclaimed Asphalt Crusher/Grinder (EU ID No. 003) shall be tested for visible emissions annually between October 1 and September 30 (once per federal fiscal year) with a target date 60 days prior to or on the date of March 24. The emissions test reports shall be submitted to the Air Compliance Section of the Southwest District of the Department and the Pinellas County Department of Environmental Management, Air Quality Division as soon as practical, but no later than 45 days after each test is completed. {Permitting Note: The testing period for the RAP crushing unit does not have to be conducted simultaneously with the testing period for EU ID No. 001. [40 CFR 60.8; Rules 62-297.310(7)(a) and 62-297.310(8)(b), F.A.C.] Comments: The emission unit test was performed within the required fiscal year period for 2010 and prior to the September 30 2010 deadline. 23. Test Requirements – EU ID No. 003. Testing of each affected source shall be conducted within 90-100% of the maximum permitted process rate of 90 tons/hr. A compliance test submitted at an operating rate less than 90% of the maximum permitted rate will automatically constitute an amended permit at the lesser rate plus 10% (110% of the lesser test rate) until another test, showing compliance at no less than that higher rate is submitted. Once the unit is so limited, any time the permitted rate (limited by the most recent emissions test) of the source is exceeded, a new compliance test shall be performed within 30 days of initiation of the higher rate and the test results shall be submitted to the Air Compliance Section of the Southwest District of the Department and to the Pinellas County Department of Environmental Management, Air Quality Division within 45 days of testing. Acceptance of the test by the Department will automatically constitute an amended permit at the higher rate plus 10%, up to the maximum permitted rate of 90 tons/hour for that emission unit. The actual rate (in tons/hour) of the emission unit for the test period shall be included in the test report for each test. Failure to submit the actual rate for the test period and a copy of the daily log (see Specific Condition No. 31) for the test day in the test report may invalidate the test and fail to provide reasonable assurance of compliance. [Rules 62-297.310(2) and 62-297.310(8), F.A.C.] Comments: The facility plant operator Kyle Homes, stated the facility had processed 65 tons of reclaimed asphalt produced this would amend the permit to approximately 71.5 tons /hour. The facility rate would be amended to 72 tons/hour for future operation until retesting performed. 24. Test Report- EU ID No. 003. The following shall be submitted with any compliance test report for EU ID No. 003: The material processing rate, in tons/hr. A copy of the daily & monthly records required by Specific Condition No. 31 for the month the test was conducted. Failure to submit the items mentioned above with any compliance test report for the test period may invalidate the test. [Rules 62-4-070(3) and 62-297.310(8), F.A.C.] Comments: The Southern Environmental Services will submit the test within 45 days for review and approval. 25. Test Method-Visible Emissions – EU ID No. 003. Visible emissions testing for the process emission sources identified in Specific Condition No. 13 shall be conducted using the procedures of 40 CFR 60.11 and EPA Method 9, with the following additions: The minimum distance between the observer and the emission source shall be 15 feet. The observer shall, when possible, select a position that minimizes interference from other fugitive emission sources (e.g., road dust). The required observer position relative to the sun (Method 9, Section 2.1) must be followed. For affected facilities using wet dust suppression for particulate matter control, a visible mist is sometimes generated by the spray. The water mist must not be confused with particulate matter emissions and is not to be considered a visible emission. When a water mist of this nature is present, the observation of emissions is to be made at a point in the plume where the mist is no longer visible. The visible emission compliance tests shall be at least 30 minutes in duration. The permittee may use the following as alternatives to the reference methods and procedures specified in this section: 1. If emissions from two or more sources continuously interfere so that the opacity of fugitive emissions from an individual affected source cannot be read, either of the following procedures may be used: Use for the combined emission stream the highest fugitive opacity standard applicable to any of the individual affected sources contributing to the emissions stream. Separate the emissions so that the opacity missions from each affected source can be read. [40 CFR 60.675 and Rule 62-297.310(4), F.A.C.] Comments: The consultant performed test according to the above testing specifications. General Requirements for Testing Methods and Procedures 26. Test Notification. The owner or operator shall notify the Pinellas County Department of Environmental Management, Air Quality Division at least 15 days prior to the date on which each formal compliance test is to begin of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted for the owner. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: Test Notification was received on 4/1/2010 for the April 5, 2010 and changed test to May 17, 2010, , the test was postponed due to not enough asphalt production, and third cancellation on May 17, 2010 was due to rain and was changed to 5/19/2010. These notifications were received more then 15 days prior to testing, and accepted due to weather cancellation and were acceptable. 27. Stack Sampling. The permittee shall install and maintain stack sampling facilities (as required), including ports, work platforms, access to work platforms, electrical power, and sampling equipment support. All stack sampling facilities must meet requirements of Rule 62-297, F.A.C. and any Occupational Safety and Health Administration (OSHA) Safety and Health Standards described in 29 CFR Part 1910, Subparts D and E. [Rule 62-297.310(6), F.A.C.] Comments: The Stack Sampling facilities were adequate for sampling and observing test procedures during the test. 28. Required Equipment. The owner or operator of an emission unit for which compliance tests are required shall install, operate, and maintain equipment or instruments necessary to determine process variables, such as process weight input or heat input, when such data are needed in conjunction with emission data to determine the compliance of emissions units with applicable emission limiting standards. Equipment or instruments used to directly or indirectly determine process variables, including devices such as belt scales, weigh hoppers, flow meters, and tank scales, shall be calibrated and adjusted to indicate the true value of the parameter being measured with sufficient accuracy to allow the applicable process variable to be determined within 10% of its true value. [Rule 62-297.310(5), F.A.C.] Comments: The facility maintains the equipment required to monitor the process weight, heat input, stack temperature and etc. In the control room, the gauges and temperature charts were observed to be functioning. Some of the asphalt production process parameters are monitored on a computer. Monitoring and Recordkeeping Requirements 31. Recordkeeping for Emission Unit 003. In order to demonstrate compliance with Specific Condition No.12 for the Reclaimed Asphalt Crusher/Grinder, the permittee shall comply with the following record keeping requirements: Daily Process Records – Daily record the following: Hours of operation of the RAP crushing unit (hours); Quantity of material processed (tons); and A calculation of the daily average (tons/hour) processing rate based on 1 and 2 above. Monthly Process Records – Monthly record the following: The total amount of material processed for the month (tons); The most recent consecutive 12-month rolling total of material processed (tons/consecutive 12-months); The month’s total hours of operation of the RAP crushing unit; and The most recent consecutive 12-month rolling total operating hours of the RAP crushing unit. [Rule 62-4.070(3), F.A.C. and Construction Permit 1030026-004-AC] Comments: The facility maintains these on the record sheets headed Tower Mix readings A. (See attached. The records meet the above criteria for daily and monthly requirements. (See copies) 32. Recordkeeping-Reasonable Precautions. In order to demonstrate compliance with Specific Condition No. 5, the permittee shall record the Facility Name, Facility ID, Location, Date, Time, and Operator initials when water application or sweeping is used to control unconfined emissions of particulate matter from the facility. [Rule 62-4.070(3), F.A.C.] Comments: The Plant Water/Sweeper log is maintained by the water truck operator. The log shows the date start/stop truck used and gallons with the driver’s initials. (See Log) 33. Record Retention. All daily records shall be completed within three (3) business days and all monthly records shall be completed by the end of the following month. All recordkeeping information, supporting documentation, monitoring data, and all compliance test information required by this permit shall be maintained on-site or electronically for at least five (5) years and be made available to the Department and Pinellas County Department of Environmental Management, Air Quality Division for inspection upon request. [Rules 62-4.070(3) and 62-210.300(3)(c)1.g., F.A.C.] Comments: The facility is maintaining the records on site. 34. Excess Emissions. Excess Emissions which are caused entirely or in part by poor maintenance, poor operation, or any other equipment or process failure which may reasonably be prevented during startup, shutdown, or malfunction shall be prohibited. [Rule 62-210.700(4), F.A.C.] Comments: There were no excess emissions generated on this emission unit during start up, shutdown and no malfunctions reported. 35. Excess Emissions-Reporting. In the case of excess emissions resulting from malfunctions, each owner or operator shall notify the Department in accordance with Rule 62-4.130, F.A.C. A full written report on the malfunctions shall be submitted in a quarterly report, if requested by the Department. [Rule 62-210.700(6), F.A.C.] Comments: There were no excess emissions generated on this emission unit during start up, shutdown and no malfunctions reported. 36. Startup/Shutdown/Malfunction. The permittee shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of an affected facility; or any malfunction of the air pollution control equipment. The records shall be recorded in a permanent form suitable for inspection and shall be retained for at least 5 years. [Rule 62-204.800(8), F.A.C. and 40 CFR 60.7(b)] Comments: There were no excess emissions generated on this emission unit during start up, shutdown and no malfunctions reported. Prohibited Operations 37. Asbestos Containing Materials. This facility shall not process Asbestos Containing Materials (ACM), whether regulated asbestos containing material (RACM), category I or category II, and whether friable or non-friable when received at the facility. "Asbestos" means the asbestiform varieties of serpentinite (chrysotile), riebeckite (crocidolite), cummingtonite-grunerite, anthophyllite, and actinolite-tremolite and includes trade acronyms products such as amosite. "Asbestos-containing materials", ACM, means any materials which contain more than one percent asbestos as determined by Polarized Light Microscopy. Based on a representative composite sample. "Asbestos removal project" means renovation or demolition operation in a facility that involves the removal of a threshold amount of regulated asbestos-containing material. "Category I Nonfriable Asbestos-Containing Material (ACM)" means asbestos-containing packings, gaskets, resilient floor covering, and asphalt roofing products containing more than 1 percent asbestos as determined using the method specified in Appendix A, Subpart F, 40 CFR Part 763, Section 1, Polarized Light Microscopy. "Category II Non-friable ACM" means any material, excluding Category I Nonfriable ACM, containing more than 1 percent asbestos as determined using the methods specified in Appendix A, Subpart F, 40 CFR Part 763, Section 1, Polarized Light Microscopy, that, when dry, cannot be crumbled, pulverized, or reduced to powder by hand pressure. [40 CFR 61, Subpart M; Chapter 62-257, F.A.C.; and, Rules 62-730.300 and 62-701.520, F.A.C.] Comments: The facility does not accept any construction type materials. They are only bringing in reclaimed asphalt from road bases to be processed in the Gator crusher. Annual Operating Report (AOR) 38. Annual Operating Report. The permittee shall submit each calendar year on or before March 1, a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Pinellas County Department of Environmental Management, Air Quality Division. [Rules 62-210.370(3)(a)4 and 62-210.300(3)(c)1.h., F.A.C.] Comments: The facility submitted the AOR for 2009 on 1/29/2010. The AOR was reviewed and completed on 4/21/2010. Operation Permit Renewal 39. Permit Renewal. A completed application to renew this operating permit shall be submitted to the Air Permitting Section of the Southwest District office and a copy to the Pinellas County Department of Environmental Management, Air Quality Division no later than 60 days prior to the expiration date of this permit….: Comments: The permit expires on 08/17/2010. An application is required to be submitted no later than 6/18/10. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: There have been no changes to the equipment |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: The facility normally uses reclaimed asphalt that is added to the making of new asphalt product. |
| Closing Conference: I spoke to Mr. Bane, informed him the test went well, and the facility appeared to be incompliance at this time pending the results of the stack test. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: May 25, 2010 |
| ACCESS? | ( | ARMS? | ( |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030026 70738.doc

R.E. Purcell Construction Company,Inc. Plant No. 2

1550 Starkey Road, Largo

Project Id:	70738	Permit No: 1030026-008-AO	Arms Number: 0026 003

Inspector:	Shea Jackson		Inspection Date: 5/20/2010

Source (EU):	Reclaimed Asphalt Crusher/Grinder:  90 ton/hour Gentec/Gator, Model gag-100 Crusher/Grinder with associated screening unit, and conveyers

# Description:	[The consultant Dale Wingler of Southern Environmental Sciences was already on site, performing the visible emissions test for the Crusher]

R.E. Purcell Construction Company,Inc. Plant No. 2

1550 Starkey Road, Largo

Project Id:	70738	Permit No: 1030026-008-AO	Arms Number: 0026 003

Inspector:	Shea Jackson	Inspection Date / Time: 5/20/2010  / _______

Source (EU):	Reclaimed Asphalt Crusher/Grinder:  90 ton/hour Gentec/Gator, Model gag-100 Crusher/Grinder with associated screening unit, and conveyers

# Description:	[The first emission point observed and Visible emissions test performed on was the payloader loading the crusher hopper area]

R.E. Purcell Construction Company,Inc. Plant No. 2

1550 Starkey Road, Largo

Project Id:	70738	Permit No: 1030026-008-AO	Arms Number: 0026 003

Inspector:	Shea Jackson			Inspection Date : 5/20/2010

Source (EU):	Reclaimed Asphalt Crusher/Grinder:  90 ton/hour Gentec/Gator, Model gag-100 Crusher/Grinder with associated screening unit, and conveyers

# Description:	[The second emission point that was observed and visible emissions test performed on was the first belt drop loading the grinder hopper]

R.E. Purcell Construction Company,Inc. Plant No. 2

1550 Starkey Road, Largo

Project Id:	70738	Permit No: 1030026-008-AO	Arms Number: 0026 003

Inspector:	Shea Jackson			Inspection Date : 5/20/2010

Source (EU):	Reclaimed Asphalt Crusher/Grinder:  90 ton/hour Gentec/Gator, Model gag-100 Crusher/Grinder with associated screening unit, and conveyers

# Description:	[[The third emission point that was observed and visible emissions test performed on was the grinder drop into a screener before the second belt drop]

# ]

R.E. Purcell Construction Company,Inc. Plant No. 2

1550 Starkey Road, Largo

Project Id:	70738	Permit No: 1030026-008-AO	Arms Number: 0026 003

Inspector:	Shea Jackson			Inspection Date: 5/20/2010

Source (EU):	Reclaimed Asphalt Crusher/Grinder:  90 ton/hour Gentec/Gator, Model gag-100 Crusher/Grinder with associated screening unit, and conveyers

# Description:	[The fourth emission point that the consultant performed a visible emissions test on was where the conveyor belt drops RAP into the hopper above the rotary drum.  There were no emissions observed from this point]