| 1030044 80786 |  |
| --- | --- |
| FACILITY: Suncoast Paving, Inc. | PERMIT ID: 188 |
| Tarpon Springs Facility | DISTRICT: Southwest |
| ADDRESS: 800 Anclote Road | CONTACT PHONE: |
| Tarpon Springs, FL | 727-938-2411 |
| ARMS NO: 1030044 001 | PERMIT NO: | Expiration Date: 2/21/2016 Renewal Date: 12/23/2015 |
|  | 1030044-009-AO |  |
|  |  | Test Due Date: 9/30/2000 |
| EMISSION UNIT DESCRIPTION : 100 Ton per Hour Littleford, Model 123-80 Hot-Mix Batch Asphalt Concrete Plant, Controlled by a 10' diameter dry cyclone separator followed by a venturi wet scrubber system. Current permit allows replacement of wet scrubber with AeroPulse baghouse |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | May 31, 2012 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: I reviewed file prior to inspection. |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: I met with the asphalt plant operators Jon Sprate, and Randy Tate. |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: William Camm II? |  | Yes |  | No |
|  | Comments: yes, I spoke to Mr. Camm during the inspection of the facility. The Responsible Official/Authorized Representative’s e-mail is: Bill@suncoastpaving.com |
| 4. | Is the facility contact still: William Camm II? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: Bill@suncoastpaving.com |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Permitting note: This permit is a renewal and became effective on 02/21/11 General Conditions [62-4.160, F.A.C.] 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. Permit was posted on the office wall inside bulletin board for employee reference. 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: a. A description of and cause of noncompliance; and b. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: The facility was inspected and no non compliance issues were determined, and none were required for reporting at this time. Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] Comments: There was no evidence of circumvention of the air pollution control equipment the baghouse was functions with the operations of the asphalt plant. 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] Comments: There was no processing of VOC or organic solvents for the operations of the asphalt plant at this time. No observations of spills, leaks or improper handling or release of any VOC or OS materials. This type of operation doesn’t typically use any VOC or OS materials, this conditions doesn’t really apply to this type of operation. 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An “objectionable odor” means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C.] Comments: An upwind/downwind survey of the facility was conducted. There were no odors detected during observation of facility. The wind direction – Southwesterly. 9. Unconfined Particulate Emissions: a. No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. b. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. c. Reasonable precautions include the following: (1) Paving and maintenance of roads, parking areas and yards. (2) Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. (3) Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. (4) Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. (5) Landscaping or planting of vegetation. (6) Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. (7) Confining abrasive blasting where possible. (8) Enclosure or covering of conveyor systems. Comments: There was little activity on site at this time. There was no vehicular traffic or loading of any type. The yard is wetted with water truck and swept weekly. The records for yard watering and sweeping were up to date (See attached Yard maintenance record) 1 The facility parking and yard areas are paved. 2. The facility has a water truck to reduce unconfined emissions, it was not operating at time, and there was no vehicular traffic. The watering/sweeper most recent record shows “watered and swept yard on 5/23/12.” 3. The facility maintains the yard to reduce emissions. The facility is posted for speed restriction, and there was no traffic on site at this time. (See Photos) 4. The facility keeps areas clean to reduce unconfined emissions. 5. There is no vegetation to help assist in dust control on this property . 5 Aggregate is delivered wet, There were no unconfined emissions observed coming from the stock piles during the inspection. 6. There is no use of hoods or filters to control particulate. 7. There is no sand blasting or abrasive unconfined particulate activities. 8. The aggregate loading bins are not covered, material is wet from the sprinklers, conveyors are covered to reduce emissions. Administrative Requirements 7 Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 2011 was submitted late on 4/13/12. The facility received and advisory letter and given 15 days to submit. No further enforcement action was taken according to the SES Bill Froberg. 8 Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to PCDEM (Compliance Authority) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on 2/21/2016. An application is required to be submitted no later than 12/23/2015. 1. Facility-Wide Fuel Usage - Facility-wide fuel oil consumption, including exempt sources, shall not exceed 1.2 million gallons in any consecutive 12-month period. [Rules 62-210.200 (“Potential to Emit”) and 62-210.300(3)(c)2.b., F.A.C.; Construction Permit 1030044-007-AC] Comments: Review of the facility record show the fuel usage for the 12 month period to be 24,841 gallons or 0.248 million gallons. This is well below the permit limitation, and the 12 month consecutive totals are continuing decrease due to the economy. This does not exceed the fuel limitations standard of this rule. 2. Facility-Wide Fuel Usage Records - In order to demonstrate compliance with Specific Condition No. 1. the permittee shall monthly record the type of fuel oil (i.e., No. 5 virgin blend fuel oil or on-specification No. 5 reclaimed fuel oil) and quantity, in gallons, of each type of fuel oil used at the facility. The permittee shall monthly calculate and record the most recent consecutive 12-month period total amount of fuel oil in gallons for each fuel oil type and the combined total quantity of both types of fuel oil used. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030044-007-AC] Comments: The records reviewed for the fuel #5 on-specification No. 5 reclaimed fuel oil usages showed the highest 12 month consecutive totals to be 36798.3 gallons in August 2011 and 29090.7 gallons in March of 2012. The highest monthly usage was 6281 gal for August and 2007.9 gallons for March 2012. The facility only uses the reclaimed #5 fuel on site for operations. 3. Fuel Oil Sulfur Content Limitation - The sulfur content for all fuel oils shall not exceed 1.0% by weight. [Rule 62-4.070(3) F.A.C.; Construction Permit 1030044-007-AC] Comments: I obtained a copy of the fuel analysis for the recent shipments of fuel the sulfur content was 0.2026 % by weight. The Summit Environmental Technologies, analytical laboratories certificates show the analysis was performed using method ASTM Method D4294-02. 4. Fuel Sulfur Content Record - In order to document continuing compliance with the sulfur content limitation in Specific Condition No. 3., in % by weight of the fuel oil, the permittee shall keep records on either vendor provided as-shipped analysis or on analysis of as-received samples taken at the plant. The analysis shall be determined by appropriate ASTM methods. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030044-007-AC] Comments: The ASTM method used for the sulfur content was ASTM D-4294-02 which is the appropriate lab analysis method for the determination of fuel percent by weight. The Vendor provided as shipped analysis are maintained in office file, with the purchase invoices. 5. Reclaimed Fuel Oil Specifications – The permittee shall not burn off-specification reclaimed fuel oil. For each delivery of on-specification No. 5 reclaimed fuel oil, the vendor shall provide an analysis documenting the fuel oil meets the following requirements of 40 CFR 761.20(e)(2) and (3) and 40 CFR 279.11 (July 1, 2004): Constituent/Property Allowable Level Tested Level Arsenic 5 ppm maximum <1.0 ppm Cadmium 2 ppm maximum 0.1 ppm Chromium 10 ppm maximum < 4.0 ppm Lead 100 ppm maximum 6.5 ppm Total Halogens 1000 ppm maximum 576 ppm Flash Point 100 degrees F minimum >156 F PCB’s Shall be less than 2 ppm < 1.0 ppm [Rules 62-4.070(3), and 62-710.210, F.A.C.; Construction Permit 1030044-007-AC] Comments: This was acceptable levels (See copy of certificates for shipments received) 6. Asbestos Containing Materials – This facility shall not process Asbestos Containing Materials (ACM), whether regulated asbestos containing material (RACM), category I or category II, and whether friable or non-friable when received at the facility. a. "Asbestos" means the asbestiform varieties of serpentinite (chrysotile), riebeckite (crocidolite), cummingtonite-grunerite, anthophyllite, and actinolite-tremolite and includes trade acronyms products such as amosite. b. "Asbestos-containing materials", ACM, means any materials which contain more than one percent asbestos as determined by Polarized Light Microscopy. Based on a representative composite sample. c. "Asbestos removal project" means renovation or demolition operation in a facility that involves the removal of a threshold amount of regulated asbestos-containing material. d. "Category I Nonfriable Asbestos-Containing Material (ACM)" means asbestos-containing packings, gaskets, resilient floor covering, and asphalt roofing products containing more than 1 percent asbestos as determined using the method specified in Appendix A, Subpart F, 40 CFR Part 763, Section 1, Polarized Light Microscopy. e. "Category II Non-friable ACM" means any material, excluding Category I Nonfriable ACM, containing more than 1 percent asbestos as determined using the methods specified in Appendix A, Subpart F, 40 CFR Part 763, Section 1, Polarized Light Microscopy, that, when dry, cannot be crumbled, pulverized, or reduced to powder by hand pressure. [40 CFR 61, Subpart M; Chapter 62-257, F.A.C.; and Rules 62-730.300 and 62-701.520, F.A.C.] Comments: This plant makes virgin asphalt which utilizes clean aggregates with the liquid asphalt for the production of asphalt. This facility does not process recycled asphalt for the addition of material into the asphalt processing. The facility does not receive RACM and is not equipped to mix into their asphalt production. 7. Objectionable Odor - The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants from this plant which cause or contribute to an objectionable odor. Objectionable odor is defined as “Any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance.” [Rules 62-296.320(2) and 62-210.200, Definitions-(Objectionable Odor), F.A.C., Pinellas County Code, Subsection 58-178] Comments: There were no objectionable odors detected during inspection of this facility on or off the property. 8. Unconfined Emissions of Particulate Matter - See Appendix C., Condition 9. Additional reasonable precautions may include: a. Paved parking and trafficked areas shall be maintained and kept free of particulate matter build-up. b. Sprinkling with water shall be used as necessary on paved areas, unpaved areas, and stockpiles and during loading/unloading operations. c. Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent re-entrainment, and from building and work areas to prevent particulate from being airborne. d. Landscaping or planting of vegetation. e. All aggregate brought into the facility arrives and is dumped in a damp manner. f. Curtailing operations during extremely windy conditions. g. Enclosing or covering conveyor systems or drop points. h. Posting and enforcing a 5 MPH speed limit in all traffic areas. [Rules 62-4.070(3) and 62-296.320(4)(c), F.A.C.; Construction Permit 1030044-003-AC] Comments: The facility follows reasonable precautions to prevent unconfined emissions during operations. There were no activities generating unconfined emissions at this time. 9. Recordkeeping-Reasonable Precautions - In order to demonstrate compliance with Specific Condition No. 8., the permittee shall record the Facility Name, Facility ID, Location, Date, Time, and Operator initials when water application or sweeping is used to control unconfined emissions of particulate matter from the facility. [Rule 62-4.070(3), F.A.C.] Comments: The record keeping log shows the watering and sweeping of the site on a weekly basis to prevent unconfined emissions. (See record log) 10. Fugitive Emissions Opacity Standard - In order to provide reasonable assurance that the precautions and practices taken at the plant are adequate, visible emissions of unconfined particulate matter should not exceed 10% opacity. Exceedance of this limit shall not be considered a violation in and of itself, but an indication that additional control precautions and/or practices beyond those outlined in Specific Condition No. 8. may be necessary. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030044-003-AC] Comments: There were no unconfined emissions, or activities generating emissions to determine opacity at this time. 11. Records Retention – All records shall be maintained at the facility for a minimum of 5 years and made available to the Permitting and Compliance Authorities. [Rules 62-4.070(3) and 62-210.300(3)(c)2.g., F.A.C.] Comments: The facility continues to maintain records for 5 years at the facility on file with Mr. Jon Spraten in personal computer and hard copies in front office. A.2. Permitted Capacity - This emission unit is limited to the following operating parameters: EU ID No. Daily Average Maximum Production Rate of conventional (virgin) asphalt concrete (tons/hour) Maximum Production of conventional (virgin) asphalt concrete (tons/consecutive 12-month period) 001 100.0 500,000 [Rule 62-210.200 (“Potential to Emit”) F.A.C.; Construction Permit 1030044-003-AC] Comments: The tons of asphalt produced on a daily bases has steadily declined for the past 5 years The records showed the daily totals ranging from 88.7 tons/hour for June 2012. The maximum consecutive 12 month total for asphalt production was for the month of August 2011 was 14,006 tons for the 12 month consecutive total. The total forthe month of March 2012 was 10,814 tons for the 12 month consecutive total. These sums do not exceed the permitted capacity limitations above of 100 tons/hour or the 5000,000 tons for a 12 month period. (See copies) A.3. Authorized Fuel - The following fuels are allowed: b. No. 5 virgin blend fuel oil; and d. on-specification No. 5 reclaimed fuel oil. [Rule 62-210.200 (“Potential to Emit”), F.A.C.; Construction Permit 1030044-007-AC] Comments: The facility is currently using on-specification No. 5 reclaimed fuel oil for the burner operation during the processing of virgin asphalt product. This fuel is the most economical product of the two. A.4. Particulate Matter (PM) Emission Limitation – Particulate matter emissions from the asphalt plant’s baghouse shall not exceed 0.06 gr/dscf. [Rule 62-296.704(2), F.A.C.; Construction Permit 1030044-007-AC] Comments: The last annual compliance test, conducted on 8/4/2011 showed emission of 0. 0.00633 gr/dscf gr/dscf @ 8810.33 dscf/min. This 2012 year’s stack test performance is required to be submitted by 9/30/2012. The facility is searching for a job which will be large enough to perform stack test at the process rate for the maximum capacity of 100 tons/hour. (See Test files ) A.5. Visible Emission (VE) Limitation - Visible emissions from the asphalt plant’s baghouse shall not be equal to or greater than 20% opacity. [Rule 62-296.704(2), F.A.C.] Comments: The visible emissions test was not performed by air quality staff at this time as the plant was not in processing asphalt , the operation consisted of asphalt in plant ready for batching, was not able to perform a method 9 test, no emissions observed. The visible emissions test was performed on August 4, 2011 during the stack test. The opacity result was 0% , and reviewed to be acceptable. A.6. Compliance Tests - During each federal fiscal year (October 1st - September 30th), the emissions unit shall be tested to demonstrate compliance with the emissions standards for particulate matter and visible emissions. [Rule 62-297.310(7)(a)4., F.A.C.; Construction Permit 1030044-007-AC] Comments: A visible emissions test was performed on August 4, 2011 during the stack testing for the 2011 federal fiscal year. The opacity result was 0% test was reviewed to be acceptable for 2011. During this inspection I informed Mr. Camm this time for testing is the same as last year. The stack test should be performed before September 30th 2012. . I asked him to let A.Q. division know if unable to test due to low production. A.7. Test Requirements - Tests shall be conducted in accordance with the applicable requirements specified in Appendix D (Common Testing Requirements) of this permit, when on-specification No. 5 reclaimed fuel oil is used in the asphalt concrete production. If No. 5 virgin blend fuel oil is used during a compliance test, the facility is limited to burn No. 5 virgin blend fuel oil only. Once the facility is so limited, operation with on-specification No. 5 reclaimed fuel oil is allowed for no more than 400 hours, until a compliance test with on-specification No. 5 reclaimed fuel oil is successfully completed. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: The facility has not and will not likely change fuel from on-specification No. 5 reclaimed fuel oil to the No. 5 virgin blend fuel oil due to cost of reclaim lower then virgin product. This facility has conducted the previous test and the August 4th 2011 test according to appendix D requirements. The information meth the minimum requirements for identifying the emission unit and the specification for the operations that demonstrated the test was performed as required and the test results are valid. . IE. the facility notified AQ division 15 days prior to testing. The test was performed within 90 – 100% of the maximum process rate of 100 tph. The stack test length was 60 minutes, and was performed annually during the fiscal year. The test was received by AQ division within 45 days of test date on 8/24/2011. The source is in compliance with this condition. A.8. Test Method(s) - Required tests shall be performed in accordance with the following reference method(s). Method(s) Description of Method 1-4 Traverse Points, Velocity and Flow Rate, Gas Analysis, and Moisture Content 5 or 5A Determination of Particulate Matter Emissions from Stationary Sources 9 Visual Determination of the Opacity of Emissions from Stationary Sources The above method(s) are described in Appendix A of 40 CFR 60 and are adopted by reference in Rule 62-204.800, F.A.C. No other method(s) may be used unless prior written approval is received from the Department. [Rules 62-204.800 and 62-297.100, F.A.C.; and Appendix A of 40 CFR 60] Comments: The facility did use the above test methods when determining compliance with the permit for their most recent test performed on August 4, 2011. The test information provided was the approved listed methods and in accordance with Appendix A the documentation was provided in the test report which fulfilled the identifying information and test results to demonstrate compliance and a valid test. A.9. Test Notification - The permittee shall notify the Compliance Authority in writing at least 15 days prior to any required tests. The notification must include the following information: the date, time, and location of each test; the name and telephone number of the facility’s contact person who will be responsible for coordinating the test; and the name, company, and the telephone number of the person conducting the test. Permitting Note: The notification should also include the relevant emission unit ID No(s)., test method(s) to be used, and pollutants to be tested. [Rules 62-4.070(3) and 62-297.310(7)(a)9., F.A.C.] Comments: The facility’s consultant did notify the air quality department 15 days prior to this test. Notification for test performance received 7/29/2011 only 6 days prior to 8/4/2011. The facility was allowed short notice due to difficulty of obtaining the job size needed to meet the maximum capacity for testing. A.10. Test Reports -The permittee shall prepare and submit reports for all required tests in accordance with the requirements specified in Appendix D (Common Testing Requirements) of this permit. The following information for the test period shall be submitted with any compliance test report: a. Production rate of hot-mix asphalt concrete in tons/hr. b. Type and amount of fuel used (on-specification No. 5 reclaimed fuel oil or No. 5 virgin blend fuel oil). c. Fuel oil analysis of the sulfur content of the fuel oil used. d. Reclaimed fuel oil analysis to document compliance with the on-specification No. 5 reclaimed fuel oil limits, if on-specification No. 5 reclaimed fuel oil was used to fire the dryer. e. Average pressure drop across the baghouse during the test runs. f. A copy of the log the day the test was conducted and the monthly log for the month the test was conducted. Failure to submit the items mentioned above with any compliance test report for the test period may invalidate the test(s). [Rules 62-4.070(3) and Rule 62-297.310(8), F.A.C.; Construction Permit 1030044-007-AC] Comments: The facility’s consultant did provide the above information and docuents for (a-f) when the test report and results were submitted to Pinellas County Air Quality for review on 8/24/2011. The test report was reviewed and determine to be in compliance with limitations and acceptable process rate results. A.11. Operation Records - In order to demonstrate compliance with Specific Condition A.1., A.2., and A.3., the following records shall be kept: Daily: a. facility name, facility ID No., emission unit ID No., and description (i.e., Suncoast Paving, Inc., 1030044, EU 001, hot mix asphalt batch plant); b. date; c. pressure drop across the baghouse during normal operation, in inches of water; d. total asphalt concrete production of conventional (virgin) asphalt concrete (tons); e. hours of operation while producing conventional (virgin) asphalt concrete; f. daily average production rate of conventional (virgin) asphalt concrete (tons/hour); Monthly: g. facility name, facility ID No., emission unit ID No., and description (i.e., Suncoast Paving, Inc., 1030044, EU 001, hot mix asphalt batch plant); h. month/year; i. total tons of conventional (virgin) asphalt concrete produced (tons/month); j. most recent 12 consecutive month rolling total of asphalt concrete production (tons/12 consecutive month period); k. total operating hours of the asphalt batch plant’s dryer (hours/month); l. most recent 12 consecutive month rolling total of hours of operation (hours/12 consecutive month period); m. type (No. 5 virgin blend fuel oil or on-specification No. 5 reclaimed fuel oil) and quantity (gallons) of fuel oil used to fire the asphalt concrete plant's dryer; and n. most recent 12 consecutive month rolling total of the quantity of all fuel oils burned in the dryer. Daily records shall be completed within three (3) business days and monthly records shall be completed by the end of the following month. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030044-007-AC] Comments: The records were reviewed and were formatted as required for the specific information needed for subsets a-n. The records were observed for October 2011 through May 2012. The checks had been marked and maintenance and records performed by plant operator Randy Tate. (See copies) A.12. Operation and Maintenance (O & M) Plan for Particulate Matter Control - For air pollution control devices and collection systems, the permittee shall maintain and implement an O & M Plan to include a schedule for the maintenance and inspection of each control device, collection systems, and auxiliary equipment. The performance parameters shall include operating rates and efficiencies. Such parameters and records shall include, at a minimum, the following: a. Performance Parameters: i. Operating parameters of the baghouse; ii. Time table for the routine maintenance of the baghouse as specified by the manufacturer; iii. Time table for routine periodic observations of the baghouse sufficient to ensure proper operation; iv. A list of the type and quantity of the required spare parts for the baghouse which are stored on the premises of the permit applicant. b. Operation and Maintenance Log - A record log which will indicate at a minimum: i. When maintenance and observations were performed. ii. What maintenance and observations were performed. iii. Who performed said maintenance. iv. Acceptable parameter ranges for each operational check. [Rule 62-4.070(3), F.A.C. and Pinellas County Code No. 58-128] Comments: I reviewed the O & M records. Mr. Tate performs maintenance and records the daily, weekly and monthly checks for the baghouse maintenance items and the pressure drops to maintain below 6.0” pressure H20. The highest reading was 4.5” pressure. (See copies) |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: no changes |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: no process changes, no recycled materials |
| Closing Conference: I informed Mr. Camm the facility appeared to be incompliance, but I would have to check on the Independence Excavating rock crushers operation being located on his site, and whether his permit had conditions which allowed for their operation of the crusher on his site. I later found the permit for Independence Excavating crusher is listed under 7775019 Mr. Camm stated the Independence Excavating was operating independently from him and was only using his property to crush materials from a job which they had bid on. Mr. Camm stated he would not be crushing asphalt for his operations. The AQ division checked with FDEP and they determined this was not a violation of the Suncoast Paving’s permit conditions, and no modification of Suncoast Paving’s permit was required because the crushed material will not be used in the manufacturing of asphalt at this plant. The Suncoast Paving facility is in compliance of their permit requirement sat this time. (see Independence Excavating report under H:\users\wpdocs\airqual\Air_Compliance\AQI\7775019 83135.doc |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: June 15, 2012 |
| ACCESS? | ( | ARMS? | ( |

Suncoast Paving, Inc.  Tarpon Springs Facility

800 Anclote Road, Tarpon Springs

Project Id:	80786	Permit No: 1030044-009-AO	Arms Number: 0044 001

Inspector:	Shea Jackson	Inspection Date / Time: 5/31/2012  / _______

Source (EU):	100 Ton per Hour Littleford, Model 123-80 Hot-Mix Batch Asphalt Concrete Plant, Controlled by  a 10' diameter dry cyclone separator followed by a venturi wet scrubber system.  Current permit allows replacement of wet scrubber with AeroPulse baghouse

# Description:	[The baghouse O & M records were being maintained as required]

Suncoast Paving, Inc.  Tarpon Springs Facility

800 Anclote Road, Tarpon Springs

Project Id:	80786	Permit No: 1030044-009-AO	Arms Number: 0044 001

Inspector:	Shea Jackson	Inspection Date / Time: 5/31/2012  / _______

Source (EU):	100 Ton per Hour Littleford, Model 123-80 Hot-Mix Batch Asphalt Concrete Plant, Controlled by  a 10' diameter dry cyclone separator followed by a venturi wet scrubber system.  Current permit allows replacement of wet scrubber with AeroPulse baghouse

# Description:	[The asphalt plant was not in  operation at this time, no asphalt processing, storage silo holding material for batch loading trucks.   There was no vehicular traffic at this time or loadings. ]

Suncoast Paving, Inc.  Tarpon Springs Facility

800 Anclote Road, Tarpon Springs

Project Id:	80786	Permit No: 1030044-009-AO	Arms Number: 0044 001

Inspector:	Shea Jackson	Inspection Date / Time: 5/31/2012  / _______

Source (EU):	100 Ton per Hour Littleford, Model 123-80 Hot-Mix Batch Asphalt Concrete Plant, Controlled by  a 10' diameter dry cyclone separator followed by a venturi wet scrubber system.  Current permit allows replacement of wet scrubber with AeroPulse baghouse

# Description:	[Independence Excavating rock crusher on site.  There was no crushing at this time ]

Suncoast Paving, Inc.  Tarpon Springs Facility

800 Anclote Road, Tarpon Springs

Project Id:	80786	Permit No: 1030044-009-AO	Arms Number: 0044 001

Inspector:	Shea Jackson	Inspection Date / Time: 5/31/2012  / _______

Source (EU):	100 Ton per Hour Littleford, Model 123-80 Hot-Mix Batch Asphalt Concrete Plant, Controlled by  a 10' diameter dry cyclone separator followed by a venturi wet scrubber system.  Current permit allows replacement of wet scrubber with AeroPulse baghouse

Description:	[Independence Excavating rock crusher on site.  There was no crushing at this time ]

Suncoast Paving, Inc.  Tarpon Springs Facility

800 Anclote Road, Tarpon Springs

Project Id:	80786	Permit No: 1030044-009-AO	Arms Number: 0044 001

Inspector:	Shea Jackson	Inspection Date / Time: 5/31/2012  / _______

Source (EU):	100 Ton per Hour Littleford, Model 123-80 Hot-Mix Batch Asphalt Concrete Plant, Controlled by  a 10' diameter dry cyclone separator followed by a venturi wet scrubber system.  Current permit allows replacement of wet scrubber with AeroPulse baghouse

# Description:	[The baghouse O & M records were being maintained as required]