| 1030044 74694 |  |
| --- | --- |
| FACILITY: Suncoast Paving, Inc. | PERMIT ID: 188 |
| Tarpon Springs Facility | DISTRICT: Southwest |
| ADDRESS: 800 Anclote Road | CONTACT PHONE: |
| Tarpon Springs, FL | 727-938-2411 |
| ARMS NO: 1030044 001 | PERMIT NO: | Expiration Date: 11/18/2010 Renewal Date: 9/19/2010 |
|  | 1030044-006-AO |  |
|  |  | Test Due Date: 6/15/2000 |
| EMISSION UNIT DESCRIPTION : 100 Ton per Hour Littleford, Model 123-80 Hot-Mix Batch Asphalt Concrete Plant, Controlled by a 10' diameter dry cyclone separator followed by a venturi wet scrubber system. Current permit allows replacement of wet scrubber with baghouse |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | August 17, 2010 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: Permit review prior to inspection |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: I met on site with Mr. Bill Camm |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: William Camm II? |  | Yes |  | No |
|  | Comments: Yes, The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: William Camm II? |  | Yes |  | No |
|  | Comments: Yes The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: The facility did did not have a copy of the permit on-site. Mr. Camm maintains a copy of the permit on the bulletin board in front office. Emission and Operating Limitations Operational Limits. This facility is limited to the following hours of operation and maximum process rates: Maximum Hours of Operation per consecutive 12-month period Daily Average Maximum Throughput (virgin / conventional asphalt concrete production in tons/hour) Maximum Throughput (virgin / conventional asphalt concrete production in tons/consecutive 12 month period) 3,120 100.0 500,000 [Rule 62-210.300(3)(c)1., F.A.C. and Construction Permit No. 1030044-003-AC] Comments: The Maximum Hours of Operation per consecutive 12-month period highest reported month for operating hours was 323.9 hours for the month of August 2009. This does not exceed 3120 hour limitation. The Daily Average Maximum Throughput (virgin / conventional asphalt concrete production in tons/hour) highest reported production day was __88.7_ tons/hour of virgin/conventional asphalt concrete production, on a daily average basis on June 22, 2010, and does not exceed 100 ton and _66,277_ tons of asphalt concrete production in any consecutive 12 month period for the month of July 2009, does not exceed 500,000 ton limitation.. Reviewed records for the months of July 2009 – July 2010. The above permit limitations have not been exceeded. The source is in compliance at this time. (See Records) Particulate Matter Emission Limitations. Particulate matter (PM) emissions from the Hot-Mix Asphalt Batch Plant (EU ID No. 001) shall not exceed 0.06 grains per dry standard cubic foot. [Rule 62-296.704(2), F.A.C. and Construction Permit No. 1030044-003-AC] Comments: The last annual compliance test, conducted on June 4, 2009 showed emission of 0.0273 grains/dscf. The Results for this year pending submittal and review. This year’s test is required to be submitted by _9/19/2010__. Fuel Usage and Specifications. The facility is limited to the following fuel usage: Type of Fuel. The facility is limited to using the following fuel(s): Maximum Heat Input Rate on Monthly Average Basis (MMBtu/hr) Maximum Fuel Consumption Rate (gallons/hour) Fuel Type Maximum Weight Percent Sulfur (%) 49.3 400.0* “On-Specification” Reclaimed No. 5 fuel oil 1.0 New No. 5 Virgin Blend fuel oil * The plant is limited to using a maximum of 400 gallons of fuel oil per hour. The total fuel consumption by the dryer burner shall not exceed 1.2 million gallons/year B. Used Oil Specifications. The permittee shall not burn “off-specification” used oil. For each delivery of “on-specification” reclaimed/used fuel oil, the vendor shall provide an analysis* documenting the fuel oil meets the following requirements of 40 CFR 761.20(e)(2) and (3) [July 1, 2004] and 40 CFR 279.11 [July 1, 2004]: Constituent/Property Allowable Level Arsenic 5 ppm maximum Cadmium 2 ppm maximum Chromium 10 ppm maximum Lead 100 ppm maximum Total Halogens 1000 ppm1 maximum Flash Point 100 degrees F minimum PCB’s Shall be less than 2 ppm2 1Levels over 1000 ppm require additional testing (ref. 40 CFR 279.11) 2Required to be capable of firing on-specification used oil during startup and shutdown. Firing of 2 ppm or greater PCB containing used oil is prohibited. Used oil shall not be blended to meet this requirement. * Copies of the analysis shall be maintained at the facility for a minimum of 5 years and made available to the Air Compliance Section of the Southwest District of the Department and/or the Pinellas County Department of Environmental Management, Air Quality Division upon request. [Rules 62-4.070(3) and 62-210.300(3)(c)1., F.A.C.; Construction Permit 1030044-003-AC] Comments: A. The highest fuel usage was 12,296.7 Burner fuel gallons for month of December 2009. The total burner fuel consumption for the 12 month period was 44,231 gallons, which is below the 1.2 million gallon limitation. The highest fuel/hour average was during June 22th 2010 at 239 gals/hour, at 35 MMBtu /hour. This is below the maximum fuel consumption rate limitation of 400 gal/ hour and 49.3 MMBtu/hour. B. The fuel oil analysis report showed the content for 7/20/2010 from Summit Environmental Technologies Lab as follows: (B) Arsenic = < 1.0 pm , Cadmium = 0.22 ppm, Chromium = < 4.0, Lead = 9.7 ppm, Total Halogens = 232 ppm , Viscosity = 291 SUS , PCB’s = <1.0ppm and Sulfur content of 0.2030. The oil was within the tables” Specifications and allowable levels as permitted. (See fuel analysis certificate attached) Fuel Sulfur Content Recordkeeping. In order to document continuing compliance with the sulfur content limitations of 1.0% S, by weight of the fuel oil used in the asphalt concrete plant's dryer, the permittee shall keep records on either vendor provided as-shipped analysis or on analysis of as-received samples taken at the plant. The analysis shall be determined by ASTM methods ASTM D4057-88 and ASTM D129-91, ASTM D2622-94 or ASTM D4294-90, adopted and incorporated by reference in Rule 62-297.440(1), F.A.C. The above records shall be maintained at the facility for a minimum of 5 years and made available to the Air Compliance Section of the Southwest District of the Department and the Pinellas County Department of Environmental Management, Air Quality Division upon request. [Rules 62-4.070(3) and 62-210.300(3)(c)1., F.A.C.; Construction Permit 1030044-003-AC] Comments: The sulfur analysis report showed the sulfur content to be 0.2030%. This is below limitation. Objectionable Odor. The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants from this plant which cause or contribute to an objectionable odor. Objectionable odor is defined as “Any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance.” [Rules 62-296.320(2) and 62-210.200, Definitions-(Objectionable Odor), F.A.C., Pinellas County Code, Subsection 58-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- No Odors; Wind direction - Southeasterly Upwind odor level detected-No odors detected during inspection General Visible Emission (VE) Limit. Visible emissions from the asphalt concrete plant shall not be equal to or greater than 20% opacity. [Rules 62-296.704(2) and 62-210.300(3)(c)1., F.A.C.; Construction Permit No. 1030044-003-AC] Comments: The last annual visible emissions test, conducted on _6/4/2009__ demonstrated an opacity of _2__%. An AQD VE test was performed during this site visit Yes No. There was no opacity observed, because the plant was not in operation. Reasonable Precautions of Unconfined Emissions of Particulate Matter. All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320, F.A.C. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. At a minimum, the following precautions shall be taken by the permittee: Paved parking and trafficked areas shall be maintained and kept free of particulate matter build-up. Sprinkling with water shall be used as necessary on paved areas, unpaved areas, and stockpiles and during loading/unloading operations. Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent re-entrainment, and from building and work areas to prevent particulate from being airborne. Landscaping or planting of vegetation. All aggregate brought into the facility arrives and is dumped in a damp manner. Curtailing operations during extremely windy conditions. Enclosing or covering conveyor systems or drop points. Posting and enforcing a 5 MPH speed limit in all traffic areas. [Rules 62-296.320(4)(c) and 62-210.300(3)(c)1.e., F.A.C.] Comments: There were no unconfined emissions observed there was no vehicular movement, plant was not in operation. The sweeper log showed the facility sweeps weekly to remove track out. Fugitive Emissions Opacity Standard. In order to provide reasonable assurance that the precautions and practices taken at the facility are adequate, all sources of unconfined particulate matter shall not exceed 10% opacity. Exceedance of this limit shall not be considered a violation in and of itself, but an indication that additional control precautions and/or practices beyond those outlined in Specific Condition No. 9 may be necessary. [Rule 62-4.070(3), F.A.C.] Comments: There was no opacity observed during the plant inspection. The facility is operating at very low production at this time. Operating Changes. Any proposed change to this source which will cause the limitations of this permit to be exceeded, such as design-parameters changes or an increase in emissions may be considered a modification and must be reported. The permittee shall notify the Air Permitting Section of this office of any changes and receive written approval from this office of the changes prior to implementing the changes. [Rule 62-4.070(3), F.A.C.] Comments: The facility has located the baghouse adjacent to the plant, but has not connected it to operations for processing. The scrubber is still the control unit for the plant at this time. Circumvention. The permittee shall not allow any person to circumvent any air pollution control device, or allow the emission of air pollutants without the applicable air pollution control device operating properly. [Rule 62-210.650, F.A.C.] Comments: The facility continues to use the scrubber for the air pollution control device. Mr. Camm stated they are trying to obtain a contract which would be sufficient for testing the baghouse and performing the stack test for permit application. He stated the plant has to run at 70% in order to function correctly. The stack temperature can not be controlled at 50% of the operating capacity of the plant. Excess Emissions. Excess Emissions which are caused entirely or in part by poor maintenance, poor operation, or any other equipment or process failure which may reasonably be prevented during startup, shutdown, or malfunction shall be prohibited. [Rule 62-210.700(4), F.A.C.] Comments: There have been no excess emissions or upset conditions. The maintenance records show equipment is being monitored daily. Monitoring and Recordkeeping Requirements Recordkeeping. In order to demonstrate compliance with Specific Condition No. 3 for the hot-mix asphalt batch plant, the permittee shall comply with the following recordkeeping requirements: Daily records – Daily record the following: The pressure drop across the baghouse during normal operation, in inches of water. Total asphalt concrete production, in tons, of virgin/conventional asphalt concrete. Hours of producing virgin/conventional asphalt concrete. Daily average production rate of asphalt concrete produced, in tons/hr. of virgin/conventional asphalt concrete Monthly Records – Monthly record the following: Total tons of virgin/conventional asphalt concrete produced, and calculate and record the most recent combined consecutive 12 month rolling total, in tons. Total operating hours of the asphalt batch plant’s dryer along with a consecutive 12 month rolling total, in hours. The quantity of each of the 2 types of fuel used to fire the asphalt concrete plant's dryer along with the overall monthly average MMBTU/hr. heat input rate. {Permitting Note: Daily records shall be completed within 3 business days and monthly records shall be completed by the end of the following month. These records shall be maintained at the facility for at least 5 years and made available to the Air Compliance Section of the Southwest District of the Department and the Pinellas County Department of Environmental Management, Air Quality Division upon request} [Rules 62-4.070(3) and 62-210.300(3)(c)1., F.A.C.; Construction Permit No. 1030044-003-AC] Comments: Reviewed records for the months of _July 2009 – July 2010_. A copy of the records is attached as an example of the record format. The baghouse is not connected, condition A.1. is not applicable at this time. The records for the other conditions met the requirements of A and B, and were up to date. (See attached) Wet Scrubber System O&M Plan. The dry cyclone separator, wet spray chamber, and wet scrubber shall be operated and maintained in accordance with the Operation and Maintenance (O&M) Plan that was submitted as part of the application dated September 18, 1990. The O&M Plan documentation logs shall be maintained at the facility for a minimum of 3 years. The O&M Plan shall include but not be limited to: The operating parameters of the control device. Timetable for the routine maintenance of the pollution control device as specified by the manufacturer. Timetable for routine periodic observations of the pollution control device sufficient to ensure proper operation. A list of the type and quantity of the required spare parts for the pollution control device, which are stored on the premises. A record log which will indicate, at a minimum: 1. When maintenance and observations were performed. 2. What maintenance and observations were performed? 3. Who performed said maintenance? [Rule 62-4.070(3), F.A.C. and Pinellas County Code No. 58-128] Comments: Reviewed records for the months of Jan 1, 2010 – August 12, 2010. A copy of the records is attached as an example of the record format. The record for the plan maintenance includes the check of the scrubber, and nozzles and is signed by the operator. Baghouse System O&M Plan. The permittee [when applying for an operating permit amendment in accordance with Specific Conditions 32 and 33] shall submit a new operation and maintenance plan for the baghouse system. The plan shall include the parameters and information specified by Pinellas County Code 58-128, 62-296.700(6)(a)(2), F.A.C. and 62-296.700(6)(b), F.A.C. where applicable and shall be submitted to the Pinellas County Department of Environmental Management, Air Quality Division for approval regardless of whether the facility is applying for an amended operating permit, early renewal for operating permit, or normal renewal for operating permit. [Rule 62-4.070(3), F.A.C. and Pinellas County Code No. 58-128] Comments: This is not applicable at this time, the baghouse has not been connected to the processes of the asphalt plant. They are proposing to test with baghouse by September 21, 2010. Recordkeeping-Reasonable Precautions. In order to demonstrate compliance with Specific Condition No. 9, the permittee shall record the Facility Name, Facility ID, Location, Date, Time, and Operator initials when water application or sweeping is used to control unconfined emissions of particulate matter from the facility. [Rule 62-4.070(3), F.A.C.] Comments: The sweeping log is maintained showing sweeps made on monthly bases Record Retention. All daily records shall be completed within three (3) business days and all monthly records shall be completed by the end of the following month. All recordkeeping information, supporting documentation, monitoring data, and all compliance test information required by this permit shall be maintained on-site or electronically for at least five (5) years and be made available to the Department and Pinellas County Department of Environmental Management, Air Quality Division for inspection upon request. [Rules 62-4.070(3) and 62-210.300(3)(c)1.g., F.A.C.] Comments: The records were available back to _1996_. Excess Emissions-Reporting. In the case of excess emissions resulting from malfunctions, each owner or operator shall notify the Department in accordance with Rule 62-4.130, F.A.C. A full written report on the malfunctions shall be submitted in a quarterly report, if requested by the Department. [Rule 62-210.700(6), F.A.C.] Comments: There was no upset or excess emissions, or malfunctions during the 2009 – 2010 period. Startup/Shutdown/Malfunction. The permittee shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of an affected facility; or any malfunction of the air pollution control equipment. The records shall be recorded in a permanent form suitable for inspection and shall be retained for at least 5 years. [Rule 62-204.800(8), F.A.C. and 40 CFR 60.7(b)] Comments: The facility did not experience any malfunctions during this reporting period. Test Methods and Procedures Test Frequency. – In order to document compliance with Specific Condition Nos. 4 and 8, the Hot-Mix Asphalt Batch Plant (EU ID No. 001) shall be concurrently tested for visible emissions (VE) and particulate matter. Wet Scrubber system testing. If the wet scrubber system is to remain in service through the period of 60 days prior to June 15, or any date thereafter; test this asphalt plant for particulates and visible emissions annually within 60 days prior to or on the date of June 15. The test reports shall be submitted to the Pinellas County Department of Environmental Management, Air Quality Division and the Air Compliance Section of the Southwest District of the Department within 45 days of testing. Baghouse system testing. The newly installed baghouse system shall have visible emissions and particulate tests conducted within 30 days after initial operation. Subsequent tests shall be conducted annually within 60 days prior to or on the date of the initial test. The test reports shall be submitted to the Pinellas County Department of Environmental Management Air Quality Division and the Air Compliance Section of the Southwest District of the Department within 45 days of testing. The required test report shall be submitted to the Air Compliance Section of the Southwest District of the Department and the Pinellas County Department of Environmental Management, Air Quality Division as soon as practical, but no later than 45 days after each test is completed. The test report submitted shall meet all applicable requirements of Rule 62-297, F.A.C. [Rules 62-4.070(3), 62-297.310(7)(a), and 62-297.310(8)(b), F.A.C.] Comments: The facility was granted a extension until September to obtain a job which would allow them to test at a maximum capacity. Mr. Camm stated there were no jobs in the area of the size needed to operate the plant at 70% capacity, the minimum operational capacity of the plant. Test Method. In order to document compliance with Specific Condition No. 21 for the hot-mix asphalt batch plant, the permittee shall comply with the following test methods: Compliance with the emission limitations of Specific Condition No. 4 shall be determined using EPA Methods 1, 2, 3, 4, and 5 or 5A. Compliance with the visible emissions limitations of Specific Condition No. 8 shall be determined using EPA Method 9. These test methods are contained in 40 CFR 60, Appendix A, and adopted by reference in Chapter 62-297, F.A.C. [Rules 62-210.300(3)(c)1., 62-297.310(4)(a)2., 62-297.401(5) & (9)(c), F.A.C. and 40 CFR 60.93(b)(1)] . Comments: The facility will have their consultant perform these test methods, when they are able to obtain a job which would make it feasible to test. Test Requirements. Testing of emissions of the hot-mix asphalt batch plant to show compliance shall be conducted within 90-100% of the maximum permitted process rate of 100 tons/hour. A compliance test submitted at an operating rate less than 90% of the maximum permitted rate will automatically constitute an amended permit at the lesser rate plus 10% (110% of the lesser test rate) until another test, showing compliance at no less than that higher rate is submitted. Once the unit is so limited, any time the permitted rate (limited by the most recent emissions test) of the source is exceeded, a new compliance test shall be performed within 30 days of initiation of the higher rate and the test results shall be submitted to the Air Compliance Section of the Southwest District of the Department and to the Pinellas County Department of Environmental Management, Air Quality Division within 45 days of testing. Acceptance of the test by the Department will automatically constitute an amended permit at the higher rate plus 10%, up to the maximum permitted rate of 100 tons/hour for that emission unit. The actual rate (in tons/hour) of the emission unit for the test period shall be included in the test report for each test. Failure to submit the actual rate for the test period and a copy of the daily log (see Specific Condition No. 14) for the test day in the test report may invalidate the test and fail to provide reasonable assurance of compliance. [Rules 62-4.070(3) and 62-297.310(2), F.A.C.] Comments: The facility is attempting to find a job which would allow them to test within the 90 – 100 % of the maximum permitted rate. Stack Sampling. The permittee shall install and maintain stack sampling facilities (as required), including ports, work platforms, access to work platforms, electrical power, and sampling equipment support. All stack sampling facilities must meet requirements of Rule 62-297, F.A.C. and any Occupational Safety and Health Administration (OSHA) Safety and Health Standards described in 29 CFR Part 1910, Subparts D and E. [Rule 62-297.310(6), F.A.C.] Comments: The facility will insure the conditions for allowing the inspector to access, observation areas and perform audit adequately safely. Required Equipment. The owner or operator of an emission unit for which compliance tests are required shall install, operate, and maintain equipment or instruments necessary to determine process variables, such as process weight input or heat input, when such data are needed in conjunction with emission data to determine the compliance of emissions units with applicable emission limiting standards. Equipment or instruments used to directly or indirectly determine process variables, including devices such as belt scales, weigh hoppers, flow meters, and tank scales, shall be calibrated and adjusted to indicate the true value of the parameter being measured with sufficient accuracy to allow the applicable process variable to be determined within 10% of its true value. [Rule 62-297.310(5), F.A.C.] Comments: The facility regularly calibrates its equipment as required. Special Compliance Test. When the Department or Pinellas County, after investigation, has good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it shall require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and to provide a report on the results of said tests to the Department. [Rule 62-297.310(7)(b), F.A.C.] Comments: This is not applicable at this time, no special test have been required. Notifications Test Notification. The owner or operator shall notify the Pinellas County Department of Environmental Management, Air Quality Division at least 15 days prior to the date on which each formal compliance test is to begin of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted for the owner. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: The County has not been notified for the test as the facility was granted an extension. I informed Mr. Camm to be sure to contact us as soon as possible for testing. He stated he was trying to get a job large enough,, as soon as they had a job large enough he would be able to perform stack test. New Equipment Notification. The permittee shall provide written notification to the Pinellas County Department of Environmental Management, Air Quality Division of the date the wet scrubber system is permanently removed from service in preparation for replacement with the baghouse system, postmarked no later than 5 days after such date. [Rules 62-4.070(3) and 62-297.310(7)(a)9., F.A.C.; 40 CFR 60.8(d)] Comments: I informed Mr. Camm of this condition. He stated he was aware he needed to notify us of the change. Prohibited Operations Asbestos Containing Materials. This facility shall not process Asbestos Containing Materials (ACM), whether regulated asbestos containing material (RACM), category I or category II, and whether friable or non-friable when received at the facility. "Asbestos" means the asbestiform varieties of serpentinite (chrysotile), riebeckite (crocidolite), cummingtonite-grunerite, anthophyllite, and actinolite-tremolite and includes trade acronyms products such as amosite. "Asbestos-containing materials", ACM, means any materials which contain more than one percent asbestos as determined by Polarized Light Microscopy. Based on a representative composite sample. "Asbestos removal project" means renovation or demolition operation in a facility that involves the removal of a threshold amount of regulated asbestos-containing material. "Category I Nonfriable Asbestos-Containing Material (ACM)" means asbestos-containing packings, gaskets, resilient floor covering, and asphalt roofing products containing more than 1 percent asbestos as determined using the method specified in Appendix A, Subpart F, 40 CFR Part 763, Section 1, Polarized Light Microscopy. "Category II Non-friable ACM" means any material, excluding Category I Nonfriable ACM, containing more than 1 percent asbestos as determined using the methods specified in Appendix A, Subpart F, 40 CFR Part 763, Section 1, Polarized Light Microscopy, that, when dry, cannot be crumbled, pulverized, or reduced to powder by hand pressure. [40 CFR 61, Subpart M; Chapter 62-257, F.A.C.; and, Rules 62-730.300 and 62-701.520, F.A.C.] Comments: There were no asbestos containing materials observed at this facility. They do not use recycled materials back into the asphalt mix process. The facility uses virgin materials only at this time.. Annual Operating Report (AOR) Annual Operating Report. The permittee shall submit each calendar year on or before March 1, a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Pinellas County Department of Environmental Management, Air Quality Division. [Rules 62-210.370(3)(a) and 62-210.300(3)(c)1., F.A.C.] Comments: The annual operating report for calendar year 2009 was submitted on _3/2/2010 and review was completed by 4/28/2010. Operation Permit Operating Permit Amendment. In conjunction with the O&M plan specified in Specific Condition No. 16 and the test report specified in Specific Condition 21(B), the applicant must apply for an operating permit amendment to fully incorporate the changes resulting from replacement of the wet scrubber system with the baghouse system. [Rule 62-4.070(3), F.A.C.] Comments: Mr. Camm is aware of this condition and has been trying to work toward the removal of the scrubber and the installation of the baghouse. Permit Renewal. In the event the baghouse system is not installed, this operating permit shall be renewed in accordance with normal timelines. A completed application to renew this operating permit shall be submitted to the Air Permitting Section of the Southwest District office and a copy to the Pinellas County Department of Environmental Management, Air Quality Division no later than 60 days prior to the expiration date of this permit… [Rules 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The facilities permit expires 11/18/2010, and renewal is due by 9/19/2010. I informed Mr. Camm he was very close to this date. I inquired if he was going to be able to make it before the due dates, and incurring a violation. He stated he was not sure he was trying to comply, but is dependent of contracting a job which would be large enough to perform test. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: There have been no changes to the emission unit at this time. |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: They do not recycle materials at this plant. |
| Closing Conference: I informed Mr. Camm they needed to test as soon as possible. The facility is in compliance at this time, pending stack testing and permit renewal. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: August 23, 2010 |
| ACCESS? | ( | ARMS? | ( |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030044 74694.doc