1030118 006 72260

| FACILITY: Schneller, LLC | PERMIT ID: 976 |
| --- | --- |
|  | DISTRICT: Southwest |
| ADDRESS: 6200 49th St. No. | CONTACT PHONE: |
| Pinellas Park, FL | 727-521-2393 |
| ARMS NO: 1030118 006 | PERMIT NO: | Expiration Date: 2/12/12 Renewal Date: 7/2/11 |
|  | 1030118-011-AV |  |
|  |  | Test Due Date: NA |
| EMISSION UNIT DESCRIPTION : MEK Parts Cleaning Operations: MEK and a kerosene parts washer parts cleaning stations are located at the screen printing area, color mixing area. The tanks are approximated 8 gal. in capacity with self closing lids |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | 11 November 2009 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Mark Stewart? |  | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Will Jones? |  | Yes |  | No |
|  | Comments: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
|  |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [APPENDIX TV-6, TITLE V CONDITION 12(12)] Comments: Mr. Jones showed me an electronic copy of the permit. Annual Operating Report for Air Pollutant Emitting Facility. (a) The Annual Operating Report for Air Pollutant Emitting Facility (DEP Form No. 62-210.900(5)) shall be completed each year. (b) The annual operating report shall be submitted to the appropriate Department of Environmental Protection (DEP) division, district or DEP-approved local air pollution control program office by March 1 of the following year. (c) Beginning with 2007 annual emissions, emissions shall be computed in accordance with the provisions of Rule 62-210.370(2), F.A.C., for purposes of the annual operating report. [APPENDIX TV-6, TITLE V CONDITION 24(3)] Comments: The facility submitted the 2008 EAOR in March 2009, therefore in compliance with this permit condition. Renewals. Prior to one hundred eighty (180) days before the expiration of a permit issued pursuant to Chapter 62-213, F.A.C., the permittee shall apply for a renewal of a permit using forms incorporated by reference in the specific rule chapter for that kind of permit. [APPENDIX TV-6, TITLE V CONDITION 5] Comments: The permit application is due to be submitted on, or before xxxx. 2. General Pollutant Emission Limiting Standards: Objectionable Odor Prohibited - No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200, and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: I reminded Mr. Jones that the permit renewal application is due to be submitted on, or before July 2nd, 2011. 3. General Particulate Emission Limiting Standards: General Visible Emissions Standard - Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1 & 62-296.320(4)(b)4, F.A.C.] Comments: This facility is not a source of particulate emissions. The property around the building is paved or has slab concrete. There were no fugitive dust emissions that I could see anywhere. I did not perform a Method 9, VE test, but, as I observed the stack tests being performed, there were never any visible emissions emanating from the incinerator stack.. 4. Prevention of Accidental Releases (Section 112(r) of CAA)- a. The permittee shall submit its Risk Management Plan (RMP) to the Chemical Emergency Preparedness and Prevention Office (CEPPO) RMP Reporting Center when, and if, such requirement becomes applicable. b. The permittee shall submit to the permitting authority Title V certification forms or a compliance schedule in accordance with Rule 62-213.440(2), F.A.C. [40 CFR 68] Comments: I examined a copy, of the facility’s Tier II Report (Plan) to the State Emergency Response Commission (SERC). The report lists the chemicals, MSDS’, quantities, location on the premises, and the names, phone numbers of the agencies and individuals to be contacted in the case of an Emergency. The SERC is the Agency in the State of Florida which is charged with the responsibility of implementing the Emergency Planning and Community Right-To-Know Act, EPCRA, Title III, of the CAA and mitigating the effects of a release or spill of hazardous materials. This is the RMP required by Section 112(r) of the CAA. The facility submitted the RMP with its permit renewal. The RMP was sent to the correct State Agency. However, Section 112(r) of the CAA does not apply to this facility since it does not use any of the pollutants listed in 40 CFR 68.130 in relation to any of the regulated Emission Units. 5. Insignificant Emissions Units and/or Activities - Appendix I-1, List of Insignificant Emissions Units and/or Activities, is a part of this permit. [Rules 62-213.440(1), 62-213.430(6), and 62-4.040(1)(b), F.A.C.] 6. Unregulated Emissions Units and/or Activities - Appendix U-1, List of Unregulated Emissions Units and/or Activities, is a part of this permit. [Rule 62-213.440(1), F.A.C.] Comments: The list of Insignificant and Unregulated Emission Units and/or activities remains the same. No emissions units or activities have been added. 7. General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. (a) Ensure all lids, caps, covers on cans and other containers are properly fitted and maintained such that vapor emissions are minimized. (b) Repair all leaks in piping, process equipment, and storage containers immediately and/or removing solvents to secure containers until repairs can be effected. (c) All VOCs from solvent washing (equipment cleanup) shall be directed into containers that prevent evaporation into the atmosphere. (d) For each parts cleaner, comply with each of the following requirements: 1. Equip the cleaner with a cover. The cover shall be so designed that it can be easily operated with one hand. 2. Equip the cleaner with a facility for draining cleaned parts. The drainage facility shall be constructed internally so that parts are enclosed under the cover while draining if the solvent volatility is greater than 0.6 pounds per square inch (31 millimeters of mercury or 4.1 kilopascals) measured at 100 degrees Fahrenheit (38 degrees Celsius), except that the drainage facility may be external for the applications where an internal type cannot fit into the cleaning system. 3. Provided a permanent, conspicuous label summarizing the operating requirements. 4. Store waste solvent only in covered containers. 5. Close the cover whenever parts are not being handled in the cleaner. 6. Drain the cleaned parts for at least 15 seconds or until dripping ceases. 7. If used, supply a solvent spray that is a solid fluid stream (not a fine, atomized, or shower-type spray) at a pressure which does not cause excessive splashing. [Rule 62-296.320(1)(a), F.A.C., previous Title V permit 1030118-010-AV] (Permitting Note: The volatility of MEK is greater than 0.6 pounds per square inch measured at 100 degrees Fahrenheit. The volatility of kerosene is less than 0.6 pounds per square inch measured at 100 degrees Fahrenheit). Comments: There were no leaks or spills. The doors to the permanent Total Enclosure were kept closed at all times. The parts cleaners had self closing covers and they opened with a foot pedal, thus allowing hands –free operation. The parts cleaners had internal mesh platforms which were being used for draining cleaned parts. The operating instructions were in extra large type letters on the top of the covers. Solvent spray was not being used. MEK (no longer a HAP by EPA) was used in the parts cleaner as the solvent. 9. Statement of Compliance – The annual statement of compliance pursuant to Rule 62-213.440(3)(a)2., F.A.C. shall be submitted to this office, the EPA, and the Air Program of the Pinellas County Department of Environmental Management (PCDEM), within 60 days after the end of the calendar year using DEP Form No. 62-213.900(7), F.A.C. [Rules 62-4.070(3), 62-213.440(3), and 62-213.900(7), F.A.C.] Comments: Schneller submitted the 2008 SOC on 2 February 2009. D.1. VOC Emissions Limitations - In order to qualify for an exemption from Rule 62-296.511, F.A.C., Reasonably Available Control Technology (RACT), Solvent Metal Cleaning, VOC emissions from the parts cleaning operations shall not exceed 2.7 tons per any consecutive 12-month period. [Rule 62-296.500(3)(a), F.A.C.] Comments: The running cumulative 12 month total VOC emissions at the end of September 2009 were 1.887 tons. D.2. Monthly Records - Records shall be kept of usage of all VOC containing materials to document compliance with the limitations of condition No. D.1. The records shall include, but not be limited to, the following: (a) facility name, month, and year; (b) quantity of each VOC solvent used for parts cleaning; (c) quantity of VOC solvent removed for disposal; and (d) calculated VOC emissions for the month (lbs) and for the most recent consecutive 12-month period (tons). Records of all calculations used to determine VOC emissions, and supporting documentation (MSD sheets, EPA data sheets, purchase orders, etc.) shall be kept for each solvent which includes sufficient information to determine VOC emissions. Daily records shall be completed within five business days and monthly records shall be completed by the end of the following month. The above records shall be maintained for five years and made available to the Department and the Air Program of the PCDEM upon request. [Rules 62-213.440(1)(b)2.b., 62-4.070(3), F.A.C.; Pinellas Co. Code, Section 58-90] Comments: The facility was keeping records for this EU that were in compliance with permit requirements above. |
|  |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating. Yes No Comments: The Rotogravure Printer is no longer on the premises, but the facility has stated that it wants to keep it in the permit in case it decides to bring it back. |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: Emission Units reductions have come as the result of less business. |
| Closing Conference: I informed Mr. Jones that the facility was in compliance pending submittal of acceptable stack test results. |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: 11 January 2010 |
| ACCESS? |  | EASIIR |  |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030118 006 72260.doc