| 1030118 75612 |
| --- |
| FACILITY: Schneller, LLC | PERMIT ID: 171 |
|  | DISTRICT: Southwest |
| ADDRESS: 6200 49th St. No. | CONTACT PHONE: |
| Pinellas Park, FL | 727-521-2393 |
| ARMS NO: 1030118 003 | PERMIT NO: | Expiration Date: 2/12/12 Renewal Date: 8/16/11 |
|  | 1030118-011-AV |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Coating Line:(Building No. 2) Liberty Machine Co. coating machine with a combination reverse roll and knife-over-roll; 4.5 MMBtu/hour drying oven; with emission controlled by a Grehnrich & Grehnrich, Model HDFT-40H thermal incinerator at 1200° F |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | November 10, 2010 |  |  | INS1 |  | INS2 | ( | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: The facility provided the required minimum 15 day notification prior to the test. The tests performed today will be due 45 days or less from today. That is, on or before 26 December 2010. |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: Mrs. Jennifer West, the new contact at Schneller and Mr. Michael Kubrin, the Facilities Project Engineering Manager, (based in Kent, Ohio) were present during the inspection and stack tests, answered my questions and provided the VOC, CAM, and O & M Logs for the four (4) Emission Units. Testing was performed by Environmental Sciences Group, composed of Cory Houchin and Tim O’Dell. |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Mark Stewart? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Rich Atkins? |  | Yes |  | No |
|  | Comments: The new facility contact is Jennifer West. Rich Akins is no longer employed by Schneller. The facility contact’s e-mail is: |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [APPENDIX TV-6, TITLE V CONDITION 12(12)] Comments: The facility had a copy of the permit on-site. Annual Operating Report for Air Pollutant Emitting Facility. (a) The Annual Operating Report for Air Pollutant Emitting Facility (DEP Form No. 62-210.900(5)) shall be completed each year. (b) The annual operating report shall be submitted to the appropriate Department of Environmental Protection (DEP) division, district or DEP-approved local air pollution control program office by March 1 of the following year. (c) Beginning with 2007 annual emissions, emissions shall be computed in accordance with the provisions of Rule 62-210.370(2), F.A.C., for purposes of the annual operating report. [APPENDIX TV-6, TITLE V CONDITION 24(3)] Comments: The facility submitted the 2009 AOR on 2/8/10. Renewals. Prior to one hundred eighty (180) days before the expiration of a permit issued pursuant to Chapter 62-213, F.A.C., the permittee shall apply for a renewal of a permit using forms incorporated by reference in the specific rule chapter for that kind of permit. [APPENDIX TV-6, TITLE V CONDITION 5] Comments: I pointed out to Mrs. West and Mr. Kubrin that the permit application is due to be submitted on, or before 8/16/11. 2. General Pollutant Emission Limiting Standards: Objectionable Odor Prohibited - No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200, and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: There were no odors inside or outside of the production buildings or on the Schneller property when I arrived. 3. General Particulate Emission Limiting Standards: General Visible Emissions Standard - Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1 & 62-296.320(4)(b)4, F.A.C.] Comments: This facility is not a source of particulate emissions. The property around the building is paved or has slab concrete. There were no fugitive dust emissions that I could see anywhere. 4. Prevention of Accidental Releases (Section 112(r) of CAA)- a. The permittee shall submit its Risk Management Plan (RMP) to the Chemical Emergency Preparedness and Prevention Office (CEPPO) RMP Reporting Center when, and if, such requirement becomes applicable. b. The permittee shall submit to the permitting authority Title V certification forms or a compliance schedule in accordance with Rule 62-213.440(2), F.A.C. [40 CFR 68] Comments: I examined a copy, of the facility’s Tier II Report (Plan) to the State Emergency Response Commission (SERC). The report lists the chemicals, MSDS’, quantities, location on the premises, and the names, phone numbers of the agencies and individuals to be contacted in the case of an Emergency. The SERC is the Agency in the State of Florida which is charged with the responsibility of implementing the Emergency Planning and Community Right-To-Know Act, EPCRA, Title III, of the CAA and mitigating the effects of a release or spill of hazardous materials. This is the RMP required by Section 112(r) of the CAA. The facility submitted the RMP with its permit renewal. The RMP was sent to the correct State Agency. However, Section 112(r) of the CAA does not apply to this facility since it does not use any of the pollutants listed in 40 CFR 68.130 in relation to any of the regulated Emission Units. 5. Insignificant Emissions Units and/or Activities - Appendix I-1, List of Insignificant Emissions Units and/or Activities, is a part of this permit. [Rules 62-213.440(1), 62-213.430(6), and 62-4.040(1)(b), F.A.C.] 6. Unregulated Emissions Units and/or Activities - Appendix U-1, List of Unregulated Emissions Units and/or Activities, is a part of this permit. [Rule 62-213.440(1), F.A.C.] Comments: The list of Insignificant and Unregulated Emission Units and/or activities remains the same. No emissions units or activities have been added. 7. General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. (a) Ensure all lids, caps, covers on cans and other containers are properly fitted and maintained such that vapor emissions are minimized. (b) Repair all leaks in piping, process equipment, and storage containers immediately and/or removing solvents to secure containers until repairs can be effected. (c) All VOCs from solvent washing (equipment cleanup) shall be directed into containers that prevent evaporation into the atmosphere. (d) For each parts cleaner, comply with each of the following requirements: 1. Equip the cleaner with a cover. The cover shall be so designed that it can be easily operated with one hand. 2. Equip the cleaner with a facility for draining cleaned parts. The drainage facility shall be constructed internally so that parts are enclosed under the cover while draining if the solvent volatility is greater than 0.6 pounds per square inch (31 millimeters of mercury or 4.1 kilopascals) measured at 100 degrees Fahrenheit (38 degrees Celsius), except that the drainage facility may be external for the applications where an internal type cannot fit into the cleaning system. 3. Provided a permanent, conspicuous label summarizing the operating requirements. 4. Store waste solvent only in covered containers. 5. Close the cover whenever parts are not being handled in the cleaner. 6. Drain the cleaned parts for at least 15 seconds or until dripping ceases. 7. If used, supply a solvent spray that is a solid fluid stream (not a fine, atomized, or shower-type spray) at a pressure which does not cause excessive splashing. [Rule 62-296.320(1)(a), F.A.C., previous Title V permit 1030118-010-AV] (Permitting Note: The volatility of MEK is greater than 0.6 pounds per square inch measured at 100 degrees Fahrenheit. The volatility of kerosene is less than 0.6 pounds per square inch measured at 100 degrees Fahrenheit). Comments: There were no leaks or spills. The doors to the permanent Total Enclosure were kept closed at all times. The parts cleaners had self closing covers and they opened with a foot pedal, thus allowing hands–free operation. The parts cleaners had internal mesh platforms which were being used for draining cleaned parts. The operating instructions were in extra large type letters on the top of the covers. Solvent spray was not being used. MEK was used in the parts cleaner as the solvent. 9. Statement of Compliance – The annual statement of compliance pursuant to Rule 62-213.440(3)(a)2., F.A.C. shall be submitted to this office, the EPA, and the Air Program of the Pinellas County Department of Environmental Management (PCDEM), within 60 days after the end of the calendar year using DEP Form No. 62-213.900(7), F.A.C. [Rules 62-4.070(3), 62-213.440(3), and 62-213.900(7), F.A.C.] Comments: The 2009 ASOC was received (stamped at AQD) on 2/26/2010. B.1. Permitted Capacity - The maximum VOC input rate to the thermal incinerator shall not exceed 256 lbs./hour (daily average basis). [Rule 62-210.200(PTE), F.A.C.; Permit No. 1030118-012-AC] (Permitting Note: See Specific Condition No. B.7. for possible adjustments to the current permitted VOC loading rate based on the most recent compliance test.) Comments: The highest average VOC input rate occurred in the month of August 2010 and it was recorded as 165.39 lbs per hour. B.2. VOC Emission Limitations –VOC emissions shall not exceed the following: (a) 20.0 tons per any consecutive 12-month period; and (b) 3.8 lbs VOC/gal. of coating, excluding water, delivered to the coating line, if using low solvent compliance coatings; or (c) shall be controlled by a thermal incinerator that provides for the reduction of at least 90 percent* of the VOCs which enter the incinerator such that the reduction would result in total (considering capture and destruction efficiency) VOC emissions equivalent to 7.86 lbs. VOC/gal. of solids, or less. [Rules 62-210.200(PTE), 62-296.504(2) and (3), F.A.C.; 1030118-007-AC] *(Permitting Note: The facility has opted to comply with 40 CFR 63, Subpart JJJJ (see condition below) by maintaining an organic HAP control efficiency of no less than 95%. (See Specific Condition B.3. and Appendix 40 CFR 63, Subpart JJJJ, Section 63.3370) The 95% destruction efficiency is more stringent than Rule 62-296.504(3), F.A.C., therefore compliance with 40 CFR 63, Subpart JJJJ ensures compliance with the 90% VOC RACT requirement.) Comments: The Destruction Efficiency during the test hovered around 98.5 %. The highest 12 month running cumulative total VOC emissions were recorded at the end of the month of October 2010 as 3.259 tons of VOCs. B.3. Federal NESHAPs Requirements - This emissions unit shall comply with the applicable provisions of 40 CFR 63, Subparts A (General Provisions to 40 CFR 63) and JJJJ (Paper and Other Web Coating) as adopted and incorporated by reference in Rule 62-204.800(11)(b), F.A.C., and referenced below*. The complete MACT standard is in the attached Appendix 40 CFR 63, Subpart JJJJ, which is a part of this permit. 40 CFR 63 Subpart JJJJ Applicable Provision References * 63.3280 What is in this subpart? 63.3290 Does this subpart apply to me? 63.3300 Which of my emission sources are affected by this subpart? 63.3310 What definitions are used in this subpart? 63.3320 What emission standards must I meet? 63.3321 What operating limits must I meet? 63.3321 (a) 63.3330 When must I comply? 63.3330 (a) 63.3340 What general requirements must I meet to comply with the standards? 63.3350 If I use a control device to comply with the emission standards what monitoring must I do? 63.3350 (a) 63.3350 (b) 63.3350 (e) 63.3350 (f) 63.3360 What performance tests must I conduct? 63.3360(a) 63.3360(e), except (3)(ii) 63.3360(f) 63.3360(g) 63.3370 How do I demonstrate compliance with the emission standards? 63.3370(a)(4) 63.3370(j), except (4)(ii), (iii), and (iv) 63.3370(k)(1), except (v) and (vi) 63.3370(k)(3)(i) 63.3400 What notifications and reports must I submit? 63.3400(a) 63.3400(b)(1) (Initial notification previously submitted) 63.3400(c), except (2)(vi) 63.3400(d) 63.3400(e) 63.3400(f) 63.3400(g) 63.3410 What records must I keep? 63.3400(a)(1)(ii)(v) 63.3400(a)(2) 63.3420 What authorities may be delegated to the States? Table 1 to Subpart JJJJ of Part 63 - Operating Limits if Using Add-On Control Devices and Capture System Table 1, Items (1) and (3) Appendix A to JJJJ of Part 63 - Applicability of 40 CFR 63 General Provisions to Subpart JJJJ * (Permitting Note: These applicability references are based upon current operations as reflected in the Title V permit renewal application dated 01/06/06, additional information response dated 3/28/06, and air construction permit application dated 7/13/06. Any change in operations may change the applicable provisions.) [Rules 62-204.800(11) and 62-213.400, F.A.C.; 40 CFR 63, Subparts A and JJJJ] Comments: Schneller was in compliance with the record-keeping and reporting requirements of 40 CFR 63 Subpart JJJJ. B.4. Visible Emission (VE) Limitations - No visible emissions (defined as ≤5 percent opacity) are allowed from the incinerator, except that visible emissions not exceeding 20 percent opacity are allowed for up to three minutes in any one hour period. [Rule 62-296.401(1)(a), F.A.C.] Comments: I did not perform a Method 9, VE, but when I arrived the EU was operating and there were no emissions emanating from the stack. B.5. Testing Requirements - In order to demonstrate compliance with condition Nos. B.1. through B.4.: (a) The permittee shall test the incinerator for visible emissions within 8 to 12 months prior to expiration of the permit. (b) The permittee shall test the incinerator for VOC emissions, including the destruction efficiency, within 365 to 425 days after the effective date of this permit, again within 31 to 33 months after the effective date of the permit, and again within 8 to 10 months prior to submittal of the Title V permit renewal application. (c) The permittee shall demonstrate the capture efficiency for the coating line concurrently with the destruction efficiency test by either: 1) show the enclosures continue to meet the requirements given in Procedure T for a Permanent Total Enclosure (EPA Method 204, Criteria for and verification of a Permanent or Temporary Total Enclosure) or 2) conduct a capture efficiency test for a temporary total enclosure pursuant to Rule 62-297.450, F.A.C. [Rules 62-297.310(7), 62-297.450(1)(a), and 62-297.440(7), F.A.C.] B.6. VOC Emissions Testing - VOC emissions testing at the incinerator inlet and outlet shall be conducted using EPA Method 25, or Attachment 3 of EPA 450/2-78-041, or alternate sampling procedures approved in writing by the Department (i.e., ASP No. 96-I-01, attached). When conducting a compliance test, a sample of each coating shall be taken and an EPA Method 24 test performed. The coating sample must be at least 1 liter and be representative of the coating as applied during the test. Data provided from the coating formulator may be submitted in lieu of the Method 24 test if the certification form in EPA 450/3-84-019 is properly completed for each affected coating. [Rules 62-4.070(3), 62-296.500(2)(b), and 62-297.401, F.A.C.] B.8. Visible Emissions Testing - VE testing shall be conducted on the incinerator using DEP Method 9, be a minimum of 60 minutes in duration, and be conducted concurrently with one of the VOC compliance tests. The minimum requirements for stationary point source emission test procedures shall be in accordance with Chapter 62-297, F.A.C. [Rule 62-297.310(4)(a)2, F.A.C.] Comments: This inspection was performed during stack testing, which included Methods 1-4, 9, 24 and 25 A. These tests correspond to the requirement to testing within 8 to 10 months prior to the submittal of the Title V permit renewal application. B.7. Operating Rate During Testing - Compliance testing shall occur, when the incinerator is operating within 90-100% of the maximum VOC loading rate allowed by this permit (256 lbs. VOC input/hour), if feasible. If it is impracticable to test at this rate, an incinerator may be tested at less than 90% of its maximum VOC loading rate. In this case, subsequent operation is limited to 110 percent of the test load until a new test is conducted. Once the unit is so limited, operation at higher capacities is allowed for no more than 15 consecutive days for the purpose of additional compliance testing to regain the authority to operate at a higher rate, not to exceed the maximum rate allowed by this permit (256 lbs. VOC input/hour). Testing at conditions that are not representative of normal operating conditions may invalidate the test. [Rule 62-297.310(2), F.A.C.] Comments: The VOC Process rate during the test will be submitted with the test results. B.9. Compliance Test Notification - The permittee shall notify the Air Program of the PCDEM at least 15 days prior to the date on which each formal compliance test is to begin (except for the capture efficiency test, see specific condition B.10.) of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted for the owner. [Rule 62-297.310(7)(a)9, F.A.C.] Comments: The facility provided the required minimum 15 day notification prior to the test. The tests performed toady will be due 45 days or less from today. That is, on or before 26 December 2010. B.10. Capture Efficiency Test Notification - Should a capture efficiency test using a temporary total enclosure be required, the permittee shall notify the Air Programs of the Department’s Southwest District and the Air Program of the PCDEM 30 days prior to performing any capture efficiency test. [Rule 62-297.450(4)(d), F.A.C.] Comments: A Capture Efficiency Test is not required at this facility. B.11. Modification Notification and Testing - A modification, as defined in Rule 62-210.200, is prohibited without prior approval by the Department, however if any other physical or operational change is made to the control system, the owner or operator shall notify the Air Programs of the Department’s Southwest District and the Air Program of the PCDEM of the change within 10 working days after making such change. The Department shall require the owner or operator of the affected activity, process, or emissions unit to conduct a new capture efficiency test and/or stack test if the Department has reason to believe (based on engineering calculations or empirical evidence) that a physical or operational change to the capture system has decreased the overall emissions reduction efficiency of the system. [Rule 62-297.450(4)(c), F.A.C.] Comments: There were no changes or additions to the equipment, the processes or materials used according to the best of my observations. B.12. Test Report Requirements - The owner or operator of an emissions unit for which a compliance test is required shall file a report with the Air Program of the PCDEM on the results of each such test. The required test report shall be filed with the Air Program of the PCDEM as soon as practical but not later than 45 days after the last sampling run of each test is completed. The test report shall provide, at minimum, the information required in Rule 62-297.310(8), F.A.C. In addition the report shall include the following: (a) overall VOC destruction efficiency and VOC capture efficiency results; (b) utilization rates of the coating(s) during the tests, in gallons per hour; (c) VOC loading rate to the incinerator during the test, in lbs./hour; (d) inlet and outlet VOC concentration of the incinerator and supporting calculations; (e) results of the Method 24 tests, or a certification by the coating manufacturer of the composition of the coating if it is supported by actual batch formulations; (f) incinerator operating parameters such as temperature and flow rates; (g) EPA audit results, if applicable; (h) a copy of the daily log for each test day (see condition B.14.); and (i) a copy of the monthly log for the month the test was conducted (see condition B.14.) Failure to submit the above data or the actual operating conditions may invalidate the test. [Rules 62-4.070(3) & 62-297.310(8), F.A.C.] Comments: The results of the test will be evaluated for content, accuracy, timeliness of submittal and compliance with the emissions limiting standards when they are submitted. Submittal in this case is due on or before 26 December 2010. B.13. Compliance Assurance Monitoring (CAM) - This emissions unit is subject to the CAM requirements contained in the attached Appendix CAM. Failure to adhere to the monitoring requirements specified does not necessarily indicate an exceedance of a specific emissions limitation, however, it may constitute good reason to require compliance testing pursuant to Rule 62-297.310(7)(b), F.A.C. [40 CFR 64; and Rules 62-204.800 and 62-213.440(1)(b)1.a., F.A.C.] Comments: The facility was in compliance with the Compliance Emissions Monitoring (CAM) requirements, for submittal, timeliness of submittal, recordkeeping, and compliance with the minimum temperature and differentia pressure required of EU 003. I examined computer logs which revealed compliance with the minimum points set for the parameters mentioned above. The temperature was recorded as being above 1,400 degrees and the differential pressure was typically around 0.04 “ H2O (the delta P minimum required is 0.008” H2O). Schneller, Inc. APPENDIX CAM Inspection note: this is a modified version of the CAM Plan for inspection purposes. (05/15/06 ver) Compliance Assurance Monitoring Requirements 40 CFR 64.7 Operation of Approved Monitoring: 1. Commencement of Operation - The owner or operator shall conduct the monitoring required under this appendix upon the effective date of this Title V permit. [40 CFR 64.7(a)] Comments: The monitoring required under this subpart commenced on the effective date of the permit. 2. Proper Maintenance - At all times, the owner or operator shall maintain the monitoring, including but not limited to, maintaining necessary parts for routine repairs of the monitoring equipment. [40 CFR 64.7(b)] Comments: The facility maintains spare parts for the routine repairs of the devices. 3. Continued Operation - Except for, as applicable, monitoring malfunctions, associated repairs, and required quality assurance or control activities (including, as applicable, calibration checks and required zero and span adjustments), the owner or operator shall conduct all monitoring in continuous operation (or shall collect data at all required intervals) at all times that the pollutant-specific emissions unit is operating. Data recorded during monitoring malfunctions, associated repairs, and required quality assurance or control activities shall not be used for purposes of this part, including data averages and calculations, or fulfilling a minimum data availability requirement, if applicable. The owner or operator shall use all the data collected during all other periods in assessing the operation of the control device and associated control system. A monitoring malfunction is any sudden, infrequent, not reasonably preventable failure of the monitoring to provide valid data. Monitoring failures that are caused in part by poor maintenance or careless operation are not malfunctions. [40 CFR 64.7(c)] Comments: I examined database records which showed continuous monitoring of the parameters. 4. Response to Excursions or Exceedences: (a) Upon detecting an excursion or exceedance, the owner or operator shall restore operation of the pollutant-specific emissions unit (including the control device and associated capture system) to its normal or usual manner of operation as expeditiously as practicable in accordance with good air pollution control practices for minimizing emissions. The response shall include minimizing the period of any startup, shutdown or malfunction and taking any necessary corrective actions to restore normal operation and prevent the likely recurrence of the cause of an excursion or exceedance (other than those caused by excused startup or shutdown conditions, if allowed by this permit). Such actions may include initial inspection and evaluation, recording that operations returned to normal without operator action (such as through response by a computerized distribution control system), or any necessary follow-up actions to return operation to within the indicator range, designated condition, or below the applicable emission limitation or standard, as applicable. (b) Determination of whether the owner or operator has used acceptable procedures in response to an excursion or exceedance will be based on information available, which may include but is not limited to, monitoring results, review of operation and maintenance procedures and records, and inspection of the control device, associated capture system, and the process. [40 CFR 64.7(d)(1) & (2)] 5. Documentation of need for improved monitoring - If the owner or operator identifies a failure to achieve compliance with an emission limitation or standard for which the approved monitoring did not provide an indication of an excursion or exceedance while providing valid data, or the results of compliance or performance testing document a need to modify the existing indicator ranges or designated conditions, the owner or operator shall promptly notify the permitting authority and, if necessary, submit a proposed modification to the Title V permit to address the necessary monitoring changes. Such a modification may include, but is not limited to, reestablishing indicator ranges or designated conditions, modifying the frequency of conducting monitoring and collecting data, or the monitoring of additional parameters. [40 CFR 64.7(e)] Comments: There were no exceedences recorded or reported of the automated database or the EU itself. 40 CFR 64.8 Quality Improvement Plan (QIP) Requirements. 6. Based on the results of a determination made under CAM Condition Comments: A QIP has not been required of this facility. 7. Elements of a QIP: (a) The owner or operator shall maintain a written QIP, if required, and have it available for inspection. (b) The plan initially shall include procedures for evaluating the control performance problems and, based on the results of the evaluation procedures, the owner or operator shall modify the plan to include procedures for conducting one or more of the following actions, as appropriate: (1) Improved preventive maintenance practices. (2) Process operation changes. (3) Appropriate improvements to control methods. (4) Other steps appropriate to correct control performance. (5) More frequent or improved monitoring (only in conjunction with one or more steps under CAM Condition Comments: A QIP has not been required of this facility. 8. If a QIP is required, the owner or operator shall develop and implement a QIP as expeditiously as practicable and shall notify the permitting authority if the period for completing the improvements contained in the QIP exceeds 180 days from the date on which the need to implement the QIP was determined. [40 CFR 64.8(c)] Comments: A QIP has not been required of this facility. 13. Following implementation of a QIP, upon any subsequent determination pursuant to CAM Condition Comments: A QIP has not been required of this facility. 14. Implementation of a QIP shall not excuse the owner or operator of a source from compliance with any existing emission limitation or standard, or any existing monitoring, testing, reporting or recordkeeping requirement that may apply under federal, state, or local law, or any other applicable requirements under the Act. [40 CFR 64.8(e)] Comments: A QIP has not been required of this facility. 40 CFR 64.9 Reporting And Recordkeeping Requirements. 15. General reporting requirements. (a) Commencing from the effective date of this permit, the owner or operator shall submit monitoring reports semi-annually to the permitting authority in accordance with Rule 62-213.440(1)(b)3.a., F.A.C. (b) A report for monitoring under this part shall include, at a minimum, the information required under Rule 62-213.440(1)(b)3.a., F.A.C., and the following information, as applicable: (1) Summary information on the number, duration and cause (including unknown cause, if applicable) of excursions or exceedences, as applicable, and the corrective actions taken; (2) Summary information on the number, duration and cause (including unknown cause, if applicable) for monitor downtime incidents (other than downtime associated with zero and span or other daily calibration checks, if applicable); and (3) A description of the actions taken to implement a QIP during the reporting period as specified in CAM Conditions 6. through Comments: The facility has submitted the CAM Reports in a timely manner and has indicated no exceedences have been incurred since its inception. 14. Upon completion of a QIP, the owner or operator shall include in the next summary report documentation that the implementation of the plan has been completed and reduced the likelihood of similar levels of excursions or exceedences occurring. [40 CFR 64.9(a)] Comments: The facility has submitted the CAM Reports in a timely manner and has indicated no exceedences have been incurred since its inception. 16. General recordkeeping requirements: (a) The owner or operator shall comply with the recordkeeping requirements specified in Rule 62-213.440(1)(b)2., F.A.C. The owner or operator shall maintain records of monitoring data, monitor performance data, corrective actions taken, any written quality improvement plan required pursuant to CAM Conditions 6. through Comments: Mrs. West provided continuous recorder charts for the temperature and differential pressure that indicated compliance with the parameters at all times. However, after a thorough examination of the data and receiving answers to my questions re: the same, I concluded that the data on the charts was invalid to demonstrate compliance. I reached that conclusion and Mrs. West and Mr. Kubrin were in agreement with my observations, that both the temperature and differential pressure traces across the chart represented 1,400 deg F and 0.045 “H2O even when the entire coating line was not in operation, i.e. when the chart should have reflected no pressure and the temperature should have been recorded as zero or near zero. As a result of this discovery, I inquired if the data was recorded on another media. Mrs. West called the Kent, Ohio office and after speaking with the person in charge of software concerns, she was able to show me the digital data uploaded to a PC for the temperature and differential pressure recorded on a minute by minute frequency. That saved data showed the temperature of the incinerator and the Delta P in compliance when it was operational, and, when it was not operational (near 57deg F) and the differential pressure at 0.0 when the line was not running also. I suggested to Mrs. West that the chart recording needed to be “de-bugged” before it could be used to try to demonstrate compliance. The facility was in compliance with recordkeeping of temperature and differential pressure and in compliance with the minimums for both parameters during the times when it was operating. B.14. VOC Containing Material Usage Records - Records shall be kept of usage of all VOC containing materials to document compliance with the limitations of condition Nos. B.1. and B.2. The records shall include, at a minimum, the following: Daily record the following: (a) facility name, and date; (b) Emission Unit No. and description; (c) applicable rule, i.e., Rule 62-296.504, F.A.C.; (d) substrate type coated; (e) “As Applied” coatings and clean up solvents that were used, and the amount of each used in gallons; (f) VOC content, “As Applied”, of each coating used, in lbs VOC/gal of coating and lbs VOC/gal of solids, the VOC content of each clean up solvent used, in lbs VOC/gal of solvent, and the resultant daily average lbs VOC/gal of solids after controls, based on the latest approved test results; (g) hours of operation; (h) hourly VOC input (daily average) to the incinerator (lbs/hr); (i) hourly VOC output (daily average) from the incinerator (lbs/hr); and (j) resultant lbs VOC/gal of solids after control for each coating. Monthly, record the following: (k) facility name, month, and year; and (l) calculated VOC emissions for the month (lbs) and for the most recent consecutive 12-month period (tons). Records of all calculations used to determine VOC emissions, and supporting documentation ("As Supplied", "As Applied" sheets, MSD sheets, EPA data sheets, purchase orders, etc.) shall be kept for each coating and solvent which includes sufficient information to determine VOC emissions. Daily records shall be completed within five business days and monthly records shall be completed by the end of the following month. The above records shall be maintained for five years and made available to the Department and the Air Program of the PCDEM upon request. [Rules 62-213.440(1)(b)2.b., 62-296.500(2)(b), and 62-4.070(3), F.A.C.; Pinellas Co. Code, Section 58-90] Comments: I examined materials usage and VOC emission logs that were in compliance with items (a) thru (l) above. See copy of examples attached). B.15. Operation and Maintenance (O & M) Plan - Not federally enforceable. The attached O & M Plan, (or the plan as revised with prior approval of the Air Program of the PCDEM, shall be followed for the thermal incinerator. The O & M documentation logs that are a part of the plan shall be maintained for a minimum of two years. At a minimum the plan shall include the following: (a) operating parameters of the pollution control device; (b) time table for routine maintenance of the pollution control device as specified by the manufacturer; (c) time table of routine weekly, bi-weekly, or monthly observations of the pollution control device; (d) list of the type and quantity of the required spare parts for the pollution control device which are stored on the premises; and (e) a record log which indicates at a minimum: 1. when maintenance and observations were performed; 2. what maintenance and observations were performed; 3. who performed said maintenance and observations; and 4. acceptable parameter ranges for each operational check. [Pinellas County Code, Section 58-128] Comments: The facility was in compliance with the routine weekly, bi-weekly and monthly observations of the control device with a log that demonstrated when maintenance and observations were made, what maintenance and observations were made and who performed the maintenance, along with the acceptable parameter ranges for the checks. STANDARDIZED PERMIT CONDITIONS 40 CFR 63 (NESHAP) Subpart JJJJ – National Emission Standards for Hazardous Air Pollutants: Paper and Other Web Coating (also includes applicable provisions of 40 CFR 63 Subpart A – General Provisions to 40 CFR 63 NESHAPs) Department of Environmental Protection Bureau of Air Regulation Permit Writers Tools Standardized Conditions (Last Updated 08/25/06) (Source for Subpart JJJJ: Federal Register dated 12/04/02) NOTE: This appendix was created for Schneller, Inc., Permit No. 1030118-011-AV (Title V Air Operation Permit Renewal). Cover page, headers and footers were added to Standardized Conditions referenced above by the FDEP Southwest District Air Permitting Section on September 7, 2006. Sec. 63.3320 What emission standards must I meet? (a) If you own or operate any affected source that is subject to the requirements of this subpart, you must comply with these requirements on and after the compliance dates as specified in Sec. 63.3330. (b) You must limit organic HAP emissions to the level specified in paragraph (b)(1), (2), (3), or (4) of this section. (1) No more than 5 percent of the organic HAP applied for each month (95 percent reduction) at existing affected sources, and no more than 2 percent of the organic HAP applied for each month (98 percent reduction) at new affected sources; or (2) No more than 4 percent of the mass of coating materials applied for each month at existing affected sources, and no more than 1.6 percent of the mass of coating materials applied for each month at new affected sources; or (3) No more than 20 percent of the mass of coating solids applied for each month at existing affected sources, and no more than 8 percent of the coating solids applied for each month at new affected sources. (4) If you use an oxidizer to control organic HAP emissions, operate the oxidizer such that an outlet organic HAP concentration of no greater than 20 parts per million by volume (ppmv) by compound on a dry basis is achieved and the efficiency of the capture system is 100 percent. (c) You must demonstrate compliance with this subpart by following the procedures in Sec. 63.3370. Comments: Schneller demonstrated a Destruction Efficiency of better than 98% during testing, thus in compliance with this limitation since the requirement is greater than 95%. Sec. 63.3321 What operating limits must I meet? (a) For any web coating line or group of web coating lines for which you use add-on control devices, unless you use a solvent recovery system and conduct a liquid-liquid material balance, you must meet the operating limits specified in Table 1 to this subpart or according to paragraph (b) of this section. These operating limits apply to emission capture systems and control devices, and you must establish the operating limits during the performance test according to the requirements in Sec. 63.3360(e)(3). You must meet the operating limits at all times after you establish them. (b) If you use an add-on control device other than those listed in Table 1 to this subpart or wish to monitor an alternative parameter and comply with a different operating limit, you must apply to the Administrator for approval of alternative monitoring under Sec. 63.8(f). Comments: Schneller performed the tests described above and set the parameters for temperature and pressure drop. Sec. 63.3330 When must I comply? (a) If you own or operate an existing affected source subject to the provisions of this subpart, you must comply by the compliance date. The compliance date for existing affected sources in this subpart is December 5, 2005. You must complete any performance test required in Sec. 63.3360 within the time limits specified in Sec. 63.7(a)(2). (b) If you own or operate a new affected source subject to the provisions of this subpart, your compliance date is immediately upon start-up of the new affected source or by December 4, 2002, whichever is later. You must complete any performance test required in Sec. 63.3360 within the time limits specified in Sec. 63.7(a)(2). (c) If you own or operate a reconstructed affected source subject to the provisions of this subpart, your compliance date is immediately upon startup of the affected source or by December 4, 2002, whichever is later. Existing affected sources which have undergone reconstruction as defined in Sec. 63.2 are subject to the requirements for new affected sources. The costs associated with the purchase and installation of air pollution control equipment are not considered in determining whether the existing affected source has been reconstructed. Additionally, the costs of retrofitting and replacing of equipment that is installed specifically to comply with this subpart are not considered reconstruction costs. You must complete any performance test required in Sec. 63.3360 within the time limits specified in Sec. 63.7(a)(2). Comments: Schneller complied with the testing required under this subpart before the December 5th, 2005 date . Sec. 63.3350 If I use a control device to comply with the emission standards, what monitoring must I do? (a) A summary of monitoring you must do follows: If you operate a web coating line, and have the following: Then you must: (1) Intermittently-controlled work stations ..... (2) Solvent recovery unit ................................ (3) Control Device........................................ (4) Capture system........................................... Record parameters related to possible exhaust flow bypass of control device and to coating use (§ 63.3350(c)). Operate continuous emission monitoring system and perform quarterly audits or determine volatile matter recovered and conduct a liquid-liquid material balance (§ 63.3350(d)). Operate continuous parameter monitoring system (§ 63.3350(e)). Monitor capture system operating parameter (§ 63.3350(f)). (b) Following the date on which the initial performance test of a control device is completed to demonstrate continuing compliance with the standards, you must monitor and inspect each capture system and each control device used to comply with Sec. 63.3320. You must install and operate the monitoring equipment as specified in paragraphs (c) and (f) of this section. (c) Bypass and coating use monitoring. If you own or operate web coating lines with intermittently-controlled work stations, you must monitor bypasses of the control device and the mass of each coating material applied at the work station during any such bypass. If using a control device for complying with the requirements of this subpart, you must demonstrate that any coating material applied on a never-controlled work station or an intermittently-controlled work station operated in bypass mode is allowed in your compliance demonstration according to Sec. 63.3370(n) and (o). The bypass monitoring must be conducted using at least one of the procedures in paragraphs (c)(1) through (4) of this section for each work station and associated dryer. (1) Flow control position indicator. Install, calibrate, maintain, and operate according to the manufacturer's specifications a flow control position indicator that provides a record indicating whether the exhaust stream from the dryer was directed to the control device or was diverted from the control device. The time and flow control position must be recorded at least once per hour as well as every time the flow direction is changed. A flow control position indicator must be installed at the entrance to any bypass line that could divert the exhaust stream away from the control device to the atmosphere. (2) Car-seal or lock-and-key valve closures. Secure any bypass line valve in the closed position with a car-seal or a lock-and-key type configuration. A visual inspection of the seal or closure mechanism must be performed at least once every month to ensure that the valve or damper is maintained in the closed position, and the exhaust stream is not diverted through the bypass line. (3) Valve closure continuous monitoring. Ensure that any bypass line valve or damper is in the closed position through continuous monitoring of valve position when the emission source is in operation and is using a control device for compliance with the requirements of this subpart. The monitoring system must be inspected at least once every month to verify that the monitor will indicate valve position. (4) Automatic shutdown system. Use an automatic shutdown system in which the web coating line is stopped when flow is diverted away from the control device to any bypass line when the control device is in operation. The automatic system must be inspected at least once every month to verify that it will detect diversions of flow and would shut down operations in the event of such a diversion. (d) Solvent recovery unit. If you own or operate a solvent recovery unit to comply with Sec. 63.3320, you must meet the requirements in either paragraph (d)(1) or (2) of this section depending on how control efficiency is determined. (1) Continuous emission monitoring system (CEMS). If you are demonstrating compliance with the emission standards in Sec. 63.3320 through continuous emission monitoring of a control device, you must install, calibrate, operate, and maintain the CEMS according to paragraphs (d)(1)(i) through (iii) of this section. (i) Measure the total organic volatile matter mass flow rate at both the control device inlet and the outlet such that the reduction efficiency can be determined. Each continuous emission monitor must comply with performance specification 6, 8, or 9 of 40 CFR part 60, appendix B, as appropriate. (ii) You must follow the quality assurance procedures in procedure 1, appendix F of 40 CFR part 60. In conducting the quarterly audits of the monitors as required by procedure 1, appendix F, you must use compounds representative of the gaseous emission stream being controlled. (iii) You must have valid data from at least 90 percent of the hours during which the process is operated. (2) Liquid-liquid material balance. If you are demonstrating compliance with the emission standards in Sec. 63.3320 through liquid-liquid material balance, you must install, calibrate, maintain, and operate according to the manufacturer's specifications a device that indicates the cumulative amount of volatile matter recovered by the solvent recovery device on a monthly basis. The device must be certified by the manufacturer to be accurate to within +/-2.0 percent by mass. (e) Continuous parameter monitoring system (CPMS). If you are using a control device to comply with the emission standards in Sec. 63.3320, you must install, operate, and maintain each CPMS specified in paragraphs (e)(9) and (10) and (f) of this section according to the requirements in paragraphs (e)(1) through (8) of this section. You must install, operate, and maintain each CPMS specified in paragraph (c) of this section according to paragraphs (e)(5) through (7) of this section. (1) Each CPMS must complete a minimum of one cycle of operation for each successive 15-minute period. You must have a minimum of four equally spaced successive cycles of CPMS operation to have a valid hour of data. (2) You must have valid data from at least 90 percent of the hours during which the process operated. (3) You must determine the hourly average of all recorded readings according to paragraphs (e)(3)(i) and (ii) of this section. (i) To calculate a valid hourly value, you must have at least three of four equally spaced data values from that hour from a continuous monitoring system (CMS) that is not out-of-control. (ii) Provided all of the readings recorded in accordance with paragraph (e)(3) of this section clearly demonstrate continuous compliance with the standard that applies to you, then you are not required to determine the hourly average of all recorded readings. (4) You must determine the rolling 3-hour average of all recorded readings for each operating period. To calculate the average for each 3-hour averaging period, you must have at least two of three of the hourly averages for that period using only average values that are based on valid data (i.e., not from out-of-control periods). (5) You must record the results of each inspection, calibration, and validation check of the CPMS. (6) At all times, you must maintain the monitoring system in proper working order including, but not limited to, maintaining necessary parts for routine repairs of the monitoring equipment. (7) Except for monitoring malfunctions, associated repairs, or required quality assurance or control activities (including calibration checks or required zero and span adjustments), you must conduct all monitoring at all times that the unit is operating. Data recorded during monitoring malfunctions, associated repairs, out-of-control periods, or required quality assurance or control activities shall not be used for purposes of calculating the emissions concentrations and percent reductions specified in Sec. 63.3370. You must use all the valid data collected during all other periods in assessing compliance of the control device and associated control system. A monitoring malfunction is any sudden, infrequent, not reasonably preventable failure of the monitoring system to provide valid data. Monitoring failures that are caused in part by poor maintenance or careless operation are not malfunctions. (8) Any averaging period for which you do not have valid monitoring data and such data are required constitutes a deviation, and you must notify the Administrator in accordance with Sec. 63.3400(c). (9) Oxidizer. If you are using an oxidizer to comply with the emission standards, you must comply with paragraphs (e)(9)(i) through (iii) of this section. (i) Install, calibrate, maintain, and operate temperature monitoring equipment according to the manufacturer's specifications. The calibration of the chart recorder, data logger, or temperature indicator must be verified every 3 months or the chart recorder, data logger, or temperature indicator must be replaced. You must replace the equipment whether you choose not to perform the calibration or the equipment cannot be calibrated properly. (ii) For an oxidizer other than a catalytic oxidizer, install, calibrate, operate, and maintain a temperature monitoring device equipped with a continuous recorder. The device must have an accuracy of +/-1 percent of the temperature being monitored in degrees Celsius, or +/-1[deg] Celsius, whichever is greater. The thermocouple or temperature sensor must be installed in the combustion chamber at a location in the combustion zone. (iii) For a catalytic oxidizer, install, calibrate, operate, and maintain a temperature monitoring device equipped with a continuous recorder. The device must be capable of monitoring temperature with an accuracy of +/-1 percent of the temperature being monitored in degrees Celsius or +/- 1 degree Celsius, whichever is greater. The thermocouple or temperature sensor must be installed in the vent stream at the nearest feasible point to the inlet and outlet of the catalyst bed. Calculate the temperature rise across the catalyst. (10) Other types of control devices. If you use a control device other than an oxidizer or wish to monitor an alternative parameter and comply with a different operating limit, you must apply to the Administrator for approval of an alternative monitoring method under Sec. 63.8(f). (f) Capture system monitoring. If you are complying with the emission standards in Sec. 63.3320 through the use of a capture system and control device for one or more web coating lines, you must develop a site-specific monitoring plan containing the information specified in paragraphs (f)(1) and (2) of this section for these capture systems. You must monitor the capture system in accordance with paragraph (f)(3) of this section. You must make the monitoring plan available for inspection by the permitting authority upon request. (1) The monitoring plan must: (i) Identify the operating parameter to be monitored to ensure that the capture efficiency determined during the initial compliance test is maintained; and (ii) Explain why this parameter is appropriate for demonstrating ongoing compliance; and (iii) Identify the specific monitoring procedures. (2) The monitoring plan must specify the operating parameter value or range of values that demonstrate compliance with the emission standards in Sec. 63.3320. The specified operating parameter value or range of values must represent the conditions present when the capture system is being properly operated and maintained. (3) You must conduct all capture system monitoring in accordance with the plan. (4) Any deviation from the operating parameter value or range of values which are monitored according to the plan will be considered a deviation from the operating limit. (5) You must review and update the capture system monitoring plan at least annually. Comments: Schneller complies with the Control Device Parameter Temperature and the Capture System Parameter Pressure Drop. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: 10 December 2010 |
| ACCESS? | ( | ARMS? | ( |

H:\USERS\WPDOCS\Airqual\Air_Compliance\AQI\1030118 003 75612.doc

| AIRS ID 1030118 | OWNER Schneller, LLC | FACILITY NAME Schneller, LLC |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE 08/08/2011 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE 04/22/2009 |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

# Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report |  |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : | CAM |
| DONE N/A | Other : | Quad JJJJ |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

# Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 10 November 2010 | 23 January 2011 |  |  |  |
| COMMENTS |

# Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs |  |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) |  |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

# Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

# Other Comments

Prepared by:	   Jose Rodriguez		Date: 	23 January 2011

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.