| 1030155 80840 |  |
| --- | --- |
| FACILITY: Coastal Steel Construction, Inc. | PERMIT ID: 34 |
| 31st Street Facility | DISTRICT: Southwest |
| ADDRESS: 1000 31st Street South | CONTACT PHONE: |
| St. Petersburg, FL | 727-327-7123 |
| ARMS NO: 1030155 001 | PERMIT NO: | Expiration Date: 2/23/2015 Renewal Date: 12/25/2014 |
|  | 1030155-003-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Spray Paint Area for Coating Structual Steel Fabrications. (RACT) The facility uses an airless spray system. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | July 3, 2012 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Greg Best? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Ron Wayman? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | General Conditions [62-4.160, F.A.C.] 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: A description of and cause of noncompliance; and The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: There was no noncompliance episodes recorded in the compliance year Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] Comments: There’s no pollution control equipment at the facility 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] Comments: The cutting oils and paint solvent drums were sealed. There were no drums uncovered and no leaks or spills observed. There was no evidence of overspray on the walls or concrete floor of the paint area. Additionally, the quantity of thinner used is recorded as used for cleaning. 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An “objectionable odor” means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C.] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- none ; Wind direction – E/ 10 mph Upwind odor level detected- none No odors inside or outside of the property that could be attributed to the use of paints or solvents. 9. Unconfined Particulate Emissions: No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. Reasonable precautions include the following: Paving and maintenance of roads, parking areas and yards. Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. Landscaping or planting of vegetation. Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. Confining abrasive blasting where possible. Enclosure or covering of conveyor systems. Comments: There were no unconfined particulate emissions observed. Coastal Steel Construction has paved parking around the facility with landscaping and there was no fugitive dust emissions observed. An airless spray system is used to apply paint. Administrative Requirements 7 Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 11’ was submitted on 2/10/12. 8 Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to PCDEM (Compliance Authority) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on 2/23/15. An application is required to be submitted no later than 12/25/14. A.2. Material Use Limit: The maximum total raw material usage of coatings and solvents shall not exceed 4,908 gallons per any consecutive 12-month period. [Construction Permit AC52-267942] Comments: The highest usage total for the 12-mo period = 1,481.532 gallons (May, 12’). The records are attached to the compliance file. A.3. Material VOC Content: This facility is limited to the use of coatings that do not exceed 3.5 pounds of VOC per gallon of coating, excluding water, delivered to the coating applicator (“as applied”). Unless directed into containers that prevent evaporation into the atmosphere, the use of solvent washings shall be included in the “as applied” VOC coating content. [Rules 62-296.513(2)(a)2. and (2)(c), F.A.C.] Comments: The only coating used at Coastal Steel Construction Is Gray Paint with a VOC content = 3.430 lbs of VOC /gallon of coating. A.4. VOC Emission Limitations: The facility is subject to the following limitations: Total facility Volatile Organic Compound (VOC) emissions shall not exceed 9.9 tons per any consecutive 12-month period. Emissions attributed to use of coatings shall not exceed 8.5 tons per any consecutive 12-month period. Emissions attributable to use of solvents shall not exceed 1.4 tons per any consecutive 12-month period. {Permitting Note: The VOC emission limitations above indirectly limit the potential HAP emissions below the Title V permitting thresholds of Chapter 62-213, F.A.C., since all of the HAPs are expected to be VOCs.} [Rule 62-210.200(PTE), F.A.C.; Construction Permit AC52-267942] Comments: The highest emissions total contributed to coatings per 12-mo period = 2.401 tons/yr (May, 12’). The highest emissions total contributed to solvents per 12-mo period = 0.042 tons/yr (April, 12’) A.5. General Standards - Objectionable Odor: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200(“Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, §58- 178] A.6. General Standards - Visible Emissions: Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1& 4, F.A.C.] Comments: There were no objectionable odors detected and no visible emissions observed during the inspection. The facility was not operating its spray painting operation. A.7. General Standards - (VOC) Emissions and/or (OS) Emissions: The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The facility shall comply with the following: All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials. All VOC/OS from washings (equipment clean-up) shall be directed into containers that prevent evaporation into the atmosphere or become subject to Specific Condition No. A.3. Tightly cover or close all VOC and/or solvent containers when they are not in use. Prevent excessive air turbulence across exposed VOCs. Immediately confine and clean up VOC spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rule 62-296.320(1)(a), F.A.C.; Pinellas County Code, §58-178] Comments: There were no leaks, spills or fugitive emissions observed. The airless spray system had no holes in the hose assembly. The RO stated that residual thinners and paint washings are confined to 55 gallon drums that are sealed and removed off-site for recycling. The gray paint and thinner drums were sealed (not in use during the time of inspection). There was no air turbulence observed. The facility does not use fans for ventilation instead the steel assembly and paint operation building has two openings on east and west sides of the 500 sq ft structure. Any spills of paint or thinner are immediately cleaned by Coastal Steel Construction. The clean up rags are disposed in sealed in 55 gallon drums for recycling. A.8. General Standards - Unconfined Particulates: All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320, F.A.C. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. Reasonable precautions to prevent emissions of unconfined particulate matter at this facility shall include, but not be limited to the following: Watering the facility’s grounds as needed. Ceasing of paint operations if overspray is observed leaving the facility property line. In order to provide reasonable assurance that the above measures are being implemented and that they are effective in controlling unconfined emissions of particulate matter, visible emissions from any facility area should not exceed 5% opacity. If this value is exceeded it will not be considered a violation in and of itself, but an indication that additional controls may be required. [Rules 62-4.070(3) and 62-296.320(4)(c), F.A.C.] Comments: There were no unconfined particulate emissions observed during the inspection. There was no dust observed from the grounds area and the facility was not spray painting. A.9. VOC Recordkeeping: In order to document compliance with the limitations of Specific Condition Nos. A.2., A.3., and A.4., the permittee shall maintain a log at the facility which documents the following: Daily: Facility name, Facility ID No. (1030155), Emission Unit No. & Description (001-Surface Coating Operations), and applicable rule [62-296.513(2)] The application method and substrate type (metal, plastic, paper, etc.) The amount and type of coatings (including catalyst and reducer for multi-component coatings) and solvent used in gallons at each point of application, including exempt compounds The VOC content as applied in each coating and solvent The date for each application of coating and solvent The amount of each Surface Preparation, Clean-Up, Wash-Up of solvent (including exempt compounds) used in gallons and the VOC content of each Monthly: Facility name, Facility ID No. (1030155), Emission Unit No. & Description (001-Surface Coating Operations) The total raw material usage of coatings and solvents (gallons) The VOC emissions from the use of coatings (tons) The VOC emissions from the use of solvents (tons) The most recent consecutive 12-month total of raw material (coatings and solvents) used (gallons) The most recent consecutive 12-month total of the total facility VOC emissions (tons) The most recent consecutive 12-month total of VOC emissions from the use of coatings (tons) The most recent consecutive 12-month total of VOC emissions from the use of solvents (tons) Supporting documentation (MSD sheets, purchase orders, U. S. EPA "VOC DATA SHEETS”, etc.) shall be kept for each paint, coating, thinner, solvent and other material used in the painting and coating operations which includes sufficient information to determine VOC emissions. These records shall be retained on file at the facility for at least three (3) years and shall be made available to the Department and the Pinellas County Department of Environmental Management (PCDEM) upon request. [Rules 62-4.070(3), 62-4.160(14)(b), 62-296.500(2)(b), and 62-296.513(2), F.A.C.; Pinellas County Code §58-90] Comments: The records were in compliance with the provisions of the condition. Copies of the monthly records are attached to the compliance file. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no pollution prevention activities during the compliance year. |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |