| 1030214 84656 |  |
| --- | --- |
| FACILITY: Life-Like Acquisitions, Inc. | PERMIT ID: 189 |
| Lifoam Industries, LLC | DISTRICT: Southwest |
| ADDRESS: 2601 Anvil Street | CONTACT PHONE: |
| St. Petersburg, FL | 727-345-1410 |
| ARMS NO: 1030214 001 | PERMIT NO: | Expiration Date: 6/19/2017 Renewal Date: 4/20/2017 |
|  | 1030214-013-AF |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Polystryene Product Line, Consisting of 2 Bead Pre-expander Machines, and 10 Compression Molding Machines (1) Hirsch Model HE 800, one (1) Hirsch Model HE 1200, three (3) Hirsch Model HE 1300, and five (5) Hirsch Model HE 1400) |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | December 19, 2012 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Ronald R. Hess? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: John Presser? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | General Conditions [62-4.160, F.A.C.] 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: a. A description of and cause of noncompliance; and b. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: No non-compliance events during the compliance year 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] Comments: No circumvention observed during the inspection. 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] Comments: No organic solvents are used in the process ant the facility only uses polystyrene pellets to produce Styrofoam ice chests. The polystyrene product line is housed in a closed in 5000 sq ft building. There is limited air turbulence in the building due to air conditioning/heating. Bags of polystyrene pellets are sealed. No other solvents are used on site. All fittings, valve lines to the molding machines, pre-expander machines and boilers are properly maintained. The facility shuts down every Friday for preventative maintenance activities to ensure all fittings/valves are not leaking. Any leaks or spills are cleaned immediately. 7. General Standards: Volatile Organic Compounds (VOC) and Organic Solvents (OS) Emissions - The permittee shall comply with the following: Maintain tightly fitting covers, lids, etc., on all containers of VOC and organic solvents (OSs) when they are not being handled, tapped, etc. Prevent excessive air turbulence across exposed VOC/OS. Where possible and practical, procure/fabricate a tightly fitting cover for any open tough, basin, bath, etc., of VOC/OS so that it can be covered when not in use. All fittings, valve lines, etc. utilizing VOC/OS materials shall be properly maintained. All solvents from equipment clean up shall be directed into containers that prevent evaporation into the atmosphere. All VOC/OS spills shall be attended to immediately and the waste properly disposed of, recycled, etc. [Rule 62-296.320(1)(a), F.A.C.; Construction Permit 1030214-005-AC] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- No odor detected; Wind direction – E/5 mph Upwind odor level detected-No odor detected 8. General Standards: Objectionable Odor - No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200 (Definition of Objectionable Odor), F.A.C.; Pinellas County Code, Section 58-178] Comments: No objectionable odor detected during the inspection Permit Administrative Requirements 9. Annual Operating Report - On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 11’ was submitted on 2/21/12. 10. Operation Permit Renewal Application - A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to Pinellas County Air Quality Division (PCAQD) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on 6/19/17. An application is required to be submitted no later than 4/20/17. A.2. Dispersion of Air Pollutants - In order to provide reasonable dispersion of air pollutants, there shall be no device that: a. reduces the vertical momentum of the exhaust gas from the building vents; or b. reduces the vertical dispersion of the exhaust gas from the building vents. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030214-005-AC] Comments: There are no devices at the facility that reduces the vertical momentum of the exhaust gas A.3. Pentane (VOC) Emission Limitation - The maximum total emissions of pentane (a volatile organic compound (VOC)) from the usage of polystyrene beads shall not exceed 93.0 tons per any consecutive 12-month period. This limitation is based on the following calculation and that no more than two (2) expanders are operating: 3,800,000 lbs. of beads/year x 0.0544 (% pentane) x 0.9 (10% residual pentane contained in the product) x (1 ton/2,000 lbs.) = 93.0 tons/year. (Pentane Limitation Note - Since the percentage of pentane in the polystyrene beads may vary, the maximum total usage of polystyrene beads may change based on a linear relationship. A constant value of “10%” residual pentane is considered to be contained in the product and shall be used in determining pentane emissions. Also, the VOC emissions from the exempt boiler are expected to be less than 1 ton/year.) [Rule 62-210.200 (Definition of Potential to Emit), F.A.C.; Construction Permit 1030214-005-AC] Comments: During the compliance year of Nov, 11’ – Nov, 12’’the highest 12-mo total pentane emissions = 37.0105 tons/yr (April, 12”). A copy of the records are attached to the compliance file. The facility followed this methodology to obtain its calculation. A.4. Volatile Organic Compound (VOC) Emission Limitation - The only VOC authorized to be released from this emissions unit is pentane. (Title V Applicability Note - There will be no emissions of any Hazardous Air Pollutants (HAPs) as defined in Rule 62-210.200, F.A.C.) [Rule 62-210.200, (definitions of Title V Source), F.A.C.; Construction Permit 1030214-005-AC] Comments: During the compliance year the facility only emitted pentane. No other VOC or HAP emissions. The facility continues to produce products only using the polystyrene bead material. A.5. Recordkeeping Requirements - In order to document compliance with Specific Condition No. A.3., the permittee shall maintain the following logs/records: for each day polystyrene beads are used, document or record the lot number of the beads used, the pounds of each lot number used, the “as received” pentane content of each lot number used, and the pounds and tons of pentane emitted per lot number used; monthly calculate and record the total quantity of polystyrene beads used, in pounds, along with the associated pentane content; monthly calculate and record the most recent consecutive 12-month period total of polystyrene beads used, in tons; monthly calculate and record the total pentane emissions in pounds and tons, from the usage of polystyrene beads and their associated pentane content, and assuming 10% of the pentane is retained in the product; and monthly calculate and record the most recent consecutive 12-month period total of pentane emissions, in tons. These records shall be kept at the facility for a minimum of three (3) years and made available to the Department and Pinellas County Air Quality Division upon request. Daily records shall be completed within three (3) business days. The monthly records shall be completed by the end of the following month. Where appropriate, the monthly values recorded in "lbs." shall be converted to "tons" in order to demonstrate compliance. The permittee shall also maintain documentation, such as all Material Safety Data Sheets, purchasing records, etc. for all polystyrene beads, which includes sufficient information to determine pentane emissions. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030214-005-AC] Comments: The attached record copy has the following: Ex Day 4 from the Sep, 12’ report Daily Bead lot# is recorded (207P56069) Daily calculation of total lbs of polystyrene beads used 11,015 lbs (summed from daily) and associated % pentane content (day 4 and 5 from the same bag lot) Monthly most recent 12-mo total of polystyrene beads used (12-mo total 140,992 lbs or 70.496 tons Expandable Polystyrene (EPS) is used. Monthly total pentane emissions in lbs and converted in tons from polyester beads and the pentane content (5741.8992 lbs or 2.8709 tons) Most recent consecutive 12-mo consecutive total of pentane emissions in tons. (37.0105 tons/yr) |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no pollution prevention activities during the compliance year. |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |