| 1030214 80587 |
| --- |
| FACILITY: Life-Like Acquisitions, Inc. | PERMIT ID: 189 |
| Lifoam Industries, LLC | DISTRICT: Southwest |
| ADDRESS: 2601 Anvil Street | CONTACT PHONE: |
| St. Petersburg, FL | 727-345-1410 |
| ARMS NO: 1030214 001 | PERMIT NO: | Expiration Date: 5/30/2012 Renewal Date: 3/31/2012 |
|  | 1030214-012-AF |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Polystryene Product Line, Consisting of 2 Bead Pre-expander Machines, and 10 Compression Molding Machines (1) Hirsch Model HE 800, one (1) Hirsch Model HE 1200, three (3) Hirsch Model HE 1300, and five (5) Hirsch Model HE 1400) |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | November 3, 2011 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Ronald R. Hess? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: John Pressler? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: This permit became effective on 3/29/11. Rule General Conditions [62-4.160, F.A.C.] 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: a. A description of and cause of noncompliance; and b. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: No non-compliance events during the compliance year Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] Comments: No circumvention observed during the inspection 9. Unconfined Particulate Emissions: a. No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. b. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. c. Reasonable precautions include the following: (1) Paving and maintenance of roads, parking areas and yards. (2) Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. (3) Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. (4) Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. (5) Landscaping or planting of vegetation. (6) Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. (7) Confining abrasive blasting where possible. (8) Enclosure or covering of conveyor systems. Comments: No unconfined particulate emissions observed. Roads are paved and there is landscaping around the premises Administrative Requirements 7 Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 10’ was submitted on 2/14/11. Permit General Condtions 7. General Standards – Volatile Organic Compound and Organic Solvent Emissions: The permittee shall comply with the following: Maintain tightly fitting covers, lids, etc., on all containers of VOCs and organic solvents (OSs) when they are not being handled, tapped, etc. Prevent excessive air turbulence across exposed VOCs/OSs. Where possible and practical, procure/fabricate a tightly fitting cover for any open tough, basin, bath, etc., of VOCs/OSs so that it can be covered when not in use. All fittings, valve lines, etc. utilizing VOCs/OSs materials shall be properly maintained. All solvents from equipment clean up shall be directed into containers that prevent evaporation into the atmosphere. All VOCs/OSs spills shall be attended to immediately and the waste properly disposed of, recycled, etc. [Rule 62-296.320(1)(a), F.A.C.; Construction Permit 1030214-005-AC] Comments: a) No organic solvents are used in the process. The facility only uses polystyrene pellets to produce Styrofoam ice chests b) The facility prevents excessive air turbulence c) Bags of polystyrene pellets are sealed. No other solvents are used on site. d) All fittings, valve lines to the molding machines, pre-expander machines and boilers are properly maintained. The facility shuts down on Friday for preventative maintenance activities to ensure all fittings/valves are not leaking E&f) any leaks or spills are cleaned immediately 8. General Standards – Objectionable Odor: No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200, (Objectionable Odor), F.A.C. and Pinellas County Code, Section 58-178] Comments: No objectionable odor detected during the inspection 9. Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: Air Quality received the 2009 EAOR on March 1st. The EAOR contained the amount of polystyrene used/pentane emissions and natural gas utilized for the boiler during the calendar year. An electronic calculation sheet was included. 10. Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to Pinellas County Air Quality Division (PCAQD) no later than 60 days prior to the expiration date of the operation permit. …. [Rules 62-4.030, 62-4.050, 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.; Construction Permit 1030214-011-AC] Comments: The facility contact was made aware of the renewal application submittal deadline and expiration date. Air Quality will check to verify the renewal has been completed and submitted by March, 12’ A.2. Dispersion of Air Pollutants: In order to provide reasonable dispersion of air pollutants, there shall be no device that (a) reduces the vertical momentum of the exhaust gas from the building vents, or (b) reduces the vertical dispersion of the exhaust gas from the building vents. [Construction Permit 1030214-005-AC] Comments: There are no devices at the facility that reduces the vertical momentum of the exhaust gas A.3. Pentane Emission Limitation: The maximum total pentane emissions from the usage of polystyrene beads shall not exceed 93.0 tons per any consecutive 12-month period. This limitation is based on the following calculation and that no more than two (2) expanders are operating: 3,800,000 lbs. of beads/yr. x 0.0544 (% pentane) x 0.9 (10% residual pentane contained in the product) x (1 ton/2,000 lbs.) = 93.0 tons/yr. (Note: Since the percent of pentane in the polystyrene beads may vary, the maximum total usage of polystyrene beads may change based on a linear relationship. A constant value of “10%” residual pentane is considered contained in the product and shall be used in determining pentane emissions. Also, the VOC emissions from the boilers are expected to be less than 1 ton/yr.) [Rule 62-210.200, (Potential to Emit), F.A.C.; Construction Permit 1030214-005-AC] Comments: During the compliance year of Nov, 10’ – Oct, 11’the highest 12-mo total pentane emissions = 40.7647 tons/yr (Mar, 11”). A copy of the records are attached to the compliance file. A.4. Volatile Organic Compound Emission Limitation: The only VOC authorized to be released from this emission unit is pentane. Title V Applicability Note: There will be no emissions of any Hazardous Air Pollutants (HAPs) as defined in Rule 62-210.200, F.A.C.) [Rule 62-210.200, (Modification and Title V Source), F.A.C.; Construction Permit 1030214-005-AC] Comments: During the compliance year the facility only emitted pentane. No other VOC or HAP emissions. The facility continues to produce products only using the polystyrene bead material. A.5. Recordkeeping Requirements: In order to document compliance with Specific Condition A.3., the permittee shall maintain the following logs/records: For each day polystyrene beads are used, document or record the lot number of the beads used, the pounds of each lot number used, the “as received” pentane content of each lot number used, and the pounds and tons of pentane emitted per lot number used; Monthly calculate and record the total quantity of polystyrene beads used, in pounds, along with the associated pentane content; Monthly calculate and record the most recent consecutive 12-month period total of polystyrene beads used, in tons; Monthly calculate and record the total pentane emissions in pounds and tons, from the usage of polystyrene beads and their associated pentane content; and Monthly calculate and record the most recent consecutive 12-month period total of pentane emissions, in tons. These records shall be kept at the facility for a minimum of three (3) years and made available to the Department and Pinellas County Air Quality Division upon request. The monthly records shall be completed by the end of the following month. Where appropriate, the monthly values recorded in "lbs." shall be converted to "tons" in order to demonstrate compliance. The permittee shall also maintain documentation, such as all Material Safety Data Sheets, purchasing records, etc. for all polystyrene beads, which includes sufficient information to determine pentane emissions. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030214-005-AC] Comments: The attached record copy has the following: Ex Day 1 from the March, 11’ report Daily Bead lot# is recorded (101P56006) Monthly calculation of total lbs of polystyrene beads used 8,598.9699 lbs (summed from daily) and associated % pentane content Monthly most recent 12-mo total of polystyrene beads used (12-mo total 207,082 lbs or 103.541 tons EPS used ) Monthly total pentane emissions in lbs and converted in tons from polyester beads and the pentane content (8598.9699 lbs or 4.299 tons) Most recent consecutive 12-mo consecutive total of pentane emissions in tons. (36.4652 tons/yr) |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: No P2 activities during the compliance year. Facility is performing recycling of boxes. The facility closes on Friday’s to perform routine maintenance on the 2 bead pre-expander machines and the 10 compression molding machines |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030214 | OWNER Life-Like Acquisitions, Inc. | FACILITY NAME Lifoam Industries, LLC |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE November 3, 2011 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE June 6, 2008 |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | 2/14/11 reviewed 2010 AOR |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 11/3/11 | 11/10/11 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs | Copy of the logs appended to the compliance file |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) | Raw materials; polystyrene beads with assoc lot #’s. %pentane reported, lbs of pentane emissions produced |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.