| 1030216 80762 |  |
| --- | --- |
| FACILITY: Carpenter Technology Corporation | PERMIT ID: 589 |
| Dynamet Incorporated | DISTRICT: Southwest |
| ADDRESS: 14000 49th Street North | CONTACT PHONE: |
| Clearwater, FL | 727-535-5591 |
| ARMS NO: 1030216 002 | PERMIT NO: | Expiration Date: 10/8/2013 Renewal Date: 8/9/2013 |
|  | 1030216-006-AO & 1030216-007-AC |  |
|  |  | Test Due Date: 8/9/2013 |
| EMISSION UNIT DESCRIPTION : Shot Blasting Operation: MMC Spinblast system to clean titanium sheets, emissions are controlled by a Torit Downflo II Dust collector |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | May 1, 2012 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: B.R. Riffee? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Jeff Tomich? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: These permits (1030216-006-AO and 1030216-007-AC) were issued simultaneously and became effective on 10/8/08. The construction permit (expires 12/31/2010) modification is to add four new pickling lines to Emission Unit 001 (EU 001) Mineral Acid Cleaning; increases the maximum processing rate of titanium in Emission Unit 002 (EU 002), Shotblasting System, from 2,000 tons per year (TPY) to 2,500 TPY; emission limitations for EU 001 and EU 002 were removed; testing requirements for EU 001 were removed; Nitric acid limitations were removed as it is no longer used for cleaning. This permit or a copy thereof shall be kept at the work site of the permitted activity. [62-4.160 F.A.C. - General Condition 12.] Comments: The facility did did not have a copy of the permit on-site. A.4. General Pollutant Emission Limiting Standards: Objectionable Odor Prohibited - The permittee shall not cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200 (“Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: There were no odors detected during the time of inspection A.5. General Pollutant Emission Limiting Standards: Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions - The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1)(a), F.A.C.] Comments: The facility keeps the shot pellets in plastic lined 55 gallon drums. There were 2 drums on-site during the inspection and no leaks were evident. A.6. General Particulate Emission Limiting Standards: General Visible Emissions Standard - No person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1., F.A.C.] Comments: There were no visible emissions observed from the Torit Downflo II dust collector. A.7. General Pollutant Emission Limiting Standard: Unconfined Emissions of Particulate Matter - All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter at this facility. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing, and handling. Reasonable precautions to be taken shall include procedures listed below. a. Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. b. Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. [Rule 62-296.320(4)(c)2. and 3., F.A.C.] Comments: There were no unconfined particulate matter emissions observed during the inspection. The roads around the facility are paved. There were no unconfined emissions from the Torit dust collector A.8. Special Compliance Tests - When the Department or the Pinellas County Department of Environmental Management (PCDEM), after investigation, has good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it shall require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and to provide a report on the results of said tests to the Department and to the PCDEM. [Rule 62-297.310(7)(b), F.A.C.] Comments: There was no special compliance test required during the compliance year A.9. Modification - Unless otherwise exempt by rule, the permittee shall not initiate any construction, reconstruction, or modification at the facility and shall not install/modify any pollution control device at the facility without obtaining prior authorization from the Department. Modification is defined as: Any physical change or changes in the method of operations or addition to a facility that would result in an increase in the actual emissions of any air pollutant subject to air regulations, including any not previously emitted, from any emission unit or facility. [Rules 62-210.200, (“Modification”) and 62-210.300(1)(a), F.A.C.] Comments: There was no modification, construction or reconstruction at Dynamet during the compliance year. A.10. Operation and Maintenance Plan - The MAPCO fume scrubber and Torit dust collector shall be operated and maintained in accordance with the Operation and Maintenance (O&M) Plan submitted with the response received on July 9, 2008, to the Department’s request for additional information or as revised with the prior approval from the PCDEM. The O&M Plan documentation shall be retained at the facility for at least 2 years and made available to the Department and PCDEM upon request. At a minimum, the O&M plan shall include: a. The operating parameters of the pollution control device. b. Time table for the routine maintenance of the pollution control device as specified by the manufacturer. c. Time table of routine daily, weekly, bi-weekly, or monthly observations and inspections of the pollution control device. d. A list of the type and quantity of the required spare parts for the pollution control device which are stored on the premises. e. A maintenance log which will indicate, as a minimum: 1. When maintenance and observations were performed. 2. What maintenance and observations were performed. 3. Who performed said maintenance and observations. 4. Acceptable parameter ranges for each operational check. [62-4.070(3), F.A.C.; Pinellas County Code, Section 58-128] Comments: There were no changes to the Grit Blasting Operation O&M plan during the compliance year. The plan meets the provisions for this condition. A.11. Annual Operating Report (AOR) - On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. Note, the annual operating report for calendar year 2008 shall be submitted by May 1, 2009. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Air Compliance section of the Pinellas County Department of Environmental Management. An emission factor of 27.7 pounds of shot per ton of titanium blasted shall be used to calculate particulate matter emissions (before control) for EU 002. [Rule 62-210.370(3), F.A.C.] Comments: The EAOR was received 2/21/12 and reviewed on 2/27/12 A.12. Operation Permit Renewal Application - An air pollution operation permit renewal application shall be submitted to the Air Permitting Section of this office with a copy to the Pinellas County Department of Environmental Management at least 60 days prior to the expiration date of the operation permit….[Rules 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on10/8/13. An application is required to be submitted no later than 8/9/13. C. Conditions Specific to EU 002 (Shotblasting System) C.1. Maximum Process Rate - The throughput of titanium metal processed in the shotblaster shall not exceed 2,500 tons in any 12 consecutive month period. [Rule 62-210.200, F.A.C. (“Potential to Emit”)] Comments: The highest 12-mo consecutive total = 1,565.25 tons/yr (May, 11’ - April, 12’) C.2. Proper Operation of Control Equipment - No person shall circumvent any air pollution control device, or allow the emission of air pollutants without the applicable air pollution control device (Torit dust collector) operating properly. In order to provide reasonable assurance that the PM emissions from the shotblasting system are being effectively controlled by the dust collector control device, visible emissions from the dust collector exhaust shall not exceed 5% opacity. [Rules 62-4.070(3) and 62-210.650, F.A.C. (“Circumvention”)] Comments: There was no circumvention observed of the Torit dust collector C.3. Visible Emission (VE) Testing Requirement – In order to determine compliance with the visible emissions limitation of Specific Condition No. C.2., the dust collector exhaust shall be tested for visible emissions within 60 days of permit renewal (every 5 years). [Rules 62-297.310(7)(a)1., and 62-297.310(7)(a)4.a., F.A.C.] Comments: The facility performed the last test on March 7, 2008 and a copy of the test was received by AQD on March 19, 2008. Another VE test will be needed upon permit renewal on August 9, 2013. C.4. Test Notifications - The permittee shall notify the Air Compliance Section of the Pinellas County Department of Environmental Management in writing at least 15 days prior to the date on which the compliance test is to begin. The notice shall include, the date, time, and place of each test, and the test contact person who will be responsible for coordinating and having each test conducted. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: Air Quality received the last test notification on February 13, 2008 for the test performed on February 28, 2008. C.5. Visible Emission Test Method - Visible emission testing shall be conducted in accordance with EPA Method 9, contained in 40 CFR 60, Appendix A and adopted by reference in Rule 62-204.800, F.A.C. The visible emissions compliance test shall be conducted by a certified observer and be a minimum of 30 minutes in duration. The test observation period shall include the period during which the highest opacity can reasonably be expected to occur. The minimum requirements for source sampling and reporting shall be in accordance with the requirements of Chapter 62-297, F.A.C. [Rules 62-297.310(4) and 62-297.401(9), F.A.C.] Comments: The VE test on March 7, 2008 was conducted by Air Testing & Consulting, Ken Givens, who is a certified ETA observer. The consultant followed the Method 9 EPA requirements. C.6. Operating Rate During Testing - Compliance testing shall be conducted while operating at process rates representative of normal operations. If the Department determines the tested rates are not representative of normal operating conditions, a new compliance test may be required at a higher process rate. [Rule 62-4.070(3) F.A.C.] Comments: The facility performed the test at normal operating rates in 08’. C.7. Test Report Requirements - The test results shall be submitted to the Air Compliance Section of the Pinellas County Department of Environmental Management within 45 days of testing. The test report submittal shall meet all applicable requirements of Chapter 62-297, F.A.C. Each test report shall include a statement of the actual process rate during the test period in tons/hour. [Rules 62-4.070(3) and 62-297.310(8), F.A.C.] Comments: The facility performed the last test on March 7, 2008 and a copy of the test was received by AQD on March 19, 2008. The test report was submitted within 45 days of testing. C.8. Titanium Processing Recordkeeping – In order to document compliance with the limitations of Specific Condition No. C.1., the permittee shall keep a log of the quantity of titanium processed in the shotblaster. The log shall record the following at a minimum: Daily a. name, facility ID No., emission unit ID No., and description (i.e., Dynamet, Inc., 1030216, EU 002, Shotblasting System); b. day, month, and year; and c. daily quantity, in pounds, of titanium processed; Monthly d. month and year; e. monthly total, in pounds, of titanium processed based on c. above; and f. most recent 12 consecutive month period cumulative process rate (in tons per 12 consecutive month period) based on e. above. [Rule 62-4.070(3) F.A.C.] Comments: The Titanium Process records meet the provision of the condition and a copy is appended to the compliance file. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No lower production Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |