| 1030223 80635 |
| --- |
| FACILITY: Catalina Yachts, Morgan Division | PERMIT ID: 26 |
|  | DISTRICT: Southwest |
| ADDRESS: 7200 Bryan Dairy Road | CONTACT PHONE: |
| Largo, FL | 727-544 6681 |
| ARMS NO: 1030223 001 | PERMIT NO: | Expiration Date: 12/8/2014 Renewal Date: 2/1/2014 |
|  | 1030223-011-AV |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Fiberglass Boat Manufacturing: Activities conducted in six buildings: Tooling Building, Lamination Building Grinding Building, Assembly Building, Varnishing Building, and the Small Lamination/Storage Building |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | June 25, 2012 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Michael Quinn? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Michael Quinn? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: Michael Quinn? |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: this permit, effective 12/8/09 is for the renewal of Title V Air Operation Permit and the incorporation of a construction permit, No. 1030223-010-AC for changes to Emission Unit ID No. 001: the use of an existing building as a dedicated varnishing building for wooden parts, and the use of an existing Small Storage Building for lamination and gelcoating activities associated with manufacturing dinghies and small parts. 2. General Pollutant Emission Limiting Standards. Objectionable Odor Prohibited. No person shall cause, suffer, allow, or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200 (Definition “Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178; Construction Permit 1030223-010-AC] Comments: There were no styrene odors detected during the inspection. All doors of the lamination bay and small storage building were closed. 3. General Particulate Emission Limiting Standards. General Visible Emissions Standard. Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1. & 4., F.A.C.] Comments: There were no visible emissions observed during the inspection 4. Prevention of Accidental Releases (Section 112(r) of CAA). If required by 40 CFR 68, the permittee shall submit to the implementing agency: A. A risk management plan (RMP) when, and if, such requirement becomes applicable; and B. Certification forms and/or RMPs according to the promulgated rule schedule. [40 CFR 68] Comments: Not applicable to the facility. 5. Insignificant Emissions Units and/or Activities. Appendix I-1, List of Insignificant Emissions Units and/or Activities, is a part of this permit. [Rules 62-213.440(1), 62-213.430(6) and 62-4.040(1)(b), F.A.C.] Comments: There were no insignificant emission units or activities reported since the last inspection performed on February 8, 2010. 6. General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The permittee shall comply with the following: Each building's fans and/or ventilation systems shall be operating whenever usage of materials containing VOC/OS's occurs and shall remain operating for at least 1 hour after the usage has been completed. The capture rate of miscellaneous other VOC/OS emissions clean-up shall not be less than 40%. Compliance with the 40% capture rate shall be considered satisfied by complying with Attachment C – Standard Operating Procedures for Clean-up Solvent Usage. NOTE – When determining the miscellaneous solvent emission rate(s), the percent of solids in the recovered solvents shall be documented and accounted for in the emission calculations. All materials containing VOC/OS's shall be stored in closed original containers and/or in small automatic closing safety cans. Clean-up solvent washings shall be directed into containers that prevent evaporation into the atmosphere. All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions, and spills of materials containing VOC/OS's. Work practice controls shall include limiting the amount of clean-up solvents issued to employees and employees shall use gloves whenever handling resins. Immediately attend to all spills of materials containing VOC/OS's as appropriate. [Rule 62-296.320(1)(a), F.A.C. and Construction Permit 1030223-010-AC] Comments: All 11 ventilation fans in the lamination bay were operating including the 4 fans on the north side, the 4 fans on the south and the 3 operating on the roof. Michael Quinn stated the fans are in operation for at least 1 hour after layup. Catalina Yachts complies with the Standard Operating Procedures for Clean-Up Solvent Usage It was observed that gelcoat and resin products were in sealed 55 gallon drums and that small worker pails were covered when not in use. All solvents observed, MMA, resin and gelcoat are stored in closed leak-tight containers. All clean-up washings and rags are disposed in sealed 55 gallon drums and removed off-site for recycling. There were no leaks observed with the HVLP spray gun applicators and hose assembly. If there are leaks associated with the spray equipment, it is repaired or replaced. Mr. Quinn stated that workers have gloves when handling solvent clean-up activities All solvent spills are confined and cleaned up. 7. Emissions of Unconfined Particulate Matter. Pursuant to Rules 62-296.320(4)(c)1., 3. & 4., F.A.C., reasonable precautions to prevent emissions of unconfined particulate matter at this facility include the following requirements (also see Condition 57. of APPENDIX TV-6, TITLE V CONDITIONS): The north wall of the grinding building shall contain a filter with the exhaust fan. Frequent cleanings and sweeping of floors, equipment, and finished products. Supervisory inspections during operation(s) to ensure that all activities are being conducted in a manner to minimize emissions. Application of water to paved and unpaved areas accommodating vehicular traffic, as necessary. Enclosure or covering of activities or equipment where necessary. As an indicator that adequate control measures/practices are adequate, visible emissions from the property line, exhaust fans, doors, and vents shall not exceed 5% opacity. If this level is exceeded, it shall not be considered a violation in and of itself, but may allow the Department to require additional controls or work practices. [Rule 62-296.320(4)(c)2., F.A.C. and Construction Permit 1030223-010-AC] Comments: There were no unconfined particulate matter emissions observed. The exhaust fan of the grinding building north wall had a filter. Inspections are performed to ensure all grinding activity emissions are minimized. The roads are paved surrounding the facility There were no visible emissions from the exhaust fans or bay doors. 8. When appropriate, any recording, monitoring, or reporting requirements that are time-specific shall be in accordance with the effective date of the permit, which defines day one. [Rule 62-213.440, F.A.C.] Comments: The facility keeps monthly usages and emissions records that were reviewed by Air Quality. It is in accordance with the effective date of the permit December 8, 2009 9. Special Compliance Tests. When the Department, after investigation, has good reason (such as complaints, increased visible emissions, or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it may require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emission unit and to provide a report on the results of said tests to the Department. [Rule 62-297.310(7)(b), F.A.C.] Comments: There were no special compliance tests required since the last inspection performed on February 8, 2010. 10. Statement of Compliance. The annual statement of compliance pursuant to Rule 62-213.440(3)(a)2., F.A.C., shall be submitted to the Department and EPA within 60 (sixty) days after the end of the calendar year using DEP Form No. 62-213.900(7), F.A.C. [Rules 62-213.440(3) and 62-213.900, F.A.C.] {Permitting Note: This condition implements the requirements of Rules 62-213.440(3)(a)2. & 3., F.A.C. (see Condition 51. of APPENDIX TV-6, TITLE V CONDITIONS)} Comments: The 2011 Statement of Compliance Report was received on March 1, 2012. A.2. The permittee shall comply with the following: Emissions of total HAP's shall not exceed 240 tons per any consecutive 12 month period. Emissions of total volatile organic compounds (VOC's), which includes chemicals such as Styrene and Methyl Methacrylate, shall not exceed 240 tons per any consecutive 12 month period. [Rules 62-4.160(2) and 62-210.200(PTE), F.A.C.; Construction Permit 1030223-005-AC] Comments: The highest 12-mo total HAP emissions = 16.32 tons/yr (Jan, 12’) and the highest VOC emissions = 36.53 tons/yr (Jan, 12’) A.3. A monthly log based on the tracking of individual HAP's associated with monomer usage, total HAP's and/or VOC containing material used in association with manufacturing activities shall be kept for this facility to document compliance with the emission limitations of Condition No. A.2. Note, if any month results in total HAP's and/or total VOC's emissions being within 10% of its associated allowable emission limit as shown in Condition No. A.2., the logs required below shall be then kept daily. The daily logs shall include a cumulative total to demonstrate compliance with Condition No. A.2. At a minimum, the logs shall contain the following: Facility Name, Date, and Emission Unit ID (1030223 001). Identify and quantify each resin, coating, solvent, chemical, etc. used at the facility that contains HAP's and/or VOC's. At the permittee's option, "purchases" may be used where "usage" is specified, except when daily recordkeeping is required. If this option is utilized, no materials may be used which is not purchased and the material shall not be used in multiple application methods with different emission factors. The total tons of each individual HAP (e.g., Styrene, MMA, etc.) emissions for the month. The total HAP emissions for the month in tons. The total VOC emissions for the month in tons. The total HAP emissions, in tons, for the most recent consecutive 12 month period. The total VOC emissions, in tons, for the most recent consecutive 12 month period. Record the method of application (where applicable) for each material used (see Table below). Emissions of Styrene, Methyl methacrylate (MMA), and other volatile organic compounds (VOCs) shall be determined as follows until notified by the Department or the Pinellas County Department of Environmental Management. Note, Styrene and MMA are each considered a VOC and HAP. Styrene emissions shall be determined using the following equation: where: Ms = amount of styrene containing material used (in tons) EF = emission factor (lb/ton) for styrene monomer content (from table below) The applicable styrene emission factor shall be obtained (interpolated/extrapolated, if applicable) from the following table, in conjunction with the percent of available non-vapor suppressed (NVS) styrene monomer in the resin/gelcoat: % Monomer Resin** Hand (Non-Spray) Layup Resin** Mechanical Atomized Spray Layup Resin Mechanical Nonatomized* Spray Layup Gel Coat** Mechanical Atomized Spray Layup Gelcoat Mechanical Nonatomized* Spray Layup 18 39 51 39 138 67 19 41 54 41 148 70 20 43 58 43 158 79 21 45 61 45 168 88 22 48 64 47 178 97 23 50 68 49 189 106 24 52 71 51 200 115 25 55 75 54 211 124 26 57 78 56 221 133 27 59 82 58 233 142 28 62 86 60 244 151 29 64 90 62 256 160 30 67 94 64 269 169 31 69 97 66 281 178 32 71 102 68 295 187 33 74 105 71 308 196 34 77 112 74 322 205 35 80 118 77 336 214 36 83 127 80 354 223 37 86 136 83 371 232 38 90 146 86 390 241 39 92 156 89 408 250 40 95 166 93 427 259 41 98 176 96 446 268 42 100 187 99 466 278 43 112 192 102 477 287 44 117 202 105 495 296 45 122 212 108 513 305 46 127 221 111 532 314 47 133 232 115 551 323 48 138 242 118 571 332 49 143 252 121 590 341 50 148 263 124 609 350 * Nonatomized means any application technology in which the resin is not broken into droplets or an aerosol as it travels from the application equipment to the surface of the part. Nonatomized resin application technology includes, but is not limited to, flowcoaters, chopper flowcoaters, and pressure fed resin rollers. In addition, the device must be operated according to the manufacturer’s directions, including instructions to prevent the operation of the device at excessive spray pressures. ** The emission factors in these columns are based on a weighted average using the following assumptions: - Using the Unified Emission Factors - 20% by weight of the facility's usage of resins and gelcoats are for reinforced plastic composites production for items such as hatches and doors, but not for hulls and decks. - Using the National Marine Manufacturer Association's Factors – 80% by weight of the facility's usage of resins and gelcoats are for items such as decks and hulls. MMA emissions shall be determined by the following equations: where: Mmma = amount of MMA containing material used (in tons) Cmma = MMA content (percent/100) Other VOC emissions shall be determined by the following equation for each material unless otherwise approved by the Department in writing. These values shall be used in conjunction with the above Styrene and MMA emissions to determine total VOC: where: Mvoc = amount of VOC containing material used (in tons) Cvoc = VOC content (percent/100) Each log, where applicable, shall have attached the documentation for all chemicals captured for disposal or recycle. Documentation of each chemical captured shall use a mass balance method to determine usage/emissions (amount used minus amount collected for disposal or recycle). When determining the VOC emissions and HAP emission rates, the percent of solids in the recovered materials shall be documented and accounted for in the emission calculations, if applicable. The monthly logs shall be completed by the end of the following month. Daily logs (if required) shall be completed within 3 business days. Supporting documentation (MSDS sheets, purchase orders, etc.) shall be kept for each material, which includes sufficient information to determine VOC emissions and HAP emissions. The total HAP and total VOC emission summary, calculations, and records used to determine emissions shall be recorded in a permanent form suitable for inspection by the Department or PCDEM upon request. The logs/records shall be kept at the facility for a minimum of 5 years and made available to the Department and PCDEM upon request. [Rule 62-213.440(1)(b), F.A.C.; Construction Permit 1030223-010-AC] Comments: The facility follows the provisions of the condition. A copy of the material usage and emissions estimates log is attached to the compliance file. As an example: gelcoat atomized spray (styrene) 32% monomer material: white blending wg-1939 =7500 lbs used /2000lbs/ton x 97 (emission factor; lb/ton) = 363.75 lbs of styrene emissions A.4. This emission unit is subject to and shall comply with the applicable provisions* of the MACT standards of 40 CFR 63, Subparts A and VVVV (incorporated into Attachment B, which is a part of this permit). Note, these requirements are for only Open Molding Resin and Gel Coat Operations using Emissions Averaging Option and/or Compliant Materials Option. Requirements relating to add-on-control devices have been deleted, since this emission unit does not utilize add-on-control devices. Additionally, when demonstrating compliance with 40 CFR 63, Subpart VVVV, either the Emissions Averaging Option or the Compliant Materials Option may be used, but each time a compliance option is used, it must be used for a minimum of 12 consecutive months before switching to the other option. *An applicability reference table is included as an attachment to this permit (Attachment A). The table is based upon information provided in an email from Catalina Yachts, dated October 17, 2008. Therefore, any change in operations may change the applicable provisions and in some cases, may require a construction permit. [Rule 62-204.800(11)(b)59., F.A.C.] Comments: Catalina Yachts has always used the emissions averaging option. Additionally, the facility has not changed its operation that would require a construction permit. E.U. ID No. Brief Description -002 Wood Shop B.1. Operational Limitation. The cyclone(s) and baghouse shall be in operation whenever the sawdust producing machines are operating. Comments: This condition is not relevant to this emission unit only to EU 002. B.3. Excess emissions resulting from startup, shutdown, or malfunction shall be permitted providing (1) best operational practices to minimize emissions are adhered to and (2) the duration of excess emission shall be minimized but in no case exceed two hours in any 24 hour period unless specifically authorized by the Department for a longer duration. [Rule 62-210.700(1), F.A.C.] B.4. Excess emissions which are caused entirely or in part by poor maintenance, poor operation, or any other equipment or process failure which may reasonably be prevented during startup, shutdown, or malfunction shall be prohibited. [Rule 62-210.700(4), F.A.C.] Comments: Mike Quinn is aware of the B.3 requirement. There were no excess emissions observed during the inspection. B.5. In case of excess emissions resulting from malfunctions, each source shall notify the Air Compliance Section of the Department and PCDEM in accordance with Section 62-4.130, F.A.C. A full written report on the malfunctions shall be submitted in a quarterly report, if requested by the Department. [Rule 62-210.700(6), F.A.C.] B.6. The permittee shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of this facility which results in excess emissions; any malfunction of the air pollution control equipment; and any periods during which a continuous monitoring system or monitoring device is inoperative. [Rules 62-4.070(3) and 62-210.700, F.A.C.] Comments: The RO is aware of the B.5 and B.6 requirement. There were no instances of excess emissions reported by the facility since the last inspection performed on February 8, 2010. B.7. The permittee shall comply with Attachment D, which is the "Operation and Maintenance Plan" for the Wood Shop's emission control equipment (baghouse). The Operation and Maintenance (O&M) Plan documentation logs shall be maintained at the facility for a minimum of 5 years. At a minimum the O&M Plan shall include: The operating parameters of the pollution control device. Time table for routine maintenance of the pollution control device as specified by the manufacturer. Time table for routine periodic observations of the pollution control device sufficient to ensure proper operation. A list of the type and quantity of required spare parts for the pollution control device, which are stored on the premises. A record log, which will indicate at a minimum: When maintenance and observations were performed. What maintenance and observations were performed. Who performed said maintenance and observations. Acceptable parameter ranges for each operational check. [Pinellas County Code, Section 58-128] Comments The requirement is specific to the wood shop EU 002 and does not apply to this emission unit. § 63.5689 What parts of my facility are covered by this subpart? The affected source (the portion of your boat manufacturing facility covered by this subpart) is the combination of all of the boat manufacturing operations listed in paragraphs (a) through (f) of this section. (a) Open molding resin and gel coat operations (including pigmented gel coat, clear gel coat, production resin, tooling gel coat, and tooling resin) is the only part covered by the subpart (b) Closed molding resin operations. (c) Resin and gel coat mixing operations. (d) Resin and gel coat application equipment cleaning operations. (e) Carpet and fabric adhesive operations. § 63.5692 How do I know if my boat manufacturing facility is a new source or an existing source? a) A boat manufacturing facility is a new source if it meets the criteria in paragraphs (a)(1) through (3) of this section. (1) You commence construction of the affected source after July 14, 2000. (2) It is a major source. (3) It is a completely new boat manufacturing affected source where no other boat manufacturing affected source existed prior to the construction of the new source. (b) For the purposes of this subpart, an existing source is any source that is not a new source. Comments: The facility is an existing source. Catalina Yacht was constructed in 1970 and is a major source. § 63.5698 What emission limit must I meet for open molding resin and gel coat operations? (a) You must limit organic HAP emissions from the five open molding operations listed in paragraphs (a)(1) through (5) of this section to the emission limit specified in paragraph (b) of this section. Operations listed in paragraph (d) are exempt from this limit. (1) Production resin. (2) Pigmented gel coat. (3) Clear gel coat. (4) Tooling resin. (5) Tooling gel coat. (b) You must limit organic HAP emissions from open molding operations to the limit specified by equation 1 of this section, based on a 12-month rolling average. (c) The open molding emission limit is the same for both new and existing sources. (d) The materials specified in paragraphs (d)(1) through (3) of this section are exempt from the open molding emission limit specified in paragraph (b) of this section. (2) Pigmented, clear, and tooling gel coat used for part or mold repair and touch up. The total gel coat materials included in this exemption must not exceed 1 percent by weight of all gel coat used at your facility on a 12-month rolling-average basis. You must keep a record of the amount of gel coats used per month for which you are using this exemption and copies of calculations showing that the exempt amount does not exceed 1 percent of all gel coat used. (3) Pure, 100 percent vinylester resin used for skin coats. This exemption does not apply to blends of vinylester and polyester resins used for skin coats. The total resin materials included in the exemption cannot exceed 5 percent by weight of all resin used at your facility on a 12-month rolling-average basis. You must keep a record of the amount of 100 percent vinylester skin coat resin used per month that is eligible for this exemption and copies of calculations showing that the exempt amount does not exceed 5 percent of all resin used. Comments: The compliance report submitted semiannually lists materials used during the six-month period. § 63.5701 What are my options for complying with the open molding emission limit? You must use one or more of the options listed in paragraphs (a) through (c) of this section to meet the emission limit in §63.5698 for the resins and gel coats used in open molding operations at your facility. (a) Maximum achievable control technology (MACT) model point value averaging (emissions averaging) option. (1) Demonstrate that emissions from the open molding resin and gel coat operations that you average meet the emission limit in §63.5698 using the procedures described in §63.5710. Compliance with this option is based on a 12-month rolling average. Comments: The facility has selected point value averaging as their compliance method. § 63.5704 What are the general requirements for complying with the open molding emission limit? (a) Emissions averaging option. For those open molding operations and materials complying using the emissions averaging option, you must demonstrate compliance by performing the steps in paragraphs (a)(1) through (5) of this section. (1) Use the methods specified in §63.5758 to determine the organic HAP content of resins and gel coats. Y (2) Complete the calculations described in §63.5710 to show that the organic HAP emissions do not exceed the limit specified in §63.5698. (3) Keep records as specified in paragraphs (a)(3)(i) through (iv) of this section for each resin and gel coat. (i) Hazardous air pollutant content. (ii) Amount of material used per month. (iii) Application method used for production resin and tooling resin. This record is not required if all production resins and tooling resins are applied with nonatomized technology. (iv) Calculations performed to demonstrate compliance based on MACT model point values, as described in §63.5710. (4) Prepare and submit the implementation plan described in §63.5707 to the Administrator and keep it up to date. (5) Submit semiannual compliance reports to the Administrator as specified in §63.5764. Comments: The facility is following MACT emissions averaging procedure (see latest compliance report due semiannually for July 1, 2011 – December 31, 2011). § 63.5707 What is an implementation plan for open molding operations and when do I need to prepare one? (a) You must prepare an implementation plan for all open molding operations for which you comply by using the emissions averaging option described in §63.5704(a). (b) The implementation plan must describe the steps you will take to bring the open molding operations covered by this subpart into compliance. For each operation included in the emissions average, your implementation plan must include the elements listed in paragraphs (b)(1) through (3) of this section. (1) A description of each operation included in the average. (2) The maximum organic HAP content of the materials used, the application method used (if any atomized resin application methods are used in the average), and any other methods used to control emissions. (3) Calculations showing that the operations covered by the plan will comply with the open molding emission limit specified in §63.5698. (c) You must submit the implementation plan to the Administrator with the notification of compliance status specified in §63.5761. (d) You must keep the implementation plan on site and provide it to the Administrator when asked. (e) If you revise the implementation plan, you must submit the revised plan with your next semiannual compliance report specified in §63.5764. Comments: The facility submitted its implementation plan on August 25, 2007. The implementation plan meets the conditions of §63.5707. It was submitted with notification of compliance and is kept on-site. There have been no updates to the implementation plan since 2007. § 63.5710 How do I demonstrate compliance using emissions averaging? (a) Compliance using the emissions averaging option is demonstrated on a 12-month rolling-average basis and is determined at the end of every month (12 times per year). The first 12-month rolling-average period begins on the compliance date specified in §63.5695. (b) At the end of the twelfth month after your compliance date and at the end of every subsequent month, use equation 1 of this section to demonstrate that the organic HAP emissions from those operations included in the average do not exceed the emission limit in §63.5698 calculated for the same 12-month period. (Include terms in equation 1 of §63.5698 and equation 1 of this section for only those operations and materials included in the average.) (c) At the end of every month, use equation 2 of this section to compute the weighted-average MACT model point value for each open molding resin and gel coat operation included in the average. Comments: The emissions averaging example calculation is attached to the semi-annual report. § 63.5731 What standards must I meet for resin and gel coat mixing operations? (a) All resin and gel coat mixing containers with a capacity equal to or greater than 208 liters, including those used for on-site mixing of putties and polyputties, must have a cover with no visible gaps in place at all times. (b) The work practice standard in paragraph (a) of this section does not apply when material is being manually added to or removed from a container, or when mixing or pumping equipment is being placed in or removed from a container. (c) To demonstrate compliance with the work practice standard in paragraph (a) of this section, you must visually inspect all mixing containers subject to this standard at least once per month. The inspection should ensure that all containers have covers with no visible gaps between the cover and the container, or between the cover and equipment passing through the cover. (d) You must keep records of which mixing containers are subject to this standard and the results of the inspections, including a description of any repairs or corrective actions taken. Comments: The facility is not a resin and gel coat mixing operation § 63.5734 What standards must I meet for resin and gel coat application equipment cleaning operations? (a) For routine flushing of resin and gel coat application equipment (e.g., spray guns, flowcoaters, brushes, rollers, and squeegees), you must use a cleaning solvent that contains no more than 5 percent organic HAP by weight. For removing cured resin or gel coat from application equipment, no organic HAP content limit applies. (b) You must store organic HAP-containing solvents used for removing cured resin or gel coat in containers with covers. The covers must have no visible gaps and must be in place at all times, except when equipment to be cleaned is placed in or removed from the container. On containers with a capacity greater than 7.6 liters, the distance from the top of the container to the solvent surface must be no less than 0.75 times the diameter of the container. Containers that store organic HAP-containing solvents used for removing cured resin or gel coat are exempt from the requirements of 40 CFR part 63, subpart T. Cured resin or gel coat means resin or gel coat that has changed from a liquid to a solid. § 63.5737 How do I demonstrate compliance with the resin and gel coat application equipment cleaning standards? (a) Determine and record the organic HAP content of the cleaning solvents subject to the standards specified in §63.5734 using the methods specified in §63.5758. (b) If you recycle cleaning solvents on site, you may use documentation from the solvent manufacturer or supplier or a measurement of the organic HAP content of the cleaning solvent as originally obtained from the solvent supplier for demonstrating compliance, subject to the conditions in §63.5758 for demonstrating compliance with organic HAP content limits. (c) At least once per month, you must visually inspect any containers holding organic HAP-containing solvents used for removing cured resin and gel coat to ensure that the containers have covers with no visible gaps. Keep records of the monthly inspections and any repairs made to the covers. Comments: The facility is not a resin and gel coat application equipment cleaning operation § 63.5758 Methods for Determining Hazardous Air Pollutant Content How do I determine the organic HAP content of materials? (a) Determine the organic HAP content for each material used. To determine the organic HAP content for each material used in your open molding resin and gel coat operations, carpet and fabric adhesive operations, or aluminum recreational boat surface coating operations, you must use one of the options in paragraphs (a)(1) through (6) of this section. (5) Information from the supplier or manufacturer of the material. You may rely on information other than that generated by the test methods specified in paragraphs (a)(1) through (4) of this section, such as manufacturer's formulation data, according to paragraphs (a)(5)(i) through (iii) of this section. (i) Include in the organic HAP total each organic HAP that is present at 0.1 percent by mass or more for OSHA-defined carcinogens as specified in 29 CFR 1910.1200(d)(4) and at 1.0 percent by mass or more for other compounds. For example, if toluene (not an OSHA carcinogen) is 0.5 percent of the material by mass, you do not have to include it in the organic HAP total. (ii) If the organic HAP content is provided by the material supplier or manufacturer as a range, then you must use the upper limit of the range for determining compliance. If a separate measurement of the total organic HAP content using the methods specified in paragraphs (a)(1) through (4) of this section exceeds the upper limit of the range of the total organic HAP content provided by the material supplier or manufacturer, then you must use the measured organic HAP content to determine compliance. (iii) If the organic HAP content is provided as a single value, you may assume the value is a manufacturing target value and actual organic HAP content may vary from the target value. If a separate measurement of the total organic HAP content using the methods specified in paragraphs (a)(1) through (4) of this section is less than 2 percentage points higher than the value for total organic HAP content provided by the material supplier or manufacturer, then you may use the provided value to demonstrate compliance. If the measured total organic HAP content exceeds the provided value by 2 percentage points or more, then you must use the measured organic HAP content to determine compliance. (6) Solvent blends. Solvent blends may be listed as single components for some regulated materials in certifications provided by manufacturers or suppliers. Solvent blends may contain organic HAP which must be counted toward the total organic HAP content of the materials. When detailed organic HAP content data for solvent blends are not available, you may use the values for organic HAP content that are listed in Table 5 or 6 to this subpart. You may use Table 6 to this subpart only if the solvent blends in the materials you use do not match any of the solvent blends in Table 5 to this subpart and you know only whether the blend is either aliphatic or aromatic. However, if test results indicate higher values than those listed in Table 5 or 6 to this subpart, then the test results must be used for determining compliance. Comments: The facility determines the HAP content from the manufacturer/supplier its formulation data § 63.5761 What notifications must I submit and when? (a) You must submit all of the notifications in Table 7 to this subpart that apply to you by the dates in the table. The notifications are described more fully in 40 CFR part 63, subpart A, General Provisions, referenced in Table 8 to this subpart. (b) If you change any information submitted in any notification, you must submit the changes in writing to the Administrator within 15 calendar days after the change. Comments: : The facility does not need to submit any notifications at this time. The facility submitted it initial notification as required under Subpart VVVV. It is attached to the compliance file. § 63.5764 What reports must I submit and when? (a) You must submit the applicable reports specified in paragraphs (b) through (e) of this section. To the extent possible, you must organize each report according to the operations covered by this subpart and the compliance procedure followed for that operation. (b) Unless the Administrator has approved a different schedule for submission of reports under §63.10(a), you must submit each report by the dates in paragraphs (b)(1) through (5) of this section. (1) If your source is not controlled by an add-on control device (i.e., you are complying with organic HAP content limits, application equipment requirements, or MACT model point value averaging provisions), the first compliance report must cover the period beginning 12 months after the compliance date specified for your source in §63.5695 and ending on June 30 or December 31, whichever date is the first date following the end of the first 12-month period after the compliance date that is specified for your source in §63.5695. If your source is controlled by an add-on control device, the first compliance report must cover the period beginning on the compliance date specified for your source in §63.5695 and ending on June 30 or December 31, whichever date is the first date following the end of the first calendar half after the compliance date that is specified for your source in §63.5695. (2) The first compliance report must be postmarked or delivered no later than 60 calendar days after the end of the compliance reporting period specified in paragraph (b)(1) of this section. (3) Each subsequent compliance report must cover the applicable semiannual reporting period from January 1 through June 30 or from July 1 through December 31. (4) Each subsequent compliance report must be postmarked or delivered no later than 60 calendar days after the end of the semiannual reporting period. (5) For each affected source that is subject to permitting regulations pursuant to 40 CFR part 70 or 71, and if the permitting authority has established dates for submitting semiannual reports pursuant to 40 CFR 70.6(a)(3)(iii)(A) or 40 CFR 71.6(a)(3)(iii)(A), you may submit the first and subsequent compliance reports according to the dates the permitting authority has established instead of according to the dates in paragraphs (b)(1) through (4) of this section. (c) The compliance report must include the information specified in paragraphs (c)(1) through (7) of this section. (1) Company name and address. (2) A statement by a responsible official with that official's name, title, and signature, certifying the truth, accuracy, and completeness of the report. (3) The date of the report and the beginning and ending dates of the reporting period. (4) A description of any changes in the manufacturing process since the last compliance report. (5) A statement or table showing, for each regulated operation, the applicable organic HAP content limit, application equipment requirement, or MACT model point value averaging provision with which you are complying. The statement or table must also show the actual weighted-average organic HAP content or weighted-average MACT model point value (if applicable) for each operation during each of the rolling 12-month averaging periods that end during the reporting period. (6) If you were in compliance with the emission limits and work practice standards during the reporting period, you must include a statement to that effect. (7) If you deviated from an emission limit or work practice standard during the reporting period, you must also include the information listed in paragraphs (c)(7)(i) through (iv) of this section in the semiannual compliance report. (i) A description of the operation involved in the deviation. (ii) The quantity, organic HAP content, and application method (if relevant) of the materials involved in the deviation. (iii) A description of any corrective action you took to minimize the deviation and actions you have taken to prevent it from happening again. (iv) A statement of whether or not your facility was in compliance for the 12-month averaging period that ended at the end of the reporting period. Comments: There are three reports required by the facility. First, the compliance report due semiannually. This report is due 60 days after the end date. January 1st – June 30th, the report is due by September 1st. July 1st – December 30th, the report is due by March, 1st. Second, AOR, due March 1st for the preceding calendar year. Third, the Statement of Compliance due by March 1st. § 63.5767 What records must I keep? You must keep the records specified in paragraphs (a) through (d) of this section in addition to records specified in individual sections of this subpart. (a) You must keep a copy of each notification and report that you submitted to comply with this subpart. (b) You must keep all documentation supporting any notification or report that you submitted. (c) If your facility is not controlled by an add-on control device (i.e., you are complying with organic HAP content limits, application equipment requirements, or MACT model point value averaging provisions), you must keep the records specified in paragraphs (c)(1) through (3) of this section. Comments: Catalina Yachts has a copy of the notification of compliance, its semi-annual reports and statement of compliance on-site. § 63.5770 In what form and for how long must I keep my records? (a) Your records must be readily available and in a form so they can be easily inspected and reviewed. (b) You must keep each record for 5 years following the date that each record is generated. (c) You must keep each record on site for at least 2 years after the date that each record is generated. You can keep the records offsite for the remaining 3 years. (d) You can keep the records on paper or an alternative media, such as microfilm, computer, computer disks, magnetic tapes, or on microfiche. Comments: Air Quality during the inspection reviewed its records that have been on-site for the past 5 years. Table 1 to Subpart VVVV of Part 63—Compliance Dates for New and Existing Boat Manufacturing Facilities As specified in §63.5695, you must comply by the dates in the following table: Table 3 to Subpart VVVV of Part 63—MACT Model Point Value Formulas for Open Molding Operations1 As specified in §§63.5710(d) and 63.5714(a), you must calculate point values using the formulas in the following table: For this operation— And this application method— Use this formula to calculate the MACT model plant value for each resin and gel coat— 1. Production resin, tooling resin a. Atomized 0.014 × (Resin HAP%)2.425 b. Atomized, plus vacuum bagging with roll-out 0.01185 × (Resin HAP%)2.425 c. Atomized, plus vacuum bagging without roll-out 0.00945 × (Resin HAP%)2.425 d. Nonatomized 0.014 × (Resin HAP%)2.275 e. Nonatomized, plus vaccum bagging with roll-out 0.0110 × (Resin HAP%)2.275 f. Nonatomized, plus vacuum bagging without roll-out 0.0076 × (Resin HAP%)2.275 2. Pigmented gel coat, clear gel coat, tooling gel coat All methods 0.445 × (Gel coat HAP%)1.675 1Equations calculate MACT model point value in kilograms of organic HAP per megagrams of resin or gel coat applied. The equations for vacuum bagging with roll-out are applicable when a facility rolls out the applied resin and fabric prior to applying the vacuum bagging materials. The equations for vacuum bagging without roll-out are applicable when a facility applies the vacuum bagging materials immediately after resin application without rolling out the resin and fabric. HAP% = organic HAP content as supplied, expressed as a weight-percent value between 0 and 100 percent. [66 FR 44232, Aug. 22, 2001; 66 FR 50504, Oct. 3, 2001] Table 5 to Subpart VVVV of Part 63—Default Organic HAP Contents of Solvents and Solvent Blends As specified in §63.5758(a)(6), when detailed organic HAP content data for solvent blends are not available, you may use the values in the following table: Solvent/solvent blend CAS No. Average organic HAP content, percent by mass Typical organic HAP, percent by mass 1. Toluene 108–88–3 100 Toluene. 2. Xylene(s) 1330–20–7 100 Xylenes, ethylbenzene. 3. Hexane 110–54–3 50 n-hexane. 4. n-hexane 110–54–3 100 n-hexane. 5. Ethylbenzene 100–41–4 100 Ethylbenzene. 6. Aliphatic 140 0 None. 7. Aromatic 100 2 1% xylene, 1% cumene. 8. Aromatic 150 9 Naphthalene. 9. Aromatic naptha 64742–95–6 2 1% xylene, 1% cumene. 10. Aromatic solvent 64742–94–5 10 Naphthalene. 11. Exempt mineral spirits 8032–32–4 0 None. 12. Ligroines (VM & P) 8032–32–4 0 None. 13. Lactol spirits 64742–89–6 15 Toluene. 14. Low aromatic white spirit 64742–82–1 0 None. 15. Mineral spirits 64742–88–7 1 Xylenes. 16. Hydrotreated naphtha 64742–48–9 0 None. 17. Hydrotreated light distillate 64742–47–8 0.1 Toluene. 18. Stoddard solvent 8052–41–3 1 Xylenes. 19. Super high-flash naphtha 64742–95–6 5 Xylenes. 20. Varol®solvent 8052–49–3 1 0.5% xylenes, 0.5% ethyl benzene. 21. VM & P naphtha 64742–89–8 6 3% toluene, 3% xylene. 22. Petroleum distillate mixture 68477–31–6 8 4% naphthalene, 4% biphenyl. Table 6 to Subpart VVVV of Part 63—Default Organic HAP Contents of Petroleum Solvent Groups As specified in §63.5758(a)(6), when detailed organic HAP content data for solvent blends are not available, you may use the values in the following table: Solvent type Average organic HAP content, percent by mass Typical organic HAP, percent by mass Aliphatic (Mineral Spirits 135, Mineral Spirits 150 EC, Naphtha, Mixed Hydrocarbon, Aliphatic Hydrocarbon, Aliphatic Naptha, Naphthol Spirits, Petroleum Spirits, Petroleum Oil, Petroleum Naphtha, Solvent Naphtha, Solvent Blend.) 3 1% Xylene, 1% Toluene, and 1% Ethylbenzene. Aromatic (Medium-flash Naphtha, High-flash Naphtha, Aromatic Naphtha, Light Aromatic Naphtha, Light Aromatic Hydrocarbons, Aromatic Hydrocarbons, Light Aromatic Solvent.) 6 4% Xylene, 1% Toluene, and 1% Ethylbenzene. Table 7 to Subpart VVVV of Part 63—Applicability and Timing of Notifications As specified in §63.5761(a), you must submit notifications according to the following table: If your facility— You must submit— By this date— 1. Is an existing source subject to this subpart An initial notification containing the information specified in §63.9(b)(2) No later than the dates specified in §63.9(b)(2). 4. Is complying with organic HAP content limits, application equipment requirements; or MACT model point value averaging provisions A notification of compliance status as specified in §63.9(h) No later than 30 calendar days after the end of the first 12-month averaging period after your facility's compliance date. § 63.4 Prohibited activities and circumvention. (b) Circumvention. No owner or operator subject to the provisions of this part shall build, erect, install, or use any article, machine, equipment, or process to conceal an emission that would otherwise constitute noncompliance with a relevant standard. Such concealment includes, but is not limited to (1) The use of diluents to achieve compliance with a relevant standard based on the concentration of a pollutant in the effluent discharged to the atmosphere; (2) The use of gaseous diluents to achieve compliance with a relevant standard for visible emissions; and (3) The fragmentation of an operation such that the operation avoids regulation by a relevant standard. Comments: There has been no circumvention to the operation of the facility. This includes the HVLP spray gun applicators and hose assembly. The exhaust stack on west side of the main lamination building and small lamination storage building were both in operation with the bay doors closed. There was no evidence of circumvention to these devices. The exhaust fans remain in operation at least 2 hours after layup. There was no use of diluents, gaseous diluents or fragmentation of the operation to achieve compliance. § 63.9 Notification requirements. (h) Notification of compliance status. (1) The requirements of paragraphs (h)(2) through (h)(4)of this section apply when an affected source becomes subject to a relevant standard. (2) (i) Before a title V permit has been issued to the owner or operator of an affected source, and each time a notification of compliance status is required under this part, the owner or operator of such source shall submit to the Administrator a notification of compliance status, signed by the responsible official who shall certify its accuracy, attesting to whether the source has complied with the relevant standard. The notification shall list - (A) The methods that were used to determine compliance; (B) [Reserved.] (C) The methods that will be used for determining continuing compliance, including a description of monitoring and reporting requirements and test methods; (D) The type and quantity of hazardous air pollutants emitted by the source (or surrogate pollutants if specified in the relevant standard), reported in units and averaging times and in accordance with the test methods specified in the relevant standard; (E) An analysis demonstrating whether the affected source is a major source or an area source (using the emissions data generated for this notification); (F) A description of the air pollution control equipment (or method) for each emission point, including each control device (or method) for each hazardous air pollutant and the control efficiency (percent) for each control device (or method); and (G) A statement by the owner or operator of the affected existing, new, or reconstructed source as to whether the source has complied with the relevant standard or other requirements. (ii) The notification must be sent before the close of business on the 60th day following the completion of the relevant compliance demonstration activity specified in the relevant standard (unless a different reporting period is specified in the standard, in which case the letter must be sent before the close of business on the day the report of the relevant testing or monitoring results is required to be delivered or postmarked). For example, the notification shall be sent before close of business on the 60th (or other required) day following completion of the initial performance test and again before the close of business on the 60th (or other required) day following the completion of any subsequent required performance test. If no performance test is required but opacity or visible emission observations are required to demonstrate compliance with an opacity or visible emission standard under this part, the notification of compliance status shall be sent before close of business on the 30th day following the completion of opacity or visible emission observations. Notifications may be combined as long as the due date requirement for each notification is met. (3) After a title V permit has been issued to the owner or operator of an affected source, the owner or operator of such source shall comply with all requirements for compliance status reports contained in the source’s title V permit, including reports required under this part. After a title V permit has been issued to the owner or operator of an affected source, and each time a notification of compliance status is required under this part, the owner or operator of such source shall submit the notification of compliance status to the appropriate permitting authority following completion of the relevant compliance demonstration activity specified in the relevant standard. (5) If an owner or operator of an affected source submits estimates or preliminary information in the application for approval of construction or reconstruction required in § 63.5(d) in place of the actual emissions data or control efficiencies required in paragraphs (d)(1)(ii)(H) and (d)(2) of § 63.5, the owner or operator shall submit the actual emissions data and other correct information as soon as available but no later than with the initial notification of compliance status required in this section. (6) Advice on a notification of compliance status may be obtained from the Administrator. Comments: The facility submitted its notification of compliance status on September 25, 2007. There have been no updates to this notification. § 63.10 Recordkeeping and reporting requirements. (a) Applicability and general information. (1) The requirements of this section apply to owners or operators of affected sources who are subject to the provisions of this part, unless specified otherwise in a relevant standard. (2) For affected sources that have been granted an extension of compliance under subpart D of this part, the requirements of this section do not apply to those sources while they are operating under such compliance extensions. (3) If any State requires a report that contains all the information required in a report listed in this section, an owner or operator may send the Administrator a copy of the report sent to the State to satisfy the requirements of this section for that report. (4)(ii) After a State has been delegated the authority to implement and enforce recordkeeping and reporting requirements established under this part, the owner or operator of an affected source in such State subject to such requirements shall submit reports to the delegated State authority (which may be the same as the permitting authority). In addition, if the delegated (permitting) authority is the State, the owner or operator shall send a copy of each report submitted to the State to the appropriate Regional Office of the EPA, as specified in paragraph (a)(4)(i) of this section. The Regional Office may waive this requirement for any reports at its discretion. (5) If an owner or operator of an affected source in a State with delegated authority is required to submit periodic reports under this part to the State, and if the State has an established timeline for the submission of periodic reports that is consistent with the reporting frequency(ies) specified for such source under this part, the owner or operator may change the dates by which periodic reports under this part shall be submitted (without changing the frequency of reporting) to be consistent with the State’s schedule by mutual agreement between the owner or operator and the State. For each relevant standard established pursuant to section 112 of the Act, the allowance in the previous sentence applies in each State beginning 1 year after the affected source’s compliance date for that standard. Procedures governing the implementation of this provision are specified in § 63.9(i). (6) If an owner or operator supervises one or more stationary sources affected by more than one standard established pursuant to section 112 of the Act, he/she may arrange by mutual agreement between the owner or operator and the Administrator (or the State permitting authority) a common schedule on which periodic reports required for each source shall be submitted throughout the year. The allowance in the previous sentence applies in each State beginning 1 year after the latest compliance date for any relevant standard established pursuant to section 112 of the Act for any such affected source(s). Procedures governing the implementation of this provision are specified in § 63.9(i). (7) If an owner or operator supervises one or more stationary sources affected by standards established pursuant to section 112 of the Act (as amended November 15, 1990) and standards set under part 60, part 61, or both such parts of this chapter, he/she may arrange by mutual agreement between the owner or operator and the Administrator (or the State permitting authority) a common schedule on which periodic reports required by each relevant (i.e., applicable) standard shall be submitted throughout the year. The allowance in the previous sentence applies in each State beginning 1 year after the stationary source is required to be in compliance with the relevant section 112 standard, or 1 year after the stationary source is required to be in compliance with the applicable part 60 or part 61 standard, whichever is latest. Procedures governing the implementation of this provision are specified in § 63.9(i). (b) General recordkeeping requirements. (1) The owner or operator of an affected source subject to the provisions of this part shall maintain files of all information (including all reports and notifications) required by this part recorded in a form suitable and readily available for expeditious inspection and review. The files shall be retained for at least 5 years following the date of each occurrence, measurement, maintenance, corrective action, report, or record. At a minimum, the most recent 2 years of data shall be retained on site. The remaining 3 years of data may be retained off site. Such files may be maintained on microfilm, on a computer, on computer floppy disks, on magnetic tape disks, or on microfiche. [§§63.567 and 63.5770 specify additional recordkeeping requirements.] (2) The owner or operator of an affected source subject to the provisions of this part shall maintain relevant records for such source of – (xii) Any information demonstrating whether a source is meeting the requirements for a waiver of recordkeeping or reporting requirements under this part, if the source has been granted a waiver under paragraph (f) of this section; (xiv) All documentation supporting initial notifications and notifications of compliance status under § 63.9. (d) General reporting requirements. (1) Not-withstanding the requirements in this paragraph or paragraph (e) of this section, the owner or operator of an affected source subject to reporting requirements under this part shall submit reports to the Administrator in accordance with the reporting requirements in the relevant standard(s). [§ 63.5764 specifies additional reporting requirements.] (f) Waiver of recordkeeping or reporting requirements. (1) Until a waiver of a recordkeeping or reporting requirement has been granted by the Administrator under this paragraph, the owner or operator of an affected source remains subject to the requirements of this section. (2) Recordkeeping or reporting requirements may be waived upon written application to the Administrator if, in the Administrator’s judgment, the affected source is achieving the relevant standard(s), or the source is operating under an extension of compliance, or the owner or operator has requested an extension of compliance and the Administrator is still considering that request. (3) If an application for a waiver of record-keeping or reporting is made, the application shall accompany the request for an extension of compliance under § 63.6(i), any required compliance progress report or compliance status report required under this part (such as under § 63.6(i) and § 63.9(h)) or in the source’s title V permit, or an excess emissions and continuous monitoring system performance report required under paragraph (e) of this section, whichever is applicable. The application shall include whatever information the owner or operator considers useful to convince the Administrator that a waiver of recordkeeping or reporting is warranted. (4) The Administrator will approve or deny a request for a waiver of recordkeeping or reporting requirements under this paragraph when he/she - (i) Approves or denies an extension of compliance; or (ii) Makes a determination of compliance following the submission of a required compliance status report or excess emissions and continuous monitoring systems performance report; or (iii) Makes a determination of suitable progress towards compliance following the submission of a compliance progress report, whichever is applicable. (5) A waiver of any recordkeeping or reporting requirement granted under this paragraph may be conditioned on other recordkeeping or reporting requirements deemed necessary by the Administrator. (6) Approval of any waiver granted under this section shall not abrogate the Administrator’s authority under the Act or in any way prohibit the Administrator from later canceling the waiver. The cancellation will be made only after notice is given to the owner or operator of the affected source. Comments: The facility has met its reporting and recordkeeping requirements since 2007. ATTACHMENT C Standard Operation Procedures for Cleanup Solvent Usage Catalina Yachts, Morgan Division Standard Operating Procedures for Cleanup Solvent Usage The cleanup solvents at Catalina Yachts, Morgan Division are used for a variety of different operations. The solvents are used for brush and roller cleaning, spray gun cleaning, tool cleaning, and product wipe down. The following procedures will be utilized to ensure at least a 40% initial solvent capture efficiency. 1. The brushes and rollers are soaked in a closed solvent container until clean. Thesolvent is re-used several times until it is no longer usable as a cleaning agent. The spent solvent is then place in drums to be recycled. The approximate capture efficiency of this operation is roughly 90%. 2. The gel-coat and chopper spray guns are soaked in a closed solvent container for initially cleaning. Then some solvent is sprayed through the guns into a closed capture container. This spent solvent is also stored for recycling. The capture efficiency of this operation is around 50%. 3. Solvent is also used to clean boats prior to shipping. Solvent dampened rags and brushes are used in this cleaning process. The solvent is stored in closed safety cans during this process. The solvent capture rate of this operation is unknown, but assumed small. 4. All solvents shall be kept in closed containers. All solvent dampened rags shall be stored in closed containers. The net overall initial solvent capture rate from these operations should be at least 40%. Comments: Brushes, rollers, gun heads and tips are soaked in closed containers. The facility does not soak the gel-coat or chopper spray guns. Solvent is used to clean boats and is kept in closed red safety cans. All solvent rags are stored in closed containers |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no pollution prevention activities since the last inspection on February 8, 2010. |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030223 | OWNER Catalina Yachts, Morgan Division | FACILITY NAME |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE June 25, 2012 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE February 8, 2010 |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | Received 3/1/12 and reviewed 3/12/12 |
| DONE N/A | Statement of compliance | Received 3/1/12 and reviewed 3/5/12 |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual | Subpt VVVV ,SAMs reports rec 3/1/12 rev 3/5/12 |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| June 25, 2012 | June 25, 2012 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs | Copy of usage and emission estimates attached to comp file |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) |  |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.