| 1030223 002 70974 |
| --- |
| FACILITY: Catalina Yachts, Morgan Division | PERMIT ID: 27 |
|  | DISTRICT: Southwest |
| ADDRESS: 7200 Bryan Dairy Road | CONTACT PHONE: |
| Largo, FL | 727-544 6681 |
| ARMS NO: 1030223 002 | PERMIT NO: | Expiration Date: 4/1/2009 Renewal Date: 10/3/2008 |
|  | 1030223-007-AV |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Woodshop consisting of The sawdust producing machines are vented with individual ducting systems through 1 of 2 cyclones that exhaust to a central baghouse, which has 3 exhaust stacks. Does not include small hand held equipment |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | February 8, 2010 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Michael Quinn? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: mike@catalinayachts.com |
| 4. | Is the facility contact still: Michael Quinn? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: mike@catalinayachts.com |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Section II. Facility-wide Conditions. This permit or a copy thereof shall be kept at the work site of the permitted activity. [APPENDIX TV-4, TITLE V CONDITION 12(12)] Comments: Comments: reviewed on-site permit 2. General Pollutant Emission Limiting Standards. Objectionable Odor Prohibited. No person shall cause, suffer, allow, or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. [Rule 62-296.320(2), F.A.C., Pinellas County Code, Section 58-178; AC52-262880] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor detected- None ; Wind direction – E/10 mph Upwind odor detected-None No odors detected around the perimeter of the facility. All doors of the lamination bay were closed. All 11 ventilation fans were operating including the 4 fans on the north side, the 4 fans on the south and the 3 operating on the roof. 3. General Particulate Emission Limiting Standards. General Visible Emissions Standard. Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1. & 4., F.A.C.] Comments: No particulate emissions observed 4. Prevention of Accidental Releases (Section 112(r) of CAA). If required by 40 CFR 68, the permittee shall submit to the implementing agency: A. A risk management plan (RMP) when, and if, such requirement becomes applicable; and B. Certification forms and/or RMPs according to the promulgated rule schedule. [40 CFR 68] Comments: Does not apply to this condition 5. Insignificant Emissions Units and/or Activities. Appendix I-1: List of Insignificant Emissions Units and/or Activities, is a part of this permit. [Rules 62-213.440(1), 62-213.430(6) and 62-4.040(1)(b), F.A.C.] Comments: There are no insignificant emission units as a part of this permit 6. General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds or organic solvents without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The permittee shall comply with the following: A. Each building's fans and/or ventilation systems shall be operating whenever usage of materials containing VOC/OS's occurs and shall remain operating for at least 1 hour after the usage has been completed. B. The capture rate of miscellaneous other VOC/OS emissions clean-up shall not be less than 40%. Compliance with the 40% capture rate shall be considered satisfied by complying with Attachment No. 1 – Standard Operating Procedures for Clean-up Solvent Usage. NOTE – When determining the miscellaneous solvent emission rate(s), the percent of solids in the recovered solvents shall be documented and accounted for in the emission calculations. C. All materials containing VOC/OS's shall be stored in closed original containers and/or in small automatic closing safety cans. D. Clean-up solvent washings shall be directed into containers that prevent evaporation into the atmosphere. E. All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions, and spills of materials containing VOC/OS's. F. Work practice controls shall include limiting the amount of clean-up solvents issued to employees and employees shall use gloves whenever handling resins. G. Immediately attend to all spills of materials containing VOC/OS's as appropriate. [Rule 62-296.320(1)(a), F.A.C. and AC52-262880] Comments: An inspection of each work/lamination station (8 in operation during the inspection) revealed that: Based on observation, brushes and rollers are soaked in closed solvent Based on observation and interview of workers, the gel-coat and chopper spray guns are soaked in a closed solvent container Based on observation, solvent is used to clean boats prior to shipping All solvents observed, MMA, resin and gelcoat are stored in closed containers Some of the solvent materials are stored in small safety cans Spray equipment, rollers observed did not leak Mr. Quinn stated that solvent clean-up is performed with gloves Further stated, the procedure is to immediately attend to all spills based on the O&M Plan 7. Emissions of Unconfined Particulate Matter. Pursuant to Rules 62-296.320(4)(c)1., 3., & 4., F.A.C., reasonable precautions to prevent emissions of unconfined particulate matter at this facility include the following requirements (see Condition No. 57 of Appendix TV-4, Title V Conditions): A. The north wall of the grinding building shall contain a filter with the exhaust fan. B. Frequent cleanings and sweeping of floors, equipment, and finished products. C. Supervisory inspections during operation(s) to ensure that all activities are being conducted in a manner to minimize emissions. D. Application of water to paved and unpaved areas accommodating vehicular traffic, as necessary. E. Enclosure or covering of activities or equipment where necessary. As an indicator that adequate control measures/practices are adequate, visible emissions from the property line, exhaust fans, doors, and vents shall not exceed 5% opacity. If this level is exceeded, it shall not be considered a violation in and of itself, but may allow the Department to require additional controls or work practices. [Rule 62-296.320(4)(c)2., F.A.C. and AC52-262880] Comments: No unconfined emissions 9. Statement of Compliance. The annual statement of compliance pursuant to Rule 62-213.440(3)(a)2., F.A.C., shall be submitted to this office and the EPA within 60 (sixty) days after the end of the calendar year using DEP Form No. 62-213.900(7), F.A.C. [Rules 62-213.440(3) and 62-213.900, F.A.C.] {Permitting Note: This condition implements the requirements of Rules 62-213.440(3)(a)2. and 3., F.A.C. (see Condition No. 51 of Appendix TV-4, Title V Conditions)} Comments: The latest Annual Statement of Compliance was submitted on 2/23/09 Essential Potential to Emit (PTE) Parameters B.1. Operational Limitation. The cyclone(s) and baghouse shall be in operation whenever the sawdust producing machines are operating. [Rule 62-210.200(PTE), F.A.C.] Comments: No dust emissions were observed Local Applicable Requirements B.3. The permittee shall comply with Attachment No. 2, which is the "Operation and Maintenance Plan" for the Wood Shop's emission control equipment (baghouse). The Operation and Maintenance (O&M) Plan documentation logs shall be maintained at the facility for a minimum of 5 years. At a minimum the O&M Plan shall include: A. The operating parameters of the pollution control device. B. Time table for routine maintenance of the pollution control device as specified by the manufacturer. C. Time table for routine periodic observations of the pollution control device sufficient to ensure proper operation. D. A list of the type and quantity of required spare parts for the pollution control device, which are stored on the premises. E. A record log, which will indicate at a minimum: 1. When maintenance and observations were performed. 2. What maintenance and observations were performed. 3. Who performed said maintenance and observations. 4. Acceptable parameter ranges for each operational check. [Pinellas County Code, Section 58-128] Comments: facility meets A-E of this condition Excess Emissions B.4. Excess emissions resulting from startup, shutdown, or malfunction shall be permitted providing (1) best operational practices to minimize emissions are adhered to and (2) the duration of excess emission shall be minimized but in no case exceed two hours in any 24 hour period unless specifically authorized by the Department for a longer duration. [Rule 62-210.700(1), F.A.C.] Comments: No excess emissions reported during the compliance year due to startup, shutdown or malfunction B.5. Excess emissions which are caused entirely or in part by poor maintenance, poor operation, or any other equipment or process failure which may reasonably be prevented during startup, shutdown, or malfunction shall be prohibited. [Rule 62-210.700(4), F.A.C.] Comments: No excess emissions reported during the compliance year due to poor maintenance or poor operation B.6. In case of excess emissions resulting from malfunctions, each source shall notify the Air Compliance Section of the Department and PCDEM in accordance with Section 62-4.130, F.A.C. A full written report on the malfunctions shall be submitted in a quarterly report, if requested by the Department. [Rule 62-210.700(6), F.A.C.] Comments: Not applicable during the compliance year. No excess emissions B.7. The permittee shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of this facility which results in excess emissions; any malfunction of the air pollution control equipment; and any periods during which a continuous monitoring system or monitoring device is inoperative. [Rules 62-4.070(3) and 62-210.700, F.A.C.] Comments: Not applicable during the compliance year. No excess emissions B.8. When the Department, after investigation, has good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department Rule or in a permit issued pursuant to those rules is being violated, it may require the owner or operator of the emission unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and to provide a report on the results of said tests to the Department. [62-297.310(7)(b), F.A.C.] Comments: A compliance test was not necessary during the compliance year |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No not applicable ; dust collector last year was 0% opacity Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030223 | OWNER Catalina Yachts, Morgan Division | FACILITY NAME |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE March 9, 2010 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | Received 3/15/09 Reviewed 4/15/09 |
| DONE N/A | Statement of compliance | 09’ SOCR reviewed 4/30/09 |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual | Reviewed 9/15/09 |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 2/8/10 | 3/9/10 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs | Copy of the monthly totals (Nov, 09’) |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) | Usage rate of resins and gel coat supplied |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record