| 1030240 005 57346 |
| --- |
| FACILITY: Cox Target Media, Inc. | PERMIT ID: 2709 |
| Val-Pak Direct Marketing Systems, Inc. | DISTRICT: Southwest |
| ADDRESS: 8605 Largo Lakes Drive | CONTACT PHONE: |
| Largo, FL | 727-399-3098 |
| ARMS NO: 1030240 005 | PERMIT NO: | EXPIRATION DATE: |
|  | 1030240-012-AF | 5/7/08 |
| EMISSION UNIT DESCRIPTION : Line 4: Harris Graphics Model M-110 lithographic heatset press (line speed of 1,000 feet/minute) with a TEC Systems CP-215 natural gas fired dryer with a heat input rate of 2.63 MMBtu/hour, which exhausts to a TEC Systems Quantum 2000 catalytic oxidizer. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | 15 February 2007 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review | ( | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry | ( | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: John Chidlow? | ( | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: John Chidlow? | ( | Yes |  | No |
|  | Comments: |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: The facility ( did □ did not have a copy of the permit on-site. Section A. FACILITY WIDE CONDITIONS: Emission and Operation Limitations A4. HAP Emissions – Emissions of Hazardous Air Pollutants (HAPs) from this facility shall not exceed 8.0 tons in any 12 consecutive month period of any individual HAP, nor 16.0 tons in any 12 consecutive month period of any combination of HAPs (i.e. total HAPs). [Rule 62-210.200 (203)(Potential to Emit), F.A.C., as requested by permittee to stay below the Title V major level; permit 1030240-011-AC] (HAP Limitation Compliance Note: Compliance with the facility-wide HAP limitations of Specific Condition No. A4. above shall be determined from calculation of HAPs based Specific Condition Nos. B20., C3., and Footnotes.) Comments: The highest reported emissions were 0.0000525 tons total HAP/12-month period at the end of the month of January 2007. Reviewed records for the months of January 2006 thru and including January 2007. A5. Fugitive VOC (Volatile Organic Compound) Emissions - All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials. This includes draining all VOC containing fluids into closed containers during lengthy periods of time when a press line is not operating and the catalyst bed is allowed to cool. [Rule 62-296.320(1), F.A.C.] (VOC Permitting Note: There is no separate facility-wide VOC limit. Rather there are separate VOC limits for the heat-set and cold-set areas (see Specific Condition Nos. B1. and C1.) Total facility allowable VOC emission rate is the sum of these two limits: 80.17 + 10.83 = 91.0 TPY).) Comments: The highest 12 mos. running cumulative total was recorded as the end of the month of June 2006, when it was 3.87 tons of VOC’s. A6. Objectionable Odors - The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rule 62-296.320(2), F.A.C.: and Pinellas County Code, Section 58-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- none; Wind direction – NW Upwind odor level detected- None. Recordkeeping Requirements A7. Tons/Year Limitations - Compliance with “tons/year" emission limitations in this permit shall be based on any 12 consecutive month period total, or a Department approved optional recordkeeping scheme (e.g., 13 - "4-week" periods per year). [Rule 62-4.070(3), F.A.C., permit 1030240-011-AC] Comments: Emissions were recorded on a monthly basis and A running 12 mos. cumulative was recorded for VOC’s and HAP’s. A8. VOC/HAP Records - Supporting documentation ("As Supplied", "As Applied" sheets, MSD (Material Safety Data) sheets, EPA data sheets, purchase orders, etc.) shall be kept for each ink and VOC/OS (organic solvent)/HAP containing material utilized at the facility, including "non-VOC" solutions in use. This documentation shall include sufficient information to: provide reasonable assurance that any "non-VOC" solution/solvent in use at the facility indicates no VOC content based on an EPA Method 24 or 24A test; b. provide the basis for any electronic recordkeeping used for reporting emissions limitations or utilization rates required in Specific Conditions of this permit. [Rule 62-4.070(3), F.A.C., and Pinellas County Code, Section 58-90] Comments: Supporting Documentation for the VOC and HAPS was available, including” as applied” sheets, “as supplied” sheets, MSD’s and purchase orders. A9. Non-VOC Material Substitution - The substitution of a non-VOC containing material* for an existing production material containing VOC shall not require recordkeeping, however, a log entry is required at the time of material substitution stating that a "non-VOC solution/solvent has been substituted for (specify material). [Rule 62-4.070(3) and Pinellas County Code, Section 58-90] (*Permitting Note: A "non-VOC" material is defined as a material which indicates no VOC content per an EPA Method 24 or 24A test.) Comments: Mr. Chidlow stated that there had not been substitutions-of non VOC containing materials for an existing material containing VOC’s. A10. Record Retention - All recordkeeping information, supporting documentation, and all compliance test information required by this permit shall be retained at the facility for the most recent two year period and shall be made available to the Florida Department of Environmental Protection (the Department) or the Air Quality Division of the Pinellas County Department of Environmental Management (PCDEM), upon request. [Rule 62-4.070(3),F.A.C., and Pinellas County Code, Section 58-90] Comments: Records were available going back 2 years, for emission unit 005 ( Press Line 4) that was installed in January of 2005. Records were available going back let 2002 for EU numbers 001 and 003. Reporting Requirements A11. Annual Operating Report AOR - The permittee shall submit to the Air Program of the Southwest District Office of the Department `ort for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. Total HAP emissions and emissions of individual HAPs that equal or exceed 0.1 tons/year shall be reported in the AOR. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be submitted. [Rule 62-210.370(3), F.A.C.; Pinellas County code Subsection 58-90(3) & (9)] Comments: The annual operating report for calendar year 2005 was submitted on 2/28/06. A12. Process Changes - the permittee shall report any proposed process changes, including, but not limited to, (a) any proposed significant change of VOC/OS species, or (b) any proposed increase in the production rate, to the Air Programs of the Southwest District Office of the Department and the PCDEM for proper processing. Any physical change in, change in the method of operation of, or addition to a stationary source or facility, which increases the actual emissions of any air pollutant may be considered a "Modification". [Rule 62-210.300, F.A.C.] Comments: There were no changes or modifications to the facility. A13. Use of New HAP Containing Materials - The Air Permit Section of the Department and the Air Quality Division of the PCDEM shall be notified in writing at least 7 days prior to the planned use of any new material(s) containing a HAP not previously identified and used, unless otherwise authorized by the Department or the PCDEM. [Rule 62-4.070(3), F.A.C.; permit 1030240-009-AC] Comments: Mr. Chidlow notified the AQD and the FDEP in November of 2006 in advance of the use of a material that would decrease the amount of HAPS emitted and would create and insignificant increase in VOCs, i.e. 0.024 tons per year. A14. Changes to Air Management System - Changes to the air management systems of this facility (including air conditioning and other air handling equipment) may render the assumed VOC capture efficiencies ineffective. The PCDEM shall be notified when a change is contemplated, or when any portion of an existing air management system is damaged in any manner. This notification shall include discussion of any potential impact on VOC emissions. [Rule 62-4.070(3), F.A.C.; permit 1030240-009-AC] Comments: Mr. Chidlow stated that there bad not been any changes lot the Air Handling System and I did not observe anything in the System that looked new or different from years past. Section B. HEAT-SET LITHOGRAPHIC PRESS LINES CONDITIONS (Note: (#) indicates a footnote that appears at the end of the permit beginning on page 16). Heat-Set Press Lines Emission Limitations B1. VOC Emissions - The sum total volatile organic compound (VOC) emissions from the Heat-Set Lithographic Press Operations Line Nos. 1, 2 3, and 4 shall not exceed 80.17 tons in any 12 consecutive month period (1). This value includes the stack and fugitive emissions from the printing inks, fountain solution, plant-wide wash solutions(2), natural gas combustion (0.22 TPY(3)), and miscellaneous heat-set fugitives (considered for the purposes of this permit to be a maximum of 1.0 TPY or less). [Rule 62-296.320(1)(a), F.A.C.; permit 1030240-011-AC] Comments: The highest reported emissions were 24.39 tons of voc’s for both heat set Emission Units combined, as a 12 mos. running cumulative total at the end of the month of December 2006. B2. Visible Emissions (VE) - Visible emissions from each of the catalytic oxidizer exhaust stacks shall not exceed 5% opacity except that visible emissions not exceeding 20% opacity are allowed for up to three minutes in any one hour period. [Rule 62-296.401(1)(a), F.A.C.] B13. VE Test Method - Compliance with the visible emission limitation of Specific Condition No. B2. shall be demonstrated using DEP Method 9. The visible emissions test shall be conducted by a certified observer and be a minimum of sixty (60) minutes in duration and include the period during which the highest opacity emissions can reasonably be expected to occur. During any year in which the VOC destruction efficiency stack test on the catalytic oxidizer is required, the visible emission test shall be conducted in association with the VOC stack test (see condition below). [Rules 62-4.070(3), and 62-297.310(4)(a)(2), F.A.C.; permit 1030240-011-AC] Comments: The last DEP Method 9 visible emissions test, conducted on 2/10/06 demonstrated an opacity of 0.0%. An AQD VE test was performed during this site visit □ Yes or ( No. Heat-Set Press Lines Operational Limitations/Requirements B3. Material Usage - In order to insure compliance with the allowable annual emission rate in Specific Condition No. B1., the following material usage limitations (totals for all heat-set press lines combined) shall apply for any 12 consecutive month period: a. Heat-Set Printing Inks: 1,060,000 lbs; Heat-Set Press Fountain Solution*: 7,500 gallons; (*The permittee shall not use a VOC solution to dilute "Fountain Solution".) c. Wash Solutions(2) (plant-wide): 17,500 gallons (less disposal and reuse). [Rules 62-4.070(3) and 62-296.320(1)(a), F.A.C.; permit 1030240-011-AC] Comments: The total lbs of ink in both heat setlines was 782,640 lbs as a running 12 mos. cumulative total at the end of the month of January 2007. B4. Catalytic Oxidizer Operation Requirement and Outage Reporting - No heat-set press line shall operate unless the associated catalytic oxidizer (Quantum 4000 catalytic oxidizer for Heat-set Press Line Nos. 1, 2, and 3; Quantum 2000 catalytic oxidizer for Heat-set Press Line No. 4) is operational and the catalyst bed gas inlet temperature is between 600o F, and 1,100o F, except as stipulated below. There shall be an automatic cutoff device which shall not allow any heat-set press to operate unless the applicable catalytic oxidizer is operating at a temperature above 600(F. However, in the event of a catalytic oxidizer outage/malfunction, the permittee shall be allowed to operate the press lines without the catalytic oxidizer in service for a period to time not to exceed 48 hours. There shall be a maximum of two such 48 hour periods in any 12 month period. a. The following shall apply during these periods of catalytic oxidizer outage: (1) the permittee shall take reasonable steps to minimize VOC emissions visible emissions and odors; (2) PCDEM shall be notified of the problems with the catalytic oxidizer immediately (not including weekends or holidays) of the occurrence (Rule 62-4.130, F.A.C.); (3) PCDEM shall be informed of the steps taken to correct the problem and anticipated time frame to correct the problem; and (4) PCDEM shall be advised when the catalytic oxidizer was brought back on line. b. Documentation of the catalytic oxidizer outage shall be keep as follows: the identification of the catalytic oxidizer and the time of the start of the breakdown; reason for breakdown, and the steps taken to correct the problem; (3) the date and time PCDEM was notified and to whom reported; (4) detailed information on the quantity of each ink and fountain solution used during the outage period, and (5) the time catalytic oxidizer was brought back on line. The estimated amount of VOC emitted during the outage period shall be calculated and included in the monthly VOC emission records and the oxidizer outage report. The PCDEM shall be provided with a detailed written report on the outage, including the information in b. above, within seven working days. [Rules 62-4.070(3), 62-4.130, 62-210.650, 62-210.700(4), F.A.C.; permits 1030240-009-AC and 1030240-011-AC] Comments: Reviewed records for the months of January 2006 thru January 2007. A copy of the records are attached as an example of the record format. B5. Heat-Set Press Line Nos. 1, 2, and 3 Catalytic Oxidizer Destruction Efficiency - The VOC destruction efficiency of the Quantum 4000 catalytic oxidizer shall not fall below 90% removal. [Rules 62-210.650, 62-296.320(1)(a), and 62-212.300, F.A.C.; permit 1030240-009-AC] Comments: The catalytic destructions efficiency was 94.9% during the stack test of 2003. B6. Heat-Set Press Line No. 4 Catalytic Oxidizer Destruction Efficiency - The VOC destruction efficiency of the Heat-set Lithographic Press Printing Line No. 4 Quantum 2000 catalytic oxidizer shall not fall below 90% removal. [Rules 62-210.650, 62-296.320(1)(a), and 62-212.300, F.A.C.; permit 1030240-011-AC] Comments: In a test performed on March 2nd, 2005, the Quantum 2000 Incinerator showed a destruction efficiency of 97%. B7. Heat-Set Press Line Nos. 1, 2 and 3 Catalytic Oxidizer Exhaust Stack Flow Rate - The gas flow rate from the exhaust stack of the Quantum 4000 catalytic oxidizer shall be at least 2,700 scfm when operating two or three heat-set lithographic presses. There shall be no device on the exhaust stack which will interfere with the upward flow of the exhaust gases. [Rules 62-210.650, 62-296.320(1)(a), 62-4.070(3) F.A.C.; permit 1030240-009-AC] Comments: The gas flow rate from the exhaust of the Quantum 4,000 catalytic oxidizer was 4,249 SCFM during the last stack test in 2003. B8. Heat-Set Press Line No. 4 Catalytic Oxidizer Exhaust Stack Flow Rate - The gas flow rate from the exhaust stack of the Heat-set Lithographic Press Printing Line No. 4 Quantum 2000 catalytic oxidizer shall be at least 1,000 scfm when the press line is in operation. There shall be no device on the exhaust stack which will interfere with the upward flow of the exhaust gases. [Rules 62-210.650, 62-296.320(1)(a)(Circumvention), and 62-4.070(3) F.A.C.; permit 1030240-011-AC] Comments: The gas flow rate from the exhaust of the Quantum 2,000 catalytic oxidizer was 1,121 SCFM during the last stack test in 2003. B9. Catalytic Oxidizer O&M Plan - The catalytic oxidizers shall be operated and maintained in accordance with the applicable Operation and Maintenance (O&M) Plans (see Attachments 2 and 3) attached to this permit, or a later issue of the O&M plan approved by the Air Quality Division of the PCDEM. The O&M plan shall meet the requirements of Pinellas County Code, Section 58-128, and shall include at a minimum: a. the operating parameters for the catalytic oxidizer; b. the timetable for routine catalytic oxidizer maintenance; c. the timetable for routine periodic observations of the pollution control device sufficient to insure proper operation; d. a list of the type and quantity of catalytic oxidizer spare parts which are stored on the premises; a record log which indicates, at a minimum: when catalytic oxidizer maintenance and observations were performed; what catalytic oxidizer maintenance and observations were performed; who performed said maintenance and observations; 4. acceptable parameter ranges for each operational check. The O&M plan documentation logs shall be maintained at the facility for a minimum of the most recent two year period and shall be made available to Air Quality Division of the PCDEM, or the Department, upon request. [Rule 62-4.070(3), F.A.C., and Pinellas County Code, Sec. 58-128; construction permits 1030240-009-AC and 1030240-011-AC] Comments: The facility was in compliance with its O and M plan and items a. thru e. B10. Exhaust Flow - Whenever practical, the exhaust air flow through all the dryers shall be maintained during periods when Wash Solution(2) is being utilized. [Rule 62-4.070(3), F.A.C.] Comments: The exhaust air flow through all the dryers was maintained at all times, including periods when Wash Solution was being utilized. B11. Bypass Stacks - The permittee shall not utilize a bypass stack which vents a dryer to the atmosphere at any time while ink is being applied. If ink is not being applied and best operational practices to minimize emissions are adhered to, then it is permitted to utilize a bypass stack only during periods of start up, shutdown, or malfunction. The permittee shall keep records of the date and time of commencement and completion of each time period that a bypass stack is either, utilized for more than 5 minutes in any one hour time period, or b. manually selected by the press operator for any amount of time. The records shall include the reason for utilization of the bypass stack. They shall be maintained at the facility for a minimum of the most recent two-year period and made available to Air Quality Division of the PCDEM, or the Department, upon request. [Rules 62-210.700 & 62-4.070(3), F.A.C.; permits 1030240-009-AC & 1030240-011-AC] Comments: The presses have an automatic lockout system that shuts them down if and when the By Pass Stack opens. As a result of the lockout, ink is not applied but to avoid accumulation of gases in the Dryers, the fans continue working as a safety measure to avoid explosive levels of VOC’s. Heat-Set Compliance Testing Requirements B12. VE Testing - In order to document compliance with Specific Condition No. B2., the permittee shall test each of the catalytic oxidizer stack outlets for visible emissions annually within 60 days prior to the base test date of February 12 of each year*. A copy of the test data shall be submitted to the Air Quality Division of the PCDEM and the Air Compliance Section of the Southwest District Office of the Department within 45 days of testing. [Rules 62-297.310(7)(a)4. and 62-297.310(8), F.A.C.] (* VE Testing Note: During the year in which the VOC destruction efficiency stack test on the catalytic oxidizer is required, the annual visible emission test shall be conducted in association with the stack test (see Condition B14. below).) Comments: The facility notified the AQD with 15 days advance notice of VF testing that was scheduled for February 1st, 2007. B14. Catalytic Oxidizer Destruction Efficiency Testing - Within the six (6) month period prior to the expiration date of this permit and prior to submittal of the operation permit renewal application (see Specific Condition No. D1.), the permittee shall test the catalytic oxidizer stacks inlets and outlets to determine VOC destruction efficiency and document compliance with Specific Condition Nos. B5. through B8. A Method 9 VE test shall be performed simultaneously with one of the three Method 25/25A runs required in order to determine VOC destruction efficiency. A copy of the test data shall be submitted to the Air Quality Division of the PCDEM and the Air Compliance Section of the Southwest District Office of the Department within 45 days of testing. [Rule 62-297.310, F.A.C.] B15. Catalytic Oxidizer VOC Destruction Efficiency Test Methods - Compliance with the emissions and testing requirements of Specific Condition Nos. B1., B5., B6., B7., B8., and B14. shall be demonstrated using EPA Methods 1, 2, 3, 4, and 25 or 25A (see Specific Condition No. B14.). [Rule 62-297.401, F.A.C.] Comments: I reminded Mssrs. Chidlow and Allen of the requirement to test the incinerator 6 months prior to the expiration date of this permit. B19. Testing Notification - The permittee shall notify the Air Quality Division of the PCDEM at least 15 days prior to the date on which each formal compliance test is scheduled, of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating each test. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: I read the permit condition requirement above to Messrs. Chidlow and Allen Heat-Set Recordkeeping Requirements B20. VOC/ HAP Material Usage and Emission Records(1); - In order to document compliance with the requirements of Specific Condition Nos. B1. (Heat-set (VOC limit), B3. (material usage limits), and A4. (Facility-wide HAP limit), VOC/HAP containing material usage and emission records shall be maintained. In order to account for their different catalytic oxidizer control efficiencies, separate material usage and emission entries shall be kept for materials used on EU 001 (Heat-set Press Line Nos. 1, 2 and 3) and for materials used on EU 005 (Heat-set Lithographic Printing Line No. 4). These records shall be updated at least monthly and shall be completed by the end of the following month. The records shall include the following: a. the facility name, facility ID No. (1030240), and emission unit name and emission unit number (i.e., Heat-set Press Lines, EU’s 001/005); b. the month and year; c. the quantity of "As Applied" ink (by name or identification number) used, indicating the amount of each used (pounds) and the Line it was used on (i.e., either used on Heat-set Press Line Nos. 1,2 and 3 (EU 001), or used on Heat-set Press Line No. 4 (EU 005))`; d. VOC and HAP content (as applied, percent by weight) for each type of ink utilized, e. a calculation of potential VOC and HAP emissions(1); (pounds per month) from each ink based on the information in c. though d. above; and controlled VOC and HAP emissions based on the most recent tested applicable catalytic oxidizer control efficiency (records shall indicate control efficiency used); f. the quantity of Fountain Solution utilized (pounds per month), less disposal and/or reuse; g. a calculation of fugitive and controlled VOC and HAP emissions (pounds per month) from Fountain Solution(1) based on f. above, the VOC and HAP contents (percent by weight) for Fountain Solution, and any applicable oxidizer control efficiency (records shall indicate control efficiency used); the plant-wide usage (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC) (each shown separately), less disposal and/or reuse; a calculation of VOC and HAP emissions (pounds/month) from Blanket Wash and MRC based on h. above, their respective VOC and HAP contents (per cent by weight) and any applicable oxidizer control efficiency (records shall indicate control efficiency used) j. a monthly total for all of the above Heat-Set VOC and HAP emissions; and a cumulative most recent 12 consecutive month running total of Heat-Set VOC and HAPs emissions and material usages (i.e. for Heat-Set inks, for Heat-Set Fountain Solutions, and for plant-wide Wash Solutions(2)). Each 12 consecutive month VOC total shall include an assumed 1.0 tons/year for miscellaneous heat-set fugitive emission and 0.22 tons/year for natural gas combustion(3) (or the calculated tons/year VOC emissions based on actual natural gas usage for that 12 month period). Substitution of a "non-VOC" containing solution shall not require utilization records, however a log entry is still required stating that a "non-VOC solution is in use". A "non-VOC" solution is defined as a solution which indicates no VOC content per an EPA Method 24 test. [Rule 62-4.070(3), F.A.C., and Pinellas County Code Section 58-90; permits 1030240-009-AC and 1030240-011-AC] Comments: The facility was keeping records that complied with items a. thru j. B21. Emission Calculations - Controlled emission calculations shall be based on the most recent tested VOC destruction efficiency for the applicable catalytic oxidizer. The controlled emission calculations shall be based on the revised VOC destruction efficiency effective on the date of testing, unless otherwise notified in writing by the Air Quality Division of the PCDEM or the Department. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Sect. 58-90; permits 1030240-009-AC and 1030240-011-AC] Comments: The emission calculations were based on the most recent destructors efficiency for each Incinerator. Section D. OPERATION PERMIT RENEWAL D1. Operation Permit Renewal Application - The permittee shall submit an application for renewal of the Federally Enforceable State Operation Permit (FESOP) to the Air Permitting Section of Southwest District Office of the Department no later than sixty (60) days prior to the expiration date of that permit . A copy of the application shall also be sent to the Air Quality Division of the PCDEM. [Rules 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), ), 62-210.900 and 62-297.310(7)(a), F.A.C.] Comments: The permit expires on 5/7/08. An application is required to be submitted no later than 3/8/08. I read this permit condition to Messrs. Chidlow and Allen. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating ( Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / ( No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: I informed Messrs. Chidlow and Allen that it appeared that ValPak was in compliance with procedures and Emissions. I committed to calling Mr. Allen to set up an appointment for compliance assistance. |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: February 21, 2007 |
| ACCESS? | ( | ARMS? | ( |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030240 005 57346.doc