| 1030240 88744 |
| --- |
| FACILITY: Cox Target Media, Inc. | PERMIT ID: 208 |
| Val-Pak Direct Marketing Systems, Inc. | DISTRICT: Southwest |
| ADDRESS: 8575 Largo Lakes Drive | CONTACT PHONE: |
| Largo, FL | 727-568-4200 |
| ARMS NO: 1030240 001 | PERMIT NO: | Expiration Date: 9/19/2018 Renewal Date: 7/21/2018 |
|  | 1030240-015-AF |  |
|  |  | Test Due Date: 4/24/2013 |
| EMISSION UNIT DESCRIPTION: Heatset Lithographic Press Line 1: 6 printing units with a TEC Model 1200 gas dryer; Line 2 has 4 printing units with a TEC Model CP-215 gas dryer. A Quantum 4000 Catalytic incinerator controls emissions |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | March 5, 2014 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: David Fox? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: David_fox@valpak.com |
| 4. | Is the facility contact still: Linette Diaz? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: Linette_diaz@valpak.com? |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | ***The facility will be shutdown by 12/31/14. all operations will be moved to the st. Petersburg facility SECTION 4. APPENDIX B - General Conditions [62-4.160, F.A.C.] 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: a. A description of and cause of noncompliance; and b. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. IN MNC SNC N/A Comments: There were no periods of noncompliance reported during the compliance year 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. IN MNC SNC N/A Comments: A copy of the permit was was not kept at the worksite. SECTION 4. APPENDIX C - Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] IN MNC SNC N/A Comments: There was no circumvention observed to the catalytic incinerator. 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] IN MNC SNC N/A Comments: All equipment, pipes, hoses, lids, fittings, etc. were being operated and maintained in a manner which minimized leaks and fugitive emissions. There were no spills. All containers were tightly closed. All cleanup rags are disposed in 55 gallon sealed drums that are stored for later recycling. 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An “objectionable odor” means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C.] IN MNC SNC N/A Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- None; Wind direction – S/10 Upwind odor level detected-None 9. Unconfined Particulate Emissions: a. No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. b. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. c. Reasonable precautions include the following: (1) Paving and maintenance of roads, parking areas and yards. (2) Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. (3) Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. (4) Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. (5) Landscaping or planting of vegetation. (6) Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. (7) Confining abrasive blasting where possible. (8) Enclosure or covering of conveyor systems. IN MNC SNC N/A Comments: There were no unconfined emissions observed during the inspection. There is landscaping, grass and other foliage surrounding the facility property. 7. Annual Operating Report - On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] IN MNC SNC N/A Comments: The 2012 AOR was received 3/27/13 and reviewed on 4/12/13. 8. Operation Permit Renewal Application - A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to Pinellas County Air Quality Division no later than 60 days prior to the expiration date of this operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] IN MNC SNC N/A Comments: The permit expires on 9/19/18. An application is required to be submitted no later than 7/21/18. 10. Hazardous Air Pollutant Emissions - Total HAP emissions from this facility shall not exceed 16.0 tons in any consecutive 12-month period. [Rule 62-210.200 (Definition “Potential to Emit”), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: Highest 12-mo total for the Largo facility is 0.11 tons/yr (Oct, 13’) 11. Combined Facility Hazardous Air Pollutant and Volatile Organic Compound Emission Limitations - HAP and VOC emissions from this facility and the Cox Target Media, Inc./Valpak Direct Marketing Inc. Saint Petersburg facility (Facility ID 1030509) shall not exceed the following: a. 95.0 tons of VOC in any consecutive 12-month period; b. 8.0 tons of any individual HAP in any consecutive 12-month period; and c. 23.0 tons of total HAPs in any consecutive 12-month period. (Permitting Note: Cox Target Media, Inc. has a Valpak Direct Marketing Systems, Inc. printing facility located at 1 Valpak Avenue North, Saint Petersburg, Pinellas County which is currently permitted by 1030509-014-AF. The two Valpak facilities (Facility ID Nos. 1030240 and 1030509) are addressed under separate permits with common emission limitations for individual HAPs, total HAPs, and VOC to maintain total emissions from both facilities below Title V permitting thresholds.) [Rule 62-210.200 (Definition “Potential to Emit”), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: Highest 12-mo consecutive total HAP emissions for both the Largo and St. Petersburg facilities = 0.2085 tons/yr (Jan, 13’). The Highest 12-mo consecutive total VOC emissions for both the Largo and St. Petersburg facilities = 14.08 tons/yr (Jan, 13’) 12. General Standards - Objectionable Odor - No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200 (Definition “Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: There were no objectionable odors/organic solvents detected during the inspection. 13. General Pollutant Emission Limiting Standards – Volatile Organic Compounds Emissions or Organic Solvent Emissions - The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, organic solvents (OS) or VOCs without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Florida Department of Environmental Protection (the Department) or the Pinellas County Department of Environmental Management (PCDEM). Work practices to minimize emissions shall include the following: a. Equipment, pipes, hoses, lids, fittings, etc. shall be operated/maintained in such manner as to minimize leaks, fugitive emissions, and spills of solvent materials. This includes draining all OS/VOC-containing fluids into closed containers during lengthy periods of time when a press is not operating. b. All OS/VOCs from washings (e.g. equipment clean-up) shall be directed into containers that prevent evaporation into the atmosphere. c. Tightly cover or close all OS/VOC containers when they are not in use. d. Prevent excessive air turbulence across exposed OS/VOCs. e. Immediately confine and clean up OS/VOC spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rules 62-4.070(3) and 62-296.320(1)(a), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: All unused and spent printing inks were sealed in 55 gallon drums. There were no observed structural/pipe leaks leading to the RTO. The press areas were clean. All VOC washings, maintenance grease or other types of solvent material is immediately disposed in sealed 55 gallon drums to prevent evaporation. 14. Tons/Year Limitations - Compliance with “tons/year" emission limitations in this permit shall be based on any consecutive 12-month period total, or a Department approved optional recordkeeping scheme (e.g., 13 - "4-week" periods per year). [Rule 62-4.070(3), F.A.C., Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The facility performs a 12-month consecutive total for HAP and VOC emissions 15. Hazardous Air Pollutant/Volatile Organic Compound Records - Supporting documentation ("As Supplied", "As Applied" sheets, Material Safety Data Sheets (MSDS), EPA data sheets, purchase orders, etc.) shall be kept for each ink and HAP-/organic solvent (OS)-/VOC-containing material utilized at the facility, including "non-VOC" solutions in use. This documentation shall include sufficient information to: a. Provide reasonable assurance that any "non-VOC" solution/solvent in use at the facility indicates no VOC content based on an EPA Method 24 or 24A test; and b. Provide the basis for any electronic recordkeeping used for reporting emissions limitations or utilization rates required in Specific Conditions of this permit. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Section 58-90; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: Supporting documentation for the ink and solvent VOC contents were reviewed by Air Quality. The facility satisfies both provisions of the condition. The basis of the electronic recordkeeping is to tag each material used with its MSD sheet information. 16. Non-Volatile Organic Compound Material Substitution - The substitution of a non-VOC containing material* for an existing production material containing VOC shall not require recordkeeping; however, a log entry is required at the time of material substitution stating that a "non-VOC” solution/solvent has been substituted for (specify material). (*Permitting Note: A "non-VOC" material is defined as a material which indicates no VOC content per an EPA Method 24 or 24A test.) [Rule 62-4.070(3); Pinellas County Code, Section 58-90; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: Based on a review of the records, no substitutions were made during the compliance year 17. Combined Facility Emission Records - In order to document compliance with the requirements of Specific Condition No. 11, combined facility emission records shall be maintained (for Facility ID Nos. 1030240 and 1030509). These records shall be updated at least monthly and shall be completed by the end of the following month. The records shall include the following: a. The facility name, facility ID No. (e.g. 1030240 or 1030509); b. The month and year; c. A monthly total for each individual HAP, total HAP, and VOC emissions for each facility separately; d. A monthly total of each individual HAP, total HAP, and VOC emissions for this facility and the Cox Target Media Inc. Saint Petersburg facility (Facility ID 1030509) combined; e. The cumulative total emissions of each individual HAP, total HAP, and VOC emissions for the most recent consecutive 12-month period for each facility separately; and f. The cumulative total emissions of each individual HAP, total HAP, and VOC emissions for the most recent consecutive 12-month period for this facility and the Cox Target Media Inc. Saint Petersburg facility (Facility ID 1030509) combined. For the Largo facility, the consecutive 12-month VOC total shall include an assumed 1.0 tons for miscellaneous heat-set fugitive emission and 0.22 tons for natural gas combustion(3) (or the calculated tons/year VOC emissions based on actual natural gas usage for that 12-month period). [Rule 62-4.070(3), F.A.C.; Pinellas County Code Section 58-90; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The facility meets the condition of this provision. A copy of the record is attached to the report. 18. Record Retention - All recordkeeping information, supporting documentation, monitoring data, and all compliance test information required by this permit shall be retained at the facility for the most recent three (3) year period and shall be made available to the Florida Department of Environmental Protection (the Department) or the Air Quality Division of Pinellas County upon request. [Rule 62-4.070(3), F.A.C.; Pinellas County Code Section 58-90; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The facility has kept its records for more than 3 years 19. Changes to Air Management System - Changes to the air management systems of this facility (including air conditioning and other air handling equipment) may render the assumed VOC capture efficiencies ineffective. The PCAQD shall be notified when a change is contemplated, or when any portion of an existing air management system is damaged in any manner. This notification shall include discussion of any potential impact on VOC emissions. [Rule 62-4.070(3), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: There were no changes to the air management system in the facility during the compliance year. A.1. Volatile Organic Compound Emissions - The sum total VOC emissions from the Heat-Set Lithographic Press Operations Line Nos. 1 and 2 shall not exceed 80.17 tons in any consecutive 12-month period(1). This value includes the stack and fugitive emissions from the printing inks, fountain solution, plant-wide wash solutions(2), natural gas combustion (0.22 TPY(3)), and miscellaneous heat-set fugitives (considered for the purposes of this permit to be a maximum of 1.0 TPY or less). [Rule 62-296.320(1)(a), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The highest 12-mo consecutive total VOC at the Largo Plant =1.41 tons/yr (Mar, 13’) A.2. Material Usage - In order to insure compliance with the allowable annual emission rate in Specific Condition No. A.1., the following material usage limitations (totals for both heat-set press lines combined) shall apply for any consecutive 12-month period: a. Heat-Set Printing Inks: 1,060,000 lbs; b. Heat-Set Press Fountain Solution: 7,500 gallons - the permittee shall not use a VOC solution to dilute the "Fountain Solution". c. Wash Solutions(2) (plant-wide): 17,500 gallons (less disposal and reuse). [Rules 62-4.070(3) and 62-296.320(1)(a), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The highest 12-mo heat-set printing ink used = 51,470 lbs (Oct, 13’) The highest heat-set press fountain solution =691.6 gallons (Sept, 13’) The highest wash solutions plant-wide =336 gallons (Mar, 13’) A.3. Heat-Set Press Line Nos. 1 and 2 Catalytic Oxidizer Destruction Efficiency - The VOC destruction efficiency of the Heat-Set Lithographic Press Printing Line Nos. 1 and 2 Quantum 4000 catalytic oxidizer shall not fall below 90% removal. [Rules 62-210.650, 62-296.320(1)(a), and 62-212.300, F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The test was performed on 7/11/13 for this facility. Based on the VOC Destruction Efficiency Test the efficiency = 98.3% A.4. Heat-Set Press Line Nos. 1 and 2 Catalytic Oxidizer Exhaust Stack Flow Rate - The gas flow rate from the exhaust stack of the Heat-Set Lithographic Press Printing Line Nos. 1 and 2 Quantum 4000 catalytic oxidizer shall be at least 2,700 standard cubic feet per minute (scfm) when operating from both heat-set lithographic presses. There shall be no device on the exhaust stack which will interfere with the flow of the exhaust gases. [Rules 62-4.070(3), 62-210.650, and 62-296.320(1)(a), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The exhaust stack flow rate of the Heat-Set Lithographic Press (Printing Lines 1, 2 and 3) Quantum 4000 catalytic oxidizer was 3,300 scfm and was in compliance with the provision. A.5 Exhaust Flow - Whenever practical, the exhaust air flow through all the dryers shall be maintained during periods when Wash Solution(2) is being utilized. [Rule 62-4.070(3), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: During the inspection, it was observed the exhaust air flow through the air dryers was in operation during printing. A.6. Bypass Stacks - The permittee shall not utilize a bypass stack which vents to the atmosphere at any time while ink is being applied. If ink is not being applied and best operational practices to minimize emissions are adhered to, then it is permitted to utilize a bypass stack only during periods of start up, shutdown, or malfunction. The permittee shall keep records of the date and time of commencement and completion of each time period that a bypass stack is utilized and ink is applied. The records shall include the reason for utilization of the bypass stack. They shall be maintained at the facility for a minimum of the most recent three-year period and made available to Air Quality Division of the Pinellas County upon request. [Rules 62-4.070(3) and 62-210.700, F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: According to the records and Ms. Diaz, the By-Pass Stack was never used while ink was being applied. A.7. Compliance Test Requirements - Compliance tests shall be conducted in accordance with the applicable requirements specified in Appendix D (Common Testing Requirements) of this permit. [Rule 62-297.310, F.A.C.] IN MNC SNC N/A Comments: The facility met the compliance test requirements as specified in Appendix D (Common Testing Requirements). This includes the common testing requirements and records/reports. Appendix D is found in the electronic version of the permit in the Air Quality database with a hard copy in the permit file. A.8. Compliance Test Methods - Required compliance tests shall be performed in accordance with the following reference methods. Methods Description of Method and Comments 1-4 Traverse Points, Velocity and Flow Rate, Gas Analysis, and Moisture Content 9 Visual Determination of the Opacity of Emissions from Stationary Sources 25/25A Determination of Total Gaseous Nonmethane Organic Emissions as Carbon/Determination of Total Gaseous Organic Concentration Using a Flame Ionization Analyzer The above methods are described in Appendix A of 40 CFR 60 and are adopted by reference in Rule 62-204.800, F.A.C. No other methods may be used unless prior written approval is received from the Department. [Rule 62-204.800, F.A.C.; Appendix A of 40 CFR 60] IN MNC SNC N/A Comments: The facility performed Method 25A and the other listed methods for the VOC Destruction Efficiency Test. A.9. Catalytic Oxidizer Destruction Efficiency Testing - Within the six (6) month period prior to the expiration date of this permit and prior to submittal of the operation permit renewal application (see Specific Condition No. A.18.), the permittee shall test the catalytic oxidizer stack inlets and outlets to determine VOC destruction efficiency and document compliance with Specific Condition Nos. A.3. and A.4. A Method 9 VE test shall be performed simultaneously with one (1) of the three (3) Method 25/25A runs required in order to determine VOC destruction efficiency. A copy of the test data shall be submitted to the Air Quality Division of the Pinellas County within 45 days of testing. [Rule 62-297.310, F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The test for 1030240 -001 was performed on 7/11/13. The permit was due to expire on 10/24/13. A.10. Additional Catalytic Oxidizer Testing Requirements - Compliance with the VOC destruction efficiency requirement and the controlled stack emission limitations shall be conducted using the methods and procedures as described in the attached FDEP DARM Guidance Memos (see attached FDEP DARM Guidance Memos DARM-OGG-2 and DARM-OGG-04 (Attachment 1)). During the compliance test, the VOC content of the ink shall either be determined by using data from the most recent MSDS or an EPA Method 24A test. The data on the VOC concentration in each ink shall be submitted with the compliance test results. The amount of each ink used during the compliance test shall be determined using available meters or other information and shall be submitted with the compliance test report. Any alternative method for determining VOC content may only be used after written approval is obtained from the Department. [Rules 62-4.070 (3) and 62-297.310, F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The VOC content of the ink is based on the MSDS. A.11. Press Line Nos. 1 and 2 Operation During Testing - All testing of the TEC Systems Quantum 4000 catalytic oxidizer in accordance Specific Condition No. A.9. shall be accomplished while simultaneously operating Heat-Set Lithographic Press Line Nos. 1 and 2 at 90 - 100% of the maximum "Printing Ink" utilization rate (defined as both heat-set press lines in operation under normal conditions). Failure to submit a statement of the status of the operation of the press lines during the test period or operating at conditions which do not reflect normal operating conditions, may invalidate the test. The test report shall also include the catalytic oxidizer exhaust gas temperature, the catalytic oxidizer stack gas flow rate and velocity, the change in temperature across the catalyst bed, and the inlet and outlet VOC concentrations from the catalytic oxidizer emission tests. [Rules 62-4.070(3) and 62-297.310(2) and (8), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The print ink utilization rate = 94% A.12. Testing Notification - The permittee shall notify the Air Quality Division of the Pinellas County at least 15 days prior to the date on which each formal compliance test is scheduled, of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating each test. (Permitting Note - The notification should also include the relevant emission unit ID No(s)., test method(s) to be used, and pollutants to be tested.) [Rules 62-4.070(3) and 62-297.310(7)(a)9., F.A.C.] IN MNC SNC N/A Comments: Air Quality received/postmarked the testing notification on 6/26/13. The test was performed on 7/11/13. A.13. Compliance Test Reports - The permittee shall prepare and submit reports for all required compliance tests in accordance with the requirements specified in Appendix D (Common Testing Requirements) of this permit. [Rule 62-297.310(8), F.A.C.] IN MNC SNC N/A Comments: The VOC Destruction Efficiency Test was conducted in accordance with Appendix D (common testing requirements). A.14. Hazardous Air Pollutant/Volatile Organic Compound Material Usage and Emission Records(1) - In order to document compliance with the requirements of Specific Condition Nos. A.1. (Heat-Set VOC limit), A.2. (material usage limits), and 10 (Facility-wide HAP limit), HAP-/VOC-containing material usage and emission records shall be maintained. These records shall be updated at least monthly and shall be completed by the end of the following month. The records shall include the following: a. The facility name, facility ID No. (1030240), and EU name and EU number (e.g., Heat-set Press Lines, EU No. 001); b. The month and year; c. The quantity of "As Applied" ink (by name or identification number) used, indicating the amount of each used (e.g. pounds) and the Line it was used on (i.e., used on Heat-set Press Line Nos. 1 and 2 (EU No. 001); d. HAP and VOC content (as applied, percent by weight) for each type of ink utilized, e. A calculation of potential HAP and VOC emissions(1); (pounds per month) from each ink based on the information in C. and D. above; and controlled HAP and VOC emissions based on the most recent tested applicable catalytic oxidizer control efficiency; f. The quantity of Fountain Solution utilized (pounds per month); g. The quantity of Fountain Solution disposed and/or reused (pounds per month); h. The quantity of Fountain Solution utilized (pounds per month), less disposal and/or reuse; i. A calculation of fugitive and controlled HAP and VOC emissions (pounds per month) from Fountain Solution(1) based on h. above, the HAP and VOC contents (percent by weight) for Fountain Solution, and any applicable oxidizer control efficiency, including control efficiency used; j. The plant-wide usage (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC) (each reported separately); k. The plant-wide disposal and/or reuse (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC) (each reported separately); l. The plant-wide usage (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC), less disposal and/or reuse (each reported separately); m. A calculation of HAP and VOC emissions (pounds/month) from Blanket Wash and MRC based on l. above, their respective HAP and VOC content (percent by weight) and any applicable oxidizer control efficiency, including control efficiency used; n. A monthly total for all of the above Heat-Set HAP and VOC emissions; and a cumulative most recent consecutive 12-month running total of Heat-Set HAP and VOC emissions and material usages (i.e. for Heat-Set inks, for Heat-Set Fountain Solutions, and for plant-wide Wash Solutions(2)). Each consecutive 12-month VOC total shall include an assumed 1.0 tons/year for miscellaneous heat-set fugitive emission and 0.22 tons/year for natural gas combustion(3) (or the calculated tons/year VOC emissions based on actual natural gas usage for that 12 month period). Substitution of a "non-VOC" containing solution shall not require utilization records, however a log entry is still required stating that a "non-VOC solution is in use". A "non-VOC" solution is defined as a solution which indicates no VOC content per an EPA Method 24 test. [Rule 62-4.070(3), F.A.C.; Pinellas County Code Section 58-90; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: Cox Target Media (Val-Pak) Largo, meets the provisions of the condition. A copy of the record is attached to the compliance file. A.15. Emission Calculations - Controlled emission calculations shall be based on the most recent tested VOC destruction efficiency for the catalytic oxidizer. The controlled emission calculations shall be based on the revised VOC destruction efficiency effective on the date of testing, unless otherwise notified in writing by the Air Quality Division of the Pinellas County. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Sect. 58-90; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The most recent test reviewed by AQD showed the destruction efficiency = 98.3% A.16. Catalytic Oxidizer Operation Requirement and Outage Reporting - No heat-set press line shall operate unless the associated catalytic oxidizer (Quantum 4000 catalytic oxidizer for Heat-set Press Line Nos. 1 and 2) is in operation and the catalyst bed gas inlet temperature is between 600o F and 1,100o F, except as stipulated below. There shall be an automatic cutoff device which shall not allow any heat-set press to operate unless the applicable catalytic oxidizer is operating at a temperature above 600(F. However, in the event of a catalytic oxidizer outage/malfunction, the permittee shall be allowed to operate the press lines without the catalytic oxidizer in service for a period to time not to exceed 48 hours. There shall be a maximum of two (2) such 48-hour periods in any consecutive 12-month period. a. The following shall apply during these periods of catalytic oxidizer outage - 1. The permittee shall take reasonable steps to minimize VOC emissions, visible emissions (VE), and odors; 2. PCAQD shall be notified of the problems with the catalytic oxidizer immediately (not including weekends or legal holidays) of the occurrence; 3. PCAQD shall be informed of the steps taken to correct the problem and anticipated time frame to correct the problem; and 4. PCAQD shall be advised when the catalytic oxidizer was brought back on line. b. Documentation of the catalytic oxidizer outage shall be kept as follows - 1. The identification of the catalytic oxidizer and the time of the start of the breakdown; 2. Reason for breakdown, and the steps taken to correct the problem; 3. The date and time PCDEM was notified and to whom reported; 4. Detailed information on the quantity of each ink and fountain solution used during the outage period, and 5. The time catalytic oxidizer was brought back on line. The estimated amount of VOC emitted during the outage period shall be calculated and included in the monthly VOC emission records and the oxidizer outage report. The PCAQD shall be provided with a detailed written report on the outage, including the information in B. above, within seven (7) working days (i.e. excluding week-ends and legal holidays). [Rules 62-4.070(3), 62-4.130, 62-210.650, and 62-210.700(4), F.A.C.; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The catalytic oxidizer was operating during the inspection. Cox Target Media did not report an outage of the catalytic oxidizer during the compliance year. A.17. Catalytic Oxidizer Operation and Maintenance Plan - The catalytic oxidizers shall be operated and maintained in accordance with the applicable Operation and Maintenance (O&M) Plans (see Attachment 2) attached to this permit, or a later issue of the O&M plan approved by the Air Quality Division of the Pinellas County. The O&M plan shall meet the requirements of Pinellas County Code, Section 58-128, and shall include at a minimum: a. The operating parameters for the catalytic oxidizer; b. The timetable for routine catalytic oxidizer maintenance, as specified by the manufacturer; c. The timetable for routine periodic observations (e.g. weekly, bi-weekly, monthly, etc.) of the pollution control device sufficient to insure proper operation; d. A list of the type and quantity of the required catalytic oxidizer spare parts which are stored on the premises; and e. A record log which indicates, at a minimum: 1. When catalytic oxidizer maintenance and observations were performed; 2. What catalytic oxidizer maintenance and observations were performed; 3. Who performed said maintenance and observations; and 4. Acceptable parameter ranges for each operational check. The O&M plan documentation logs shall be maintained at the facility for a minimum of the most recent three-year period and shall be made available to Air Quality Division of the Pinellas County, or the Department, upon request. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Sec. 58-128; Construction Permit No. 1030240-013-AC] IN MNC SNC N/A Comments: The daily and monthly maintenance record logs were reviewed. The logs contain, the following, when the cat oxidizer maintenance was performed, what observations were performed, who performed them and the acceptable parameter ranges. FOOTNOTES (1) Heat-Set Presses Source Assumptions: a. HAP/VOC emissions from inks are based upon the assumption that there is a 100% capture efficiency in the drying ovens and that 20% of the VOCs are retained in the printed product and are not released to the atmosphere. b. HAP/VOC emissions from Wash Solutions(2) are assumed 100% fugitive and for dispersion modeling purposes, exit the building through the catalytic oxidizer stack. c. HAP/VOC emissions from "Fountain Solution" are assumed 50% fugitive and 50% controlled. For dispersion modeling purposes, the fugitive portion is assumed to exit the building through the catalytic oxidizer stack. d. Hourly emission rates are based on monthly averages, except for compliance tests. e. The capture efficiency of all fugitive emissions in the manufacturing area is assumed to be 100% and all fugitive emissions are assumed to be directed toward the catalytic oxidizer for destruction. (2) Wash Solutions consist of Blanket Wash and Meter Roller Cleaner (MRC) from the entire facility (i.e. includes both Heat-Set and Cold-Set wash solutions). (3) VOC emissions from natural gas combustion of 0.22 tons/year are based on an estimated maximum facility natural gas usage rate of 80 million cubic ft per year. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no pollution prevention activities reported during the compliance year |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030240 | OWNER Cox Target Media, Inc. | FACILITY NAME Val-Pak Direct Marketing Systems, Inc. |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE March 5, 2014 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE February 29, 2012 |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | rec 3/27/13; reviewed on 4/12/13 |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| March 5, 2014 | March 11, 2014 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) | Visible emissions test performed with Method 25A,;7/11/13 |
| DONE N/A | Review of facility records and logs | Copy of records attached to inspection report |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) | Reviewed process rate |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) | Temperature of catalytic incinerator was observed to operating between 600 deg F and 1,100 deg F and in compliance |
| DONE N/A | Stack test(s) | Method 25A performed on 7/11/13; permit renewal |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.