| 1030240 80610 |
| --- |
| FACILITY: Cox Target Media, Inc. | PERMIT ID: 2709 |
| Val-Pak Direct Marketing Systems, Inc. | DISTRICT: Southwest |
| ADDRESS: 8575 Largo Lakes Drive | CONTACT PHONE: |
| Largo, FL | 727-568-4200 |
| ARMS NO: 1030240 005 | PERMIT NO: | Expiration Date: 10/24/2013 Renewal Date: 8/25/2013 |
|  | 1030240-014-AF |  |
|  |  | Test Due Date: 4/24/2013 |
| EMISSION UNIT DESCRIPTION : Line 4: Harris Graphics Model M-110 lithographic heatset press (line speed of 1,000 feet/minute) with a TEC Systems CP-215 natural gas fired dryer with a heat input rate of 2.63 MMBtu/hour, which exhausts to a TEC Systems Quantum 2000 catalytic oxidizer. |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | February 29, 2012 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: David Fox? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Don Gignac? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: This permit became effective on 10/24/2008. The permit authorizes the construction/modification of the addition of combined emission limitations for individual hazardous air pollutants (HAPs), total HAPs, and volatile organic compounds (VOCs) for both Cox Target Media facilities (Facility ID Nos. 1030240 (located at 8575 Largo Lakes Drive, Largo, Pinellas County) and 1030509 (located at 1 Valpak Avenue North, Saint Petersburg, Pinellas County)); the addition of a recordkeeping condition to document HAP and VOC combined emissions from the two Cox Target Media facilities; the revision of the visible emission (VE) limitation for Emission Unit (EU) Nos. 001 and 005 – Heat-Set Lithographic Press Lines, from 5% to 20%; the removal of the VE testing requirement for EU Nos. 001 and 005; the addition of a facility-wide special compliance testing condition; and the addition of recordkeeping requirements to document disposal/reuse of solutions. This permit or a copy thereof shall be kept at the work site of the permitted activity. [62-4.160 F.A.C. – General Condition 12.] Comments: The facility did did not have a copy of the permit on-site. 3. Operating Hours Limitation: This facility is permitted for continuous operation (i.e. permitted for 8,760 hours per year). [Rule 62-210.200 (Definition “Potential to Emit”), F.A.C.; Construction Permit 1030240-011-AC] Comments: The facility operated 8 hrs/day 5 days/wk or 2,080 hrs/yr 4. Hazardous Air Pollutant Emissions: Total HAP emissions from this facility shall not exceed 16.0 tons in any consecutive 12-month period. [Rule 62-210.200 (Definition “Potential to Emit”), F.A.C.; Construction Permit 1030240-011-AC] (Notes:Compliance with the facility-wide HAP limitation of Specific Condition No. 4. above shall be determined from calculation of HAPs based Specific Condition Nos. 36, 40, and Footnotes. Compliance with Specific Condition 5.B. will demonstrate compliance with the individual facility HAP emission limitation. There are separate VOC limits for the heat-set and cold-set areas (see Specific Condition Nos. 20. and 38.), the total facility allowable VOC emission rate is the sum of these two limits: 80.17 + 10.83 = 91.0 TPY.) Comments: The highest reported total HAP 12 month total highest = 0.31 tons/yr (Aug, 11’). Records reviewed for June, 11’ – Jan, 12’ 5. Combined Facility Hazardous Air Pollutant and Volatile Organic Compound Emission Limitations: HAP and VOC emissions from this facility and the Cox Target Media, Inc./Valpak Direct Marketing Inc. Saint Petersburg facility (Facility ID 1030509) shall not exceed the following: 95.0 tons of VOC in any consecutive 12-month period; 8.0 tons of any individual HAP in any consecutive 12-month period; and 23.0 tons of total HAPs in any consecutive 12-month period. [Rule 62-210.200 (Definition “Potential to Emit”), F.A.C.; Construction Permit Application received March 7, 2008] Comments: Highest VOC emissions 12-mo consecutive total for combined St. Pete and Largo facilities = 9.22 tons/yr (June, 11’). Highest individual HAP for the combined (Xylene) = 0.13533 tons/yr (Aug, 11’). Highest total HAP emissions for the combined facilities = 1.7401 tons/yr (Aug, 11’). 6. General Particulate Emission Limiting Standards - General Visible Emissions Standard: Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1. and 4., F.A.C.] Comments: There were no fugitive-dust or particulate dust emissions emanating from this facility. The entire surroundings are paved. 7. General Standards - Objectionable Odor: No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200 (Definition “Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: There were no odors outside of the facility. VOCs were detectable inside the printing area, but all ink and solvent containers were closed and had lids. 8. General Pollutant Emission Limiting Standards – Volatile Organic Compounds Emissions or Organic Solvent Emissions: The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, organic solvents (OS) or VOCs without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Florida Department of Environmental Protection (the Department) or the Pinellas County Department of Environmental Management (PCDEM). Work practices to minimize emissions shall include the following: Equipment, pipes, hoses, lids, fittings, etc. shall be operated/maintained in such manner as to minimize leaks, fugitive emissions, and spills of solvent materials. This includes draining all OS/VOC-containing fluids into closed containers during lengthy periods of time when a press is not operating. All OS/VOCs from washings (e.g. equipment clean-up) shall be directed into containers that prevent evaporation into the atmosphere. Tightly cover or close all OS/VOC containers when they are not in use. Prevent excessive air turbulence across exposed OS/VOCs. Immediately confine and clean up OS/VOC spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rules 62-4.070(3) and 62-296.320(1)(a), F.A.C.] Comments: All equipment, pipes, hoses, lids, fittings, etc. were being operated and maintained in a manner which minimized leaks and fugitive emissions. There were no spills. All containers were tightly closed. 9. Special Compliance Tests: When the Department or the Air Quality Division of the Pinellas County Department of Environmental Management (PCDEM), after investigation, has good reason (such as complaints, increased VE or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it may require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and to provide a report on the results of said tests to the Department. [Rule 62-297.310(7)(b), F.A.C.] Comments: No special tests have been ordered or deemed necessary. 10. Special Compliance Test Method: As necessary, compliance with the emissions limitation specified in Specific Condition No. 6 shall be determined using EPA Method 9 contained in 40 CFR 60, Appendix A and adopted by reference in Chapter 62-297, F.A.C. The Method 9 compliance test shall be conducted by a certified observer and be a minimum of 30 minutes in duration. The test observation period shall include the period during which the highest opacity can reasonably be expected to occur. The minimum requirements for stationary point source emission test procedures and reporting shall be in accordance with Chapter 62-297, F.A.C. and 40 CFR 60 Appendix A. [Rules 62-297.310(4)(a)2., 62-297.310(7)(a)4., and 62-297.401(9), F.A.C.] Comments: Air Quality did not perform a Method 9 VE and there were no fugitive emissions emanating from the stack. 11. Special Compliance Test Report Submittal: A copy of the test data for all compliance tests required by this permit shall be submitted to the Air Quality Division of the PCDEM as soon as practical but no later than 45 days after the testing is completed. The minimum requirements for reporting shall be in accordance with Chapter 62-297, F.A.C. Failure to submit the actual operating conditions may invalidate the test. [Rules 62-4.070(3) and 62-297.310(8)(b), F.A.C.] Comments: There were no special test reports needed during the compliance year. 12. Tons/Year Limitations: Compliance with “tons/year" emission limitations in this permit shall be based on any consecutive 12-month period total, or a Department approved optional recordkeeping scheme (e.g., 13 - "4-week" periods per year). [Rule 62-4.070(3), F.A.C., Construction Permit 1030240-011-AC] Comments: The facility reports its emission total in tons/yr a 12-month period total (12-mo consecutive total. 13. Hazardous Air Pollutant/Volatile Organic Compound Records: Supporting documentation ("As Supplied", "As Applied" sheets, Material Safety Data Sheets (MSDS), EPA data sheets, purchase orders, etc.) shall be kept for each ink and HAP-/organic solvent (OS)-/VOC-containing material utilized at the facility, including "non-VOC" solutions in use. This documentation shall include sufficient information to: Provide reasonable assurance that any "non-VOC" solution/solvent in use at the facility indicates no VOC content based on an EPA Method 24 or 24A test; and Provide the basis for any electronic recordkeeping used for reporting emissions limitations or utilization rates required in Specific Conditions of this permit. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Section 58-90] Comments: A review of the facility’s usages during the compliance year determined that there were no material substitutions during the compliance year. The electronic spreadsheet indicates the emission limits, permitted allowable rates, for HAP and VOC. The spreadsheet is based on the total amount of lbs of material used for heatset inks, fountain solutions, wash solutions, etc. Further, the material is reported in lbs of HAP and VOC. 14. Non-Volatile Organic Compound Material Substitution: The substitution of a non-VOC containing material* for an existing production material containing VOC shall not require recordkeeping, however, a log entry is required at the time of material substitution stating that a "non-VOC solution/solvent has been substituted for (specify material). [Rule 62-4.070(3); Pinellas County Code, Section 58-90] Comments: A review of Val-Pak’s usage records during the compliance year determined that there were no material substitutions during the compliance year. Mr. Gignac stated that no material was substituted during the compliance year. 15. Combined Facility Emission Records: In order to document compliance with the requirements of Specific Condition No. 5, combined facility emission records shall be maintained (for Facility IDs 1030240 and 1030509). These records shall be updated at least monthly and shall be completed by the end of the following month. The records shall include the following: The facility name, facility ID nos. (e.g. 1030240 or 1030509); The month and year; A monthly total for each individual HAP, total HAP, and VOC emissions for each facility separately; A monthly total of each individual HAP, total HAP, and VOC emissions for this facility and the Cox Target Media Inc. Saint Petersburg facility (Facility ID 1030509) combined. The cumulative total emissions of each individual HAP, total HAP, and VOC emissions for the most recent consecutive 12-month period for each facility separately; and The cumulative total emissions of each individual HAP, total HAP, and VOC emissions for the most recent consecutive 12-month period for this facility and the Cox Target Media Inc. Saint Petersburg facility (Facility ID 1030509) combined. For the Largo facility, the consecutive 12-month VOC total shall include an assumed 1.0 tons for miscellaneous heat-set fugitive emission and 0.22 tons for natural gas combustion(3) (or the calculated tons/year VOC emissions based on actual natural gas usage for that 12-month period). [Rule 62-4.070(3), F.A.C.; Pinellas County Code Section 58-90] Comments: The VOC and HAP logs were in-compliance with A. though F above. (sample logs are attached to the compliance file) 16. Record Retention: All recordkeeping information, supporting documentation, monitoring data, and all compliance test information required by this permit shall be retained at the facility for the most recent three (3) year period and shall be made available to the Florida Department of Environmental Protection (the Department) or the Air Quality Division of the PCDEM, upon request. [Rule 62-4.070(3), F.A.C.; Pinellas County Code Section 58-90] Comments: Val-Pak has records existing since 2002. 17. Annual Operating Report: The permittee shall submit each calendar year on or before March 1, a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the Annual Operating Report (AOR) package sent by the Department, or a hardcopy may be sent to the Air Quality Division of the PCDEM, with a copy to the Air Compliance Section of the Department’s Southwest District Office. [Rule 62-210.370(3), F.A.C.; Pinellas County Code Subsection 58-90(3) and (9)] Comments: 2010 EAOR postmarked/received 4/1/10 and reviewed 4/18/11 18. Modification: Unless otherwise exempt by rule, the permittee shall not initiate any construction, reconstruction, or modification at the facility and shall not install/modify any pollution control device at the facility without obtaining prior authorization from the Department. Modification is defined as any physical change or changes in the method of operations or addition to a facility that would result in an increase in the actual emissions of any air pollutant subject to air regulations, including any not previously emitted, from any emission unit or facility. [Rules 62-210.200 (Definition “Modification”) and 62-210.300(1)(a), F.A.C.] Comments: There were no modifications or new construction observed or reported at Cox Target Media during the compliance year. 19. Changes to Air Management System: Changes to the air management systems of this facility (including air conditioning and other air handling equipment) may render the assumed VOC capture efficiencies ineffective. The PCDEM shall be notified when a change is contemplated, or when any portion of an existing air management system is damaged in any manner. This notification shall include discussion of any potential impact on VOC emissions. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030240-009-AC] Comments: There were no changes to the air management system during the compliance year Emission Unit Nos. 001 and 005 - Heat-Set Lithographic Press Line Nos. 1, 2, 3, and 4 20. Volatile Organic Compound Emissions: The sum total VOC emissions from the Heat-Set Lithographic Press Operations Line Nos. 1, 2 3, and 4 shall not exceed 80.17 tons in any consecutive 12-month period (1). This value includes the stack and fugitive emissions from the printing inks, fountain solution, plant-wide wash solutions(2), natural gas combustion (0.22 TPY(3)), and miscellaneous heat-set fugitives (considered for the purposes of this permit to be a maximum of 1.0 TPY or less). [Rule 62-296.320(1)(a), F.A.C.; Construction Permit 1030240-011-AC] Comments: The highest 12 month running cumulative total of VOCS was recorded at the end of the month of June, 2011 when 2.02 tons of VOCs were emitted for EUs 001 and 005 at the Cox Target Media 1030240 facility. Records reviewed from May, 11’ – Jan, 12’ 21. Material Usage: In order to insure compliance with the allowable annual emission rate in Specific Condition No. 20., the following material usage limitations (totals for all heat-set press lines combined) shall apply for any consecutive 12-month period: Heat-Set Printing Inks: 1,060,000 lbs; Heat-Set Press Fountain Solution: 7,500 gallons - the permittee shall not use a VOC solution to dilute the "Fountain Solution". Wash Solutions(2) (plant-wide): 17,500 gallons (less disposal and reuse). [Rules 62-4.070(3) and 62-296.320(1)(a), F.A.C.; Construction Permit 1030240-011-AC] EU 005 The highest total of heat-set inks used = 1,990 lbs (Sept, 11’) The highest heat-set press fountain solution used = 27 gallons (Sept, 11’) The highest wash solutions used = 0 gallons 22. Catalytic Oxidizer Operation Requirement and Outage Reporting: No heat-set press line shall operate unless the associated catalytic oxidizer (Quantum 4000 catalytic oxidizer for Heat-set Press Line Nos. 1, 2, and 3; Quantum 2000 catalytic oxidizer for Heat-set Press Line No. 4) is in operation and the catalyst bed gas inlet temperature is between 600o F and 1,100o F, except as stipulated below. There shall be an automatic cutoff device which shall not allow any heat-set press to operate unless the applicable catalytic oxidizer is operating at a temperature above 600(F. However, in the event of a catalytic oxidizer outage/malfunction, the permittee shall be allowed to operate the press lines without the catalytic oxidizer in service for a period to time not to exceed 48 hours. There shall be a maximum of two (2) such 48-hour periods in any consecutive 12-month period. The following shall apply during these periods of catalytic oxidizer outage: The permittee shall take reasonable steps to minimize VOC emissions, visible emissions (VE), and odors; PCDEM shall be notified of the problems with the catalytic oxidizer immediately (not including weekends or legal holidays) of the occurrence; PCDEM shall be informed of the steps taken to correct the problem and anticipated time frame to correct the problem; and PCDEM shall be advised when the catalytic oxidizer was brought back on line. Documentation of the catalytic oxidizer outage shall be keep as follows: The identification of the catalytic oxidizer and the time of the start of the breakdown; Reason for breakdown, and the steps taken to correct the problem; The date and time PCDEM was notified and to whom reported; Detailed information on the quantity of each ink and fountain solution used during the outage period, and The time catalytic oxidizer was brought back on line. The estimated amount of VOC emitted during the outage period shall be calculated and included in the monthly VOC emission records and the oxidizer outage report. The PCDEM shall be provided with a detailed written report on the outage, including the information in B. above, within seven (7) working days (i.e. excluding week-ends and legal holidays). [Rules 62-4.070(3), 62-4.130, 62-210.650, and 62-210.700(4), F.A.C.; Construction Permits 1030240-009-AC and 1030240-011-AC] Comments: The catalytic oxidizer was operating during the inspection. Cox Target Media did not report an outage of the catalytic oxidizer during the compliance year. 24. Heat-Set Press Line No. 4 Catalytic Oxidizer Destruction Efficiency: The VOC destruction efficiency of the Heat-Set Lithographic Press Printing Line No. 4 Quantum 2000 catalytic oxidizer shall not fall below 90% removal. [Rules 62-210.650, 62-212.300, and 62-296.320(1)(a), F.A.C.; Construction Permit 1030240-011-AC] Comments: The VOC destruction efficiency of the Heat-Set Lithographic Press Printing Line No. 4 Quantum 2000 catalytic oxidizer was tested & determined to be 97.2 % on 2/12/08. 26. Heat-Set Press Line No. 4 Catalytic Oxidizer Exhaust Stack Flow Rate: The gas flow rate from the exhaust stack of the Heat-Set Lithographic Press Printing Line No. 4 Quantum 2000 catalytic oxidizer shall be at least 1,000 scfm when the press line is in operation. There shall be no device on the exhaust stack which will interfere with the flow of the exhaust gases. [Rules 62-4.070(3), 62-210.650, and 62-296.320(1)(a), F.A.C.; Construction Permit 1030240-011-AC] Comments: The gas flow rate from the exhaust stack of the Heat-Set Lithographic Press Printing Line No. 4 Quantum 2000 catalytic oxidizer was determined to be 1,150 SCFM, thus, in compliance. 27. Catalytic Oxidizer Operation and Maintenance Plan: The catalytic oxidizers shall be operated and maintained in accordance with the applicable Operation and Maintenance (O&M) Plans (see Attachments 2 and 3) attached to this permit, or a later issue of the O&M plan approved by the Air Quality Division of the PCDEM. The O&M plan shall meet the requirements of Pinellas County Code, Section 58-128, and shall include at a minimum: The operating parameters for the catalytic oxidizer; The timetable for routine catalytic oxidizer maintenance, as specified by the manufacturer; The timetable for routine periodic observations (e.g. weekly, bi-weekly, monthly, etc.) of the pollution control device sufficient to insure proper operation; A list of the type and quantity of the required catalytic oxidizer spare parts which are stored on the premises; and A record log which indicates, at a minimum: When catalytic oxidizer maintenance and observations were performed; What catalytic oxidizer maintenance and observations were performed; Who performed said maintenance and observations; and Acceptable parameter ranges for each operational check. The O&M plan documentation logs shall be maintained at the facility for a minimum of the most recent three-year period and shall be made available to Air Quality Division of the PCDEM, or the Department, upon request. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Sec. 58-128; Construction Permits 1030240-009-AC and 1030240-011-AC] Comments: The facility was in compliance with A. through E. of permit condition 27. (see copies of logs, attached). 28. Exhaust Flow: Whenever practical, the exhaust air flow through all the dryers shall be maintained during periods when Wash Solution(2) is being utilized. [Rule 62-4.070(3), F.A.C.] Comments: During the inspection, it was observed the exhaust air flow through the air dryers was in operation during printing. Don Gignac, who escorted Air Quality during the inspection, stated the flow is maintained through the Dryers and into the incinerator when applying wash solution (no printing taking place). 29. Bypass Stacks: The permittee shall not utilize a bypass stack which vents to the atmosphere at any time while ink is being applied. If ink is not being applied and best operational practices to minimize emissions are adhered to, then it is permitted to utilize a bypass stack only during periods of start up, shutdown, or malfunction. The permittee shall keep records of the date and time of commencement and completion of each time period that a bypass stack is utilized and ink is applied. The records shall include the reason for utilization of the bypass stack. They shall be maintained at the facility for a minimum of the most recent three-year period and made available to Air Quality Division of the PCDEM, or the Department, upon request. [Rules 62-4.070(3) and 62-210.700, F.A.C.] Comments: According to the records and Mr. Gignac, the By-Pass Stack was never used while ink was being applied. 30. Catalytic Oxidizer Destruction Efficiency Testing: Within the six (6) month period prior to the expiration date of this permit and prior to submittal of the operation permit renewal application (see Specific Condition No. 43.), the permittee shall test the catalytic oxidizer stacks inlets and outlets to determine VOC destruction efficiency and document compliance with Specific Condition Nos. 23, 24, 25, and 26. A Method 9 VE test shall be performed simultaneously with one (1) of the three (3) Method 25/25A runs required in order to determine VOC destruction efficiency. A copy of the test data shall be submitted to the Air Quality Division of the PCDEM and the Air Compliance Section of the Southwest District Office of the Department within 45 days of testing. [Rule 62-297.310, F.A.C.] Comments: I discussed the stack test requirement with Mr. Gignac. I stated that the test will need to be performed no later than 6 months prior to the permit expiration date 10/24/13. 31. Catalytic Oxidizer Volatile Organic Compound Destruction Efficiency Test Methods: Compliance with the emissions and testing requirements of Specific Condition Nos. 20, 23, 24, 25, 26, and 30 shall be demonstrated using EPA Methods 1, 2, 3, 4, and 25 or 25A (see Specific Condition No. 30). [Rule 62-297.401, F.A.C.] 32. Additional Catalytic Oxidizer Testing Requirements: Compliance with the VOC destruction efficiency requirement and the controlled stack emission limitations shall be conducted using the methods and procedures as described in the attached FDEP DARM Guidance Memos (see attached FDEP DARM Guidance Memos DARM-OGG-2 and DARM-OGG-04 (Attachment 1)). During the compliance test, the VOC content of the ink shall either be determined by using data from the most recent MSDS or an EPA Method 24A test. The data on the VOC concentration in each ink shall be submitted with the compliance test results. The amount of each ink used during the compliance test shall be determined using available meters or other information and shall be submitted with the compliance test report. Any alternative method for determining VOC content may only be used after written approval is obtained from the Department. [Rules 62-4.070 (3) and 62-297.310, F.A.C.; Construction Permit 1030240-011-AC] Comments: There were no tests due to be performed during this on-site inspection. 34. Press Line No. 4 Operation During Testing: All testing of the TEC Systems Quantum 2000 catalytic oxidizer in accordance Specific Condition No. 30 shall be accomplished while operating Heat-Set Lithographic Press Printing Line No. 4 at 90 - 100% of the maximum "Printing Ink" utilization rate (defined as the press line operating under normal production conditions). Failure to submit a statement of the status of the operation of the print line during the test period or operating at conditions which do not reflect normal operating conditions, may invalidate the test. The test report shall also include the catalytic oxidizer exhaust gas temperature, the catalytic oxidizer stack gas flow rate and velocity, the change in temperature across the catalyst bed, and the inlet and outlet VOC concentrations from the catalytic oxidizer emission tests. [Rules 62-4.070(3), 62-297.310(2), and 62-297.310 (8), F.A.C.; Construction Permit 1030240-009-AC] 35. Testing Notification: The permittee shall notify the Air Quality Division of the PCDEM at least 15 days prior to the date on which each formal compliance test is scheduled, of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating each test. [Rule 62-297.310(7)(a)9., F.A.C.] Comments: Testing was not being performed on this incinerator today. 36. Hazardous Air Pollutant/Volatile Organic Compound Material Usage and Emission Records(1): In order to document compliance with the requirements of Specific Condition Nos. 20 (Heat-Set VOC limit), 21 (material usage limits), and 4 (Facility-wide HAP limit), HAP-/VOC-containing material usage and emission records shall be maintained. In order to account for their different catalytic oxidizer control efficiencies, separate material usage and emission entries shall be kept for materials used on EU 001 (Heat-Set Press Line Nos. 1, 2 and 3) and for materials used on EU 005 (Heat-set Lithographic Printing Line No. 4). These records shall be updated at least monthly and shall be completed by the end of the following month. The records shall include the following: The facility name, facility ID No. (1030240), and EU name and EU number (e.g., Heat-set Press Lines, EU’s 001/005); The month and year; The quantity of "As Applied" ink (by name or identification number) used, indicating the amount of each used (e.g. pounds) and the Line it was used on (i.e., either used on Heat-set Press Line Nos. 1,2 and 3 (EU 001), or used on Heat-set Press Line No. 4 (EU 005)); HAP and VOC content (as applied, percent by weight) for each type of ink utilized, A calculation of potential HAP and VOC emissions(1); (pounds per month) from each ink based on the information in C. and D. above; and controlled HAP and VOC emissions based on the most recent tested applicable catalytic oxidizer control efficiency; The quantity of Fountain Solution utilized (pounds per month); The quantity of Fountain Solution disposed and/or reused (pounds per month); The quantity of Fountain Solution utilized (pounds per month), less disposal and/or reuse; A calculation of fugitive and controlled HAP and VOC emissions (pounds per month) from Fountain Solution(1) based on H. above, the HAP and VOC contents (percent by weight) for Fountain Solution, and any applicable oxidizer control efficiency, including control efficiency used; The plant-wide usage (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC) (each reported separately); The plant-wide disposal and/or reuse (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC) (each reported separately); The plant-wide usage (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC) (each reported separately); The plant-wide disposal and/or reuse (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC) (each reported separately); The plant-wide usage (gallons and/or pounds per month) of Blanket Wash and Meter Roller Cleaner (MRC), less disposal and/or reuse (each reported separately); A calculation of HAP and VOC emissions (pounds/month) from Blanket Wash and MRC based on H. above, their respective HAP and VOC content (percent by weight) and any applicable oxidizer control efficiency, including control efficiency used; A monthly total for all of the above Heat-Set HAP and VOC emissions; and a cumulative most recent consecutive 12-month running total of Heat-Set HAP and VOC emissions and material usages (i.e. for Heat-Set inks, for Heat-Set Fountain Solutions, and for plant-wide Wash Solutions(2)). Each consecutive 12-month VOC total shall include an assumed 1.0 tons/year for miscellaneous heat-set fugitive emission and 0.22 tons/year for natural gas combustion(3) (or the calculated tons/year VOC emissions based on actual natural gas usage for that 12 month period). Substitution of a "non-VOC" containing solution shall not require utilization records, however a log entry is still required stating that a "non-VOC solution is in use". A "non-VOC" solution is defined as a solution which indicates no VOC content per an EPA Method 24 test. [Rule 62-4.070(3), F.A.C.; Pinellas County Code Section 58-90; Construction Permits 1030240-009-AC and 1030240-011-AC] Comments: The facility was keeping records that complied with items A. through P. above. A copy of the record is attached to the compliance file. 37. Emission Calculations: Controlled emission calculations shall be based on the most recent tested VOC destruction efficiency for the applicable catalytic oxidizer. The controlled emission calculations shall be based on the revised VOC destruction efficiency effective on the date of testing, unless otherwise notified in writing by the Air Quality Division of the PCDEM or the Department. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Sect. 58-90; Construction Permits 1030240-009-AC and 1030240-011-AC] Comments: The emissions calculations recorded by the facility were based on the most recent VOC Destruction Efficiency (DE) tests in which a 97.2 % DE was determined. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No lower production Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: The highest VOC emissions (Mar, 11’) = 2.55 tons/yr. Records review Mar, 11’ – Jan, 12’ Highest total VOCS (April, 10’) = 5.8 tons/yr were emitted for EUs 001, 003, and 005 |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030240 | OWNER Cox Target Media, Inc. | FACILITY NAME Val-Pak Direct Marketing Systems, Inc. |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE March 6, 2012 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE March 3, 2010 |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | Received 4/1/11 and reviewed 4/5/11 |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| March 6, 2012 | March 9, 2012 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs | Copy of spreadsheet is attached to the compliance folder |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) |  |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.