| 1030264 74736 |
| --- |
| FACILITY: Better Business Forms, Inc. | PERMIT ID: 393 |
| Largo Plant | DISTRICT: Southwest |
| ADDRESS: 10950 Belcher Road | CONTACT PHONE: |
| Largo, FL | 727-545-8703 |
| ARMS NO: 1030264 001 | PERMIT NO: | Expiration Date: 1/28/2009 Renewal Date: 11/29/2008 |
|  | 1030264-005-AO |  |
|  |  | Test Due Date: N/A |
| EMISSION UNIT DESCRIPTION : 24 Presses. ( Flexographic, UV, and Lithographic). Current Operation permit allows for 36 presses (3 flexographic, 7 UV lithographic, and 26 cold-set lithographic) |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | September 8, 2010 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: Permit File reviewed prior to inspection |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: Mr. Barrett was not available, toured the facility with Chip Williams. |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Don Huttlin? |  | Yes |  | No |
|  | Comments: Yes The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Michael Barrett? |  | Yes |  | No |
|  | Comments: Yes The facility contact’s e-mail is: barrettm@bbfprinting.com |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: Mr. Barret maintains the, permit copy and VOC/HAP emissions records in his office. 4. Emission Limits. In order to establish the facility as a non-Title V minor source* of VOC and HAP emissions, the following emission operation limits shall apply: Pollutant Facility-wide Emission limits (tons/consecutive 12 month period) Total Volatile Organic Compounds (VOC) 49.0** Individual Hazardous Air Pollutants (HAP) 9.0 Total Hazardous Air Pollutants (HAP) 18.0 (* Title V Minor Source Note: Based on the above limitations this facility is considered a synthetic minor non-Title V source.) Exceeding the major facility threshold for HAPs and/or VOCs may subject the facility to Title V permitting and the requirements of 40 CFR 60, Subpart-KK. ** VOC - 11.2 pounds per hour, based upon a monthly average. [Construction Permit 1030264-003-AC, Rules 62-210.200(PTE), 62-210.200 (130) and 62-213.420(3)(c)1., F.A.C.] Comments: The highest reported emissions were _2.24_tons VOC and 16.7 per 12 months totals. The individual HAP .204 tons, and 1.79 tons total HAPS/12-month period for the months of Oct 2009, Feb 2010, & July 2010 respectively. Reviewed records for the months of August 2009 through July 2010. (See record copies). The emissions did not exceed the permit limitations. 5. Printing Presses. The maximum total number of operational printing presses at this facility is limited to 43. [Permit No. 1030264-003-AC] Comments: The facility is only currently operating 24 presses. 1- Lithographic web (soy ink), 9 - Lithographic web (UV ink), 1- Lithographic Sheet fed ( UV ink), 1- Silkscreen pres uses (solvent or UV ink), 6 Flexographic pressed (water base ink), 4 Flexographic presses (UV ink) and 2 Flexographic presses (water base and UV ). The economy has resulted in lay off of employees and reduction of hours the facility removed older presses. 6. Operating Changes. Any proposed change to this source that will cause the limitations of this permit to be exceeded--such as design-parameter changes or an increase in emissions may be considered a modification and must be reported. The permittee shall notify the Air Permitting Section of this office and the Pinellas County Department of Environmental Management (PCDEM) of any changes and receive written approval from this office of the changes prior to implementing the changes. [Rule 62-4.070(3), F.A.C.] Comments: There are no changes in operations projected at this time. The facility recently renewed permit for the current operations. 7. Objectionable Odor. The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants from this plant which cause or contribute to an objectionable odor. Objectionable odor is defined as “Any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance.” [Rules 62-296.320(2) and 62-210.200, Definitions - (Objectionable Odor), F.A.C. & Pinellas County Code, Section 58-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- None; Wind direction – Easterly Upwind odor level detected- No Odors detected outside of the building. 8. Work Practices. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. A. All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials. This includes returning all VOC and OS containing fluids into closed containers during lengthy periods of time when the equipment is not operating. B. All VOC/OS from washings (equipment clean-up) shall be directed into containers that prevent evaporation into the atmosphere. C. Tightly cover or close all VOC containers when they are not in use. D. Prevent excessive air turbulence across exposed VOCs. E. Immediately confine and clean up VOC spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rules 62-4.070(3) & 62-296.320(1)(a), F.A.C.] Comments: The facility work spaces were clean and organized, and the containers and wash tanks were observed to be closed during presses operations. The drum storage area which previously had drums stored on pallets have secondary containment receptacles under the drums. There were no spills observed on the floors during the tour of the facility. 10. Recordkeeping. A recordkeeping log shall be established and maintained to document compliance with Specific Condition No. 4. At a minimum, the log shall identify and quantify each ink, coating, solvent, and other material used in the printing operations which contain VOCs and/or HAPs. Documentation of solvents consumed, such as during cleanup, may use a mass balance method to determine usage (amount used minus amount collected for disposal or recycle). Monthly records shall be completed by the 10th day of the next month. The permittee shall record and calculate, at a minimum, the following: Monthly record the following: A. Facility Name, Facility ID, Emission Unit ID, Source Description, Date (Month, Day, and Year), and Operator Initials for each measurement B. List by name or identification number, each ink, coating, solvent, or other VOC/HAP containing material used in association with the printing presses during the month and the amount of each material used, in gallons List the VOC content and HAP (individual and total) content (lbs/gal) for each material listed in Item B, above. Summarize the facility-wide VOC emission rates for the most recent month (pounds/hour, monthly average) Summarize the facility-wide HAP (individual and total) emission rates for the most recent month (tons/month) Summarize the facility-wide VOC and HAP (individual and total) emission rates for the most recent consecutive 12-month period (tons/year) G. At the option of the permittee, “purchases” may be used instead of “usage” in determining VOC/HAP emissions, provided that no materials are used which are not purchased. Supporting documentation (“As Supplied” and “As Applied” sheets, MSD (Material Safety Data) sheets, purchase orders, U. S. EPA "VOC DATA SHEETS”, etc.) shall be kept for each ink, coating, solvent and other material used in the printing operations which includes sufficient information to determine VOC and HAP emissions. These records shall be retained on file at the facility for at least three years and shall be made available to the Department and the PCDEM upon request. VOC content of coatings may also be determined by using EPA Method 24 or 24A contained in 40 CFR 60, Appendix A, and adopted by reference in Rule 62-297 F.A.C. New coatings, or the same coatings supplied by a different manufacturer, shall be tested for VOC content using EPA Method 24, 24A, or the above mentioned certification prior to use. Should the permittee wish to claim credit for solvent disposed of as hazardous waste, the VOC and HAP content of the waste must also be determined. If different coatings are used from those included in the application, submit the new coating(s) test results to the Southwest District office along with the application for the operating permit. Testing procedures shall be consistent with the requirements of Rule 62-297, F.A.C. [Rules 62-4.160(14)(b) and 62-4.070(3), F.A.C. and Pinellas County Code, Section 58-90] Comments: Reviewed records for the months of January 2009 – August 2010. A. The records were all headed with facility and permit ID. B. The VOC and HAP records listed gallons used. C. There is separate logs for the recording of the Individual VOC/HAP content for each product. D. The log for the 12 month running VOC and HAP list the hours of operation, with Lbs of VOC for the lbs/hour of VOC during each month. I.E 6.05 lbs VOC/hour for July 2010. E. The record called 12 month runningVOC and monthly HAP tons emitted show 12 month totals. G. Chemical list shows products or items purchase per monthly bases. 8. The production log required by Specific Condition No. 7 shall be updated at least monthly. These records shall be maintained at the facility for a minimum of the most recent three year period and shall be made available to the Department and the Pinellas County Department of Environmental Management, Air Quality Division, upon request [Rule 62-4.070(3), F.A.C. and Pinellas County Code, Section 58-90]. Comments: Reviewed records for the months of August 2009 – July 2010. The record sheets are maintained in the Air Permit Emissions Tracking binder, in Mr. Barrett’s office. (See copies of records attached) 9. Supporting documentation (examples: "As Supplied" and "As Applied" sheets, MSD (Material Safety Data) sheets, EPA data sheets, purchase orders) shall be maintained at the facility for each ink, coating and solvent utilized at the facility. The supporting documentation shall be retained at the facility for a minimum of three years from the date of first implementation and shall provide sufficient information to determine total VOC and HAP emissions. VOC content of coatings may also be determined by using EPA Method 24 or 24A contained in 40 CFR 60, Appendix A, and adopted by reference in Rule 62-297 F.A.C. New coatings, or the same coatings supplied by a different manufacturer, shall be tested for VOC content using EPA Method 24, 24A, or the above mentioned certification prior to use. Should the permittee wish to claim credit for solvent disposed of as hazardous waste, the VOC and HAP content of the waste must also be determined. If different coatings are used from those included in the application, submit the new coating(s) test results to the Southwest District office along with the application for the operating permit. Testing procedures shall be consistent with the requirements of Rule 62-297, F.A.C. [Rules 62-4.160(14)(b) and 62-4.070(3), F.A.C.]. Comments: The MSD sheets for the products used at each presses work stationed are numbered and kept in binders in the press area first floor. The products used at each work station are cross referenced to Mr. Barrett’s records in his Master Copy Record in his office. The Master list is updated monthly and the book number is reference to which book contains the MSD sheet. Mr. Williams state he updates the MSD sheets, which are based on the purchase invoices monthly. They maintain a Master list of products. (See copy) 11. Plant Operation-Problems. If the permittee is temporarily unable to comply with any of the conditions of the permit due to breakdown of equipment or destruction by hazard of fire, wind or by other cause, the permittee shall immediately notify the Department. Notification shall include pertinent information as to the cause of the problem, and what steps are being taken to correct the problem and to prevent its recurrence, and where applicable, the owner's intent toward reconstruction of destroyed facilities. Such notification does not release the permittee from any liability for failure to comply with Department rules. [Rule 62-4.130, F.A.C.] Comments: : I did not observe any plant-operation problems during the inspection 13. Record Retention. The records required by Specific Condition No. 10 shall be maintained on-site or electronically available on-site for a minimum of the most recent three (3) year period and made available to the Department and the PCDEM, Air Quality Division, upon request. [Rule 62-4.070(3), F.A.C. and Pinellas County Code, Section 58-90] Comments: The facility records were observed back to 2007. 14. Annual Operating Report. The permittee shall submit to the PCDEM, Air Quality Division each calendar year on or before March 1, a completed DEP Form 62-210.900(5), "Annual Operating Report (AOR) for Air Pollutant Emitting Facility," for the preceding calendar year. [Rule 62-210.370(3)(a)2 F.A.C.] Comments: The annual operating report for calendar year _2009__ was submitted on 2/22/2010. 15. Permit Renewal. A completed application to renew this operating permit shall be submitted to the Air Program of the Southwest District Office of the Department and the PCDEM no later than 60 days prior to the expiration date of this permit… [Rules 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900] Comments: The permit application is due to be submitted on, or before 11/29/08 |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: No new presses on site |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Work force reduction Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Cardboard, labels, ink and clear stencil Comments: : The facility got rid of some of the older model presses, and they continue to look for better products with less VOC and HAPs. No product changes at this time |
| Closing Conference: The facility appears to be in compliance at this time. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: September 20, 2010 |
| ACCESS? | ( | ARMS? | ( |

EASSIR  (

| AIRS ID 1030264 | OWNER Better Business Forms, Inc. | FACILITY NAME Largo Plant |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE 9/17/2010 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report 2009 | 2/22/2010 and 5/28/2010 review complete |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 9/8/2010 | 9/17/2010 |  |  | Access Data base |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs |  |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) |  |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  | Access Data base |
| Applicable requirements |  |  |  | Access Data base |
| Inventory of emission units |  |  |  | Access Data base |
| Enforcement history |  |  |  | Access Data base |
| Compliance activities |  |  |  | Access Data base |
| Findings and recommendations |  |  |  | Access Data base |
| COMMENTS H:\users\wpdocs\airqual\Air_Compliance\AQI\1030264 74736.doc |

Other Comments

Prepared by:	   Shea Jackson		Date: 		9/17/2010

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.

Better Business Forms, Inc.  Largo Plant

10950 Belcher Road, Largo

Project Id:	74736	Permit No: 1030264-005-AO	Arms Number: 0264 001

Inspector:	Shea Jackson	Inspection Date / Time: 9/8/2010  / _______

Source (EU):	24 Presses. ( Flexographic,  UV, and Lithographic).  Current Operation permit allows for 36 presses (3 flexographic, 7 UV lithographic, and 26 cold-set lithographic)

# Description:	[This is the compactor for the cardboard.  There were no odors or visible emissions during the outside observations. ]

Better Business Forms, Inc.  Largo Plant

10950 Belcher Road, Largo

Project Id:	74736	Permit No: 1030264-005-AO	Arms Number: 0264 001

Inspector:	Shea Jackson	Inspection Date / Time: 9/8/2010  / _______

Source (EU):	24 Presses. ( Flexographic,  UV, and Lithographic).  Current Operation permit allows for 36 presses (3 flexographic, 7 UV lithographic, and 26 cold-set lithographic)

# Description:	[This is the cyclone for the paper shredder.  There were no odors or visible emissions during the outside observations. ]