1030278 003 66743

| FACILITY: Jabil Circuit Company | PERMIT ID: 2411 |
| --- | --- |
| Jabil Florida | DISTRICT: Southwest |
| ADDRESS: 10800 Roosevelt Boulevard | CONTACT PHONE: |
| St. Petersburg, FL | 727-803-7497 |
| ARMS NO: 1030278 001 | PERMIT NO: | Expiration Date: 5/6/07 Renewal Date: 11/7/06 |
|  | 1030278-009-AV & 1030278-011-AC |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Roosevelt facility - 10 conveyorized wave solder machines. Emissions exit the building via a trunk line to two roof-mounted stacks (25 feet high) (Bench top VOC emissions are tracked here) |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | 27 January 2009 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | +A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: The Title V permit renewal application process for this facility was finalized on 1/26/09. This inspection was performed on 1/27/09. (one day after issuance of the new permit). The permit now in force is 1030278-10-AV, which expires on 1/26/14. The construction permit, 1030278-011-AC was modified and expires on 07/02/2009. However, the AC permit modified the Title V permit renewal application and that process has concluded with the issuance of the Title V Permit on 1/26/09. Thus, no further action is due re: the expiration of the AC permit. |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: Carol Michel, Scott Erickson and Allen Peters answered my questions, provided the VOC logs and accompanied me in the tour of the facilities. |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Michael Gross? |  | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Carol A. Michel? |  | Yes |  | No |
|  | Comments: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
|  |  |  | Inspection Note: The facility is current operating under two permits, 1030278-009-AV & 1030278-011-AC. The construction permit allows authorizes a combination of the individual volatile organic compound (VOC) and total hazardous air pollutant (HAP) emission limits for each of the Emission Units 001, 003 and 004 into a global (including all three emission units) VOC limit and a global (including all three emission units) HAP limit. It also increases the global HAP limit to 5.0 tons per year (TPY). It also deletes the VOC and HAP content limits in Specific Condition No. 4 in Section III. A. of Title V Operation Permit 1030278-009-AV. The conditions from the construction permit will be indicated, otherwise the conditions are from the Title V permit. This permit or a copy thereof shall be kept at the work site of the permitted activity. [APPENDIX TV-4, TITLE V CONDITION 12(12)] Comments: Ms. Michel provided copies of Title V permit 1030278-10-AV and the modified 1030278-011-AC permit, both of which were being kept on-site. Renewals. Prior to one hundred eighty (180) days before the expiration of a permit issued pursuant to Chapter 62-213, F.A.C., the permittee shall apply for a renewal of a permit using forms incorporated by reference in the specific rule chapter for that kind of permit. [Rule 62-4.090(1), F.A.C.] Comments: The Title V permit application was submitted on time on 11/06/06. 2. General Pollutant Emission Limiting Standards. Objectionable Odor Prohibited. The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants which cause or contribute to an objectionable odor. [Rule 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- none; Wind direction – South Upwind odor level detected-none. 3. General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The facility shall comply with the following: (a) All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials. (b) All VOC/OS from washings (equipment clean-up) shall be directed into containers that prevent evaporation into the atmosphere. (c) Tightly cover or close all VOC containers when they are not in use. (d) Prevent excessive air turbulence across exposed VOC surfaces. (e) Immediately confine and clean up VOC spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rule 62-296.320(1)(a), F.A.C.] Comments: There were no detectable VOC or OS odors anywhere on the production floor. 4. Prevention of Accidental Releases (Section 112(r) of CAA). If required by 40 CFR 68, the permittee shall submit to the implementing agency: A. A risk management plan (RMP) when, and if, such requirement becomes applicable; and B. Certification forms and/or RMPs according to the promulgated rule schedule. [40 CFR 68] Comments: Section 112(r) of CAA does not apply to this facility since it does not use or emit any of the chemicals listed under 40 CFR 68.130. 5. The "Statement of Compliance" required to be submitted to this office and to the EPA shall be submitted at the same time as the Annual Operating Report. {Note to Permittee: see Appendix TV-4, Nos. 24 and 51.} [Rules 62-213.420(4), -213.440(3), and -4.070(3), F.A.C.] Comments: The Statement of Compliance of calendar year 2008 was submitted on 3/4/09. 6. Unregulated Emissions Units and/or Activities. Appendix U-1, List of Unregulated Emissions Units and/or Activities, is a part of this permit. [Rule 62-213.440(1), F.A.C.] Comments: Nothing has been added to Appendix U-1 list of Unregulated Emissions Units and/or Activities. 7. Insignificant Emissions Units and/or Activities. Appendix I-1, List of Insignificant Emissions Units and/or Activities, is part of this permit. [Rules 62-213.440(1), -213.430(6), and -4.040(1)(b), F.A.C.] Comments: Nothing has been added to Appendix I-1, List of Insignificant Emissions Units Essential Potential to Emit (PTE) Parameters 1. Capacity. Each facility shall operate no more than the following number of conveyorized wave-solder lines: EU ID No. ____Facility____ Number of conveyorized wave-solder lines 001 Roosevelt Facility 10 003 MLK Facility 10 004 Gandy Facility 16 [Application received July 23, 2001; Rules 62-4.160(2) & -210.200, F.A.C., Definitions - (PTE)] [Effective Date: January 31, 2005] Comments: There are no wave solder machines at the Roosevelt facility. There is one (1) wave solder at the MLK facility. There are six (6) wave solder machines at the Gandy facility. Emission Limitations and Standards 5. Volatile Organic Compound (VOC) and Hazardous Air Pollutant (HAP) Emissions Limitations - The following global (combined emissions from the Roosevelt, MLK, and Gandy Facilities) emission limits apply: a. total emissions of VOCs shall not exceed 242.6 tons in any 12 consecutive month period; and b. total emissions of HAPs shall not exceed 5.0 tons in any 12 consecutive month period. [Rule 62-210.200, F.A.C. (“Potential to Emit”); as requested in Construction Permit application received March 24, 2008] per 1030278-011-AC Permitting Note: These limits include VOC and HAP emissions from thinners, fluxes and non-VOC solvents. The facilities currently use isopropanol as a thinner and degreaser solvent, and a variety of alcohol-based fluxes. A change in the composition or usage that will result in an emissions increase above permitted levels will require a modification to this permit, approved by the Department prior to implementation. Comments: The highest reported emissions were 2.40 tons VOC, and 0.0 tons HAPS in the 12 period ending 12/31/08. 4. To ensure compliance with facility wide condition no. 3, the VOC content and HAP content of the thinner, flux, and degreaser solvent used at the facilities are limited as follows: (a) The maximum VOC content of each material, in pounds per gallon (lb/gal), shall not exceed the following: Material Used VOC Content Thinner 6.7 Flux 6.6 Non-VOC solvent 0.0 (b) The total HAP content of each material, in lbs/gal, shall not exceed the following: Material Used HAP Content Thinner 0.0 Flux 0.0 Non-VOC solvent 0.0 Permitting Note: The facility currently uses isopropanol, 856 Flux (or similar), and Ionox BC as its thinner, flux, and degreaser solvent, respectively. A change in the composition or usage that will result in an emissions-increase above permitted levels will require a modification to this permit, approved by the Department prior to implementation. [Effective Date: January 31, 2005] Comments: The facility eliminated the use of HAPs containing materials. Recordkeeping and Reporting Requirements 10. Facility Specific VOC and HAP Containing Materials Usage Records - Each facility (emission unit) specified in Specific Condition 4., shall maintain a log to document compliance with Specific Condition No. 5. At a minimum, the log shall identify and quantify all VOC and/or HAP containing materials used in the production of printed-circuit boards for each facility. Documentation of solvents consumed, such as during solvent cleanup, may use a mass-balance method to determine usage (amount used minus amount collected for disposal or recycle). The following information shall be recorded by the 10th day of the following month at each facility: a. facility name, facility ID No., emission unit ID No., and description (e.g., Jabil Circuit, Inc., 1030278, EU 001, Roosevelt Facility); b. monthly usage of each VOC and HAP containing material (gallons/month); c. VOC and/or HAP content (lbs/gallon) of each item in b., above; d. total HAP emissions (lbs/month or tons/month) based on b. and c., above; e. total VOC emissions (lbs/month or tons/month) based on b. and c., above; and f. cumulative total VOC and HAP emissions for the most recent 12 consecutive month period (tons/12 consecutive months) based on d. and e., above. The log shall be maintained electronically by the Environmental Health and Safety (EHS) team. The EHS team will also maintain a cumulative log for all emissions. The log shall be accessible from all three facilities. Supporting documentation (Material Safety Data Sheets, purchase orders, U.S. EPA "VOC DATA SHEETS”, etc.) shall be kept for each thinner, flux, solvent, and other VOC and/or HAP containing materials used in the production of printed circuit boards that includes sufficient information to determine VOC and HAP emissions. The records shall be maintained for five years and made available to the Department and the Pinellas County Department of Environmental Management (PCDEM) upon request. [Rules 62-4.070(3), 62-4.160, and 62-213.205(1)(i) F.A.C.] per 1030278-011-AC Comments: Reviewed records for the months of January 2008 through December 2008. The facility was in compliance with record-keeping requirements a. thru f. above. 11. Global VOC and HAP Containing Materials Usage Records - In addition to the requirements of Specific Condition No. 10., the Environmental Health and Safety team (located at the Gandy facility) shall maintain a cumulative log for all emission units. The cumulative log shall be completed by the 20th day of the following month. At a minimum, the log shall contain the following information: a. facility name, facility ID No., emission unit ID No., and description (e.g., Jabil Circuit, Inc., 1030278, EUs 001, 003 and 004, Roosevelt, MLK and Gandy Facilities); b. the global, 12 consecutive month total of VOC emissions for all three facilities (lbs or tons); and c. the global, 12 consecutive month total of HAP emissions for all three facilities (lbs or tons). The location of the Environmental Safety and Health Department can be changed by notifying the Department and the PCDEM within 15 days of the change. [Rules 62-296.500(2)(b) and 62-4.070(3), F.A.C.; Pinellas County Code, Section 58-90] per 1030278-011-AC Comments: Reviewed records for the months of Reviewed records for the months of January 2008 through December 2008. The facility was in compliance with record-keeping requirements a. thru c. above. 7. Annual Operating Report for Air Pollutant Emitting Facility. The Annual Operating Report for Air Pollutant Emitting Facility (DEP Form No. 62-210.900(5)) shall be completed each year and submitted to the PCDEM by March 1 of the following year. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 2007 was submitted on 3/3/08. |
|  |  |  | Valid Permit [Rule 62-210.300] The Title V permit renewal application process for this facility was finalized on 1/26/09. This inspection was performed on 1/27/09. (one day after issuance of the new permit). The permit now in force is 1030278-10-AV, which expires on 1/26/14. The construction permit, 1030278-011-AC was modified and expires on 07/02/2009. However, the AC permit modified the Title V permit renewal application and that process has concluded with the issuance of the Title V Permit on 1/26/09. Thus, no further action is due re: the expiration of the AC permit. |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating Yes No Comments: There are no wave solder machines at the Roosevelt facility. There is one (1) wave solder at the MLK facility. There are six (6) wave solder machines at the Gandy facility. |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: The overall reduction in emissions is due to reduced production. The facility has eliminated the use of HAPs altogether. |
| Closing Conference: The facility was found to be in compliance with applicable rules and permit conditions. |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: March 12, 2009 |
| ACCESS? | ( | ARMS? | ( |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030278 003 66743.doc