| 1030279 001 57354 |
| --- |
| FACILITY: Weber Marking Systems, Inc. | PERMIT ID: 343 |
| Tape & Label Engineering, Inc. | DISTRICT: Southwest |
| ADDRESS: 2950 47th Avenue North | CONTACT PHONE: |
| St. Petersburg, FL | 727-527-6686 |
| ARMS NO: 1030279 001 | PERMIT NO: | EXPIRATION DATE: |
|  | 1030279-005-AO | 12/17/07 |
| EMISSION UNIT DESCRIPTION: Flexographic Printing Operation: 25 Flexographic Printing Presses that will print labels on pre-manufactured, adhesive-backed paper. Inks are dried with heat and UV light by equipment associated with the presses. No controls. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | 10 April 2007 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: |  | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Joe Ibrahim? |  | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Dan Evinger? |  | Yes |  | No |
|  | Comments: |
| IN | MNC | SNC | B. Specific Conditions: |
|  |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: Mr. Evinger showed me a copy of the permit 1030279 005 AO 2. This facility shall not cause, suffer, or permit the discharge of air pollutants that cause or contribute to objectionable odor. [Rule 62-296.320(2), F.A.C.; Pinellas Co. Ordinance 52-178] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor detected- none; Wind direction – North Upwind odor detected-none. Operating Changes. Any proposed change to this source that will cause the limitations of this permit to be exceeded--such as design-parameters changes or an increase in emissions above the allowables--may be considered a modification and must be reported to this office and the Pinellas County Department of Environmental Management (PCDEM) prior to implementing the change for proper processing. [Rule 62-4.070(3), F.A.C.; Permit Number 1030279-002-AC] . Comments: Mr. Evinger stated that Weber Marking Systems is in the process of phasing out operations at its 47th Ave N facility in St. Petersburg. On 4/10/07, the day of the inspection, Weber was operating with 5 presses; 6 presses had been dismantled and shipped to Chicago and 5 others had been disconnected electrically and made non functional by separation into 2 parts each. The last day of operations at the 47th Ave. N facility in St. Petersburg will be April 27th, 2007, per Mr. Brian Gallagher, EHS Director in the Chicago Corporate Headquarters of Weber International. 5. Emission Limits. The facility is subject to the following operational limits: Pollutant Emission Limits (tons/consecutive 12 month period) Volatile Organic Compounds (VOC) 24.0 Total Hazardous Air Pollutants (HAP) 9.9 [Permit Number 1030279-002-AC] Comments: Reviewed records for the months of January 2006 thru February 2007. The highest reported emissions for VOCs were recorded in the month of August 2006 with 1.135 tons of VOCs . Total HAP emissios were 0.0 lbs for the past 12 months at the end of the month of February 2007. The laminating activities where glue was used and HAPS emitted, were eliminated in March 2006. The laminating activities were “sourced out”. The last day of operations at the 47th Ave. N facility in St. Petersburg will be April 27th, 2007, per Mr. Brian Gallagher, EHS Director in the Chicago Corporate Headquarters of Weber International. 6. Work Practices. The permittee shall not store, pump, handle, process, load, unload, or use in any process or installation volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The following procedures shall be utilized to minimize pollutant emissions: A. Maintain tightly fitting cover, lids, etc, on all containers of VOC/OS when they are not being handled, tapped, etc. B. Prevent excessive air turbulence across exposed VOC/OS's. C. Where possible and practical, procure/fabricate a tightly fitting cover for any open trough, basin, bath, etc. of VOC/OS so that it can be covered when not in use. D. All fittings, valve lines, etc. shall be properly maintained. E. All VOC/OS spills shall be attended to immediately and the waste properly disposed of, recycled, etc. [Rules 62-4.070(3) & 62-296.320(1)(a), F.A.C.] Comments: The facility kept tightly fitting covers and lids or on all containers of VOC/OS when they were not being handled. 7. Objectionable Odor. The permittee shall not cause, suffer, allow, or permit the discharge of air pollutants from this plant which cause or contribute to an objectionable odor. Objectionable odor is defined as “Any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance.” [Rules 62-296.320(2) and 62-210.200, Definitions-(Objectionable Odor), F.A.C.; Pinellas County Code, Section 58-178; Permit No. 1030279-002-AC] Comments: There were no leaks, spills or fugitive emissions in the production area and emissions were kept to a minimum in the work area. 10 Recordkeeping. In order to document compliance with VOC and HAP emission limitations in Specific Condition No. 5, the permittee shall: Monthly record the following: The amount of each VOC and/or HAP containing material* (by identification number) used** in gallons or pounds (all records shall be in the same units). The VOC and/or HAP content (percent by weight) of coatings and solvents used. Calculated monthly total VOC and total HAP emissions, in tons. The current consecutive 12-month total of VOC and total HAP, in tons. *This includes, but is not limited to, inks, coating, solvents (including perchloroethylene, ethyl acetate, and perchloroethylene contained in Cyrel) **At the permittee’s option, materials received (e.g., as determined by purchases) may be used in lieu of amount of each material used. If the cumulative previous 12-month total HAP emissions are greater than 80% of the limit specified in Specific Condition No. 5 (i.e., 7.9 tons total HAP), the permittee shall implement daily recordkeeping. The daily records shall be kept as in Specific Condition 10.A. above and shall be added to the previous 11 monthly totals to demonstrate the facility is remaining below the permitted threshold. Daily recordkeeping shall remain in effect until the previous 12 month total HAP emissions are less than 80% of the limit (7.9 tons total HAP). All records shall include the Facility ID, Emission Unit ID, and Date (Month, Day, and Year) on each page. Monthly records shall be completed within 30 days of the end of the month. Daily records (if required) shall be completed within 5 calender days. Supporting documentation (MSD sheets, purchase orders, etc.) shall be kept for each material which includes sufficient information to determine VOC and/or HAP emissions. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Section 58-90; Permit Number 1030279-002-AC] Comments: The facility was in compliance with items A. and B. above. The highest running cumulative 12 mos. total was 7.234 tons of VOCs at the end of the month of August 2006 and 0.013 tons HAPs at the end of the month of January 2006. Reviewed records for the months of January 2006 thru February 2007. 11. Record Retention. The records required by Specific Condition No. 10 shall be maintained for a minimum of the most recent three (3) year period and made available to the Department and the PCDEM upon request. [Rule 62-4.070(3), F.A.C.] Comments: I saw records dating back to 2004. 12. AOR. Submit to the Air Compliance Section of the PCDEM each calendar year on or before March 1, completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility," for the preceding calendar year. [Rule 62-210.370(3)(a)2 F.A.C.] Comments: The annual operating report for calendar year 2006 was submitted on 2/28/07. 13. Permit Renewal. A completed application to renew this operating permit shall be submitted to the Air Program of the Southwest District Office of the Department no later than 60 days prior to the expiration date of this permit. [Rules 62-4.090, 62-210.300(2), 62-210.900, and 62-4.070(3)] Comments: The permit application is due to be submitted on, or before 10/18/07. I read the permit conditions to Mr. Evinger. |
|  |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: Emissions reduction resulted from the out sourcing of laminated products “which eliminated the use of glue, the source of HAPS at Weber. |
| Closing Conference: The last day of operations at the 47th Ave. N facility in St. Petersburg will be April 27th, 2007, per Mr. Brian Gallagher, EHS Director in the Chicago Corporate Headquarters of Weber International. |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? |  | EASIIR? |  |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030279 001 57354.doc