| 1030313 80618 |
| --- |
| FACILITY: Hit Promotional Products, Inc. | PERMIT ID: 578 |
|  | DISTRICT: Southwest |
| ADDRESS: 7150 Bryan Dairy Rd. | CONTACT PHONE: |
| Largo, FL | 727-541-5561 |
| ARMS NO: 1030313 001 | PERMIT NO: | Expiration Date: 1/20/2015 Renewal Date: 11/21/2014 |
|  | 1030313-008-AF |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Bryan Dairy Rd location - Printing and Manufacturing Operations: Printing, Screening, Gluing, Non-Halogenated Solvent Degreasing |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | April 10, 2012 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Arthur W. Schmidt IV? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Jake Gaines? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit on-site was reviewed by Air Quality Staff. 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: A description of and cause of noncompliance; and The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: There were no noncompliance issues during the compliance year 7. Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 11’ was submitted 3/29/12. 8. Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to the Pinellas County Department of Environmental Management, Air Quality Division (Compliance Authority) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The facility is currently expanding its embroidery unit. It expects to submit a Title V permit request to increase its VOC limit from 95 tons/yr to 143 tons/yr. A.2. VOC/HAP Emission Limitations: Emissions of volatile organic compounds (VOCs) and hazardous air pollutants (HAPs), as defined in Rule 62-210.200, F.A.C., shall not exceed the following: Pollutant Emission Limitation VOCs 44.5 tons per any 12 consecutive month period Individual HAP 9.4 tons per any 12 consecutive month period Total HAPs 20.0 tons per any 12 consecutive month period [Rule 62-210.200(PTE), F.A.C.; Construction Permit 1030313-006-AC] Comments: Highest total VOC’s 12-mo consecutive total (Jan, 12’) = 62.546 tons/yr Individual HAP 12-mo consecutive total (Jan, 12’)(Glycol Ethers) = 3.755 tons/yr Total HAP’s 12-mo consecutive total (Jan, 12’) = 4.5766 tons/yr ***Hit Promotional has increased its VOC limit to 95 tons effective 1/13/11 facility-wide. Therefore, the VOC emission limit for this particular condition no longer applies. A.3. General Standards: Objectionable Odor: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. If the Department and/or Pinellas County Department of Environmental Management (PCDEM) receives a valid odor complaint, the Department and/or PCDEM reserves the right to require that odor control measures/work practices be implemented. [Rules 62-210.200 (“Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: No objectionable odors detected during the inspection A.4. General Standards: Volatile Organic Compound Emissions and/or Organic Solvent Emissions: The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The following procedures shall be utilized to minimize pollutant emissions: a. all equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials; b. all VOC/OS from washings (equipment clean up) shall be directed into containers that prevent evaporation into the atmosphere; c. tightly cover or close all VOC/OS containers when they are not in use; d. prevent excessive air turbulence across exposed VOC/OS; and e. immediately confine and clean up VOC/OS spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rules 62-4.070(3) and 62-296.320(1)(a), F.A.C.; Construction Permit 1030313-006-AC] Comments: All equipment observed including screen printers, did not have leaking fittings. All VOC/OS from washings were directed into sealed containers to prevent evaporation. A.5. General Standards: Visible Emissions: No person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rule 62-296.320(4)(b)1, F.A.C.] Comments: No visible emissions observed during the compliance inspection A.6. General Standards: Unconfined Particulate Matter: All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320, F.A.C. Unconfined particulate emissions generated from activities such as trimming, sanding, sawing, machining, surface grinding, or other such activities shall be controlled by good work practices and normal good housekeeping procedures. [Rules 62-4.070(3) and 62-296.320(4)(c), F.A.C.; Construction Permit 1030313-006-AC] Comments: No unconfined particulate matter observed during the compliance inspection A.7. Unconfined Particulate Matter Opacity: As an indicator that the precautions to control unconfined particulate matter emissions as required by Specific Condition No. A.6. are adequate, visible emissions from the facility should not exceed 5%. If this value is exceeded, it shall not be a violation in and of itself, but an indication that additional control precautions and/or work practices beyond those of Specific Condition No. A.6. may be necessary. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030313-006-AC] Comments: No unconfined particulate matter observed during the compliance inspection A.8. Emissions Calculations: In order to document compliance with Specific Condition No. A.2., the permittee shall calculate VOC and HAP emissions based on the following methodologies: a. Flexographic Printing Operations: Emissions = Flexographic ink usage (gallons) x VOC or HAP content (pounds/gallon) x 0.98.* (*Permitting Note: This is based on a 2% credit for VOC retention in the product.) b. All other printing operations: Emissions = Usage (gallons) x VOC or HAP Content (pounds/gallon). [Rule 62-4.070(3), F.A.C.; Construction Permit 1030313-006-AC] Comments: The facility does not use a Flexographic Printing Operation. Therefore, it only uses method b A.9. VOC Recordkeeping: In order to document compliance with the VOC emission limitations of Specific Condition No. A.2., the permittee shall maintain monthly VOC records. The records must clearly indicate which materials are used solely in flexographic printing and therefore qualify for the 2 percent VOC retention credit (see Specific Condition No. A.8.a.). The records shall contain, at a minimum, the following: a. facility name, facility ID No., emission unit ID No., and description (i.e., Hit Promotional Products, Inc., 1030313, EU 001, Printing and Manufacturing Operations); b. total quantity (gallons) of each VOC-containing material (e.g., inks, coatings, thinners, solvents, etc.) used for the month; c. VOC content (lbs/gallon) of each VOC-containing material (e.g., inks, coatings, thinners, solvents, etc.) used for the month; d. calculated monthly total (tons/month) VOC emissions (based upon b. and c. above); and e. cumulative total of the VOC emissions for the most recent 12 consecutive month period (tons per 12 consecutive month period). [Rule 62-4.070(3), F.A.C.; Construction Permit 1030313-006-AC] Comments: The facility meets a-e of the VOC recordkeeping condition. A copy of the record is provided with this inspection A.10. HAP Recordkeeping: In order to document compliance with the HAP emission limitations of Specific Condition No. A.2., the permittee shall maintain monthly HAP records which shall contain, at a minimum, the following: a. facility name, facility ID No., emission unit ID No., and description (i.e., Hit Promotional Products, Inc., 1030313, EU 001, Printing and Manufacturing Operations); b. total quantity (gallons) of each HAP containing material (i.e., inks, coatings, thinners, solvents, etc.) used for the month; c. HAP content (lbs/gallon) of each HAP-containing material (i.e., inks, coatings, thinners, solvents, etc.) used for the month; d. calculated monthly total (tons/month) HAP emissions for each individual HAP and for total HAPs (based upon b. and c. above); and e. cumulative total of the HAP emissions for each individual HAP and total HAPs for the most recent 12 consecutive month period (in tons per 12 consecutive month period). [Rule 62-4.070(3), F.A.C.; Construction Permit 1030313-006-AC] Comments: The facility meets a-e of the HAPs recordkeeping condition. A copy of the record is provided with this inspection A.11. Daily Recordkeeping: If any month results in individual HAP emissions exceeding 80% of the major source threshold (i.e., 8.0 tons of any individual HAP) for the most recent 12 consecutive month period, the facility shall keep daily records beginning on the next operational day following when the monthly calculation was completed. These records shall be added daily to the most recent eleven (11) calendar month’s emissions totals. When one month of daily records is completed, the facility shall make a determination if daily recordkeeping must be continued. If individual HAP emissions continue to exceed 80% of the individual HAP major source threshold, then daily record keeping shall continue. If individual HAP emissions do not exceed 80% of the HAP major source threshold, then the facility may return to monthly recordkeeping. The daily records shall include cumulative 12-month emission totals to demonstrate compliance with the emission limitations of Specific Condition No. A.2. The use of purchases as a proxy for usage is not allowed for the monthly and daily recordkeeping. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030313-006-AC] Comments: During no time during the compliance year did the individual HAP emission exceed 80% of the major source threshold. The highest single HAP emission, Glycol Ethers = 3.757 tons/yr (47% of 8 ton limit) A.12. Documentation: Supporting documentation (e.g., MSD sheets, “As Supplied” sheets, “As Applied” sheets, purchase orders, inventory records, production records, etc.) for the records required by Specific Condition Nos. A.9., A.10., and A.11. which include sufficient information to determine VOC and HAP emissions, shall also be kept. Based on the VOC and/or HAP emission limitations, “quantity purchased” may not be used to satisfy the requirement of “quantity used”. [Rule 62-4.070(3), F.A.C.] Comments: MSD sheets were reviewed. The facility has discontinued its use of Toluene. A.13. Records Completion and Retention: The monthly records required by Specific Condition Nos. A.9. and A.10. shall be completed by the 10th day of the following month. Daily records, if required by Specific Condition No. A.11. shall be completed within three (3) business days. The records shall be maintained in a form suitable for inspection by the Department and/or PCDEM upon request and shall be retained at the facility for at least a three (3) year period. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Section 58-90] Comments: The facility completes its records by the 10th day of each month. Daily records are completed within 3 business days. A.14. Reporting Equipment Changes: The facility shall submit an updated equipment list (Appendix E) to the Department and to the Pinellas County Department of Environmental Management (PCDEM) once a year by January 30th. Any printing operation equipment changes that would result in an increase in actual emissions could be considered a modification and may require an air construction permit prior to installation. [Rules 62-4.070(3), 62-210.200 (“Modification”), 62-210.300 (Permits Required), and 62- 210.300(3)(b)1., F.A.C.; Construction Permit 1030313-006-AC] Comments: There were no equipment changes during the compliance year |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No the facility is trying to reduce its HAP usage. The VOC emissions have increased because of facility expansion. Additionally, a third facility is planned.[jm] Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: Highest total VOC’s 12-mo consecutive total (Jan, 12’) = 62.546 tons/yr Individual HAP 12-mo consecutive total (Jan, 12’)(Glycol Ethers) = 3.755 tons/yr Total HAP’s 12-mo consecutive total (Jan, 12’) = 4.5766 tons/yr Highest total VOC = 45.34 tons/yr (May, 11’). Total HAP = 6.39 tons/yr (Dec, 10’). Individual HAP = 0.173 tons/yr individual HAP Lead (Apr, 11’) |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030313 | OWNER Hit Promotional Products, Inc. | FACILITY NAME |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE Sep 26, 2008 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE June 1, 2011 |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | Received 3/31/11 and reviewed 4/5/11 |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| Apr 10, 2012 | Apr 13, 2012 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs | Copy of 12-mo consecutive HAP and VOC totals |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) |  |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.