| 1030313 88759 |
| --- |
| FACILITY: Hit Promotional Products, Inc. | PERMIT ID: 578 |
|  | DISTRICT: Southwest |
| ADDRESS: 7150 Bryan Dairy Rd. | CONTACT PHONE: |
| Largo, FL | 727-541-5561 |
| ARMS NO: 1030313 001 | PERMIT NO: | Expiration Date: 7/7/2018 Renewal Date: 11/24/2017 |
|  | 1030313-011-AV1030313-011-AV |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : 7150 Bryan Dairy Road, Largo location - Printing and Manufacturing Operations: Printing, Screening, Gluing, Non-Halogenated Solvent Degreasing |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | June 5, 2014 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Arthur W. Schmidt IV? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: jrschmidt@hitpromo.net |
| 4. | Is the facility contact still: Jake Gaines? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: jgaines@hitpromo.net? |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | FW2. Objectionable Odor Prohibited. No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. If the Department and/or Pinellas County Air Quality Division (PCAQD) receives a valid odor complaint, the Department and/or PCAQD reserves the right to require that odor control measures/work practices be implemented. [Rules 62-210.200 (“Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: There were no objectionable odors detected during the inspection FW3. General Standards: Volatile Organic Compound Emissions and/or Organic Solvent Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The following procedures shall be utilized to minimize pollutant emissions: a. all equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials; b. all VOC/OS from washings (equipment clean up) shall be directed into containers that prevent evaporation into the atmosphere; c. tightly cover or close all VOC/OS containers when they are not in use; d. prevent excessive air turbulence across exposed VOC/OS; and e. confine and clean up VOC/OS spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rule 62-296.320(1)(a), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: All equipment observed including screen printers, did not have fittings that leaked. All VOC/OS from washings (rags) were directed into sealed containers to prevent evaporation. These red containers were marked as hazardous waste. The rags are taken off-site for recycling. FW4. General Visible Emissions. No person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity equal to or greater than 20% opacity. EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. This regulation does not impose a specific testing requirement. [Rule 62-296.320(4)(b)1, F.A.C.] IN MNC SNC N/A FW5. Unconfined Particulate Matter. No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction; alteration; demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. Unconfined particulate emissions generated from activities such as trimming, sanding, sawing, machining, surface grinding, or other such activities shall be controlled by good work practices and normal good housekeeping procedures. [Rule 62-296.320(4)(c), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A FW6. Unconfined Particulate Matter Opacity. As an indicator that the precautions to control unconfined particulate matter emissions as required by Specific Condition No. FW5. are adequate, visible emissions from the facility should not exceed 5%. If this value is exceeded, it shall not be a violation in and of itself, but an indication that additional control precautions and/or work practices beyond those of Specific Condition No. FW5. may be necessary. [Rule 62-4.070(3), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: Comments: There are no visible emissions associated with this source. The source is an OS/VOC emission facility only. FW7. Annual Operating Report. The permittee shall submit an annual report that summarizes the actual operating rates and emissions from this facility. Annual operating reports shall be submitted to the Compliance Authority by April 1st of each year. [Rule 62-210.370(3), F.A.C.] IN MNC SNC N/A Comments: The 2013 EAOR was not reviewed by AQD because it is a Title V facility. FDEP/Tallahassee is the responsible party to review this inventory. FW8. Annual Statement of Compliance. The permittee shall submit an annual statement of compliance to the compliance authority at the address shown on the cover of this permit within 60 days after the end of each calendar year during which the Title V permit was effective. [Rules 62-213.440(3)(a)2. & 3. and (3)(b), F.A.C.] IN MNC SNC N/A Comments: received 2/18/14 and reviewed 3/3/14 FW9. Prevention of Accidental Releases (Section 112(r) of CAA). If and when the facility becomes subject to 112(r), the permittee shall: a. Submit its Risk Management Plan (RMP) to the Chemical Emergency Preparedness and Prevention Office (CEPPO) RMP Reporting Center. Any Risk Management Plans, original submittals, revisions or updates to submittals, should be sent to: RMP Reporting Center, Post Office Box 10162, Fairfax, VA 22038, Telephone: (703) 227-7650. b. Submit to the permitting authority Title V certification forms or a compliance schedule in accordance with Rule 62-213.440(2), F.A.C. [40 CFR 68] IN MNC SNC N/A Comments: The facility is aware of this condition. A.2. VOC Emissions Standard (Multi-Unit). The maximum VOC emissions from E.U. Nos. 001, 002 and 003 combined shall not exceed 143.5 tons per any consecutive 12 month period. [Rule 62-210.200(PTE), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: Total VOC’s for 12-month consecutive total period (May, 13’ – April, 14’) did not exceed 143.5 tons. The highest consecutive total = 103.21 tons A.3. Individual and Total HAP Emissions Standards (Multi-Unit). The maximum HAP emissions from E.U. Nos. 001, 002 and 003 combined shall not exceed the following: Total HAPs shall not exceed 23.5 tons per any consecutive 12 month period. Any Individual HAP shall not exceed 9.4 tons per any consecutive 12 month period. {Permitting note: Because of the limits specified above, this facility is not a major source of Total HAPs or Individual HAP.} [Rule 62-210.200(PTE), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: Total HAP’s for 12-month consecutive total period (May, 13’ – April, 14’) did not exceed 23.5 tons. The highest consecutive total = 6.43 tons A.4. Emissions Calculations. In order to document compliance with Specific Condition No. A.2. and A.3., the permittee shall calculate VOC and HAP emissions based on the following equation: Emissions (in tons) = Usage x (VOC or HAP Content) /2000; Where: Usage = gallons of material used. VOC or HAP Content = pounds of VOC or HAP per gallon of material. [Rule 62-4.070(3), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: The facility does not have a flexographic printing operation. The facility uses option b to calculate emissions. A copy of the records is attached to the compliance file A.5. Reporting Requirements. See Appendix RR, Facility-Wide Reporting Requirements, for additional reporting requirements. [Rule 62-4.070(3), F.A.C.] IN MNC SNC N/A Comments: The facility reported emissions for all three emission units. It’s reported for the 12-month consecutive totals and monthly totals A.6. VOC Recordkeeping. In order to document compliance with the VOC emission limitations of Specific Condition No. A.2., the permittee shall maintain monthly VOC records for each emissions unit. The records shall contain, at a minimum, the following information. a. The facility name, facility ID No., and E.U. Nos. (i.e., Hit Promotional Products, Inc., 1030313, E.U. Nos. 001, 002 & 003). b. For each emissions unit (E.U. Nos. 001, 002 and 003) include the following information: 1) total quantity (gallons) of each VOC-containing material (e.g., inks, coatings, thinners, solvents, etc.) used for the month; 2) VOC content (lbs/gallon) of each VOC-containing material (e.g., inks, coatings, thinners, solvents, etc.) used for the month for each emissions unit; 3) total (calculated) VOC emissions (in tons) for the month. c. For E.U. Nos. 001, 002 and 003 combined, include the total (calculated) VOC emissions (in tons) for the most recent 12 consecutive month period. [Rule 62-4.070(3), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: The facility meets conditions a-c of the VOC recordkeeping provision A.7. HAP Recordkeeping. In order to document compliance with the HAP emission limitations of Specific Condition No. A.3., the permittee shall maintain monthly HAP records for each emissions unit, which shall contain, at a minimum, the following information. The facility name, facility ID No., and emission unit ID No. (i.e., Hit Promotional Products, Inc., 1030313, EU Nos. 001, 002 & 003). For each emissions unit (E.U. Nos. 001, 002 and 003) include the following information: total quantity (gallons) of each HAP containing material (i.e., inks, coatings, thinners, solvents, etc.) used for the month; the Individual HAP and Total HAPs content (lbs/gallon) of each HAP-containing material (i.e., inks, coatings, thinners, solvents, etc.) used for the month; the total (calculated) emissions (in tons) for each Individual HAP and for the Total HAPs for the month. For E.U. Nos. 001, 002 and 003 combined, include the (calculated) emissions (in tons) for each Individual HAP for the most recent 12 consecutive month period. For E.U. Nos. 001, 002 and 003 combined, include the (calculated) emissions (in tons) for the Total HAPs for the most recent 12 consecutive month period. [Rule 62-4.070(3), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: The facility meets conditions a-d of the HAP recordkeeping provision. A.8. Documentation. Supporting documentation (e.g., MSD sheets, “As Supplied” sheets, “As Applied” sheets, purchase orders, inventory records, production records, etc.) for monthly records, which includes sufficient information to determine VOC and HAP emissions, shall also be maintained. The use of purchases as a proxy for usage is not allowed for the monthly recordkeeping. [Rule 62-4.070(3), F.A.C.; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: MSD sheets were available for review A.9. Records Completion and Retention. All monthly records shall be completed by the 10th day of the following month. The records shall be maintained in a form suitable for inspection by the Department and/or PCAQD upon request and shall be retained at the facility for at least a five (5) year period. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Section 58-90; Construction Permit No. 1030313-010-AC] IN MNC SNC N/A Comments: The monthly records are completed by the 10th day of the following month. A.10. Reporting Equipment Changes. The permittee shall submit an updated equipment list (Appendix E) for each emissions unit to the Department and to the PCAQD once a year by January 30th for the previous year if equipment was added to the facility. Any printing operation equipment changes that would result in an increase in actual emissions could be considered a modification and may require an air construction permit prior to installation. {Permitting Note: Addition of equipment that would be subject to any unit specific applicable requirement (e.g. equipment meeting VOC RACT requirements in accordance with Rule 62-296.500, F.A.C.) would trigger the need for a construction permit prior to installation.} [Rules 62-4.070(3), 62-210.200 (“Modification”), 62-210.300 (Permits Required), and 62-210.300(3)(b)1., F.A.C.; Construction Permit 1030313-010-AC] IN MNC SNC N/A Comments: There were no equipment changes reported during the compliance year. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no pollution prevention activities during the compliance period |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030313 | OWNER Hit Promotional Products, Inc. | FACILITY NAME |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE June 5, 2014 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE May 29, 2013 |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | 2013 was reviewed by FDEP/Tallahassee |
| DONE N/A | Statement of compliance | Received 2/18/14 and reviewed on 3/3/14 |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| June 5, 2014 | June 9, 2014 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs | Copy of records is attached to the inspection report |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) |  |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.