| 1030313 77344 |  |
| --- | --- |
| FACILITY: Hit Promotional Products, Inc. | PERMIT ID: 3489 |
|  | DISTRICT: Southwest |
| ADDRESS: 7150 Bryan Dairy Rd. | CONTACT PHONE: |
| Largo, FL | 727-541-5561 |
| ARMS NO: 1030313 002 | PERMIT NO: | Expiration Date: 12/31/2014 Renewal Date: 7/4/2014 |
|  | 1030313-009-AC |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : 8226 118th Avenue North, Largo location - Screen Printing Operation: Phased construction for 25 Lawson Trooper Silk Screen Printer, 75 Mini Silk Screen Printers, model 1422, and 25 Lawson Electric Dryers |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | June 1, 2011 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Arthur W. Schmidt IV? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Jake Gaines? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection comment: This is the initial construction permit which became effective on January 13, 2010 EU 002 has only been in operation for 4 weeks. No HAP containing solvents are used in the factory. General Conditions [62-4.160, F.A.C.] 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: a. A description of and cause of noncompliance; and b. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: The facility did not have any noncompliance issues during the compliance year Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] Comments: No circumvention was observed during the inspection. Individual screen cleaners at workstations were capped when not in use. 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] Comments: All solvent containers were sealed when not in use. 2-55 gallon drums of screen cleaners were capped 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An “objectionable odor” means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C.] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- none ; Wind direction – E/10 mph Upwind odor level detected-none 9. Unconfined Particulate Emissions: a. No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. b. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. c. Reasonable precautions include the following: (1) Paving and maintenance of roads, parking areas and yards. (2) Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. (3) Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. (4) Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. (5) Landscaping or planting of vegetation. (6) Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. (7) Confining abrasive blasting where possible. (8) Enclosure or covering of conveyor systems. Comments: No unconfined particulate emissions observed Administrative Requirements 7 Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 11’ was submitted on 3/23/11. 8 Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to PCDEM (Compliance Authority) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on 12/31/14. An application is required to be submitted no later than 7/4/14. Emissions Standards A.2. VOC Emissions Standard (Multi-Unit): The maximum VOC emissions from E.U. ID Nos. 001 and 002 combined shall not exceed 95.0 tons per any consecutive 12 month period. [Permit Application dated 9/27/2010 and Rule 62-210.200(PTE), F.A.C.] Comments: 45.34 tons/yr (May, 11’). EU 002 began operation 5/6/11. Record attached to compliance file. A.3. Individual and Total HAP Emissions Standards (Multi-Unit): The maximum HAP emissions from E.U. ID Nos. 001 and 002 combined shall not exceed the following: a. Total HAP shall not exceed 20.0 tons per any consecutive 12 month period. b. Any Individual HAP shall not exceed 9.4 tons per any consecutive 12 month period. [Permit Application dated 9/27/2010 and Rule 62-210.200(PTE), F.A.C.] Comments: 0.173 tons/yr(Apr. 11’) Lead individual HAP 6.39 tons/yr (Dec, 10’) total HAP A.4. Emissions Calculations: In order to document compliance with Specific Condition No. A.2. and A.3., the permittee shall calculate VOC and HAP emissions based on the following equation: Flexographic Printing Operations: Emissions (in tons) = Flexographic ink usage x (VOC or HAP Content) x 0.98*/2000 Where: Flexographic ink usage = gallons of material used. VOC or HAP Content = pounds of VOC or HAP per gallon of material. * =Based on a 2% credit for VOC retention in the product. All other printing operations: Emissions (in tons) = Usage x (VOC or HAP Content) /2000 Where: Usage = gallons of material used. VOC or HAP Content = pounds of VOC or HAP per gallon of material. [Rule 62-4.070(3), F.A.C.] Comments: The facility uses only option b when calculating emissions A.5. General Standards: Objectionable Odor: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. If the Department and/or Pinellas County Air Quality Division (PCAQD) receives a valid odor complaint, the Department and/or PCAQD reserves the right to require that odor control measures/work practices be implemented. [Rules 62-210.200 (“Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: No objectionable odors detected during the inspection. Facility does not use HAP containing solvents. A.6. General Standards: Volatile Organic Compound Emissions and/or Organic Solvent Emissions: The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The following procedures shall be utilized to minimize pollutant emissions: all equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials; all VOC/OS from washings (equipment clean up) shall be directed into containers that prevent evaporation into the atmosphere; tightly cover or close all VOC/OS containers when they are not in use; prevent excessive air turbulence across exposed VOC/OS; and immediately confine and clean up VOC/OS spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rules 62-4.070(3) and 62-296.320(1)(a), F.A.C.; Construction Permit 1030313-006-AC] Comments: All equipment observed including screen printers, did not have leaking fittings. All VOC/OS from washings were directed into sealed containers to prevent evaporation. A.7. General Standards: Unconfined Particulate Matter: All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320, F.A.C. Unconfined particulate emissions generated from activities such as trimming, sanding, sawing, machining, surface grinding, or other such activities shall be controlled by good work practices and normal good housekeeping procedures. [Rules 62-4.070(3) and 62-296.320(4)(c), F.A.C.; Construction Permit 1030313-006-AC] Comments: No unconfined particulate matter observed A.8. Unconfined Particulate Matter Opacity: As an indicator that the precautions to control unconfined particulate matter emissions as required by Specific Condition No. A.7. are adequate, visible emissions from the facility should not exceed 5%. If this value is exceeded, it shall not be a violation in and of itself, but an indication that additional control precautions and/or work practices beyond those of Specific Condition No. A.7. may be necessary. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030313-006-AC] Comments: No unconfined particulate matter observed. A.9. Notification of Operation Commencement: The permittee shall notify the Compliance Authority in writing of the date of initially commencing operation of the EU No. 002, no later than 15 days after that date. Commencing operation means setting into operation of the emissions unit for any purpose. [Rule 62-4.070, F.A.C., and Rule 62-210.200, F.A.C., (Definition of Commence Operation)] Comments: The facility is under an AC and is aware that it will notify the Department and Air Quality in writing of the date of the initial commencement. A.10. VOC Recordkeeping: In order to document compliance with the VOC emission limitations of Specific Condition No. A.2., the permittee shall maintain monthly VOC records. The records must clearly indicate which materials are used solely in flexographic printing and therefore qualify for the 2 percent VOC retention credit (see Specific Condition No. A.4.a.). The records shall contain, at a minimum, the following: The facility name, facility ID No., and E.U. ID Nos. (i.e., Hit Promotional Products, Inc., 1030313, EU No. 001 & 002). For each emissions unit (E.U. No. 001 and 002) include the following information: total quantity (gallons) of each VOC-containing material (e.g., inks, coatings, thinners, solvents, etc.) used for the month; VOC content (lbs/gallon) of each VOC-containing material (e.g., inks, coatings, thinners, solvents, etc.) used for the month for each emissions unit; The total (calculated) VOC emissions (in tons) for the month. For E.U. Nos. 001 and 002 combined, include the total (calculated) VOC emissions (in tons) for the most recent 12 consecutive month period. [Rule 62-4.070(3), F.A.C.] Comments: The facility meets a-c of the VOC recordkeeping condition. A copy of the record is provided with this inspection A.11. HAP Recordkeeping: In order to document compliance with the HAP emission limitations of Specific Condition No. A.3., the permittee shall maintain monthly HAP records which shall contain, at a minimum, the following: The facility name, facility ID No., and emission unit ID No. (i.e., Hit Promotional Products, Inc., 1030313, EU No. 001 & 002). For each emissions unit (E.U. No. 001 and 002) include the following information: total quantity (gallons) of each HAP containing material (i.e., inks, coatings, thinners, solvents, etc.) used for the month; the Individual HAP and Total HAPs content (lbs/gallon) of each HAP-containing material (i.e., inks, coatings, thinners, solvents, etc.) used for the month; the total (calculated) emissions (in tons) for each Individual HAP and for the Total HAPs for the month. For E.U. Nos. 001 and 002 combined, include the (calculated) emissions (in tons) for each Individual HAP for the most recent 12 consecutive month period. For E.U. Nos. 001 and 002 combined, include the (calculated) emissions (in tons) for the Total HAPs for the most recent 12 consecutive month period. [Rule 62-4.070(3), F.A.C.] Comments: The facility meets a-d of the HAPs recordkeeping condition. A copy of the record is provided with this inspection A.12. Daily Recordkeeping: If any month results in VOC or individual HAP emissions exceeding 90% of the major source threshold (i.e., 90.0 tons of VOC or 9.0 tons of any individual HAP) for the most recent 12 consecutive month period, the facility shall keep daily records beginning on the next operational day following the date the monthly calculation was completed. These records shall be added daily to the most recent eleven (11) calendar month’s emissions totals. When one month of daily records is completed, the facility shall make a determination if daily recordkeeping must be continued. If VOC or individual HAP emissions continue to exceed 90% of the major source threshold, then daily record keeping shall continue. If VOC and individual HAP emissions do not exceed 90% of the major source threshold, then the facility may return to monthly recordkeeping. The daily records shall include cumulative 12-month emission totals to demonstrate compliance with the emission limitations of Specific Condition Nos. A.2. and A.3. [Rule 62-4.070(3), F.A.C.] Comments: Based on the reviewed monthly records the facility The faciity’s individual limits individual HAP is 9.4 tons/yr and the THAP is 20 tons/yr, VOC’s = 44.5 tons/yr. Nov, 09’ totals = 3.58 tons/yr (toluene) and THAP = 7.8 tons/yr, 34.5 tons/yr VOC’s A.13. Documentation: Supporting documentation (e.g., MSD sheets, “As Supplied” sheets, “As Applied” sheets, purchase orders, inventory records, production records, etc.) for the daily and monthly records, which includes sufficient information to determine VOC and HAP emissions, shall also be maintained. The use of purchases as a proxy for usage is not allowed for the monthly and daily recordkeeping. [Rule 62-4.070(3), F.A.C.] Comments: The facility supplied its supporting documentation for review. Additionally, the facility eliminated its use of Toluene. A.14. Records Completion and Retention: All monthly records shall be completed by the 10th day of the following month. Daily records, if required, shall be completed within three (3) business days. The records shall be maintained in a form suitable for inspection by the Department and/or PCAQD upon request and shall be retained at the facility for at least a three (3) year period. [Rule 62-4.070(3), F.A.C.; Pinellas County Code, Section 58-90] Comments: The facility completes its records by the 10th day of each month. Daily records are completed within 3 business days. A.15. Reporting Equipment Changes: The facility shall submit an updated equipment list (Appendix E) to the Department and to the PCAQD once a year by January 30th. Any printing operation equipment changes that would result in an increase in actual emissions could be considered a modification and may require an air construction permit prior to installation. (Permitting Note: Addition of equipment that would be subject to any unit specific applicable requirement (e.g. equipment meeting VOC RACT requirements in accordance with Rule 62-296.500, F.A.C.) would trigger the need for a construction permit prior to installation.) [Rules 62-4.070(3), 62-210.200 (“Modification”), 62-210.300 (Permits Required), and 62-210.300(3)(b)1., F.A.C.; Construction Permit 1030313-006-AC] Comments: There were no equipment changes since the opening of the facility 4 weeks prior. All screen printers were installed |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Eliminated Toluene; HAP Free process at this emission unit. Comments: The facility eliminated its use of Toluene and designed a screen printing process that is HAP free. |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |