| 1030400 80640 |
| --- |
| FACILITY: Lockheed Martin Aeronautics Company | PERMIT ID: 2773 |
| Pinellas Park | DISTRICT: Southwest |
| ADDRESS: 9300 28th Street North | CONTACT PHONE: |
| Pinellas Park, FL | 727-578-6940 |
| ARMS NO: 1030400 002 | PERMIT NO: | Expiration Date: 4/19/2016 Renewal Date: 2/19/2016 |
|  | 1030400-012-AF |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Miscellaneous metal parts coating of non-aerospace parts. This emission unit uses the same booths as emission unit 001a Blowtherm 30' X 14' X 12' and a Global Finishing Solutions 30' X 18' X 9'. |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | August 28, 2012 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: NOTIFICATION REQUIREMENTS B.5.Notification of Operation Commencement: The permittee shall notify the Compliance Authority in writing of the date of commencing operation of the new paint booth, no later than fifteen (15) days after that date. Commencing operation means setting into operation of any emissions unit for any purpose. [Rule 62-4.070, F.A.C., and Rule 62-210.200, F.A.C., (Definition of Commence Operation)] |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: I met on site with Kevin Rzeszut and Emily Harmon |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Steve Cobb? |  | Yes |  | No |
|  | Comments: Yes, no change The Responsible Official/Authorized Representative’s e-mail is: steve.cobb@lmco.com |
| 4. | Is the facility contact still: Kevin Rzeszut? |  | Yes |  | No |
|  | Comments: I met with Mr. Rzeszut and Emily Harmon. She will be the new contact for the facility as Mr. Rzeszut had been filling in for Apurva Desai, the previous facility contact. Ms. Harmon ESH engineer is now maintaining the records at this time. Mr. Reszut stated they will send notification of change of facility contact. The facility contact’s e-mail is: Emily Harmon ? emily.harmon@lmco.com |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( |  |  | Inspection Note: This is the permit became effective on 4/19/11{Permitting Notes: As identified in the permit application dated February 7, 2011, the facility is subject to 40 CFR 63 Subpart HHHHHH – National Emission Standards for Hazardous Air Pollutants: Paint Stripping and Miscellaneous Surface Coating Operations at Area Sources and 40 CFR 63 Subpart WWWWWW – National Emission Standards for Hazardous Air Pollutants: Area Source Standards for Plating and Polishing Operations. Subpart HHHHHH is applicable to facility’s surface coating operations (Emissions Unit Nos. 001 and 002), while Subpart WWWWWW is applicable to the chromate conversion process tank that is part of the chemical film process line. As of the effective date of this permit, these two Subparts have not been adopted by Florida Department of Environmental Protection and therefore are not integrated into this permit. C.1. Operating Limitations: This emissions unit is limited to surface coating of non-aerospace parts and components such as metal signs, metal frames, and other miscellaneous metal parts and products. [Rule 62-210.200(PTE), F.A.C.; Construction Permit 1030400-006-AC] Comments: The facility only uses the both spray booths for the spray painting of aerospace parts under emission unit 001. I observed aerospace parts spraying during inspection. This emission unit 002 is kept active under the permit for the possible use of spray painting other parts or signage. The facility has not uses the spray booths for any other coating projects other then aerospace parts. The emission unit 002 Surface Coating for non-Aerospace Parts and Components does not have material usage records. The facility is recording 0.00 under EU002 because the facility is not spray coating metal signs, frames or any other metal parts that are not aerospace. C.2. VOC RACT Emission Limiting Standards: The permittee shall comply with the following: a. VOC emissions shall not exceed 3.5 lbs. VOC/gallon of coating (excluding water) delivered to a coating applicator in a coating application system that is air dried or forced warm air dried at temperatures up to 194°F; b. all VOC emissions from solvent washings shall be considered in the emission limitations in Specific Condition C.2.a., unless the solvent is directed into containers that prevent evaporation into the atmosphere; c. compliance with Specific Condition No. C.2.a. may be demonstrated for surface coating on a 24-hour weighted average basis for a single emissions unit point with a single emission limit. [Rules 62-296.500(5), 62-296.513(2)(a)2., and 62-296.513(2)(c), F.A.C.] Comments: The facility is aware of this limitation. They currently do not have to meet this requirement when they are applying coatings on aerospace parts and components. C.3. Daily Recordkeeping Requirements: A daily usage log shall be kept to document compliance with the limitations of Condition Nos. A.2 and C.2. At a minimum the log shall contain the following: a. facility name, facility ID No. (1030400), Emissions Unit ID No. (002), Surface Coating of Non-Aerospace Parts and Components; b. date (month/day/year); c. the applicable rule – Rule 62-296.513, F.A.C; d. the application method and substrate type (metal), which is being coated; e. the amount and type of adhesive, coatings (including catalyst and reducer for multi-component coatings), solvent, including exempt compounds; f. what “As Applied” coating was used, indicating quantities used (gallons), lbs. VOC/gallon of coating (excluding water); g. the amount of surface preparation, clean-up, wash-up of solvent (including exempt compounds) used and the VOC content of each; h. a statement of what solvent was used for equipment clean-up; i. the facility shall have on hand completed EPA “As Supplied” and “As Applied” sheets, as applicable, for all paints, coatings, and solvents used. [Rules 62-4.070(3) and 62-296.500(2)(b), F.A.C.] Comments: The facility has not used the 002 for several years, so the records are maintained with zero totals for non usage. The emissions 12 month summary shows no usage for the EU002 emissions C.4. VOC Monthly Recordkeeping Requirements: In order to demonstrate compliance with the emission limitations of Specific Condition No. 4., the permittee shall monthly record the following: a. facility name, facility ID No. (1030400), Emissions Unit ID No. (002), Surface Coating of Non-Aerospace Parts and Components; b. month/year; c. the total quantity (gallons) and VOC content (lbs./gallon) of each VOC containing material used for the month; d. the calculated monthly total VOC emissions, in pounds or tons per month (based upon material VOC content); e. a cumulative total of the VOC emissions for the most recent consecutive 12-month period (tons per consecutive 12-month period). [Rule 62-4.070(3), F.A.C.] Comments: The facility has not used the 002 for several years for any spraying other then aerospace parts. The records are maintained with zero totals for non usage for miscellaneous metal parts or non aerospace parts. The emissions 12 month summary shows no usage for the EU002 emissions since not spray painting miscellaneous metal parts. C.5. HAP Monthly Recordkeeping Requirements: In order to demonstrate compliance with the emission limitations of Specific Condition No. A.2., the permittee shall monthly record the following: a. facility name, facility ID No. (1030400), Emissions Unit ID No. (002), Surface Coating of Non-Aerospace Parts and Components; b. month/year; c. the total quantity (gallons) and HAP content (lbs./gallon) of each HAP containing material used for the month; d. the calculated monthly HAP emissions for each individual HAP, in pounds or tons per month (based upon material HAP content); e. the calculated monthly HAP emissions for total HAP, in pounds or tons per month; f. a cumulative total of the HAP emissions for each individual HAP for the most recent consecutive 12-month period (tons per consecutive 12-month period); g. a cumulative total of HAP emissions for total HAP for the most recent consecutive 12-month period (tons per consecutive 12-month period). [Rule 62-4.070(3), F.A.C.] Comments: The record log sheet noted as EU 001 and 002 Individual HAP emissions Summary rolling 12 month meets the permit conditions listed for a-g. The highest monthly HAP total was August 2011 with 3600.36 lbs for Emission unit 001, 0.00 is recorded for Emission unit 002. The total for all units was 0.1.80 tons (See records). |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: The third Spray booth has been installed in the second building. |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: The facility continues to recycle and reduce VOC products. They have are maintaining 65% in regards to recycling. |
| Closing Conference: I informed Mrs. Harmon. The facility appears to be in compliance. I told her I may contact her if need additional information or records for review |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: September 3, 2012 |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030400 | OWNER Lockheed Martin Aeronautics Company | FACILITY NAME Pinellas Park |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE August 30, 2012 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report |  |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 8/28/12 | 8/31/12 |  |  | in access database |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) | 0 % opacity |
| DONE N/A | Review of facility records and logs | Up to date |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) | No emissions limitations exceedances |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) | Facility maintains operation and maintenance logs for upkeep of spray booths |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  | in access database |
| Applicable requirements |  |  |  | in access database |
| Inventory of emission units |  |  |  | in access database |
| Enforcement history |  |  |  | in access database |
| Compliance activities |  |  |  | in access database |
| Findings and recommendations |  |  |  | in access database |
| COMMENTS |

Other Comments

Prepared by:	   Shea Jackson		Date: 	8/31/12

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.