70952

| FACILITY: Quality Acrylic Baths of Clearwater, Inc. | PERMIT ID: 982 |
| --- | --- |
|  | DISTRICT: Southwest |
| ADDRESS: 12001 44th Street North | CONTACT PHONE: |
| Clearwater, FL | 727-572-6734 |
| ARMS NO: 1030433 001 | PERMIT NO: | Expiration Date: 4/8/2014 Renewal Date: 2/7/2014 |
|  | 1030433-005-AF |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Acrylic/Fiberglass Bath tub manufacturing (use of polyester resins) |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | December 23, 2009 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Monica Potter? |  | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Monica Potter? |  | Yes |  | No |
|  | Comments: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: permit No.: 1030433-005-AF became effective on 04/08/2009 for the continued operation of an acrylic bath tub manufacturing facility. This is a synthetic minor source This permit or a copy thereof shall be kept at the work site of the permitted activity. [62-4.160 F.A.C. - General Condition 12.] Comments: The facility did did not have a copy of the permit on-site. 4. Styrene/VOC Emission Limitations - Facility-wide emissions of volatile organic compounds (VOCs) and styrene, as defined in Rule 62-210.200, F.A.C., shall not exceed the following: Pollutant Emission Limitation VOCs 15.0 tons per any 12 consecutive month period Styrene 9.0 tons per any 12 consecutive month period [Rule 62-210.200, F.A.C. (“Potential to Emit”); Construction Permit 1030433-002-AC] Comments: Highest total VOC emissions = 2.26 tons/yr, highest total HAP emissions = 0.62 tons/yr, highest total styrene emissions = 0.62 tons/yr (May, 09’) 5. General Standards: Objectionable Odor - No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. If the Department or the Pinellas County Department of Environmental Management (PCDEM) receives a valid odor complaint, the Department or PCDEM reserves the right to require that additional odor control measures/work practices be implemented. These measures or practices may, for example, require that building doors and windows be closed when conducting any spray lay-up applications in order to ensure the emissions are captured and discharged with adequate dispersion. [Rules 62-210.200 (“Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: No objectionable odors were detected during the inspection 6. General Standards: Volatile Organic Compound Emissions and/or Organic Solvent Emissions - The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The following procedures shall be utilized to minimize pollutant emissions: a. All resin activities shall be conducted inside the lamination building. b. The lamination exhaust fan will operate during all spray lay-up applications and continue to operate at least 2 hours after all spray lay-up applications have ceased. c. All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions, and spills of solvent materials. d. Tightly cover or close all VOC and/or solvent containing vessels, drums, totes, etc., when they are not in use. e. Immediately confine and clean up VOC and/or solvent spills, and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. f. All solvent from solvent washings (equipment clean-up) shall be directed into containers that prevent evaporation in the atmosphere. [Rules 62-4.070(3) and 62-296.320(1), F.A.C.; Construction Permit 1030433-002-AC] Comments: The facility meets a-f of this condition. The facility has not produced tubs in the last several weeks. 7. General Standards: Unconfined Particulates - All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320, F.A.C. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. Emissions from trimming activities in the trimming booth are controlled by good work practices and an exhaust fan using a filter. Other unconfined particulate emissions generated from trimming (outside the booth), cutting, shaping, and sanding operations performed by hand tools and limited table top equipment are in general controlled by portable shop-vac vacuum collectors and normal good housekeeping procedures. As an indicator that the precautions to control unconfined particulate emissions are adequate, emissions of unconfined particulate matter from the facility should not exceed 5% opacity. If this value is exceeded, it shall not be a violation in and of itself, but an indication that additional control precautions and/or work practices may be necessary. [Rules 62-4.070(3) and 62-296.320(4)(c), F.A.C.; Construction Permit No. 1030433-002-AC] Comments: There were no unconfined particulate emissions observed. The facility has not produced tubs in past several weeks. 8. Modification - Unless otherwise exempt by rule, the permittee shall not initiate any construction, reconstruction, or modification at the facility and shall not install/modify any pollution control device at the facility without obtaining prior authorization from the Department. Modification is defined as: Any physical change or changes in the method of operations or addition to a facility that would result in an increase in the actual emissions of any air pollutant subject to air regulations, including any not previously emitted, from any emission unit or facility. [Rules 62-210.200 (“Modification”) and 62-210.300(1)(a), F.A.C.] Comments: The permit was not modified during the compliance year. 9. Emission Calculations - In order to document compliance with Specific Condition No. 4, the permittee shall calculate VOC and HAP emissions (other than styrene and MMA) based on the following methodology: Material Usage Rate x Species Concentration x Emission Factor = Species Emission Rate Styrene and MMA emission factors shall be determined in accordance with the attached Unified Emission Factors (UEF) for Open Molding of Composites table dated July 23, 2001. [Rules 62-4.070(3) and 62-210.200, F.A.C. (“Potential to Emit”)] Comments: Emission calculations are based on this procedure. A partial copy of the records are attached to the inspection report. 10. Special Compliance Tests - When the Department, after investigation, has good reason (such as complaints, increased visible emissions, or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it may require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emission unit and to provide a report on the results of said tests to the Department and the Pinellas County Department of Environmental Management (PCDEM). [Rule 62-297.310(7)(b), F.A.C.] Comments: No special compliance test required during the compliance year 11. VOC and Styrene Recordkeeping - The permittee shall keep monthly logs to document compliance with the VOC and styrene limitations in Specific Condition No. 4. Usage of materials may be based on inventory at the beginning of the month, receipt of material during the month, and inventory of the materials at the end of the month. Additionally, usage of materials may be based upon purchases, provided no materials are used which are not purchased. The monthly logs shall include, but not be limited to, the following information: a. facility name, facility ID No., emission unit ID No., and description (e.g., Quality Acrylic Baths, Inc., 1030433, E.U. 001, Acrylic Bath Tub Manufacturing); b. month, year, and method used for records (usage or purchase); c. Identify and quantify each resin, coating, solvent, chemical, etc. used at the facility that contains Styrene, MMA, and/or other VOCs. d. appropriate emission factor(s), and method(s) of application (i.e., mechanical atomized, mechanical non-atomized) used to determine styrene, MMA and/or other VOC emissions. e. monthly total of styrene emissions (tons/month); f. monthly total of VOC (including styrene) emissions (tons/ month); g. most recent 12 consecutive month period total of styrene emissions (tons/12 consecutive month period) based on e. above; and h. most recent 12 consecutive month period total of VOC (including styrene) emissions (tons/12 consecutive month period) based on f. above. Documentation of each chemical reclaimed will use a mass balance method to determine usage/emissions (amount used minus amount collected for disposal or recycle). The monthly logs shall be completed by the end of the following month. These records shall be maintained at the facility for at least 3 years and made available to the Department and the Pinellas County Department of Environmental Management (PCDEM) upon request. Supporting documentation such as styrene/VOC content, styrene/VOC emission factors used, MSDS sheets, purchase orders, “As Supplied” data sheets, etc. shall be kept for each chemical and associated products which includes sufficient information to determine emissions. If any month results in total VOC and/or styrene emissions being within 10% of the allowable emission limit in Specific Condition No. 4, for the prior 12 consecutive month period, the monthly log required shall be kept daily. The option of using purchases as a proxy for usage is not allowed for this daily recordkeeping. The daily logs shall include a cumulative 12-month emission total to demonstrate compliance with the emission limitation. These logs shall be completed with 3 business days. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030433-002-AC] Comments: Reviewed records for the months of March, 09’. A partial copy of the records are attached as an example of the record format. The records were complete. 12. Annual Operating Report (AOR) - Each calendar year on or before April 1, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. Note, the annual operating report for calendar year 2008 shall be submitted by May 1, 2009. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the to the Air Compliance section of the Pinellas County Department of Environmental Management. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 2008 was submitted on 1/16/09. The AOR was /reviewed on 4/21/09. 13. Operation Permit Renewal Application - An air pollution operation permit renewal application shall be submitted to the Air Permitting Section of the Southwest District of the Department no later than 60 days prior to the expiration date of the operation permit…. Comments: The permit expires on 4/8/14. An application is required to be submitted no later than 2/7/14. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No less production Highest total VOC emissions = 2.26 tons/yr, highest total HAP emissions = 0.62 tons/yr, highest total styrene emissions = 0.62 tons/yr (May, 09’) Highest Styrene emissions = 0.84tons/yr; Highest HAP emissions = 0.84 tons/yr; Highest VOC emissions = 2.78tons/yr; totals for the Highest month, February, 09’. Records reviewed from January, 08’ - February, 09’ Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030433 | OWNER Quality Acrylic Baths of Clearwater, Inc. | FACILITY NAME |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE 1/4/10 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | Received 1/16/09 and processed on 4/21/09 |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 12/23/09 | 1/4/10 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs | Jan, 08’ – Dec, 09’ |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) | Raw material records were reviewed |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) | Reviewed the flow coaters and the use of the spray booths. The facility changes out the filters at a magnahelic setting at 1”. |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  | EASIIR |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.