| 1030447 88179 |  |
| --- | --- |
| FACILITY: Raytheon Company | PERMIT ID: 1608 |
| C3I Manufacturing | DISTRICT: Southwest |
| ADDRESS: 7887 Bryan Dairy Road | CONTACT PHONE: |
| Largo, FL | 727-302-4793 |
| ARMS NO: 1030447 001 | PERMIT NO: | Expiration Date: 5/24/2015 Renewal Date: 2/23/2015 |
|  | 1030447-004-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Electronic Communications Manufacturing: Electrical Assembly, Paint Touch-up/refinishing, Conformal Coating, Soldering Operations, Wire Marking, Non-Metal Solvent Cleaning, Tetra-Etch Process, and Potting |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | November 19, 2013 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: yes |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: yes, I met with Mr. Pethe to review records and tour the facility |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Andy Whitney? |  | Yes |  | No |
|  | Comments: No, Mr. Pethe stated that Mr. Whtney had left employment a couple months ago, and the new AR Lincoln Sise was announced yesterday. (See attachment) I advised he needed to give written notification of change to FDEP and PCAQ is due within 30 days of change that effects permit status. Mr. Pethe stated he would submit a letterthe 1st of December2013. The Responsible Official/Authorized Representative’s e-mail is: lSise @Raytheon.com |
| 4. | Is the facility contact still: Craig A. Pethé? |  | Yes |  | No |
|  | Comments: yes, The facility contact’s e-mail is: Craig_A_Pethe@raytheon.com |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: This permit became effective on 5/25/10. The permit is a renewal that partially incorporates 1030447-029-AC. The construction permit remains effective General Conditions [62-4.160, F.A.C.] 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. Mr. Pethe showed the copy of the recent permit on his personal computer in his office. 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: A description of and cause of noncompliance; and The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: I inquired if there had been any compliance issues that need to be addressed. He stated no, nothing had occurred this year. I informed him there should be a notification to the state in writing regarding the change to the authorized representative. I advised him should be within 30 days of change, and I believe prior to the change of the authorized representative. Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] Comments: The facility is maintaining the filtration system for the spray booth. They change the filters approximately once every 3 months bases, the last change out for the emission unit referred to as the Vehicle booth was on 9/18/13. Mr. Pethe’ has an employee that oversees the filter and waste disposal, and maintains all booth and hood filter systems to ensure operating properly. I observed all filters to be in place, light paint accumulations and no gaps allowing bypass of spray.(See paint booth filter log) 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] Comments: The booth and hood areas, where most solvent products were observed to be in small 1 to 6 oz containers. I.E. Isopropyl alcohol, Acetone, and Lacquer thinner, and Loctite. The waste receptacles, solvent disposal containers, and solvents were maintained with closed tops. Solvents and hydraulic fluids were contained in flame proof closets. There were no solvent odors detected within the building areas. The only paint odor detected was inside booth with parts recently coated. The gun cleaner and spent solvent containers were covered, closed, and located inside the spray booth. The work spaces are clean and no spills observed. 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An “objectionable odor” means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C.] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- 0 ; Wind direction – northwesterly Upwind odor level detected- 9. Unconfined Particulate Emissions: No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. Reasonable precautions include the following: Paving and maintenance of roads, parking areas and yards. Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. Landscaping or planting of vegetation. Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. Confining abrasive blasting where possible. Enclosure or covering of conveyor systems. Comments: (1) Areas around the building were paved and swept clean in appearance. (2) Application of water or chemicals was not needed as roads were paved, and no demolition or heavy construction activities were on going. (3) No application of suppressants was needed all surfaces were paved and no debris or particulate was coming from inside manufacturing structures. (4) Pavement areas appeared clean swept at the time of inspection. (5) landscape plants surround the property borders, and provide buffers from adjacent facilities. (6). The facility operations performs work activities of , sanding , prep work, prior to painting inside the spray booth. (7) There was no abrasive blasting observed at this facility. (8) There are no conveyor systems associated with this facilities work activities. Administrative Requirements 7 Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year _2012__ was submitted on 4/9/13 to BF._. 8 Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to PCDEM (Compliance Authority) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on 4/24/15. An application is required to be submitted no later than 2/23/15. Not applicable at this time. A.2. Volatile Organic Compound (VOC), Total Hazardous Air Pollutants (HAPs) and Individual HAP Emission Limits: As requested by the permittee and in order to operate the facility as a Synthetic Non-Title V source of VOC and HAP emissions, the following emission limits shall apply facility- wide: Pollutant Tons/consecutive 12-month period Total VOC emissions 32.0 Total HAP emissions 17.2 Individual HAP emissions 9.5 [Rule 62-210.200(PTE), F.A.C.; Construction Permit 1030447-001-AC] Comments: The records were reviewed with Mr. Pethe. The October 2013 emissions records show a 12 month consecutive total of 3.16 tons VOC emissions and 0.57 tons HAPs emissions. The Highest month total during 2013 was for January 3.38 tons VOC emissions and .53 tons HAP emissions. These monthly totals do not exceed the emissions limitations of the permit. The monthly chart for the facility from 1999 to 2013 shows facility maintaining emissions tons below the limitations quoted in above table. There has been a steady reduction of emissions(See record) The facility has removed some of the permitted description operations, such as they are no longer are wave soldering or they do not dip coat IE conformal coating of circuit boards, this operation was out sourced to Jabil Circuits. There is no wire marking because no longer produce cables, and the Tetra Etch Process and Potting was also done away with. Mr. Pethe stated they do mostly assembly work now. The facility has downsized painting operations, increased office space , storage areas and labs. The facility has 50 % production area, 50% reduced work force. (See attachments) A.3. VOC/Organic Solvents (OS) Emissions: The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The facility shall comply with the following: All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials. All VOC/OS from washings (equipment clean-up) shall be directed into containers that prevent evaporation into the atmosphere. Tightly cover or close all VOC containers when they are not in use. Prevent excessive air turbulence across exposed VOCs. Immediately confine and clean up VOC spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rule 62-296.320(1)(a), F.A.C.; Construction Permit 1030447-001-AC] Comments: There are no VOC emissions control devices associated with this facility and its permit. All equipment, pipes, hoses, lids and fittings used were maintained in the work area, no spills observed during the tour. The facility employees are taking precautions to prevent leaks and minimize fugitive solvent evaporation during work activities. The VOC/OS washing during equipment clean up are directed back into containers to prevent evaporation into the atmosphere. All VOC containers were observed to have lids and were closed when not in use. The gun cleaner closed system for the spray booth was located inside the booth area A.4. Objectionable Odors: No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. {Permitting Note: If the Department and/or Pinellas County Department of Environmental Management (PCDEM) receives a valid odor complaint, the Department and/or PCDEM reserves the right to require that odor control measures/work practices be implemented.} [Rule 62-296.320(2), F.A.C. and Pinellas County Code, Section 58-178] Comments: There were no objectionable odors detected outside of the facility building. The only paint and solvent odors evident during this inspection were detected inside the booth areas. A.5. Unconfined Emissions of Particulate Matter (PM): Reasonable precautions to prevent emissions of unconfined particulate matter at this facility include the use of panel filter systems to control paint booth overspray emissions. [Rules 62-296.320(4)(c) and 62-4.070(3), F.A.C.; Construction Permit 1030447-001-AC] Comments: The facility emission unit vehicle spray booth is equipped with a paneled filter system to control paint booth overspray emissions. This booth is used for touch up, not painting entire vehicles. The filters appeared to be in good condition, moderate paint accumulation. Filter change out varies dependent of work demand 1 once a month to every 3 months, due to reductions in paint work levels at this time. There are ½ hoods with paneled filter systems used in the other plant work areas, observed Hood #8 touch up of painted surfaces, Hood #9 -ink usage for labeling is needed, Hood #18 epoxy work, has been temporarily shutdown . The ½ hood areas are equipped with 3 oz cup and air brush to apply paints. These precautions are taken inside the facility building, and no unconfined emissions of PM were observed by passing the filtrations systems. A.6. Fugitive Emissions Opacity Standard: In order to provide reasonable assurance the panel filter systems are adequately controlling emissions of unconfined particulate matter, visible emissions from the paint spray booths should not exceed 5 percent opacity. Exceedance of the 5% limit shall not be considered a violation in and of itself, but an indication that additional control precautions and/or practices may be necessary. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030447-001-AC] Comments: There was no visible emission observed from the spray booth. The stack exits are not visible from ground level as booth is located in toward the center of building. The spray booth was not in operations at this time. A.8. VOC/HAP Recordkeeping: A log shall be maintained to document compliance with Specific Condition No. A.2. At a minimum, the log shall identify and quantify each paint, coating, thinner, solvent, and other material used in the electronic communications equipment manufacturing operations, including all solvent metal cleaning, that contain VOCs and/or HAPs. Documentation of solvents consumed from activities such as paint gun/hose cleanup may use a mass-balance method to determine usage (amount used minus amount collected for disposal or recycle). The permittee shall record and calculate, at a minimum, the following: Monthly (log by the 21st operating day of the next month) 1. Facility Name, Date (Month /Year), Facility ID No. (1030447), and E.U. ID Nos.; 2. Monthly usage of each paint, coating, thinner, solvent, and other material which contain VOCs and/or HAPs (gallons); 3. Density (lbs/gal) and VOC/HAP content (wt %) of each item in A.8.a.2.; 4. Monthly total HAP and individual HAP emissions (lbs or tons); 5. Monthly total VOC emissions (lbs or tons); and 6. Total VOC, total HAP, and individual HAP emissions (tons) for the most recent consecutive 12-month period. If the individual HAP emissions for the most recent consecutive 12-month period exceed 80% of the major-source thresholds (i.e., 8.0 tons), the records required in Specific Condition A.8.a.1. – 4. shall be kept on a daily basis. The permittee shall use this information to ensure that the individual HAP emissions for the upcoming, consecutive 12-month period do not exceed permit limitations. Should the individual HAP emissions for the consecutive, 12-month period fall below 80% of the major-source thresholds; the recordkeeping may revert to monthly. Record the date of paint spray booth filter change-outs. Supporting documentation (MSD Sheets, purchase orders, U. S. EPA "VOC DATA SHEETS”, etc.) shall be kept for each paint, coating, thinner, solvent and other material used in the painting and coating operations which includes sufficient information to determine VOC and HAP emissions. These records shall be retained on file at the facility for at least five (5) years and shall be made available to the local, state, or federal air pollution agency upon request. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030447-001-AC] Comments: The records are maintained on Mr. Pethe’s personal computer system as observed during office meeting. The MSD sheet hard copies are printed and maintained in binders for observation by inspectors and employees . The records named “VOC Usage Report” shows r the facility information, the products listed as used, and for each product the VOC and HAP the product contains, and its content percent %, density lbs/gal for. The facility assumes all products brought into the facility as 100% used. Mr. Pethe’s had copies of the MSD sheets for all products used in personal computer and copied into binders. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No N/A Comments: This facility does not have a specific emission unit with model number. The emission unit description is not accurate as many of the named operations have ceased at this facility. IE Conformal Coating, Soldering Operations, Wire Marking Tetra-Etch Process, and Potting |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No reductions in facility production and employees Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: less HAP and VOC products in use Comments: The facility has reduced productions, to more assembly work. |
| Closing Conference: I informed Mr. Pethe the facility needs to update the responsible official change to prevent it from becoming a non compliance issue. He printed out the recent announcement for Mr. Lincoln Sise.. I told him I would contact him if there are further questions or findings, which deem corrective actions. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: November 21, 2013 |
| ACCESS? | ( | ARMS? | ( |

Raytheon Company  C3I Manufacturing

7887 Bryan Dairy Road, Largo

NO PHOTOS ALLOWED IN THIS FACILITY DUE TO MILTARY CONTRACTS

Project Id:	88179	Permit No: 1030447-004-AO	Arms Number: 0447 001

Inspector:	Shea Jackson	Inspection Date / Time: 11/19/2013  / _______

Source (EU):	Electronic Communications Manufacturing:  Electrical Assembly, Paint Touch-up/refinishing, Conformal Coating, Soldering Operations, Wire Marking, Non-Metal Solvent Cleaning, Tetra-Etch Process, and Potting

# Description:	[NO photo, ]]