1030447 001 66731

| FACILITY: Raytheon Company | PERMIT ID: 1608 |
| --- | --- |
| C3I Manufacturing | DISTRICT: Southwest |
| ADDRESS: 7887 Bryan Dairy Road | CONTACT PHONE: |
| Largo, FL | 727-302-4793 |
| ARMS NO: 1030447 001 | PERMIT NO: | Expiration Date: 6/16/10 Renewal Date: 4/17/10 |
|  | 1030447-003-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Electronic Communications Manufacturing: Electrical Assembly, Paint Touch-up/refinishing, Conformal Coating, Soldering Operations, Wire Marking, Non-Metal Solvent Cleaning, Tetra-Etch Process, and Potting |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | December 16, 2008 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review | ( | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry | ( | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Tom Greenawalt? | ( | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Craig A. Pethé? | ( | Yes |  | No |
|  | Comments: Mr. Dennis Milak is the alternate contact for this faciliy. |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
|  |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: The facility ( did □ did not have a copy of the permit on-site. OPERATIONAL AND EMISISON LIMITATIONS 4. Facility Wide Volatile Organic Compound (VOC), Total Hazardous Air Pollutants (tHAPs) and Individual HAP Emission Limits. As requested by the permittee and in order to operate the facility as a Synthetic Non-Title V source of VOC and HAP emissions, the following emission limits shall apply facility- wide: (a) The total VOC emissions shall not exceed 32.0 tons per consecutive 12-month period. (b) The total HAP emissions shall not exceed 17.2 tons in any consecutive 12- month period. (c) The highest individual HAP emissions shall not exceed 9.5 tons in any consecutive 12-month period. [Rule 62-210.200, F.A.C. – Definitions – (PTE) and Permit No. 1030447-001-AC] Comments: The highest combined total emissions were 2.6 tons VOC and 0.7 tons total HAP, at the end of the month of October 2008. Reviewed records for the last consecutive 12 months dating back to November 2007. The highest total combined single HAPS emissions at the end of the month of October 2008 was 0.028 tons Toluene. 5. VOC/Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The facility shall comply with the following: (a) All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials. (b) All VOC/OS from washings (equipment clean-up) shall be directed into containers that prevent evaporation into the atmosphere. (c) Tightly cover or close all VOC containers when they are not in use. (d) Prevent excessive air turbulence across exposed VOCs. (e) Immediately confine and clean up VOC spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rule 62-296.320(1)(a), F.A.C.] Comments: The facility was in compliance with (a) thru (e) above. There were no detectable odors anywhere in the facility. Solvents were dispensed from sealed containers. There were no spills leaks or fugitive emissions. All waste drums were clearly labeled. 6. Objectionable Odors. No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. {Permitting Note: If the Department and/or Pinellas County Department of Environmental Management (PCDEM) receives a valid odor complaint, the Department and/or PCDEM reserves the right to require that odor control measures/work practices be implemented.} [Rule 62-296.320(2), F.A.C. and Pinellas County Code, Section 58-178]] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- none; Wind direction - SSE Upwind odor level detected-none. 7. General Visible Emissions (VE) Limit. Visible Emissions (VE) from this facility shall not be equal to or greater than 20% opacity. [Rule 62-296.320(4)(b)(1), F.A.C.] Comments: There were no visible emissions emanating from this facility. 8. Unconfined Emissions of Particulate Matter (PM). Reasonable precautions to prevent emissions of unconfined particulate matter at this facility include the use of panel filter systems to control paint booth overspray emissions. [Rules 62-296.320(4)(c) and 62-4.070(3), F.A.C.; Permit No. 1030447-001-AC] Comments: The desk top touch-up spray booth and the spray booth used for touching-up HUMVEES both had relatively new filters on them. 9. Fugitive Emissions Opacity Standard. In order to provide reasonable assurance the panel filter systems are adequately controlling emissions of unconfined particulate matter, visible emissions from the paint spray booths shall not exceed 5 percent opacity. Exceedance of the 5% limit shall not be considered a violation in and of itself, but an indication that additional control precautions and/or practices may be necessary. [Rule 62-4.070(3), F.A.C.; Permit No. 1030447-001-AC] Comments: There was no painting activity going on at the time of my inspection, therefore I did not perform a Method 9, VE. RECORDKEEPING AND COMPLIANCE DOCUMENTATION REQUIREMENTS 11. Facility-Wide. A recordkeeping log shall be maintained to document compliance with Specific Condition No. 4. At a minimum, the log shall identify and quantify each paint, coating, thinner, solvent, and other material used in the electronic-communications-equipment-manufacturing operations, including all solvent metal cleaning, that contain VOCs and/or HAPs. Documentation of solvents consumed from activities such as paint gun/hose cleanup may use a mass-balance method to determine usage (amount used minus amount collected for disposal or recycle). The permittee shall record and calculate, at a minimum, the following: (a) Monthly (log by the 21st operating day of the next month) 1. Facility Name, Month/Day/Year, Facility ID No. (1030447) and E.U. ID No. 2. Monthly usage of each paint, coating, thinner, solvent, and other material which contain VOCs and/or HAPs (gallons) 3. Density (lbs/gal) and VOC and HAP content (wt %) of each item in 11(a)2 4. Monthly total HAP and individual HAP emissions (lbs or tons) 5. Monthly total VOC emissions (lbs or tons) 6. Total VOC, total HAP, and individual HAP emissions (tons) for the most recent consecutive 12-month period (b) If the HAP emissions for the most recent consecutive 12-month period exceed 80% of the major-source thresholds (i.e., exceed 20.0 tons for total HAP, 8.0 tons for individual HAP), the records required in Condition 10(a)1 – 6, above, shall be kept on a daily basis. The permittee shall use this information to ensure that the HAP emissions for the upcoming, consecutive 12-month period does not exceed permit limitations. Should HAP emissions for the consecutive, 12-month period fall below 80% of the major-source thresholds, the recordkeeping shall revert to monthly. (c) Record the date of paint spray booth filter change-outs. [Rule 62-4.070(3), F.A.C.; Permit No. 1030447-001-AC] Comments: The facility was in compliance with (a), (b) and (c) above. See sample logs attached. 13. Documentation. Supporting documentation (MSD Sheets, purchase orders, U. S. EPA "VOC DATA SHEETS”, etc.) shall be kept for each paint, coating, thinner, solvent and other material used in the painting and coating operations which includes sufficient information to determine VOC and HAP emissions. These records shall be retained on file at the facility for at least five (5) years and shall be made available to the local, state, or federal air pollution agency upon request. [Rule 62-4.070(3), F.A.C.; Permit No. 1030447-001-AC] Comments: The facility has the supporting documentation in binders, including MSDS’ for all the chemicals used at Raytheon. ANNUAL OPERATING REPORT (AOR) 14. AOR. Submit to the Air Compliance Sections of this office and the PCDEM (unless otherwise directed by the Department) for this facility, each calendar year and on or before March 1, an annual operating report [DEP Form 62-210.900(5)] for the preceding calendar year pursuant to Rule 62-210.370(3), F.A.C. The AOR shall include emissions from activities that are “exempt” from permitting, in order to demonstrate continued compliance that this facility is a synthetic Non-tile V source. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 2007 was submitted on February 20th, 2008. Operation Permit Renewal 15. Renewal of Operation Permit. A completed application to renew this operation permit shall be submitted to the Air Program of the Southwest District Office of the Department [with a copy to the PCDEM] no later than 60 days prior to the expiration date of this permit…. Comments: I read the permit condition to Mr. Milak. |
|  |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units.) Yes No Comments: There were no changes to what the facility is operating versus the description. |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical S Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no chemical substitutions or equipment changes, per Mr. Milak, and none that I could see. Emissions have diminished as the result of reduced production. |
| Closing Conference: I informed Mr. Milak that Raytheon was in compliance with applicable rules and permit conditions. |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: December 16, 2008 |
| ACCESS? | ( | EASIIR? | ( |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030447 001 66731.doc